## Slide 1: From geometries, advanced beam sources to multi-dimensional actors Current developments employing the new OpenGATE at the Medical University of Vienna
H. Fuchs
Department of Radiation Oncology, Medical University of Vienna

## Slide 2: Complex geometries
New OpenGate10
Many geometries out of the box
  Box, sphere, advanced trapezoids..
  Even images (CT, mhd)
You can even add/subtract volumes
What else is needed?
  You might get any shape
  It could be a lengthy way

## Slide 3: Complex geometries II
This object can be constructed using boolean operations
  But why?
Most complex objects to simulate exist as computer aided design (CAD) files
Standard Triangle Language (STL)
  Objects described with multiple triangles
  Standard exchange format
  For 3D printers, Inventor, AutoCAD etc
Read STL files directly with OpenGATE

## Slide 4: Complex geometries III
New geometry object „Tesselated“
  Reads STL files
  No material -> must be defined
  Works like the other geometries
A similar thing exists in Gate v9
Documentation available, example test067_stl_volume
Question
  STL is designed for a single component
  Multiple components including materials in a STEP file
  Is there interest?

## Slide 5: Advanced phase space source I
Employ phase space files
  Store all particles going through a volume
  Initial particles and secondaries as well
  Data is stored in root files
Use these for your simulation
Previous (Gate v9) phase space source lacked features
Extended phase space source “PhaseSpaceSource”

## Slide 6: Advanced phase space source II
Allows rotation/translation of source
Simulate the correct number of primary particles
  PDGCode
  Energy threshold
  Other particles simulated, but not counted in number of particles to simulate
Multi-threaded
Starting index can be supplied “entry_start”
Documentation available, example test019 and test060

## Slide 7: treatmentPlanPhsSource
You want to simulate an iontherapy treatment plan?
  Use ionbeamtherapy package in the contrib folder
    Can read treatment plans (Thx to MedAustron team)
  Needs a beam modell
  Works perfectly
What if you want to be more realistic?
  Modell your nozzle
What if
  it is confidential or
  you want to modell a secondary energy spectra?

## Slide 8: treatmentPlanPhsSource II
Employ phase space files
  Store all particles going through a volume
  Initial particles and secondaries as well
  Data is stored in root files
Create a phase space file for every monoenergetic energy
Use these to simulate your treatment plan
Compatible with iontherapy package “treatmentPlanPhsSource”
  Same options
  Plus all features of phase space source
Documentation available, example test060

## Slide 9: Multidimension images: Motivation
Biological effects actor development
  Lineal energy seems to be an interesting approach
Direct simulation of lineal energy not feasible
  AMDM
  Using tabulated values
  2 parameters per voxel in 11 bins
Currently under development
Output data
  3 physical dimensions
  Plus two vector dimensions or 3 dimensions
Parisi et al. J. Appl. Clin. Med. Phys. 2023 (24)

## Slide 10: Multidimensional images
An image is a multi-dimensional array
  plus some additional information (Offset, resolution etc.)
  Typical 1D, 2D, 3D
  Implemented in OpenGate using ITK
  Used for
    Output: e.g. dose actor (MetaImage .mhd)
    Input: e.g. image volume
A 1D image

## Slide 11: Multidimensional images II
OpenGate uses python to control the c++ part
  Acchieved using pthon bindings e.g. pybind
Very convenient
  Slightly more complex development, but worth it
Insight Toolkit (ITK)
  available for python and c++
  Itk supports multi-dimensional images
  MetaImage format support multi-dimensional images

## Slide 12: Multidimensional images III
Insight Toolkit (ITK) supports multi-dimensional images
MetaImage format support multi-dimensional images
OpenGATE
  Images from c++ side passed to python side
Can we create a 4D image with OpenGATE?
  Not easily
  most OpenGATE image code designed for 3 dimensions
    Partial extension to 4 dimensions
Can we create a 3D image with multiple histograms (e.g. vectors) or more dimesions?
  Well, not easily

## Slide 13: Multidimensional images IV
The python module of ITK is compiled from c++
  The c++ code allows almost unlimited-dimensional images
    Images as well as VectorImage for histograms etc.
  To save space, not all possibilities from c++ are available
    E.g. not all ITK pyhton wrappers are compiled
In ITK make file (to create the python module)
  Per default only image dimensions 1-3 as well as vector dimensions 1-3 are availabe
  No 4D image
  No 3D image containing as third dimension 4 histograms

## Slide 14: Multidimensional images V
Try opening a 4D image or a 4D vector image using ITK an python

## Slide 15: Multidimensional images VI
A solution
  Compile ITK manually
  Set the cmake option
    ITK_WRAP_VECTOR_COMPONENTS 2;3;4;5;6;7;8;9;10;11 ITK_WRAP_IMAGE_DIMS 2;3;4
But, your code would only run on your machine…
Currently no easy solution
  Try not to use such images on the python side
  Only in the c++ core of OpenGate

## Slide 16: Summary & Outlook
New python based OpenGATE is cool
STL capabilites from Gate v9 now in OpenGATE
Advanced phase space and treatement plan options
Combination of Python and c++
  Powerful
  Challenging for more exotic cases