## Slide 1: The innovative Super-Fine Grained Detector (Super-FGD) for T2K and its front-end electronics
NGUYEN Quoc Viet
Laboratoire Leprince-Ringuet
IRN 2024 - LLR - Ecole polytechnique

## Slide 2: T2K experiment
By changing the direction of magnetic field in the horns, we are able to create whether neutrino beam or anti-neutrino beam later.
T2K (Tokai to Kamioka) is a long-baseline neutrino oscillation experiment in Japan
NGUYEN Quoc Viet
My talk will focus on this
See Claudio’s talk for more

## Slide 3: Road to cp violation discovery
For T2K oscillation analysis 2022: over a total systematic uncertainty of 5.2% ( appearance in neutrino mode), mainly comes from neutrino interaction processes.
Today, statistic is dominant, but this will become a problem soon.
NGUYEN Quoc Viet
To be ready for Hyper Kamiokande era, we started the second phase of T2K which contains Near detector upgrade: better constrain -nucleus interactions and hence improve systematic uncertainties

## Slide 4: T2K experiment: former Near detector (ND280)
Near detector ND280 is designed to constrain the neutrino fluxcross-section
The tracker includes 2 Fine Grained Detectors (FGD) and 3 Time Projection Chambers (TPC) => measure the momentum of charged particles and particle identification.
ND280 configuration
QE event at ND280 under magnetic field
QE-like sample at ND280
NGUYEN Quoc Viet

## Slide 5: Former ND280 limitations
The polar angle acceptances are not comparable between near and far detector
The proton detection threshold is high
Only muon kinematics are used to reconstruct neutrino energy
ND280 acceptance
SK acceptance
Proton detection efficiency
Arbitrary unit
Put the ccqe Enu reconstruction plot
NGUYEN Quoc Viet

## Slide 6
Upgraded near detector ND280: configuration
2 new High Angle TPC (HA-TPC) (see Ulysse 先生 talk right after me)
New Time Of Flight detector (TOF)
1 Super-fine-grained-detector (super-FGD) => the target of the near detector where the LLR is involved
NGUYEN Quoc Viet

## Slide 7
Super FGD detector
Super-FGD: 182 × 192 × 56 scintillator cubes (2 million) with 3D readout => 2 tons of fully active target
Wavelength shifting (WLS) fibers are used to collect light from scintillator cubes. (70 km of WLS fiber in total)
One end of the fibers is connected to a Multi-Pixel Photon Counter (MPPC) the other end is mirrored. => around 60.000 channels.
1 1 1
NGUYEN Quoc Viet

## Slide 8
Super FGD assembly at J-parc (early 2023)
The cubes were shipped from Russia to Japan by plane
The Super-FGD box which carry all the cubes
NGUYEN Quoc Viet

## Slide 9
Super FGD assembly at J-parc (early 2023)
Insert the fishing lines
Insert the 2 million cubes in the Super-FGD box layer by layer
After closing the Super-FGD box, the fishing lines will be replaced by the wavelength shifting fibers
NGUYEN Quoc Viet

## Slide 10
64 channels
Front-End Board (FEB)
256 channels
X4 MPPC => 1 FEB
Super FGD detector readout

## Slide 11: Front-end board (FEB)
Front-End Board (FEB) 256 channels
The FEB is the heart of the electronic system and it’s the joined LLR + Uni Geneva project.
Each CITIROC (Cherenkov Imaging Telescope Integrated Read Out Chip) can read 32 channels
  8 CITIROC <=> 256 channels for 1 FEB.
For each channel, the input is handled by two independent signal paths:
  Low gain (LG) path
  High gain (HG) path
Signal to each channel
AMPLITUDE
TIME
LOW GAIN (LG)
HIGH GAIN (HG)
Rising edge
Falling edge
The baseline design is structured around the CITIROC readout chip.
NGUYEN Quoc Viet

## Slide 12: Overview of super-fgd electronic system
SFGD electronic
There are 16 crates in total, each mainly contains
  14 Front-End Board (FEBs)
  1 Optical Concentrator Board (OCB)
  1 backplane
NGUYEN Quoc Viet

## Slide 13: Relationship between boards
In document: the FEB is the heart of the electronic system.
In reality:
MCB: the OCB advisor
OCB: the master
FEBs: the slaves
Backplane: the whip
NGUYEN Quoc Viet

## Slide 14: MIB & FEB functional test University of Geneva
Léna Osu
Andrés Muñoz
Me
NGUYEN Quoc Viet

## Slide 15: MIB functional test (March 2023)
The set up for test
Testing ongoing
Ready to be shipped to Japan
MIB
8 connectors, 32 channels each
Debug
The MIB is used to connect the cables from MPPC board to FEB.
The MIB test is to test the function of all the lines that pass through the MIB
The test includes:
  Housekeeping test: High Voltage, temperature
  Debug line test.
  Analog channels test.
NGUYEN Quoc Viet

## Slide 16: functional test for FEB (individual test)
FEB: Device under test. This set up can easily remove and install a FEB.
Functional test for individual FEB includes:
  Housekeeping and loopback
  Calibration
  All 256 channel test
Each FEB test takes 10-12min, and there were around 230 FEBs to be tested.
X
NGUYEN Quoc Viet

## Slide 17: functional test for FEB
Box containing FEBs that pass the functional test, but not ready to send to Japan
=> Need more tests
NGUYEN Quoc Viet

## Slide 18: functional test for FEB (Burning test)
NGUYEN Quoc Viet
Early idea for the set up of burning test
And if you want to better control temperature

## Slide 19: functional test for FEB (Burning test)
FEBs were set to run 24hours without cooling plates, only with fans.
After this test, FEB will be moulted to the cooling plates, then another final test.
NGUYEN Quoc Viet
Plots from Lorenzo Giannessi

## Slide 20: functional test for FEB (vertical slide test at cern)
This was the final test with the real configuration of electronic system in 1 crate
Full crate: installation with 14FEBs
Full crate slow control test
Test all the communication lines between OCB and 14FEBs
Housekeeping test for all FEBs
After these tests, FEBs are ready to be sent to Japan
NGUYEN Quoc Viet

## Slide 21
Super-FGD installation in the pit (October 2023)
The pit of near detector complex
The SFGD and its electronic system at assembly building next to the pit
The pit from above
Install
NGUYEN Quoc Viet

## Slide 22
Super-FGD preparation for installation
Space around detector has been cleared
MIBs and cables were bundled in groups in bubble wrap, for easily connect in future
NGUYEN Quoc Viet

## Slide 23
SFGD was moved from assembly point to near the pit
SFGD installation (October 2023)
NGUYEN Quoc Viet

## Slide 24
SFGD was installed in ND280 near detector basket
SFGD installation (October 2023)
NGUYEN Quoc Viet

## Slide 25
Left frame
Right frame
A few days later, ~190 FEBs (out of ~230) were inserted into 2 frames, the rest were under debugging.
SFGD electronic installation (October 2023)
NGUYEN Quoc Viet

## Slide 26
first events with upgraded Nd280 (12/2023)
First neutrino events from un upgraded beam and detected with an upgraded detector!!!
These was a missing TPC, it was installed with missing Super-FGD electronic later in April 2024
CNRS press release: https://www.in2p3.cnrs.fr/fr/cnrsinfo/lexperience-t2k-redemarre-avec-un-detecteur-proche-ameliore
Successful beam upgrade
Big milestone because……
NGUYEN Quoc Viet

## Slide 27
first events with upgraded Nd280 (12/2023)
CNRS press release: https://www.in2p3.cnrs.fr/fr/cnrsinfo/lexperience-t2k-redemarre-avec-un-detecteur-proche-ameliore
Successful beam upgrade
Big milestone because there is no more fire at JPARC
NGUYEN Quoc Viet
First neutrino events from un upgraded beam and detected with an upgraded detector!!!
These was a missing TPC, it was installed with missing Super-FGD electronic later in April 2024

## Slide 28
Left frame
After the installation, there were many things to be done:
  Got the SFGD running stably
  Slow control and calibration
  Check all channels to study gain and dead channels.
  Complete the software analysis chain
  Stability studies
Munoz-san installing electronic cables
SuperFGD is under a very active period with many people involved
After the installation
NGUYEN Quoc Viet

## Slide 29
Calibration (High Gain)
NGUYEN Quoc Viet
Many procedures for calibration have been established: baseline/threshold tunings, High Gain/ pedestal calibration, High Voltage tuning.

## Slide 30
Calibration (Low Gain)
NGUYEN Quoc Viet
Many procedures for calibration have been established: baseline/threshold tunings, High Gain/ pedestal calibration, High Voltage tuning, Low Gain calibration.
Work by L.Giannessi

## Slide 31
Stability studies
NGUYEN Quoc Viet
Since this is a recently installed detector, many aspects must be taken care of to check its running stability. Many packages are under development for online monitor: timing monitor, hit rate stability, Light yield stability, Trigger rate stability.

## Slide 32: SuperFGD full installation (March 2024)
In March 2024, SuperFGD was fully installed with all the OCB and FEB boards

## Slide 33: SuperFGD full installation
Full hit map of SuperFGD is available. Super FGD is ready for the next beam run

## Slide 34: ND280 upgrade installation complete (last week)
In 25th April 2024, Top High-angle TPC was installed
Last week, all the TOF modules were installed => Upgraded T2K near detector: Mission complete!!!

## Slide 35
Super FGD expected performance
4 coverage (isotropic)
NGUYEN Quoc Viet

## Slide 36
Super FGD expected performance
4 coverage (isotropic)
Lower proton momentum threshold (300MeV/c)
NGUYEN Quoc Viet

## Slide 37
Super FGD expected performance
4 coverage (isotropic)
Lower proton momentum threshold (300MeV/c)
Neutron kinematics reconstruction by time of flight technique (0.6 ns time resolution)
Neutron detection through time of flight technique
Neutron detection efficiency
NGUYEN Quoc Viet

## Slide 38
Super FGD expected performance
4 coverage (isotropic)
Lower proton momentum threshold (300MeV/c)
Neutron kinematics reconstruction by time of flight technique (0.6 ns time resolution)
Improved neutrino energy resolution with hadronic kinematic in addition
NGUYEN Quoc Viet

## Slide 39
Upgraded near detector ND280: performance
At ultimate statistic, dramatic reduction on the uncertainties of all systematics parameters. These systematic play important role in neutrino energy reconstruction and thus on the oscillation analysis.
Phys. Rev. D 105, 032010
NGUYEN Quoc Viet
Me
Post fit resolution w/o SFGD
Post fit resolution w SFGD
Post fit resolution w SFGD +
Post fit resolution w SFGD
Pre-fit resolution
GUNDAM fit results, the resolution is improved with SFGD and becomes amazingly good with hadronic kinematic.
2027 statistic
Total x-sec&flux systematics at few % level

## Slide 40
Summary
Upgraded ND280 helps to better measure high angle tracks, lower momentum particles, and better reconstruction of the hadronic part.
=> It is thus more sensitive to important nuclear effects for our oscillation analyses.
NGUYEN Quoc Viet
Thanks to the upgraded detector and beam, we expect to reach 3sigma sensitivity on CP conservation exclusion by 2027
The upgraded detector and beam represents the legacy from T2K to Hyper-Kamiokande that will start with a very well known and controlled near detector and neutrino flux.
The next beam run with full configuration of upgraded ND280 will be June 5th 2024.
Stay tuned for new results with upgraded ND280!
Upgraded ND280 is actively under installation and near to completion.
To be ready for the Hyper-K period, where the statistical uncertainty is reduced and the systematic uncertainty becomes dominant,
From December 2023.
  The neutrino beam power: 760kW,
  The electromagnetic horn current: from 250 kA to 320 kA
  Neutrino intensity increases by about 10%

## Slide 41
Bonus slide: Proposal for Super-FGD use
NGUYEN Quoc Viet
To train your AI: “which cube to put in a coffee?”
To make a necklace
To measure charged particles
To measure neutrinos

## Slide 42: Back up

## Slide 43: Front-end board (FEB)
Front-End Board (FEB) 256 channels
The FEB is the heart of the electronic system and it’s the joined LLR + Uni Geneva project.
Each CITIROC (Cherenkov Imaging Telescope Integrated Read Out Chip) can read 32 channels
  8 CITIROC <=> 256 channels for 1 FEB.
For each channel, the input is handled by two independent signal paths:
  Low gain (LG) path
  High gain (HG) path
NGUYEN Quoc Viet

## Slide 44: Front-end board (FEB) cooling plate production at LLR
~230 cooling plates were produced at LLR with a lot of help from SK group and Mechanic group!!
In June 2023:
NGUYEN Quoc Viet

## Slide 47
Super FGD assembly at J-parc
NGUYEN Quoc Viet
Then the cables were attached on the MPPC64 boards and arranged.
Lena working on arranging the cables.
Move before 24

## Slide 48: MIB functional test
The MIB is used to connect the cables from MPPC board to FEB.
The MIB test (March/2023 Geneva for 224 MIB) is to test the function of all the lines that pass through the MIB
The test includes:
  Housekeeping test: High Voltage, temperature
  Debug line test.
  Analog channels test.
MIB
FEB
8 connectors, 32 channels each
Debug

## Slide 49: Next functional test for FEB
GPIO: auxiliary board that allow us to use the FEB without a backplane. It has ADCs that provide a reference for calibration
Kaladin (SOKENDAI): demultiplexer board that allows injecting signal in each channel individually with a single input signal. Controlled by the GPIO
FEB: Device under test. This set up can easily remove and install a FEB.
Functional test includes:
  Housekeeping and loopback
    Test all the backplane lines: SYNC, trigger, busy
    Test debug connector lines
    Housekeeping (HK) values (currents, temperature, voltage)
  Calibration
    Produce calibration parameters to be passed to DAQ
  All 256 channel test
    Short test of each channel
    Check ADC distribution in each channel
    Citiroc triggers, baseline, noise.

## Slide 50: T2K statistic
NGUYEN Quoc Viet

## Slide 51: T2K experiment: Current results
4 main oscillation channels in T2K: disappearance (dominated by ) and appearance (dominated by and mass hierarchy) and similar two for anti-neutrino.
Data point around the maximum CP-violating value of
A wide region of space is excluded at 3 C.L.
The constraints for appearance are still dominated by the statistical uncertainty
NGUYEN Quoc Viet

## Slide 52: High Angle Time Projection Chamber (HA-TPC)
Test beam was high energy electron beam (1-5GeV), short chamber (15 cm drift distance)
Scan in in the detector plane and along drift distance
Scan in angle: 0, 20, 30, 45, 60, 80 degree MicroMegas rotation
Resistive MicroMegas.
Bulk MicroMegas.
Cern-2022 with micro megas
NGUYEN Quoc Viet
Two new HA-TPCs
  Dimensions: 1.865 x 2.0 x 0.82 m
  Track reconstruction in 3D, PID by measuring momentum and deposited charge
Main differences with current ND280 TPC
  High-Angle TPC contains a new type of detector which is the Resistive MicroMegas (ERAM modules) with better spatial resolution.
Charged particle

## Slide 53
Six TOF planes will cover 2 HA-TPCs and SuperFGD.
Each plane of 2.2 × 2.4 m consists of 20 scintillator bars.
Both ends readout by 8 MPPCs on each end of each bar.
Precise timing measurement for particles as they traverse the TOF modules (resolution of 150 ps during commissioning at CERN).
Determine the track direction and minimise background
It is used as the cosmic trigger to calibrate SuperFGD and HA-TPCs
NGUYEN Quoc Viet
TIME OF FLIGHT DETECTOR (TOF)

## Slide 54: Neutrino-nucleus interaction: Nuclear effects
Final State Interactions (FSI): Particles in the final state re-interact before going out of the nucleus.
Fermi motion: Contribute to the energy transfer in the interaction
No nuclear effects
A nucleon strongly correlates with another nucleon. => one additional nucleon in the final state and changes the interaction topology.
NGUYEN Quoc Viet

## Slide 55: Neutrino-nucleus interaction
Neutrino energy reconstruction is based on the Charge Current Quasi-Elastic (CCQE) kinematics
=> only lepton kinematics
Only single ring is selected at SK. Unfortunately, sometime the hadronic part is below Cherenkov threshold and hence not reconstructed. These modes could mimic CCQE events. => ND280 need to carefully model the QE and the non-QE interactions
These modes also contribute to reconstructed quasi-elastic events
The nuclear effects can change the final state topology and kinematic => Bias in neutrino energy reconstruction.
NGUYEN Quoc Viet

## Slide 56: T2K experiment
T2K is the first experiment to report evidence for the neutrino appearance oscillation () in 2013 (Phys. Rev. Lett:12:061802, 2014.)
The current goal of T2K is searching for the CP violation in the lepton sector by comparing the appearance probabilities of neutrino and antineutrinos. (T2K can produce either neutrino or anti-neutrino beam). => First hint of CP violation at 3sigma CL in 2020 (Nature 580, 339-344 (2020))
By changing the direction of magnetic field in the horns, we are able to create whether neutrino beam or anti-neutrino beam later.
NGUYEN Quoc Viet

## Slide 57: T2K experiment: beam
An intense muon neutrino beam is sent through 295~km from Tokai to Kamioka, produced by high-intensity accelerated proton beam produced by the J-PARC beamline
T2K uses the off-axis beam technique => the flux is narrower at 0.6 GeV which is sensitive to the first oscillation maximum with the 295Km baseline.
Since the flux peaks at 0.6 GeV, the Quasi-Elastic (QE) is the dominant interaction.
J-PARC
NGUYEN Quoc Viet

## Slide 58: Function of different boards
LVDS
The primary function of the Optical Concentrator Board (OCB) in the sFGD electronics system is to move and organise digital data and commands.
The DAQ and slow control systems are connected to 14 FEBs in a sFGD crate via the OCB.
Moreover, OCB functions as a link between the MCB and the 14 FEBs.
Backplane: Point-to-point and multi-drop signals that transit via the backplane make up the FEB - OCB communication.
MCB is used to send digital signals such as the clock, SYNC (GTS, gate, event number), trigger.

## Slide 59
Super FGD production and pre-assembly
NGUYEN Quoc Viet
The production of the 2 million cubes was done by Uniplast (Vladimir, Russia), with a rate of ~100,000 cubes/month, and took over 1.5 years
After quality checks, all the cubes were assembled layer by layer using fishing lines before delivering.

## Slide 60
Super FGD assembly at J-parc
NGUYEN Quoc Viet
Attach MPPC boards on the sides of the box
Install LED calibration system
Install light barriers
How to read the light, LLR activity to do electronic from here. Move electronic after here