## Slide 1
Signal formation in Vertical Drift
Supervisors :
J. COLLOT – LPSC Grenoble
L. ZAMBELLI – LAPP Annecy
D. DUCHESNEAU – LAPP Annecy
DUNE France - Analysis workshop

## Slide 2: Vertical drift design
  2 volumes split by a cathode
    Electric drift field:
  X-ARAPUCA* for light detection on the cathode
  The new perforated anode technology
    Stack of 2 perforated Printed Circuit Boards (PCB)
    Etched copper electrode strips on each PCB face
    A sub-centimeter spatial resolution
    Module called Charge-Readout Planes (CRP) ~ 3x3 m
  DUNE Far detector at SURF:
    80 module CRPs for each top and bottom TPC
    Half will be produced at Grenoble
Diagram by L. Zambelli
* Light detector device
Notes: I don’t think is necessary to go into detail on this slide here but just as a reminder

## Slide 3: The perforated anode technology
Collection : +1000V
Induction2 : 0V
Induction1 : -500V
Shield : -1500V
Shield + 3 different charge readout layers:
  Induction 1 (view 0) – strip orientation -30° wrt beam axis
  Induction 2 (view 1) – strip orientation +30° wrt beam axis
  Collection (view 2) – strip orientation 90° wrt beam axis
  Induction views: Bipolar signals
  Collection view: Unipolar signal
Signal before convolution
Notes: As a reminder we have 3 different charge readout layers called :
Each layer has its own strips with different orientation which are necessary to know the position of the deposited energy on the detector
We can see on the right, a spoiler of my result from my simulation for the three views. We can see 2 bipolar signals for the induction because the collected charge is equal to 0 and an unipolar signal on the collection view.

## Slide 4: Signal formation study on anodes
Problematic:
  Use of new anode technology
  Important to know the deposited energy in the detector to measure the neutrino oscillation parameters
  Important to reconstruct the particle tracks from collected charge
CRP assembly at CERN
My work:
  Understanding the waveforms based on energy, track angle and position
  Understanding the charge lost in the anodes
  Estimate the different systematics
Study of induced signal formation on the anode
Notes: To solve these problems,

## Slide 5: Modeling signal formation
Superposition principle
Shockley-Ramo theorem:
Weighting Field is virtual field defined when the reading strip equal 1 V and all others fixed to 0 V
: geometry factor
: physics factor
Drift velocity:
The instantaneous current is induced by charge motion only
Need simulation for complex geometry
https://lar.bnl.gov/properties/trans.html
Notes: To simulate the signal formation on the strips, we usually use the famous Shockley-Ramo theorem. This theorem become directly from the Maxwell equation

## Slide 6: Induced signal simulation
CRP geometry
Hexagonal pattern
Strip dimensions
Design of a simulation on Python

## Slide 7: Induced signal simulation
CRP geometry
Hexagonal pattern
Strip dimensions
Numerical simulation on Python
Implement CRP geometry hexagonal pattern, width strips, 2 Printed Circuit Boards, 4 equipotential planes
Shield: -1 500 V
Induction 1: -500 V
Induction 2: 0 V
Collection: 1 000 V
Collection Strip
Induction strip
Step used:
Induction strip

## Slide 8: Induced signal simulation
Field calculation
Drift Field
Weighting Field
Induction 2
Collection
Bin files generation
CRP geometry
Hexagonal pattern
Strip dimensions
Induction 1
Specific geometry setting up
Solving Laplace’s equation in 3D:
3D Finite element method (FEM):
Induced signal on the readout strips:
Iterative method, step by step
Weighting field
Drift Velocity Field:
Design of a simulation on Python
Run Time: ~ 30 mins
Step used:
Run Time: ~ 2h30

## Slide 9: Field results
2D projection of drift field lines and weighting equipotential
  Induced signal in the nearby strips
Weighting Potential
Shield
Induction 1
Induction 2
Collection
FR4
Ar

## Slide 10: Induced signal simulation
Field calculation
Drift field
Weighting field
Induction 2
Collection
Bin files generation
Ionization electron
Drift velocity
Trajectory simulation
CRP geometry
Hexagonal pattern
Strip dimensions
Induced signal
Induction 1
Specific geometry setting up
Field generation with CRP geometry
kV/cm
Design of a simulation on Python

## Slide 11: Ionization electron generation
Runge Kunta like simulation
Thermal electron
  Trajectory follow drift field lines
Electron trajectories passing through a CRP’s hole
Grid of the mesh used for the field calculation
The electron trajectory is perfectly defined
Drift simulation 5 mm
Drift
e
Shield
Induction 1
Induction 2
Collection
3D linear interp

## Slide 12: Electron cloud simulation
Shield
Induction 1
Induction 2
Collection

## Slide 13: Electron cloud simulation
Border effect near to the collection electrode
The field takes dependancy which will induce a high frequency signal
Electronic response will smooth the readout induced current
Shield
Induction 1
Induction 2
Collection

## Slide 14: Data extraction
Coldbox’s data cuts
  Tracks with reconstructed angle
  in the cone with from the strip readout
  Track lengths
Event Display
Data reconstruction with LARDON (software developed by L. Zambelli)
Select horizontal track to compare with simulation
Bipolar signals induction view
Muon events
An example of cosmic ray track from the Coldbox
Reconstructed zenithal angle distribution

## Slide 15: Comparison data VS simulation
Aligned with the max
Aligned with the center
Aligned with the center
Simulated waveforms in agreement with data
Mean waveform
  Signals summation on each readout channel
     To reduce the incoherent noice
  Mean signal calculation for each track
ADC
time

## Slide 16: CRP transparency study
Using two PCB can lead to loss of total CRP transparency:
  Some electrons are collected by the induction 1 plane
  Collected charge decreases
The simulation has shown a significative effect between two bias configurations used in the coldbox tests:
  Config 1:
  Config 2:
Work on signal amplitude to explore the different causes of charge loss
Dependency on the bias voltage used

## Slide 17: CRP transparency study
Coldbox’s data with same configuration:
  dE/dx measured for muons
  Comparison of the energy reconstruction
Result:
  Increase of 6 % reconstructed energy for the “config -450 V”
  A real effect but smaller than the simulation result
Difference Simulation/Measurements need to be understood
New measurements will be taken on the 50 L TPC (R&D)
50 L TPC at CERN
active area
52 cm drift
Cosmic and Bi207 sources
Notes: Why new ? We’ve already had data from this one but unfortunately, there were few cosmic events and some problems with the adapter boards.
For those who don’t know the 50 L TPC is a small TPC for the R&D at CERN.
It has the advantage of low sensibility to the space charge effect and to have more drift than the coldbox.

## Slide 18: CRP 6 data explanation
Problem: no charge lost in the simulation and no “charging-up” effect
Luis’ work*
* Photo analysis for QA/QC of CRP anodes – Luis Manzanillas
** https://indico.fnal.gov/event/64225/contributions/288494/attachments/176651/240155/cb_crp6_iii_first_look.pdf
Laura’s work**
Effective hole diameter modified
PCB shifted between shielding and view 0
Probably glue inside the holes
Consequences: charge lost
Draw a pattern along the induction strips
An effect that would seem to be a “charging-up”

## Slide 19: Holes covering and loss charge
Focalization of drift field lines in the CRP hole
Shield
Induction 1
Induction 2
Collection
Induction 2
Collection
Field line too focused to explain the loss of charge  Electron diffusion

## Slide 20: Electron diffusion
Fick’s equation
Transverse electron diffusion could cause a loss of charge in the CRP
Average diffusion length given by:
Gaussian spatial distribution of the electrons over time
e
Electron loss on view 0 due to the diffusion
Longitudinal and transverse diffusion coefficient:
(Einstein’s relation)
For next: only transverse diffusion is used (work in progress)
longitudinal effective electron energy
electron mobility
Come in
Come out

## Slide 21: Transverse electron diffusion only
Shield
Induction 1
Induction 2
Collection
*
* https://lar.bnl.gov/properties/trans.html

## Slide 22: Field with hole shifted
Covering area : 52 %
Zoom
Work in progress
Covering exact area given by:
with , shifting,
FR4
Ar

## Slide 23: CRP6 transparency (simulation)
Work in progress
Increased charge loss
Charging-up effect can be explain that if the electrons are captured by the FR4.
i.e. shifting > 0.5 mm
But Luis has measured a shifting max ~ 0.35 mm
Even with diffusion: electron dispersion through a hole is insufficient
too focused to explain charging-up  Electron diffusion
 Have to implement the dielectric constant for the FR4
FR4
Ar
Notes: Perhaps explain that for a PCB shifting greater than 0.5 mm. However, Luis has shown that the holes shifting is equal to 0.35 mm for the maximum on the CRP6

## Slide 24: Summary
Work done:
  Numerical simulation conception to understand the formation of induction signals of all views
  Coldbox’s data extraction  simulation is good agreement with this
What’s next ?
  Keep working on the electron diffusion and the impact on the loss charge
    Same study with longitudinal diffusion
    Implement the drift field dependance  ,
  Implement the dielectric matrix to discriminate the change of medium (FR4 into Ar and vice versa)
    Solving Generalized Poisson’s equation in 3D: (no source)
  Extend the simulation in a bigger volume  track angle studies and position in the TPC (boundary conditions)