## Slide 1
Time Projection Chambers for Nuclear Fission Experiments
Malia Mehdi – 1st year PhD Student
Supervised by Matthieu Lebois & Gabriel Charles
Nuclear Pole - IJCLab

## Slide 2: Content
Introduction to the Physics Case and Experimental Features
Fission Event Reconstruction Arsenal
Ongoing Project: ICETEA
Outlook and Perspectives

## Slide 3: Content
Introduction to the Physics Case and Experimental Features
Fission Event Reconstruction Arsenal
Ongoing Project: ICETEA
Outlook and Perspectives

## Slide 4: Nuclear Fission
~160-180MeV kinetic energy shared between the 2 fragments
Mass 90 < A < 160 amu , High charge Z+, 28 < Z < 64
V.Piau, PhD thesis 2022

## Slide 5: Experimental Features
Tagging the fission events/ Kinematics of the fission fragments
  Ionization chamber: Twin Frisch-Grid ionization chamber
Measuring 𝛾 rays
  Spectroscopy/Counting with scintillators: HPGe, La(Ce)Br3,PARIS arrays (LaBr3+NaI phoswiches)
Measuring neutrons
  Counting ( neutron counters), spectroscopy with liquid scintillators

## Slide 6: Experimental Features
Tagging the fission events/ Kinematics of the fission fragments
  Mass identification from total kinetic energy-> Energy resolution (675keV<-> ~0.54 amu)
  Angle of emission
  Charge identification Z (ideally 1 charge unit)
  Timing resolution <1ns to establish correlations with gamma-ray measurements
Z+
Z’+

## Slide 7: Content
Introduction to the Physics Case and Experimental Features
Fission Event Reconstruction Arsenal
Ongoing Project: ICETEA
Outlook and Perspectives

## Slide 8: Twin Frisch-Grid ionization Chamber
Tagging the fission events/ Kinematics of the fission fragments
  Position sensitive Ionization Chamber:
    Fission tag ~ 3ns
    Mass identification of the fragments ~ 3amu
    CH4 timing resolution < 1ns (electrons)
    Kinematics
JRC Geel
V.Piau, PhD thesis 2022

## Slide 9: Twin Frisch-Grid ionization Chamber
A.Francheteau, PhD thesis (2023)
S.Marin et al. (2022)
L.Gaudefroy et al. (2017)
CEA DAM

## Slide 10: Twin Frisch-Grid ionization Chamber
Tagging the fission events/ Kinematics of the fission fragments
  Position sensitive Ionization Chamber:
    Fission tag ~ ?ns
    Energy resolution ~675keV
    Mass identification of the fragments ~ 0.54amu
    Ar+CH4 P =0.5bar, timing resolution~ 1ns
    Kinematics
A.Francheteau, PhD thesis 2023
L.Gaudefroy et al. (2017)

## Slide 11: Required Performances
Existing chamber
Fission tag ~ 4ns (ionic signal)
Mass identification of the fragments ~ 3amu
Poor angular reconstruction
What we need
Fission tag <1ns
Mass identification of the fragments <1amu<600keV
Proper angular reconstruction
Deduce the charge of the fission fragment
Compactness
New technology?

## Slide 12: Content
Introduction to the Physics Case and Experimental Features
Fission Event Reconstruction Arsenal
Ongoing Project: ICETEA
Outlook and Perspectives

## Slide 13: ICETEA - Ionization Chamber with Enhanced Timing and Energy resolution without Amplification
Gaseous ionisation chamber with included wire chamber
Tracking and calorimetery for charged particles
Expected timing resolution < 1ns
Expected Energy resolution < 600keV
Prototype to be built in 2024 – Launching mid-September
Tests with 3-⍺ source
Wire chamber
Source/Target
Energy plane: total charge collection anode plane
CH4
CH4
CH4
CH4
Readout/Electronics
?
M. Lebois, G. Charles, K. Pressard, M. Mehdi
Our alternative solution!
Frisch-Grid

## Slide 14: Content
Introduction to the Physics Case and Experimental Features
Fission Event Reconstruction Arsenal
Ongoing Project: ICETEA
Outlook and Perspectives

## Slide 15: Next Step
Development of a prototype of ICETEA by December 2024-January 2025
Commissioning of the prototype and performing new measurements on different fissionning systems (252Cf, 248Cm etc…)~Early 2025
Can we do better?