## Slide 1: Linear Polarization Analysis With Fast Beam Data
Peter Farris
4th AGATA-GRETINA/GRETA Tracking Arrays Collaboration Meeting

## Slide 2: Outline
Using Tracking Arrays as Compton Polarimeters
Attempting Linear Polarization Analysis With Fast Beam Data
A Confounding Correlation from Fast Beam Data
Accounting for the Correlation
Summary & Outlook
Courtesy of Shumpei Noji (FRIB)
12 GRETINA Quads

## Slide 3: Tracking Arrays are Powerful Compton Polarimeters
[1] Adapted from B. Alikhani, et al. Compton polarimetry with a 36-fold segmented HPGe-detector of the AGATA-type. Nucl. Instrum. Methods in Phys. Res. A, Volume 675 (2012)
[2] C. Morse, et al. The polarization sensitivity of GRETINA. Nucl. Instrum. Methods in Phys. Res. A, Volume 1025 (2022)
1
2
The first two interaction points determine the Compton scattering plane
The distribution of the Compton scattering plane orientations probes the asymmetry from linearly polarized gamma rays
Asymmetry is proportional to the amplitude in the azimuthal scattering angle distribution
Notes: Also using GRETINA’s segmentation, for every gamma ray event it gives us a collection of interaction point energies and positions as it scatters through the crystal
This makes GRETINA capable of polarimetry
This is because Compton scattering is sensitive to gamma ray polarization as we know from the klein-nishina formula
Specifically Linear Polarized gamma rays prefer to scatter perpendicularly to the polarization plane, resulting in an asymmetry in the azimuthal Compton scattering angle
And we can measure this asymmetry by finding the angle between the Compton scattering plane and a reference plane
That’s what this angle xi is here, it’s there difference between our two planes
The reference plane we use is the reaction plane which is defined by the beam direction and outgoing gamma ray
From Klein-Nishina, we know that the distribution of xi will follow a cosine for polarized gamma rays and we can see this here
These are results from a paper by Chris Morse from an p p’ experiment on Mg24 done at Argonne National Lab
The bottom panel is showing that ratio of these two curves here at the top, this one is a xi distribution for a magnesium transition, and this is from an unpolarized source
The key observable then is the amplitude of this distribution A0 which tells you the asymmetry
It tells you how much more scattering you see between your parallel and perpendicular scattering directions
here we’re seeing more in the perpendicular scattering than parallel scattering relative to the reaction plane
The magnitude of the asymmetry is proportional the amount of polarization you have while
The sign of the asymmetry distinguishes between E and M type radiation, so since this is an E type for M we would expect the inverse distribution

## Slide 4: Our Approach to Choosing Interaction Point Order
The Main Interaction assumption takes the highest energy deposition interaction point as the first
This assumption does well identifying the first interaction point, performing better than some conventional tracking algorithms
We extend this idea and choose the second highest energy deposition as our second interaction point
We only consider interaction points within a single crystal
Main Interaction
Tracking
[3] D. Weisshaar, et al. The performance of the γ-ray tracking array GRETINA for γ-ray spectroscopy with fast beams of rare isotopes, Nucl. Instrum. Methods in Phys. Res. A, Volume 847, (2017)
Energy [keV]
Counts / 1keV
Events where Main Int. and Tracking differ

## Slide 5: Polarization With Fast Beams
64Fe
Energy [keV]
keV / bin
3 FWHM
[2] C. Morse, et al. The polarization sensitivity of GRETINA. Nucl. Instrum. Methods in Phys. Res. A, Volume 1025 (2022)
Counts / deg
Normalized Counts / deg
3 FWHM gate
Counts / deg
Normalized Counts / deg
1 FWHM gate

## Slide 6: Azimuthal Scattering Angle and Doppler Corrected Energy Correlation
From the last slide, we saw fast beams we obtain a distribution that looks like there’s an asymmetry
64Fe
Energy [keV]
Gamma rays emitted from fast beams show a correlation between and
Gate
[rad]
[rad]
Normalized Counts / deg
Notes: Now lets do polarization with fast beams
On the right here, the Berkley group did a p p’ experiment so their gammas were coming from the target, but we’re looking at gamma rays from the beam
You can see that the resulting xi distribution that we get from fast beams look a lot like this one
If we look closer however, this has nothing to do with polarization but a correlation between Doppler reconstructed energy, plotted here on the y axis, and xi plotted here on the x axis
You can see a clear correlation between the reconstructed energy and xi in these halos that are most prominent in the parallel angles
So if I do an energy gate to look at events in the full energy peak, we cut out more events around the parallel directions than the perpendicular
Creating a bias in our xi distribution that mimics the distribution we’re looking for
This correlation is comes from the fact that we need the first interaction point to do both the Doppler reconstruction and calculate xi
So if we get the first interaction point wrong, there is going to be an unphysical correlation between them

## Slide 7: Energy Gate Widths Affect Distribution
Energy [keV]
keV / bin
64Fe
Chart: Gate Width [FWHM]
| 1 | 2 | 3 | 4 | 5 | 6
Main Interaction | 0.065193 | 0.04262 | 0.029653 | 0.017329 | 0.0090314 | 0.00055234
Normalized Counts / 20 deg
[rad]
Simulated FEP events
Unpolarized
Perfect tracking
Normalized Counts / 20 deg
[rad]

## Slide 8: Fast Beams Remove Independence Between and
A good calculation requires identifying the first two interaction points
A good determination of (for Doppler reconstructed energy ) requires correctly identifying the first interaction point
Thus, in fast beam data the two observables and are no longer necessarily independent
Depends on correct first two interaction points
1
1
2
Depends on correct first interaction point
[1] Adapted from B. Alikhani, et al. Compton polarimetry with a 36-fold segmented HPGe-detector of the AGATA-type. Nucl. Instrum. Methods in Phys. Res. A, Volume 675 (2012)
[4] Adapted from S. Paschalis, et al. The performance of the Gamma-Ray Energy Tracking In-beam Nuclear Array GRETINA, Nucl. Instrum. Methods in Phys. Res. A, Volume 709, (2013)

## Slide 9: Induced Correlation: Perpendicular Case
No Doppler penalty for choosing bad first point
Consider the simple case of two interaction points A and B
The cone shows all points that give the same emission angle and therefore Doppler reconstruct to same energy
When points A and B give the same , the Compton scattering plane by construction is perpendicular to both possible reaction planes
Even if first point misidentified, perpendicular scattering events tend toward photopeak center

## Slide 10: Induced Correlation: Parallel Case
Max Doppler penalty for choosing bad first point
Consider the simple case of two interaction points A and B
The cone shows all points that give the same emission angle and therefore Doppler reconstruct to same energy
When points A and B give the maximum difference in , the Compton scattering plane by construction is parallel with the reaction plane
If first point misidentified, parallel scattering events tend toward the photopeak tails

## Slide 11: Improving the Main Interaction Assumption
Main Interaction
Compton formula (difference squared between Energy term and scatter angle term)
Crystal depth coordinates
Klein-Nishina formula
Angle between two points in the global basis
Use interaction point energies and positions to find the pair of points that minimize
…
event
Int. Pts.
1st Point Candidate
2nd Point Candidate
Last point penalties

## Slide 12: New Algorithm Performance in Simulation
Chart: Two Interaction Points
| Main Int. | Compt. Form. | New Alg.
[1,1] | 0.89055 | 0.78122 | 0.90323
[0,0] | 0.10945 | 0.21878 | 0.096768
Chart: All Interaction Points
| Main Int. | New Alg.
[1,1] | 0.33032 | 0.46249
[1,0] | 0.38917 | 0.33386
[0,1] | 0.020811 | 0.015599
[0,0] | 0.25969 | 0.18762
Over all interaction points, the New Algorithm performs noticeably better than the Main Interaction
Simulated 1329 keV Full Energy Peak Events Only
Fairly equal performance between the New Algorithm and Main Interaction with two interaction points
Right 1st
Right 2nd
Wrong 1st
Wrong 2nd
Interaction Point Order
Right 1st
Wrong 2nd
Wrong 1st
Right 2nd

## Slide 13: New Algorithm Performance in Real Data
Chart: Gate Width [FWHM]
| 1 | 2 | 3 | 4 | 5 | 6
Main Interaction | 0.065193 | 0.04262 | 0.029653 | 0.017329 | 0.0090314 | 0.00055234
New Algorithm | 0.049137 | 0.023407 | 0.011755 | 0.0040529 | 0.0010782 | -0.0034105
64Fe
keV / bin
Energy [keV]
[rad]
# of interactions > 1
Normalized Counts / 20 deg

## Slide 14: Promising Polarization Results
42Cl (3n knockout)
Energy [keV]
46Ar (1p pickup)
keV / bin
Energy [keV]
[rad]
Normalized Counts / 20 deg
Counts \ 20 Deg
[rad]
Normalized Counts / 20 deg
Counts \ 20 Deg

## Slide 15: Summary & Outlook
In fast beam data, there is an induced correlation between and when the gamma ray interaction point order is incorrectly determined
It’s all about including the tails! Too narrow of an energy gate will bias your data toward the perpendicular azimuthal scattering directions
Linear polarization analysis with fast beams looks feasible, but has limitations
  Transitions must be isolated
  Transitions must be intense and have good signal to background ratios
Multiplicity gates on interaction point numbers can also help reduce the correlation at the cost of losing statistics
Let the tail wag the dog?

## Slide 16: Acknowledgment
Thanks to the Gamma Group
  Alexandra Gade
  Ava Hill
  Dirk Weisshaar
  Gabriel Grauvogel
  Marshall Basson
  Joseph Chung-Jung
  Stephen Gillespie
  Tom Parry
This work was supported by the U.S. Department of Energy, Office of Science, Office of Nuclear Physics under Contracts No. DE-SC0020451, DE-SC0019034, and DE-SC0023633
And former Gamma Group members
  Brandon Elman
  Brenden Longfellow
  Daniel Rhodes
  Elizabeth Rubino
  Jing Li
  Mark Spieker
  Sayani Biswas
  Tobias Beck

## Slide 17: Thank you!
Questions?

## Slide 18: Backup Slides

## Slide 19: Lorentz Focusing Effects Overall Distribution in GRETINA
Events that scatter along increasing/decreasing theta must be more parallel to the reaction plane
Crystals have slightly more hit intensity on the forward edge than the backward edge due to Lorentz focusing
This creates a preferred scattering direction between the two parallel angles
Intensity
[deg]
[deg]

## Slide 20: New Algorithm vs Main Interaction
64Fe

## Slide 21: New Algorithm vs Main Interaction
43Cl