## Slide 1
Towards a new measurement of
the neutron electric dipole moment
The n2EDM experiment

## Slide 2
Collaboration of 12 institutes (mainly European)
(25 permanents, 15 doc + post-doc)
Sensitivity goal: 10-27 e cm

## Slide 3
The design of the n2EDM experiment
Storage chambers where neutron frequency measurement is performed
From the measurement of two frequencies (parallel and antiparallel fields configurations)
Two main challenges
neutron statistic & magnetic field uniformity and stability
→ Ramsey’s method: required polarized neutrons
UCN

## Slide 4
Control of the magnetic field
Magnetically shielded Room (MSR): 6-layers mu-metal shield (suppression factor of 105 for quasistatic field)
MSR in the thermo-house
Storage chambers in the VT
Magnetic field generation: internal coils system (64)
- 1 main B0 coil + 63 correcting coils
Online measurements of the magnetic field:
- Hg comagnetometer (in situ): mag. field drift
- 112 Cs magnetometers : field non uniformities

## Slide 5
Based on 2016 UCN source performances
Expected sensitivity
Sensitivity improvements:
Gain with respect to the nEDM experiment:
*G. Zsigmond et al, Eur. Phys. J.A 56, 33 (2020).
Final sensitivity of 10-27 e cm → 500 days of data taking (4 years)
Number of UCN (x8): storage volume (x3) + optimized* connection source - apparatus
Electric field intensity (+35 %): HV electrode better insulated /nEDM
Systematics: mostly induced by the magnetic field non uniformities
Highly uniform and stable magnetic field (1 µT) required
Field uniformity: in the chambers
Field stability : 30 fT/min
T: storage time
E: electric field intensity
: UCN polarization
N: number of UCN

## Slide 6
French contributions to the n2EDM experiment

## Slide 7
In2p3 hardware contributions
Spin analyser (LPC)
Data monitoring interface (LPSC)
Vacuum vessel (LPC)
Switch box (LPSC)
Internal coils system (LPC)
Neutron detectors + FASTER (LPC)
Mapping robot (LPSC)
Hg polarization cell (LPSC)

## Slide 8
In2p3 hardware contributions
ANR (570 k€, 2014-2019) + ERC (200 k€, 2016-2021):
- strong implication of the technical services (4 FTE / year between 2015 and 2022)
+ data management (CCin2p3), data analysis, data blinding, systematic effects, strategy board ….

## Slide 9
Commissioning results

## Slide 10
UCN commissioning (2023)
First UCN in the apparatus in July 2023: number of neutrons too low by a factor 20 !!
Many tests performed during Fall 2023:
Number of stored UCN end of 2023 (180 s): 24,000
(still a factor 5 missing / design goal)
Electrode coating (DLC) and insulator coating (DPS): underperforming
Two culprits: coating technique and surface roughness
Test chambers under construction (coating investigation during Fall 2024)
- new insulator ring (quartz instead of PS)
- new electrodes with exchangeable parts (test of coating procedures)
Storage capacity of the chambers:
- Insulator rings: redo the DPS coating → increase of UCN statistic
nEDM insulator ring → increase of UCN statistic
- Electrodes : dummy copper electrodes → increase of UCN statistic
visual inspection : small spots peeled off
UCN transport: up to the chambers: OK !
during emptying phase: factor 2 too low / simulations

## Slide 11
Magnetic field commissioning
Magnetic field characterization (2021-2022): close collaboration between LPC and LPSC
- internal coils system simulated, built and installed by LPC
- field characterization performed by LPSC
T. Bouillaud, P. Flaux, “An exceptionally uniform magnetic field for the n2EDM experiment” (LPC-LPSC); internal review.
Performances are excellent
Part of the systematics already below requirements

## Slide 12
Apparatus commissioning
Neutron frequency measurement:
Ramsey oscillating field method: operational !
neutron polarization, transport, storage and detection: 0K !
Final polarization larger than in design goal (> 0.8) !!
Sensitivity already better than in nEDM (1.9)
Current performances:
2024 goal: first nEDM data
15 kV/cm last Wednesday !
Components | Operational | Performances
Neutrons statistic |  | 24,000
Magnetic field |  | ; systematics
High Voltage |  | +15 KV/cm
Ramsey meas. |  | a > 0.8
Hg Comagnetometer |  | T2 = 35 s → 100 s
Cs magnetometers |  | 
Components | Operational | Performances
Neutrons statistic |  | 24,000
Magnetic field |  | 
High Voltage |  | +15 KV/cm
Ramsey meas. |  | a > 0.8
Hg Comagnetometer |  | T2 = 35 s → 100 s
Cs magnetometers |  | 

## Slide 13
Perspectives and conclusions

## Slide 14
Perspectives and conclusions
First phase (2024-2026):
Sensitivity already improved / nEDM (x1.9): new result is guaranteed
final sensitivity will depend on new chambers storage properties
Systematics : part of the systematics already under control (magnetic commissioning)
Towards a final sensitivity of 10-27 e cm: two steps approach
Second phase (2028-2030):
UCN source repair/upgrade (x3): D2 container and UCN shutter exchanged, proton beam intensity, D2 solid prod.
final sensitivity will depend on UCN source performances (missing 2.2)
New operation mode: suppress the main systematic effect (false motional EDM) with magic B0 field (10 µT)
G. Pignol, A magic magnetic field to measure the neutron electric dipole moment, Phys. Lett. B, 793, 440 (2019)
Beyond 2030: nEDM measurement in superfluid Helium (SNS prototype move to Europe) ?
UCN source (PSI)

## Slide 15
Summary and requests
Summary of our involvement since 2004:
Strong involvement of the French teams in n2EDM ?
- The only CNRS staff is going to retire (LPSC) → CR recruitment (LPC or LPSC)
- Keep on implying PhD & post-doc in the project
- Collaboration agreement (common funds) up to 2026: to be secured till 2030
- Support the mission to PSI for shift duty (3.5 weeks /year/person)
- L4M @ LPSC: magnetometry developments → in2p3 support
- Maintenance of all French components (technical services: 1-2 FTE/year)
French involvement in the n2EDM experiment:
Budget :  20 %
Staff :  20 - 25 %
There was always a French co-spoke (LPC or LPSC) person since 2004 (beside 2008-2012)
n2EDM experiment is the worldwide leader: UCN source operational + preliminary measurements ongoing
- sensitivity already better than for nEDM: any improvements bring us towards 10-27 e cm

## Slide 16
Collaboration nEDM
Merci

## Slide 17
Design of the n2EDM experiment
17
Pulsed proton beam
(650 MeV, 2.2 mA)
Heavy water (300 K)
Pb spallation target
D2 crystal
(30 L @ 5 K, 4.5 kg)
n2EDM experiment
PSI UCN source: pulsed proton beam on a Deuterium crystal (5 K)
Built at PSI for the nEDM project
(start in 2011)
Production of ultracold neutrons (T < 300 neV)
Can be stored in chambers for a few minutes
Pulsed UCN source
measurement performed every cycle (7 min)
UCN source improvements since 2016:
Solid D2 improvements: x1.5
UCN source improvements in 2027:
Flap repair: x1.3
D2 container lid: x1.8
Proton beam current intensity: x1.2
Source conditioning: x1.2

## Slide 18
Control of the magnetic field
Magnetically shielded Room (MSR): 6-layers mu-metal shield (suppression factor of 105 for quasistatic field)
Active Magnetic Shield (AMS): suppress the ambient field variations around the MSR (a few µT)
Thermo-house: controlled environment (temperature, humidity)
Magnetic properties of every pieces installed are checked:
- small components : specific device (gradiometer developed at PSI)
- large pieces: at PTB Berlin (electrodes, vacuum tank …)
Stringent magnetic requirements in the MSR:
- at the vacuum tank level: < nT @ 5 cm
- close to the precession chambers: < 20 pT @ 5 cm
Any magnetic dipole on the chambers walls must be removed (cleaning procedure)
Gradiometer
A very large magnetically shielded room with an exceptional performance for fundamental physics measurements
A large 'Active Magnetic Shield' for a high–precision experiment. Eur.Phys.J.C, 2023, 83 (11), pp.1061
MSR in the thermo-house
Storage chambers in the VT

## Slide 19
Control of the magnetic field
Magnetic field generation: internal coils system (64)
- 1 main B0 coil (optimized vertical solenoid)
- 56 squared correcting coils
- 7 gradients coils (G10 , G20 , G30 , G11 , G1-1 …)
Online measurements of the magnetic field:
- Hg comagnetometer (in situ)
→ magnetic field drift + (G10)
- 112 Cs magnetometers surrounding the chambers
→ field non uniformities (G30,G50)
Offline measurements:
- magnetic field mapping (field non uniformities: G30 , G50 , G70)
- field mapping before and after the data taking
- offline corrections of some systematic effects (reproducibility)