## Slide 1
Franck Pereira Dos Santos
SYRTE
Measurements below
the standard quantum limit
in atomic interferometry
Workshop « Développement des détecteurs"
Paris, June the 17th, 2024

## Slide 2
Principle of atom interferometry
Analogy with optical interferometry
Use atom-laser interaction to deflect matter waves
Interferometer based on a sequence of 3 laser pulses

## Slide 3
Phase difference between the two paths
For a constant acceleration a,
Sampling of the positions at the three pulses
upper arm
lower arm
laser phase :
Phase of the interferometer :
: phase of the quantum wavepacket
Key advantages
Scales as T2  Benefit of cold atoms
Depends on time (T) and frequency (k)  SI traceable, accurate, bias free

## Slide 4
Mirror
3D-MOT
Detection
Laser 2
Laser 1
Position of the equiphases
defined by the mirror position
atomic measurement = measure of the relative displacement atoms/mirror
Gravimeter: a vertical accelerometer
Bring the two lasers in a co-propagating way and retroreflect them on a mirror

## Slide 5
130
140
140
70
The SYRTE gravimeter
Laser system
Control electronics,
Power supplies
Drop chamber
Performances
Short term stability
57 nm/s2 @ 1s
Long term stability
< 1 nm/s2
Better than the reference “classical” instrument = corner-cube gravimeter
Accuracy
20 nm/s2

## Slide 6
Sensitivity limits: vibrations
Typical noise in urban environnement
Without isolation platform: 2.9 · 10-6 g/Hz1/2
With platform: 7.6 · 10-8 g/Hz1/2
GAIN : factor 40
Post-correction
Seismometer
PC
v(t) → fvibS
keffgT² + fvibS
Interferometer
keffgT²
Provides additional gain from 2 to 10 depending on vibration noise conditions:
6 10-9 g/Hz1/2 (quiet, LUX) – 15 10-9 g/Hz1/2 (urban, WB lab, Trappes)

## Slide 7
Differential measurements
Sensitivity of one interferometer limited by vibration noise of the experimental platform
Cancels in differential mode (common-mode noise suppression)
 Sensitivity potentially limited by the quantum projection noise (SQL in atom interferometry)

## Slide 8
Differential interferometers
2 instrument configurations:
- Gradiometers
- Gyroscopes
Magnetic shields
Cs oven
Raman pulses
2 atomic beams
State preparation
Laser collimation
Detection
Simultaneous interferometers with two clouds of atoms and common lasers
Differential measurement gives access to acceleration difference
and therefore to the gravity gradient
Simultaneous interferometers with two conterpropagating beams
Differential measurement gives access to rotation
OPERATION AT THE SQL DEMONSTRATED IN THESE TWO CONFIGURATIONS

## Slide 9
1.4 m
Demonstrated differential acceleration sensitivity:
4x10-9 g/Hz1/2
(2.8x10-9 g/Hz1/2 per accelerometer)
Differential interferometers

## Slide 10
Differential acceleration stability : 10-11 g
Statistical uncertainty : 2 10-4 on G
Stanford, M. Kasevich
Florence, G. Tino
Statistical uncertainty:
3 10-4 on G
G measurements

## Slide 11
GW detection with atom interferometry
Why not using "perfectly" free falling test masses to measure the laser phase?
 Atom interferometry
Motivation:
At low frequencies (<10 Hz), optical GW detectors are limited by motion noise
Residual seismic noise, thermodynamical noise in the mirror, etc.
Target strain sensitivity in the future (few decades) :
Challenge: improve on the atom shot noise and use high scale factor AIs (e.g. large momentum transfer beam splitters).

## Slide 12
MIGA: towards large scale instrument
Interrogation time ; Phase sensitivity = 1/SNR ~ 1 mrad/shot
Acceleration sensitivity
Gravity gradient sensitivity
cavity
Interferometer phase shift at position x :
Rb87 atoms:

## Slide 13
MIGA implementation
π
π/2
30 cm
Launch
Detection
π
150 m
780 nm
780 nm
Parameters
L = 200 m (=> 150 m)
Finesse = 150
2T = 500 ms
n=1
(two photon transition)
N=106
Strain sensitivity
(detection noise limited)
2 10-13 @ 2Hz

## Slide 14
How to improve ?
Contribution of the detection noise:
= 1(mrad)2/Hz for 106 atoms
↗ L from hundreds of m to few kms
↗ N from 106 to 109
↗ n from 1 to 1000
Beat the SQL : < with G a metrological gain
Strain sensitivity

## Slide 15
Large momentum transfer beamsplitters
Example: Bragg diffraction in optical lattices
Courtesy: S. Abend, LUH
Momentum separations
from to
today
tomorrow

## Slide 16
A two level atom with states 1 and 2 can be represented by a pseudo-Spin ½
The state of the atom (and its dynamics)
can then be represented in the Bloch sphere
States of one atom in 1 or 2 = eigenstates of with eigenvalues +1/2 and -1/2
couple the two states
Pseudo-spin representation

## Slide 17
Phase
Superposition Evolution Recombinaison
Atom-light interaction = Coupling mode 1 and 2: &
Ramsey sequence
1
2
Atom-light interaction
Transition probability
At mid-fringe

## Slide 18
Phase
Ensemble of N atoms represented by a macrospin
Coherent atomic state
Pseudo-spin representation
Superposition Evolution Recombinaison
Ramsey sequence

## Slide 19
« Rotation around with strength »
1) Coherent state 2) Squeezed state 3) Optimized for
Rotation around
 Control of laser phase
One-axis twisting

## Slide 20
Two-body interactions in dense clouds (ex : BECs), with scattering lengths a11, a22, a12
Spin-squeezing with internal states
Mean field interaction
Rb: 1 and 2 are the two hyperfine ground state F=1 and F=2
with
This rewrites as
with
is negligible
Reduction of the ovelap between 1 and 2
is made negligible

## Slide 21
Spin-squeezing with internal states
Gross, C., Zibold, T., Nicklas, E. et al. Nature 464, 1165–1169 (2010).
Riedel, M., Böhi, P., Li, Y. et al. Nature 464, 1170–1173 (2010)
Exploit a Feshbach resonance to reduce U12
-2.5(0.6) dB
metrologically useful squeezing
(Ramsey contrast of C = 88(3)%)
-1.4 dB squeezing in a Ramsey interferometer
Spin-noise tomography: inferred gain of −8.2 dB
State-selective double well potential

## Slide 22
Spin-squeezing with internal states
Measurement enabled by a high-finesse optical cavity
|↓〉(|↑〉) atoms increase (decrease)
the index of refraction seen by the probe light.
 Frequency shift of the cavity resonance is a direct predictor of Jz
QND measurements:
Jz measurements prepare a state with reduced Jz noise.
Clock measurements
10.5(3) dB metrological gain
Stability improved by a factor 3
A second measurement
is correlated with the first one.

## Slide 23
Atoms trapped in an intra-cavity standing wave
Probe laser (blue) produces a differential light shift between two atomic states
Cavity feedback squeezing
Laser tuned to the slope
of the cavity resonance
Intracavity photon number
depends linearly on
Spin evolution similar to
one-axis twisting Hamiltonian

## Slide 24
(Wikipedia: Spontaneous parametric down-conversion)
F=1
F=2
With photons
With atoms
mF=0
mF=+1
mF=-1
mw dressing
pump
signal
idler
Generation of entanglement
Collisions allow production of correlated pairs of atoms with mF = ±1

## Slide 25
Squeezed vacuum in an interferometer
Creation of a squeezed vacuum state
with spin dynamics in the BEC prior to the interferometer sequence.
32 ms of spin dynamics
a mean number of 0.75 atoms
in the two states g and h is obtained
Realization
of a three mode
interferometer
2 dB Gain

## Slide 26
Atom-light coupling
: Rabi frequency
Precession term
Phase
z
t
Beamsplitter
Beamsplitter
Mirror
laser
laser
laser
Atom interferometry (with separated paths)
Notes: Dans le cadre de mon activité de recherche, les systèmes atomiques sont soit des horloges soit des capteurs inertiels dont le fonctionnement repose sur le principe des interféromètre à deux ondes.
Dans le cas des horloge, chaque atomes est mis dans un état de superposition cohérente d’énergie interne différentes alors que dans le cas des capteurs inertiel chaque atome est mis dans une superposition de deux état externes différentes. Dans ce cas les deux ondes partielles se séparent au cours du temps.
Dans les deux cas, l’état atomique est manipuler au travers de l’interaction atome-lumière.
Le principe d’une séquence est le suivant: l’ état de superposition évolue et accumule une phase qui est ensuite mesurer après avoir recombiner les deux chemins. La différence de phase accumulé est obtenue en évaluant la probabilité que l’état quantique soit projeté dans l’état fondamentale ou excite.
Ce que l’on appel la sensibilité, c’est la plus petite phase que l’on peut mesuré qui dans le cas de la limite quantique standard vaut 1/sqrt(N).
Typiquement dans le cas des horloges la phase est relié à la fréquence de la transition. En considérant 10^4 atomes interrogé pendant
une seconde ont atteins une mesure de la fréquence relative à quelque 10^-17.
Alors que dans le cas CI, on mesure une accélération relative de quelque 10-9 en considérant 10^6 atomes et un Tint de 100ms.

## Slide 27
Atom-light coupling
: Rabi frequency
Precession term
Phase
z
t
Beamsplitter
Beamsplitter
Mirror
laser
laser
laser
Non-linear Interaction term
Density of the BEC
Atom interferometry (with separated paths and BECs)
Challenge :
In free fall interferometers, the density drops quickly and thus the strength of the interactions
Notes: Dans le cadre de mon activité de recherche, les systèmes atomiques sont soit des horloges soit des capteurs inertiels dont le fonctionnement repose sur le principe des interféromètre à deux ondes.
Dans le cas des horloge, chaque atomes est mis dans un état de superposition cohérente d’énergie interne différentes alors que dans le cas des capteurs inertiel chaque atome est mis dans une superposition de deux état externes différentes. Dans ce cas les deux ondes partielles se séparent au cours du temps.
Dans les deux cas, l’état atomique est manipuler au travers de l’interaction atome-lumière.
Le principe d’une séquence est le suivant: l’ état de superposition évolue et accumule une phase qui est ensuite mesurer après avoir recombiner les deux chemins. La différence de phase accumulé est obtenue en évaluant la probabilité que l’état quantique soit projeté dans l’état fondamentale ou excite.
Ce que l’on appel la sensibilité, c’est la plus petite phase que l’on peut mesuré qui dans le cas de la limite quantique standard vaut 1/sqrt(N).
Typiquement dans le cas des horloges la phase est relié à la fréquence de la transition. En considérant 10^4 atomes interrogé pendant
une seconde ont atteins une mesure de la fréquence relative à quelque 10^-17.
Alors que dans le cas CI, on mesure une accélération relative de quelque 10-9 en considérant 10^6 atomes et un Tint de 100ms.

## Slide 28
Position
t
Interferometer
BEC dilution
t
Free fall interferometry

## Slide 29
Position
t
State preparation
Interferometer
One-Axis Twisting (OAT)
Interacting BEC
[1] S. S. Szigeti, et al., PRL 125, 100402 (2020).
Advantages:
  Spin-Squeezing dynamic
Disadvantages:
  Interacting ensemble during BS
  Shape deformation
  Limited amount of squeezing (G up to 7 dB)
t
Quantum-enhanced free fall interferometry

## Slide 30
Position
t
State preparation
Interferometer
One-Axis Twisting (OAT)
BEC dilution
Advantages:
  Spin-Squeezing dynamic
  Non-Interacting ensemble during atom-light interaction
  Avoid Shape deformation
  Large Quantum Gain ( up to 20 dB )
[2] R. Corgier, et al., Delta-kick Squeezing, PRL 127, 183401 (2021).
t
Quantum-enhanced free fall interferometry

## Slide 31
Strength:
(SQL)
1
Gain
Non-linear AI
Key message:
Interactions during AI
are detrimental
[1] R.Corgier et al., PRA 103, L061301 (2021)
Position
t
State preparation
Interferometer
One-Axis Twisting (OAT)
BEC dilution
Linear AI
Quantum-enhanced free fall interferometry

## Slide 32
Sensitivity 3.4 dB and 2.5 dB below the SQL
Greve, G.P., Luo, C., Wu, B. et al. Entanglement-enhanced matter-wave interferometry in a high-finesse cavity. Nature 610, 472–477 (2022). https://doi.org/10.1038/s41586-022-05197-9
Quantum-enhanced free fall interferometry (in a cavity)
QND measurements
+ cavity-mediated spin interactions
Injection of an entangled state into a Mach–Zehnder light-pulse interferometer
Sensitivity 1.7 dB below the SQL

## Slide 33
An entangled-enhanced atomic gravimeter
https://arxiv.org/abs/2404.18668

## Slide 34
1. Generation of
two-mode squeezing
2. Transfer to clock state
10000 atoms
1 atom
3. Spin-state tomography
1st pulse (mw)
2nd pulse (rf)  mag. insensitive clock state
Preparation of the input state
Gain of 5.4 dB

## Slide 35
π/2 microwave pulses for preparing and recombining coherent superpositions (more stable than Raman lasers)
4 Raman π-pulses to separate and recombine the spatial paths A spin-echo will cancel residual microwave “atom clock” phase + common mode noise.
F=2
F=1
(|2,0> + 2hk)
Realization of a gravimeter
Blackman Raman pulses couple
with 98.2 % efficiency
But not

## Slide 36
Gravimeter: Frequency chirp of Raman lasers
Change central T, find crossing point, find g
Repeat many times: noise in g due to δp
Scale factor “kT2” (-> sensitivity function)
‘’Δg error”
SQL
Measure g with -1.7dB below SQL or -3.9dB below unsqueezed state
Limited free fall durations (only 7-10ms available, including DKC, spin-dynamics etc)
Results

## Slide 37
Conclusion
Differential interferometers have reached the SQL (with state of the art performances)
Different protocols to beat the SQL implement in clocks and atom interfrometers
Squeezed clocks have been demonstrated, at the best level of performance (optical clocks)
State of the art squeezed (separated paths) atom interferometers still to be demonstrated