## Slide 1: Methodology of electromagnet design
G. DILASSER

## Slide 2: Presentation outline
Targets, constraints & variables
Legacy magnet design methodology
Numerical methods and software
Magnet design as an optimization problem

## Slide 3: “Targets” & “Constraints”
Desired properties of
Center field
Field harmonics
Some integral of
…
“Targets”
Electromagnetism
Mechanics
General / technical
Thermic
Material science
Electricity
“Project constraints”
Thermal loads from experiment
Bore aperture
Outer dimensions
Maximum weight
Fringe field
Current ramp time
Conductor properties
Manufacturable length
Superconductor critical surface
Mechanical strength of the windings
Superconducting magnet safety in case of quench
Hotspot temperature
Discharge voltage
“Physics constraints”
$$$

## Slide 4: “Variables”
In fact, we are not only designing a magnet but an integrated system comprising:
Overall dimensions?
Material fractions?
Coolant section?
One (or more) conductor(s) | Winding geometry | External servitudes (PSU, coolers, etc)
Winding configuration?
Number of layers, turns?
Operating current?
Operating temperature?
Available refrigeration power?

## Slide 5: Methodology for superconducting magnets
Homogenized properties
Known conductor properties
Electromagnetism
Electricity
Mechanics
Thermic
Material science
Magnetic simulation
Winding geom.
Laplace forces
Mechanical simulation
OK?
END
Conductor design
External circuits
Conductor shape
Material %
Cooling
Mechanical simulation
Magnetic simulation
Thermal simulation
OK?
Y
N
Y
N
Eddy losses
Cool-down
Over-field
Conductor
mechanic
START
Target
Margins
Hotspot
Discharge

## Slide 6: Coupled magnetic / mechanical design
Designing the winding shape is an iterative process:
Assumptions on homogenized winding properties (engineering current density, Young modulus, etc)
Magnetostatic simulations to get a winding shape generating the desired magnetic field
Simulations of the homogenized windings mechanical strength under the Laplace forces
Magnetic simulation
Winding geom.
Laplace forces
Mechanical simulation
OK?
Y
N
START
Target
Constrained geometry
Material
Mechanical simulation software
Ansys (Ansys Inc.)
Cast3M (CEA)
Electromag. simulation software
Opera (Dassault)
Roxie (CERN)
RAT (Little Beasts Engineering)

## Slide 7: Conductor definition
With on the windings computed, we can also design a conductor:
Conductor
Auxiliaries
Quench
Normal operation
Design supercond.
Design stabilizer
Design insulation
% SC
% Cu
Ins. thickness
Geometrical aspect
Margins
Hotspot
Discharge
Discharge
Power supply
Conductor cryogeny
% cryo.
Cryoplant
Thermal loads
AC/DC
Defined conductor
General / technical
Electricity
Thermic
Material science
Cu
LHe
SC + Cu

## Slide 8: Thermal design
 | Superconducting magnet | Resistive magnet
Normal operation | Transient thermal losses (Eddy currents, stick-slip motions, etc.) Thermal loads from experiment (for ex. radiation from beam or plasma) | 
 | Cryostat losses (conduction & radiation) Magnet cool-down / warm-up time Choice and design of the cold source Minimization of the cryostat losses | Steady-state Joule losses Design of the continuous cooling (typ. water flowrate)
Default case | Simulation of quench dynamics (hotspot, thermal gradients, voltages) Area devoted to cryo in the conductor Design of the quench detection and protection systems | 
The thermal design depends on the resistive / superconducting nature of the magnet:

## Slide 9: Numerical methods
Numerical techniques:
  95% old-fashioned FEA in static cases
  Some Fast Multipole Method (FMM) to speed up magnetostatic computation
  Some Partial Element Equivalent Circuit (PEEC) for High-Temperature Superconductors
Major difficulties do not reside in the numerical methods:
  Having good fits of material properties at low and under high
  Highly non-linear current-voltage law for superconductor
Hardest problem to simulate remains the quench of superconducting coils:
  Intrinsically dynamic
  Coupled physics: electromagnetic + thermohydraulic + electrical network (+ mechanical)

## Slide 10: Panorama of software used
Usage | Software | Editor | Usage
Magnetic simulations | Opera | Dassault Systèmes | Reference tool for magnetic simulations
 | Roxie | CERN | Used only for accelerator magnets
 | RAT | Little Beasts Engineering | Cheaper / free alternative to Opera gaining traction
Mechanical simulations | Ansys | Ansys Inc. | Reference tool for mechanical / thermal simulations
 | Cast3M | CEA (LM2S) | For specific mechanical simulations
Thermal simulations | THEA | CryoSoft | Thermo-hydraulic of magnet cooling and quenches
 | Comsol | Comsol Inc. | Mostly used for thermal simulations
Material properties | Hepak | Cryodata (formerly NIST) | Properties of Helium
 | Cryocomp | Eckels Engineering | Properties of solids at cryogenic temperatures
CAD | SolidWorks | Dassault Systèmes | CAD and light thermal / mechanical simulations
 | NX | Siemens PLM Software | CAD and technical drawing
Optimization | NAG Library | Numerical Algorithm Group Ltd. | Design optimization with mathematical programming
 | Alesia | CEA (LEAS) | Project management and evolutionary algorithms
Miscellaneous | Matlab, Python... | Various | Various in-house codes
Resistive magnets | HiFiMagnets | CNRS (LNCMI) | Toolchain to design resistive magnets based on C++ open-source library Feel++ used at LNCMI

## Slide 11: Conventional sequential workflow
Homogenized magnetic sim.
Homogenized mechanical sim.
Stresses & deformations
Conductor & auxiliaries
Winding geometry
Laplace forces
Peak field & Stored energy
Quench model
Cryostat thermal design
Conductor geometry
Conductor mechanic
Detailed magnetic sim.
Design update
Overfield
Margins
Hotspot
Voltages
Local stresses

## Slide 12: Some kind of optimization problem
Current tendency is to rephrase the design problem as optimization problem:
New design approach leverages evolutionary algorithms:
  Population of design candidates combining magnet & conductor properties
  Compute candidate fitness through parallel physic simulations
  Recombine next generation from best current candidates and mutate
Methodology implemented in ALESIA with several algorithms
(genetic algorithm, particle swarm optimization, differential evolution, covariance matrix
adaptation evolution strategy, etc.)
Goal is either: Maximize some measurement of Minimize magnet cost | Under many constraints but most notably: Laplace forces do not tear the windings apart Thermal losses do not make them burn
 | Under many constraints but most notably: Laplace forces do not tear the windings apart Thermal losses do not make them burn

## Slide 13: Optimization-based workflow
Parallel
Magnetic simulations
Laplace forces
Mechanical simulation
Stresses & deformations
Peak field & Stored energy
Generate new population
Fitness computation
Optimized
solution
Magnetic field
Material database
Feature extraction
Field characteristics
Hotspot temperature
Population of candidate designs
Quench model

## Slide 14: Thank you for your attention; are there any questions?
CEA Paris-Saclay
Guillaume DILASSER
Bât. 123, p. 213c
Point courrier n°11
91191 Gif-sur-Yvette Cedex
guillaume.dilasser@cea.fr

## Slide 15: Back-up slides
X