## Slide 1: Calculation softwares for magnetic modelling at Synchrotron SOLEIL
M. VALLÉAU
Magnetism & Insertion Devices Group

## Slide 2: Modelisation of the insertion devices

## Slide 3: Introduction
User request
Spectral range, polarization, taper, aperiodicity, …
Design
Radiation : SRW, Spectra
Magnetic fields : Radia
Effects on the e-beam : Radia (kick cards)
Construction
IDBuilder, Radia, SRW
Electron beam
Radia
Photon beam
SRW, Spectra
: und. period
: und. mag. fields
: deflection parameter
: resonant wavelenght

## Slide 4: Introduction
Cryogenic Permanent Magnet Undulators
Helical Undulators
In-vacuum Undulators
Wigglers
In-vacuum Wigglers
Electro-magnetic Undulators
Electro-Magnetic Polarized Helical Undulators

## Slide 5: RADIA
RADIA [1] [2] is a three-dimensional magnetostatics computer code in C++ interfaced with Mathematica
(no more maintained), Igor pro and Python. Enables to solve magnetostatic problems for current-carrying
volumes and magnetized volumes (non-linear for iron and linear anisotropic for permanent magnets).
INPUTS : menu driven with self explained dialog boxes and/or command line interface for IgorPro and
functions for Mathematica and Python.
OUTPUTS : 3D Object, Igor Binary Waves, ASCII, csv, …
>> 3D magnetic fields, field integrals along a line, 3D forces and torques between elements, angles &
trajectories of the electrons, second order kick cards, …
[1] P. Elleaume, O. Chubar, J. Chavanne, "Computing 3D Magnetic Field from Insertion Devices", proc. of the PAC97 Conference May 1997, p.3509-3511.
[2] O. Chubar, P. Elleaume, J. Chavanne, "A 3D Magnetostatics Computer Code for Insertion devices", SRI97 Conference August 1997, J. Synchrotron Rad. (1998). 5, 481-484

## Slide 6: RADIA
[1] P. Elleaume, O. Chubar, J. Chavanne, "Computing 3D Magnetic Field from Insertion Devices", proc. of the PAC97 Conference May 1997, p.3509-3511.
[2] O. Chubar, P. Elleaume, J. Chavanne, "A 3D Magnetostatics Computer Code for Insertion devices", SRI97 Conference August 1997, J. Synchrotron Rad. (1998). 5, 481-484
Electro-magnetic Undulators
Hybrid Undulators & Wigglers
Pur Permanent
Magnets Undulators

## Slide 7: IDBuilder
[3] ID Builder, Genetic Algorithm, O.Rudenko and O.Chubar, Proc. of 9th Int. Conf. on PPSN IX, p.362 (2006)
[4] O. Rudenko and O. Chubar, "An Evolutionary Approach to Shimming Undulator Magnets for Synchrotron Radiation Sources", Proc. of 9th Int. Conf. on Parallel Problem Solving from Nature PPSN IX, p.362 (2006)
[5] O. Chubar, O. Rudenko and al, Application of genetic algorithms to sorting, swapping and shimming of the SOLEIL undulator magnets, AIP Conf. Proc., 879, 359, (2007).
Advantages :
object function, arbitrary search space, search from a population, mutation and cross-over
 global optimum, multi-modal/multi-objet
Insertion Device Builder [3] [4] [5] is an IGOR PRO plugin dedicated to the magnetic assembly and optimization of IDs based on a genetic algorithm.

## Slide 8: IDBuilder
Iz
Ix
Assembly process
Correction process
SHIMMING
Magic Fingers
[3] ID Builder, Genetic Algorithm, O.Rudenko and O.Chubar, Proc. of 9th Int. Conf. on PPSN IX, p.362 (2006)
[4] O. Rudenko and O. Chubar, "An Evolutionary Approach to Shimming Undulator Magnets for Synchrotron Radiation Sources", Proc. of 9th Int. Conf. on Parallel Problem Solving from Nature PPSN IX, p.362 (2006)
[5] O. Chubar, O. Rudenko and al, Application of genetic algorithms to sorting, swapping and shimming of the SOLEIL undulator magnets, AIP Conf. Proc., 879, 359, (2007).

## Slide 9: B2E
B2E [6] is an IGOR PRO plugin dedicated to the simulation of the Synchrotron Radiation produced by a relativistic single electron traveling through an arbitrary magnetic field.
INPUTS : menu driven with self explained dialog boxes and/or command line interface.
OUTPUTS : Igor Binary Waves
[6]
Automated functions to process the measured magnetic fields and evaluate the magnetic field errors
after magnetic measurements to compute their effect on the spectral performances

## Slide 10: SRW & SIREPO
[7] O. Chubar, P. Elleaume, "Accurate And Efficient Computation Of Synchrotron Radiation In The Near Field Region",
proc. of the EPAC98 Conference, 22-26 June 1998, p.1177-1179
« Synchrotron Radiation Workshop [7] computes the synchrotron radiation from relativistic electrons with high
precision and efficiency in the near and far field range » [X]
C++ source code with pluggins for
  IGOR PRO
    INPUTS : contextual menus, txt files, Igor Binary Waves
    OUTPUTS : txt files, Igor Binary Waves
    Automated functions to calculate SR directly after mag. Meas.
  Python
    INPUTS : functions, txt files
    OUTPUTS : txt files, binary files, json,…
Enables to compute for different beams :
Synchrotron Radiation for different types of sources (bending magnets, undulators, arbitrary fields)
Wavefront propagation (including mirrors, slits, mono), for end-to-end simulations for Beamlines

## Slide 11: SRW & SIREPO
[8] Maksim S. Rakitin, Paul Moeller, Robert Nagler, Boaz Nash, David L. Bruhwiler, Dmitry Smalyuk, Mikhail Zhernenkova and Oleg Chubar ,
Sirepo: an open-source cloud-based software interface for X-ray source and optics simulations
(2018). J. Synchrotron Rad. 25, 1877-1892.
WebApp : https://www.sirepo.com [8]

## Slide 12: SPECTRA
SPECTRA [9] is used to calculate optical properties of SR
from bending magnets, wigglers and undulators and
arbitrary field distributions. Possibility to calculate
spectrum and power distributions after transmitting
through various filters and detectors
INPUTS : Graphical user interface, txt files, json
OUTPUTS : Graphical user interface, ASCII, …
[9] Tanaka, T. & Kitamura, H. (2001). SPECTRA: a synchrotron radiation calculation code. J. Synchrotron Rad. 8, 1221-1228.

## Slide 13: Validation of the models (with electron beam)
Hor. second order kicks
Ver. second order kicks
Vert. Position (mm)
Vert. Position (mm)
Hor. Position (mm)
Hor. Position (mm)

## Slide 14: Validation of the models (with photon beam)
[10] Somogyi, A et al. Journal of Synchrotron Radiation., 22(4): 1118-1129. (2015).
SRW is used to compute the effect of :
An ideal undulator (without phase errors)
The real undulator using magnetic measurements
Taking into account the optics of the machine, beam parameters,…
At SOLEIL, beamlines also uses SpotX [11] for radiation simulations including optical components of the beamline
[11] MORENO, T. et IDIR, M. SPOTX a ray tracing software for X-ray optics. Le Journal de Physique IV, 2001, vol. 11, no PR2, p. Pr2-527-Pr2-531.
[12] C. Benabderrahmane, M. Valléau, M.-E. Couprie Development of a 2 m Pr2Fe14B cryogenic permanent magnet undulator at SOLEIL Proceedings of the 11th International Conference on Synchrotron Radiation Instrumentation, Lyon Journal of Physics Conference Series, volume 425, art. 032019, 2013

## Slide 15: Modelisation of the magnets for the storage ring

## Slide 16: Introduction
Magnets for SOLEIL II

## Slide 17: OPERA
OPERA Software (DASSAULT Systems):
Modeler
Static Solver
Dynamic Solveur
Particles tracking
INPUTS : Graphical user interface, python interface
OUTPUTS : Graphical user interface, ASCII, …
Possibility to use/send step files
Transiant and frequency simulations
Thermal simulations

## Slide 18: RADIA
[1] P. Elleaume, O. Chubar, J. Chavanne, "Computing 3D Magnetic Field from Insertion Devices", proc. of the PAC97 Conference May 1997, p.3509-3511.
[2] O. Chubar, P. Elleaume, J. Chavanne, "A 3D Magnetostatics Computer Code for Insertion devices", SRI97 Conference August 1997, J. Synchrotron Rad. (1998). 5, 481-484
OPERA model for comparison
(<0,5% diff with RADIA)

## Slide 19: Validation of the models
Difference of 0.147% between meas and
model (on the b2)
Few units of difference on b4 et b6
For n>10, noise on the measurements
Multiplar components @r=8mm (T.mm)

## Slide 20: Conclusion
Radia, B2E, IDBuilder and SRW are used intensively at SOLEIL for ID developments
have an interface with Igor Pro which is our main software for driving benches, storing and analysing datas
free software
dépendance with OS versions
Radia, and OPERA are used for the design of the magnets dedicated to new ring
Very good agrement between both softwares
The accuracy is dependant of the segmentation applied
OPERA remains very expensive
Non exhaustive list of softwares, only the ones that are used
in the ID Group at SOLEIL