SPARC/FIFO status
2024-05-06
C. Flouzat

---
Timing Constraints
constraint.sdc
  1 # set sdc_version 1.6
  2
  3 # current_design pe_and_seri_top
  4
  5 #########################
  6 # Clocks;
  7 #########################
  8 #set clock_period 2.5
  9 set clock_period2 5.0
 10
 11 # Create virtual clock
 12 create_clock -name CLK_PUSH -period $clock_period [get_ports clk_push] -add
 13 create_clock -name CLK_POP -period $clock_period2 [get_ports clk_pop] -add
 14
 15 set_clock_groups -asynchronous -group [get_clocks {CLK_PUSH}] -name CLK_PUSH_group
 16 set_clock_groups -asynchronous -group [get_clocks {CLK_POP}] -name CLK_POP_group
 17
 18 set_case_analysis 1 [get_port RN]
 19
 20 set_clock_transition -min 0.2 [all_clocks]
 21 set_clock_transition -max 0.8 [all_clocks]
 22
 23 set_clock_uncertainty 0.18 -setup -from [all_clocks] -to [all_clocks]
 24 set_clock_uncertainty 0.1 -hold -from [all_clocks] -to [all_clocks]
 25
 26 set_max_fanout 5 [all_inputs]
 27 set_max_fanout 7 [current_design]
 28
 29 set_max_transition 2 [current_design]
 30 set_max_transition 0.5 [all_outputs]
 31 ###############################################################
 32 # Input constraints
 33 ###############################################################
 34 # Constraining max capacitance that can be connected each input pin (allows the tool to size the input buffers correctly)
 35 set_max_capacitance 0.50 [all_inputs]
 36 # Constraining max transition time (rise time/fall time)
 37 set_input_transition 0.200 -max [all_inputs -no_clocks]
 38 set_input_transition 0.200 -min [all_inputs -no_clocks]
 39 #######################################################################
 40 #######################################################################
 41 # Constraining loads on output pins
 42 set_load -max 0.020 [all_outputs]
 43 set_load -min 0.001 [all_outputs]
 44 #############################################################################
 45
 46 set_input_delay -min 0.1 -clock [get_clocks {CLK_PUSH}] [get_db [all_inputs] -if {.name == data_in*}] -add_delay
 47 set_output_delay -max 0.1 -clock [get_clocks {CLK_PUSH}] [get_db [all_outputs] -if {.name == push_*}] -add_delay
 48
 49 set_output_delay -max 0.1 -clock [get_clocks {CLK_POP}] [get_db [all_outputs] -if {.name == data_out*}] -add_delay
 50 set_output_delay -max 0.1 -clock [get_clocks {CLK_POP}] [get_db [all_outputs] -if {.name == pop_*}] -add_delay
 51
MAX_var.tcl
set clock_period 1.7

---
Timing Issue
Summary of flow (synthesis):
 -------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
| Snapshot | WNS (ns) | TNS (ns) | FEPS | WNS_R2R (ns) | TNS_R2R (ns) | FEPS_R2R | DRV(T) | DRV(C) | POWER(L) | UTIL | INSTS | AREA (um^2) | DRC | WALL (s) |
| | | | | | | | Tran (ns) | Load (pF) | Leakage (mW) | Density (%) | | | | |
|-------------+----------+----------+------+--------------+--------------+----------+-----------+-----------+--------------+-------------+-------+-------------+-----+----------|
| syn_generic | -0.381 | -2 | 5 | -0.381 | -2 | 5 | 0 | 0 | 0.04 | 0.00 | 21689 | 243963 | | 0:02:37 |
| syn_map | -0.602 | -445 | 3084 | -0.602 | -445 | 3084 | 0 | 0 | 0.02 | 0.00 | 9702 | 106937 | | 0:04:20 |
| syn_opt | -0.477 | -145 | 2477 | -0.477 | -145 | 2477 | 0 | 0 | 0.02 | 0.00 | 9740 | 106501 | | 0:24:26 |
 -------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
Essentially located in flag registers
Summary of flow (pnr):
| floorplan | | | | | | | | | | 74.86 | 9740 | 106501 | | 0:01:16 |
| prects | -0.023 | -0 | 7 | -0.023 | -0 | 7 | 0 | 0 | 0.02 | 73.72 | 10003 | 104886 | | 0:05:46 |
| cts | 0.032 | 0 | 0 | 0.032 | 0 | 0 | 0 | 0 | 0.02 | 74.57 | 10301 | 106096 | 0 | 0:05:31 |
| postcts | 0.032 | 0 | 0 | 0.032 | 0 | 0 | 0 | -0 | 0.02 | 95.00 | 18250 | 135162 | | 0:03:39 |
| route | -2.800 | -27 | 251 | -0.339 | -19 | 248 | -50 | -7 | 0.02 | 95.00 | 18245 | 135155 | 103148 | 0:27:12 |
| postroute | -0.387 | -1 | 13 | -0.173 | -0 | 10 | 0 | -0 | 0.02 | 95.00 | 18223 | 135162 | 113317 | 0:08:52 |
| signoff | -2.143 | -1143 | 1566 | -0.061 | -0 | 2 | | -0 | | | | | | 0:03:06 |
 ----------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
Seems there is a hold issue