## Slide 1
PEPITES an Ultra-thin monitor for charged particle beams
By : Sara Boumaiza / Supervisor : Christophe Thiebaux

## Slide 2
PEPITES an Ultra-thin monitor for charged particle beams
FUN FACTS ABOUT ME ! SECTION :
My Journey:
Background:
Bachelor degree in radiation physics
Master degree in medical physics
Research work on thin films
Current occupation:
Student at Paris Physics Master program at Université Paris Cité
Goal:
Research work in the development of diagnosis and therapy methods and equipment for cancer treatment

## Slide 3
PEPITES an Ultra-thin monitor for charged particle beams
My work :
analysis of the data collected during the first tests of PEPITES with therapeutic carbon ion beams at CNAO, to evaluate the response of the detector and its performance at several energies of the beam.

## Slide 4: 01 04 02 05 03 06 TABLE OF CONTENTS
WHAT ?
AIM
DESCRIPTION
HOW?
STRUCTURE
PRINCIPLE
WHERE?
PROSPECTS
FUTURE WORK
WHAT?
MEASUREMENTS
HOW?
DATA ANALYSIS
RESULTS
WHERE?
CNAO

## Slide 5
Radiotherapy:
Cancer treatment via external radiation beams targeted at the patient
Types of beams used :
X-rays
gamma rays
electron beams
proton beams
carbon ion beams
SMALL DETOUR
00
01/30

## Slide 6
Hadrontherapy:
A therapy method that consists of the use of hadrons (protons, carbon) as beams for cancer treatment
00
SMALL DETOUR
02/30

## Slide 7
Advantages of hadrons vs photons:
Less dose to healthy tissue
More effective against tumors resistant to X-rays
Precise allowing higher dose delivery
00
SMALL DETOUR
03/30

## Slide 8
Killing Mechanisms:
Directly through the damage of DNA or indirectly through the creation of free radicals (HO)
00
SMALL DETOUR
04/30

## Slide 9: WHAT IS PEPITES ? 01
05/30

## Slide 10: WHAT IS PEPITES ? 01
Objective:
Obtain a monitor used with mid-energy charged particle accelerators to continiously measure beam parameters
An ultra-thin profiler with minimum beam perturbation and high radiation resistency
Technology:
Use thin film techniques for detector construction and low noise electronics for readout.
Principle:
Signal generated by secondary electron emission (SEE), which is a surface phenomena that needs very little matter
06/30

## Slide 11: HOW IS IT BUILT ? 02
07/30

## Slide 12: HOW IS IT BUILT ? 02
08/30

## Slide 13: HOW IS IT BUILT ? 02
CP1 polyimide substrate :
Excellent radiations resistance
Ultra thin ( 1,5 μm )
09/30

## Slide 14: HOW IS IT BUILT ? 02
32 horizontal (vertical) gold strips of length 70 mm, width 1.85 mm, and thickness 50 nm representing the cathodes. The strips emit the secondary electrons. The signal (current from each strip) provide the horizontal (vertical) profile
10/30

## Slide 15: HOW IS IT BUILT ? 02
A 70 x 70 mm square thin film of thickness 50 nm representing the anode that collects the SEE .
11/30

## Slide 16: HOW IS IT BUILT ? 02
The process is done in vacuum insuring the integrity of the signal
12/30

## Slide 17: HOW IS IT BUILT ? 02
A beam of energy ranging from 10 MeV to 100 MeV will penetrate the profiler and create SEE .
13/30

## Slide 18: HOW IS IT BUILT ? 02
The readout is done by a low-noise and high dynamic Application
Specific Integrated Circuit (ASIC) developed at CEA
14/30

## Slide 19: WHERE IS IT USED ? 03
15/30

## Slide 20: WHERE IS IT USED ? 03
16/30
ARRONAX Nantes :
first profiler installed for permenent use
Bellow
Manipulator

## Slide 21: WHERE IS IT USED ? 03
CNAO :
national center for hadrontherapy and oncology, Pavia, Italy
17/30
CNAO : first collaboration between CNAO and LLR to develop a monitor

## Slide 22: WHAT DID WE OBTAIN ? 04
18/30
Beam route
Vacuum chamber
Electronic read-out
Vacuum pumps

## Slide 23: WHAT DID WE MEASURE ? 04
19/30

## Slide 24: WHERE IS IT USED? 03
ION SOURCE
LINAC :
Linear accelerator
SYNCHROTRON
BEAM SIGNAL
20/30
2s
t(s)

## Slide 25: WHAT DO WE OBTAIN ? 04
Total measurement time : 500 s
Pulse duration : 2 s
Number of measurements : 200
Every 200 mesurements gives one aquisition
21/30

## Slide 26: HOW WE TREAT IT ? 05
22/30

## Slide 27: HOW WE TREAT IT ? 05
For each channel :
Background noise substraction
Data extracting
Mean calculation
23/30
The following data represent the measurements on a 115 MeV Carbon beam :

## Slide 28: HOW WE TREAT IT ? 05
24/30

## Slide 29: HOW WE TREAT IT ? 05
25/30
The data is fitted to a Gaussian representing the profiles

## Slide 30: HOW WE TREAT IT ? 05
26/30
We obtain a precise representation of our beam in space

## Slide 31: HOW WE TREAT IT ? 05
27/30

## Slide 32: HOW WE TREAT IT ? 05
28/30
Conclusion :
I successfully analyzed the first measurements carried out with a carbon ion beam on PEPITES:
The data showed a good agreament with the signal caracteristics
I obtained a precise visualization of my beam in space
I showed the increase in precision when the energy increases

## Slide 33: WHERE WILL IT GO ? 06
29/30

## Slide 34: WHERE WILL IT GO ? 06
The aim is to obtain a fully functionning Ultra-thin monitor for charged particle beams for clinical use
30/30
Comparision with CNAO profiler measurements
Data acquisition with external trigger

## Slide 35
THANK YOU