## Slide 1
The SVOM ECLAIRs UGTS and Trigger overview
Stéphane Schanne
Astrophysics Department
CEA Paris-Saclay / IRFU
ECLAIRs
Trigger SVOM
2024/06/25, Xichang, China
SVOM post-launch Scientific Workshop

## Slide 2
[2] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
SVOM mission objectives
Space-based Variable Objects monitor
Space mission dedicated to the detection and study of Gamma Ray Bursts for astrophysics and related cosmology
Build a sample of well characterized GRBs (~200 in 3yrs) with spectral and temporal coverage of the prompt and afterglow phases, permitting their redshift (distance) determination
Prompt emission observation:
  trigger on all types of GRBs, including X-ray rich, short & long duration, and high-z
  fast and reliable (<12 arcmin) positions to repoint satellite for follow-up and send Alert ground community (<30 s).
  from Visible to MeV, timing and spectrum
Afterglow follow-up observation:
  from Visible (near-IR) to X-rays, accurate (~arcsec) GRB positions
  permit redshift measurement for large fraction of triggered GRBs (~1/2)
Transient events mission within the community (GW, LSST, CTA, SKA, Neutrinos…)
  send Alerts (GCN, VO-events)
  accept and perform ToO observations
GRB Trigger objectives

## Slide 3
SVOM mission overview
[3] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs french
X/g telecope (4-120 keV), FoV(2 sr)
Localisation of GRB (<12 arcmin)
Onboard trigger Alert to ground
Satellite repointing
GRM chinese
Spectrometer g (30 keV-3 MeV)
Space-based Variable Objects Monitor
SVOM GRB Trigger
GWAC chinese
Ground wide angle camera
Prompt, Large FoV
Notes: 3

## Slide 4
SVOM mission overview
[4] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
MXT french (+german & british)
X-ray telescope
Fine localization (<1 arcmin)
VT chinese
Visible Telescope
(magnitude~23)
Space-based Variable Objects Monitor
GFT french + chinese
Ground folow-up telescopes
Delayed, Narrow FoV
Notes: 4

## Slide 5
[5] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs instrument
Soft gamma-ray spectroscopic imager

## Slide 6
[6] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs instrument
Coded mask-imager with large field of view,
and spectroscopy in the soft gamma-ray band
60 cm
80 cm
Energy range 4 – 150 keV
Energy resolution 1.6 keV (at 60 keV)
Detectors 6400 CdTe (200 modules)
Detecting area 1000 cm2
Mask open fraction 40%
Field of view 2 sr (total, 1/3 of visible sky)
Localization accuracy 11.5 arcmin (at SNR=8)
Effective area ≥ 340 cm2 (10-50 keV)
≥ 200 cm2 (at 6 keV)
Sensitivity 2.5 10-8 erg cm-2 s-1 (1 s, 5-50 keV)
Time resolution 20 ms
Dead time < 5% (for 105 count/s)
Data rate < 18 Gb/day (X-band)
On-board Trigger
expect ~ 50-70 GRB/yr

## Slide 7
[7] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs instrument
Optical screen
Coded mask (Ta)
Shield (Pb+Cu)
Radiator
Optical screen
Detector plane
Interface belt
Camera electronics
Trigger & Control Unit (UGTS)
4 main subsystems:
Structure and shielding (CNES)
Coded mask (APC)
Detection Unit (IRAP)
On-Board Software of UGTS Trigger & Control Unit (CEA)
Coded mask-imager with large field of view,
and spectroscopy in the soft gamma-ray band
expect ~ 50-70 GRB/yr

## Slide 8
[8] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs flight model
ECLAIRs at CNES Toulouse, July 2022
CNES

## Slide 9
[9] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs coded mask
APC
Mask
self-supporting 40% open
Ta 0.6 mm
sandwhiched between Ti structure
56x56 cm
46x46 pixels + central cross

## Slide 10
[10] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs detection unit
IRAP
XRDPIX module
(4x8 CdTe pixels)
200 modules
arranged in 8 sectors
Detection plane FM
8 sector-readout electronics (ELS)

## Slide 11
[11] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs trigger & control unit (UGTS)
Functions
Control of instrument (cmd/ctrl, HK, FDIR, thermal ctrl, noisy pixels) + Power supply
Data acquisition: all detected counts  RawData packets  mass-memory
GRB Trigger Scientific Processing (detection and localization of new source, based on coded mask image deconvolution)
  Alert messages to ground (via VHF)
  Slew requests to satellite
Hardware : rad tolerant, ITAR-free, cold-redundant
I/O board (×2) + Power supply (×2+4)
CPU board (with FPGA and CPU) (×2)
FPGA : data acquisition and pre-processing
CPU: dual-core, 80 MHz, 2×50 Mflops OS : time partitioning hypervisor
On-Board Software + Firmware : CEA
CNES, CEA
Image Reconstruction on UGTS CPU: ~ 1 s

## Slide 12: Handover to Hervé

## Slide 13
The ECLAIRs UGTS FPGA data preprocessing
2024/06/25, Xichang, China SVOM Scientific Workshop
Hervé Le Provost
DEDIP
CEA Paris-Saclay / IRFU
ECLAIRs
Trigger SVOM

## Slide 14
[14] –Xichang Svom Meeting - 2024/06/25 – H. Le Provost
ECLAIRs trigger & control unit (UGTS) UGTS:
ECLAIRs data acquisition
GRB Trigger
  Satellite repointing
  VHF alert messages
Scientific and Technological Housekeeping
ECLAIRs camera management
  Control/Configuration, thermal control
  Noisy pixels switch off/on
Synchronization , FDIR…
Camera power supply
UGTS functions
Unité de Gestion et de Traitement Scientifique

## Slide 15
[15] –Xichang Svom Meeting - 2024/06/25 – H. Le Provost
UGTS hardware architecture
Data Acquisition
Preprocessing
FPGA = Field Programmable Gate Array (cabled logic, no update from ground)

## Slide 16
[16] –Xichang Svom Meeting - 2024/06/25 – H. Le Provost
UGTS raw data (for X-band & trigger)
Some events coming from a sector of 800 pixels (3 out of 7 physics types)
Single Event within energy Band 0-3 (SEB)
pixel number (1 out of 6400)
Front-end time stamping
Energy band and coded Energy
 events used for GRB trigger
Single Event with energy Underflow or Overflow (SEU or SEO)
pixel number (1 out of 6400)
Front-End time stamping
Energy band and coded Energy
 Energy underflow or overflow detected by front end (event not used for GRB trigger, used for Light Curves and Rec2)
Multiple Event with Coded energy (MEC)
pixel number (1 out of 6400)
Front-End time stamping
Energy band and coded Energy
 Multiple events detected by front end (event not used for GRB trigger, used for Light Curves and Rec2)
5 keV 8 keV 20 keV 50 keV 120 keV
Eband0
Eband1
Eband2
Eband3
SEU SEB0 SEB1 SEB2 SEB3 SEO
(default flight configuration)

## Slide 17
[17] –Xichang Svom Meeting - 2024/06/25 – H. Le Provost
UGTS firmware processing: Xoff
Raw Data
Photon
Data
SEB
MEC
SEU
SEO
EES
MEA
MEE
Camera
Events
UGTS
SpaceWire
Event type | Mask
SEB | 0/1
MEC | 0/1
SEU | 0/1
SEO | 0/1
SES | 0/1
MEA | 0/1
MEE | 0/1
FPGA
CPU
(2 cores)
XOFF all links
Masked
Raw Data
To XBand
Trigger
Processing
MEC
SEU
SEO
SES
MEA
MEE
SEB
SEB encoding
(noPhSeb 0/1)
Light curves counters
VHFL alert
Light curves
Flow control by individual Event type mask or inputs general XOFF

## Slide 18
[18] –Xichang Svom Meeting - 2024/06/25 – H. Le Provost
UGTS firmware processing: GlobalCnt
SEB
MEC
SEU
SEO
SES
MEA
MEE
Camera
Events
UGTS
SpaceWire
Event type | Counting enable
SEB | 0
MEC | 0
SEU | 0
SEO | 1
SES | 1
MEA | 0
MEE | 0
FPGA
MEC
SEU
SEO
SES
MEA
MEE
SEB
VHF Light curves and VHF Rec2
Global
Counter #0
Event type | Counting enable
SEB | 0
MEC | 1
SEU | 0
SEO | 0
SES | 0
MEA | 1
MEE | 1
Global Counter #1
CPU
(2 cores)
Trigger
Processing
Counters accumulate
(saturating)
(multiples)
(default flight configuration)

## Slide 19
[19] –Xichang Svom Meeting - 2024/06/25 – H. Le Provost
UGTS firmware processing: PixMask
Raw Data
Photon
Data
UGTS
SpaceWire
FPGA
CPU
XOFF all links
Trigger
Processing
SEB encoding
SEB Pixel mask by energy band |  |  |  |  |  |  | 
0 |  |  |  |  |  |  | 
Pixel #0
Pixel #6399
SEB Pixel can be mask by energy band dynamically
(default configuration: mask pixels known to be noisy)
SEB
MEC
SEU
SEO
SES
MEA
MEE
Camera
Events

## Slide 20
[20] –Xichang Svom Meeting - 2024/06/25 – H. Le Provost
UGTS at CEA: Local Test Unit (LTU)
Host computer
ELS simulator (with photon injector)
UGTS (model BB1)

## Slide 21: Handover to Stéphane

## Slide 22
Focus on the ECLAIRs UGTS Trigger Algorithms
2024/06/25, Xichang, China SVOM Scientific Workshop
Stéphane Schanne
Department of Astrophysics
CEA Paris-Saclay / IRFU
ECLAIRs
Trigger SVOM

## Slide 23
[23] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs coded mask imaging illustration
Sky image reconstruction by Detector image deconvolution

## Slide 24
[24] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs imaging: on-axis source

## Slide 25
[25] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs imaging: on-axis source

## Slide 26
[26] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs imaging: on-axis source

## Slide 27
[27] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs imaging: on-axis source
Deconvolution
[27] – Xichang Svom Meeting - 2024/06/25 - S. Schanne

## Slide 28
[28] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs imaging: off-axis source

## Slide 29
[29] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs imaging: off-axis source

## Slide 30
[30] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs imaging: off-axis source

## Slide 31
[31] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs imaging: off-axis source
Deconvolution

## Slide 32
[32] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs FM: first imaging test
CNES Toulouse (May 2021)
ECLAIRs FM in Thermal Chamber, mask mounted
57Co + 241Am radioactive sources at 115 cm in front of ECLAIRs detection plane
Mask zoom=1.66
UGTS V4.0.1 (data acquisition & imaging software)

## Slide 33
[33] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs FM: first transient source detection
Detector image (counts/pixel) Sky image (SNR)
animation with RawData output
10 s (20 images of 0.5 s exposure)
Deconvolution with zoom=1.38 (distance of source: 1.71 cm from detector)
Artificial “GRB” simulated with X-ray generator
(duration ~2 s)
target: Cu (8 keV line)
intensity change by changing current of X-ray generator
CNES Toulouse (May 2021)
ECLAIRs FM in Thermal Chamber,
mask mounted
Events/s
UGTS V4.0.1 (data acquisition & imaging)

## Slide 34
[34] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs trigger algorithms
constraints

## Slide 35
[35] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS trigger: detector instrumental effects
Vanadium (5.0 keV)
Copper (8.1 keV)
Wenjin Xie (CEA, thesis 2021-2024)
W. Xie et al A&A arXiv 2401.13619 (2024)
Detection plane inhomogeneity at low Energy (4 to 8 keV)
Config UGG_TRIG table
Estrip def for flight:
  Estrip 0,1,2 > 8 keV
  Estrip 3: 5-8 keV
Efficiencies and weights for UGTS deconvolution
Noisy pixel management
CNES Toulouse ECLAIRs (March 2021)
ECLAIRs FM without mask
Thermal Vac.
X-ray generator
Targets
Fluoresc. lines

## Slide 36
[36] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS trigger: variable background
S. Mate (IRAP)
N. Dagoneau (CEA)
Earth transit trough FoV (1 frame = 20 s, 270 frames/orbit)
Background expected : - CXB (cosmic X-ray background)
- Reflection (of CXB on athmosphere)
- Albedo (of cosmic rays in athmosphere)
Earth Transit in FoV  modulation of bkg Temporal and Spatial (on detector plane)  modelled in trigger algorithms
PIRA simulation (IRAP)

## Slide 37
[37] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS trigger: known sources catalog
Nicolas Dagoneau (CEA, thesis 2017-2020)
Most of sources excluded by B1 pointing law ( |b|>10° & Sco X-1 avoidance)
But we may be outside B1 law during >¼ of the time (GRB 14 orbits follow-up & ToO)
using 425 sources from MAXI (2-20 keV) + Swift/BAT (15-195 keV) spectra modelled (broken-powelaw), flux over ECLAIRs 4-120 keV band
24 sources : SNR > 6 in 20 s 122 sources : SNR > 6 in 20 min
counts/s on detector for given sky pointing (optical axis)
N. Dagoneau, S. Schanne et al A&A 645A (2021)
 Onboard source Catalog included for trigger algorithms

## Slide 38
[38] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs UGTS: onboard Trigger
UGTS trigger > 20s: fit bkg & strong sources
Model fit to shadowgram: CXB 6 par + 1 par/source (max 5 sources fitted)
Raw shadowgram (20 s, sources +
Earth modulated CXB)
Sky SNR image (20 s, Earth exclusion)
Sky exclusion region
Sources in FoV (example with Gal. bulge)
20 100 1000
Width of SNR distribution (stdev)
Timescale (s)
1 2 3
Galactic bulge in FoV
B1 pointing
N. Dagoneau & S. Schanne A&A 665A (2022)
Nicolas Dagoneau (CEA, thesis 2017-2020)

## Slide 39
[39] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs trigger algorithm
“explained for dummies”

## Slide 40
GRBs appear randomly on the sky
search in full FoV (2 sr, taking into account position of Earth and known sources)
Faint GRBs are the most numerous ones
 AlertThresh, SlewThresh as low as possible (with acceptable false alarm rate)
GRB spectral diversity (normal, XRF, high-z)
4 Energy strips
GRB durations and variability
 All Time-scales from 10 ms to 20 min (17 powers of 2)
[40] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS trigger: driven by GRB diversity
5 keV 8 keV 20 keV 50 keV 120 keV
Estrip 0
Estrip 1
Estrip 2
Estrip 3
    But sky-image computation takes ~1 second on UGTS hardware!
     Two trigger algorithms running in parallel (each on 1 CPU core):
    - “Image Trigger” on long time-scales (> 20s), 1 step: build sky images every 20 s, stack up to 20 min, search for new source
    - “Count-Rate Trigger” or short time-scales (< 20 s), 2 steps: first select time window with count-rate increase, then build sky image and search for new source
Notes: 40

## Slide 41
Cyclic process every 20 s, in 4 Estrips
- build detector image and clean noisy pix
- fit & subtract background shape
(Earth modulated CXB + bright sources) - deconvolution (using mask pattern)
 Sky Images of 20 s duration (remove part behind Earth)
time
- Summation of sky images (using sky image history)  Sky-images up to 20 min duration (7 time scales: 20 s to about 20 min)
- Search in each sky image: pixel SNRmax (for which SNRmax/stdev > thresh)
if not in known source catalogue, fit peak to get precise position. if SNRmax > AlertThresh  GRB-Alert to VHF if SNRmax > SlewThresh  GRB-Alert to VHF with satellite slew request
if at known source position: if SNRmax > CatThresh  CAT-source Alert with slew req.
Raw shadowgram
Reconstructed sky
Earth
[41] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS: Image Trigger (IMT) algorithm

## Slide 42
Cyclic process every 2.5 s
First step: detect excesses in count-rate
- background estimate (from temporal bkg-model)
- build counts in all Time-Windows from 10 ms to 20 s (in 4 Estrips, and in 9 detector zones)
- compute count excess significance: SNRcnt > CntThresh  stored into buffer
Second step: imaging of best excess detected up to now
- search best excess present in buffer (not too old, not yet processed)
- build detector image of best excess (over its TimeWindow and in its Estrip) and clean noisy pix - deconvolution sky Image
- search in each sky image: pixel SNRmax (for which SNRmax/stdev > thresh)
if not on Earth and not in known source catalogue, fit peak to get precise position. if SNRmax > AlertThresh  GRB-Alert to VHF if SNRmax > SlewThresh  GRB-Alert to VHF with satellite slew request
[42] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS: Count-Rate Trigger (CRT) algorithm

## Slide 43
[43] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs trigger output

## Slide 44
[44] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS: Alert output to VHF & Beidou
Number of Aller packet in Sequence
SNR
(sigma)
Max (SNR)
Max/Std
Std
Sequence of Alert packets (dozen of packets):
ObsNumber (Alert Sequence Number) + ObsType (GRB or CAT)
Trigger Time-Window (Tb, Exposure)
SNRmax in image (and Energy range)
Detection quality (image stdev…)
Position (local coordinates in FoV)
Satellite attitude and satellite position
Slew Request
Tb
T0 (PktTime)

## Slide 45
[45] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS: LightCurve output to VHF
Light-Curve around Trigger Time Window (64 packets)
Time since LC-Tb (s)
LightCurveTb
LO-RES
MID-RES
HI-RES
Hi-Priority Low-Priority

## Slide 46
[46] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS: End of AlertSequence output to VHF
Shadowgram or Subimage around best Alert in sequence (49-64 packets)
Alert Descriptor packets (AD1: best Alert, AD2-3: CRT, AD4-5: IMT)
Details about best Alert found (+ info if Slew accepted or time-out)
best Alert

## Slide 47
[47] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS: VHF post-processing at CEA (EIC/ETC)
STT: Svom Trigger Targets
a.k.a Sub Threshold Targets
UGTS VHF packets used to create STT messages
  VHF Rec1 (CRT, IMT), Alert, AlertDescr1
  Create Json message strings
  Main info for Target:
    Time Tb and Exposure
    Localization (Rad/Dec/R90)
    SNR + SlewRq …
    + Satellite Long/Lat, Earth fraction…
STT realtime service of EIC/ETC, running at FSC
  Listen for arrival of VHF pkt
  Create STT json (if needed)
  Send STT on « science.eclairs »
  Forward to GWAC (over MQTT)
Depending on filter used, we can have several STTs (up to 2/min from Rec1)
ETC = ECLAIRs Trigger Control

## Slide 48
[48] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
ECLAIRs trigger simulations & tests

## Slide 49
[49] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS: Development and test (LTU at CEA)
Simulated satellite pointing, Earth passages, satellite slews and SAA passages
Simulated photon data: GRBs from previous missions through ECLAIRs response + CBX bkg + instrumental bkg from TVAC tests
Data injected into UGTS hardware model BB1
Running UGTS software  telemetry (CCSDS)
Example: 2 orbits with 4 GRBs (3h30)
UGTS triggers (2 algorithms running in parallel, coded in C++, running in hypervisor on CPU):
Count-rate trigger (CRT) : search count excesses (10 ms - 20 s) in 4 Energy strips and 8 detector zones, imaging of best excess (each 2.5 s).
Image trigger (IMT) : systematic imaging (20 s) in 4 Energy strips, sum images up to 20 min (each 20 s)
UGTS BB1

## Slide 50
[50] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS-output: X-band UssMessages + DuplicVhf
IMT excess in SNR sky image
(20.48 sec / IMT cycle)
CRT excesses (in SNR counts, before imaging)
(2.56 sec / CRT cycle)
Earth
Sub-image from IMT, Best alert
49 packets (8x8 pixels each)
Localisation error circles of alerts in sequence
Below slew threshold
Above slew threshold
Slew requested
VHF alert sequence (output products built)
(Run through UGTS acquired on LTU : example of 2nd GRB)
Lightcurves (3 resolutions):
High/Mid/Low (0.1/0.8/6.4 s binning)
Each: 4 Ebands + Saturating + Multiples
Seconds after TimeTb
Flight software V7.0.3 (CEA delivered to CNES 2023 / 2 / 14)

## Slide 51
[51] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
Conclusions

## Slide 52
[52] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS: Conclusions (as of day 4 of SVOM life)
Many Thanks to Application Software Team at CEA (since 2017):
Project: F. Daly (manager), S. Schanne (resp. scientist)
Hardware architect and FPGA firmware dev: H. Le Provost
Onboard software architect and dev: F. Château, C. Tahoulan, USS-dev: S. Sch, P. Kestener.
Ground test software (USS: ssbpy/ssbg): N. Dagoneau, S. Sch.
Ground data analysis: W. Xie
Local Test Unit (LTU) dev and test campaigns: S. Anvar + 8 more persons
+ Thanks also to CNES support team: Ph. Guillemot, MC. Charmeau, J. Galizzi, F. Gonzalez et al.
* have left | * still there
SVOM launched successfully (many thanks to all involved) ! ECLAIRs/UGTS will start soon the hunt for GRBs and deliver Alerts to the satellite and the world!
New tasks in flight!  ECLAIRs Trigger Control (ETC)
In-flight Commissioning Phase starts tomorrow !
  first ECLAIRs data acquisition in cold case, pointing test: mid July
  Trigger tuning: July-September, first Alerts maybe beg. August, first SlewRequests maybe beg. September
Replay of in-flight data on ground (LTU, BSV)  tune trigger parameters
Delivery of Svom Trigger Targets (aka Sub-Threshold Targets  GWAC+
Surveillance of the onboard Trigger during operations:
  IS support to BA: team at CEA (+ W. Xie and D. Zhao at NAOC).

## Slide 53
backup

## Slide 54
[54] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
UGTS trigger prototype: Estimate Num GRBs
Sarah Antier (CEA, thesis 2013-2016)
Database of ~2000 GRBs detected by Batse, Fermi/GBM, Swift/BAT, and Hete-II
 GRBs with light curves, extrapolated to ECLAIRs band (4-120 keV)
Background: 100 periods of 1500 s of CXB with Earth, chosen in 1 yr B1 law
SNRmax Thresh (σ)
6.5 sigma
Alert Thresh.
10 sigma
Slew Thresh.
 | Expected ECLAIRs GRB rates (GRB/yr) | 
 | > AlertThr (6.5 ) | > SlewThr (10 )
BATSE S+L GRBs | 46 – 57 ±8 | 40 – 49 ±8
bonus low E (XRR GBM, XRF Hete) | 4 – 10 ±1 | 4 – 9 ±1
bonus ImageTrig (low fluence LGRBs Swift) | 4 – 5 ±1 | 4 - 5 ±1
Total | 54 – 72 ±10 | 47 – 63 ±7
using detection efficiency, BATSE GRB/yr norm,
ECL FoV = 1.83 sr, Duty cycle = 54% (Earth, SAA)
For each GRB, chose Bkg period and 70 positions in FoV outside Earth in 1yr B1 law  though CxgSim (counts)  through both Triggers (SSM)
B. Cordier, J. Wie, et al (astroph) White paper SVOM

## Slide 55
[55] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
Tuning prior to launch using Testruns

## Slide 56
[56] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
Example Testrun
Testrun-TS-USS-03

## Slide 57
[57] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
Count-Rate Trigger
Chronograms from Xband UssMessages

## Slide 58
[58] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
CRT: background fit and excesses

## Slide 59
[59] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
CRT: shadowgrams produced

## Slide 60
[60] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
CRT: sky analysis, Earth and sources

## Slide 61
[61] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
CRT: sky analysis, SNR and Alerts

## Slide 62
[62] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
Image Trigger
Chronograms from Xband UssMessages

## Slide 63
[63] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
IMT: shadowgram build, clean, bkg fit

## Slide 64
[64] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
IMT: deconvolution, sky sum, analysis

## Slide 65
[65] –Xichang Svom Meeting - 2024/06/25 - S. Schanne
Trigger Output to VHF

## Slide 66
[66] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
VHF Alert: TimeWindows

## Slide 67
[67] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
VHF Alert: SNR and SlewRequests

## Slide 68
[68] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
VHF Alert: LightCurve and SubImage

## Slide 69
[69] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
VHF Recurrent2: Count-Rates

## Slide 70
[70] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
VHF Recurrent1: Sky Targets
 Svom Trigger Targets (a.k.a Sub Threshold Triggers) (json messages sent out for GWAC and others interested)

## Slide 71
[71] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
VHF Recurrent1: Satellite path (1 min)

## Slide 72
[72] – Xichang Svom Meeting - 2024/06/25 - S. Schanne
X-band: Satellite path (1sec)