## Slide 1: Validation of an ECLAIRs trigger by the Burst Advocates
Wenjin XIE (NAOC, CEA); Damien TURPIN (CEA)
2024.06.25 Xichang workshop
Notes: What are the different diagnosis to ensure the astrophysical origin of a SVOM trigger

## Slide 2: Outlines:
Overview of SVOM onboard detection process
ECLAIRs trigger by a new transient : key diagnosis
Excluding false triggers caused by non-astronomical sources
Summary

## Slide 3: SVOM onboard detection process
ECLAIRs (wide FOV) : Trigger, alert, slew request
GRM (wide FOV) : Trigger, alert, but not send slew request.
MXT: : Follow up in X-ray T0 + few minutes
VT: Follow up in optical wavelength T0 + few minutes
GRM particle monitor (plastic scintillator)

## Slide 4: SVOM onboard detection process (ECLAIRs trigger)
SNR/std > 6.5
SNR/std > 8.0 request slew
Set alert to the ground
~ 2 s each cycle
Satellite accept slew
SNR/std
Observed data
(Trigger algorithm could be found in Stephane’s talk)
(std represent standard deviation of sky SNR map
taking into account bkg fluctuation)

## Slide 5: SVOM onboard detection process (ECLAIRs trigger)
ECLAIRs detect a transient source with high SNR (not catalog sources)
SNR/std > 6.5  Trigger alert  VHF receive alert  detaile check
SNR/std > 8.0 (adjustable)  slew request  request rejected (due to satellite technical setting)
SNR/std > 8.0 (adjustable)  slew request  request accepted

## Slide 6: Trigger diagnostics
ECLAIRs SNR , Position
ECLAIRs light curve
ECLAIRs, background, counts properties
GRM light curve, background
GRM particle Monitor counts
MXT X-ray counterpart (if satellite slew)
  localization
  Light curve
Dataset we could obtain in ~30 minutes
(Detail hands on section see in Damien’s talk)

## Slide 7: Burst indicate by ECLAIRs : SNR, position (T0)
SNR and SNR/std
The higher SNR value, the higher probability of a transient detection
SNR changing with the time, and the position keep in the same region (< 1 degree)
Notes: https://fsc-integration.svom.org/ifsc-tools/grb/vhf-eclgrm/sb24062001

## Slide 8: Burst indicated by ECLAIRs : light curve (T0)
Pulse rise up in the light curve figure

## Slide 9: Burst indicated by GRM: light curve (T0)
GRM: 3 detector
iFSC-Tool show in tow energy band:
50 – 300 keV
300 – 700 keV
GRM count arise during the ECLAIRs trigger
Roughly follow the shape of ECLAIRs

## Slide 10: Burst indicated by MXT: light curve, positions (T0+few minute)
A decay light curve of MXT
XRT position located in the ECLAIRs region (90%)

## Slide 11: Excluding false triggers caused by non-astronomical sources
Particle background
  ECLAIRs saturanting and multiple count
  GRM particle Monitor counts (GPM counts)
  Kp index – space environment (See in Arnaud Claret talk in next)
  SAA Edge Area region, by the satellite position
Others …... like detector noise..
Notes: single count saturant, how to separate the GRB photons ??

## Slide 12: ECLAIRs multiple count and saturant count
Many counts that are clustered in a very short time scale (1micro sec)
If a particle event hits the detector it is going to produce an increase of the multiple counts and saturant counts (E > 150 keV)
This is very useful in case we are entering in SAA or if there are solar flares events.
6400 CdTe pixels In ECLIARs detection plane

## Slide 13: GRM Particle Monitor counts
GRM Particle Monitor counts the number of high-energy particles
A fake trigger could be occur if there is high count-rate in GRM particle Monitor

## Slide 14: Space environment index Kp
Credit: https://fsc.svom.org/ifsc-tools/mission/instruments
See Arnaud’s talk (next)
If kp > 5, Take care the data of the instruments

## Slide 15: Summary
Diagnosis of a new transient:
ECLAIRs : High SNR , positions around the same region, count rate rise up in the light curve
GRM light curve rise up and roughly follow ECLAIRs
MXT X-ray counterpart (if satellite slew)
  - faiding light curve
  - localization local in the ECLAIRs (90%)
Excluding false triggers
ECLAIRs, background, counts properties (Saturated and multiple count)
GRM particle Monitor counts increase
Space environment index Kp
Note: if Burst weak, detail analysis of the X-band data is need.
Notes: https://forge.in2p3.fr/projects/burst-advocates/wiki/Validate_the_high-energy_(HE)_trigger_AND_produce_the_HE_GCN_Circular_(iFSC-tools)
https://fsc.svom.org/home
https://svom.lam.fr/ifsc-tools-doc/grb/

## Slide 16: Thank you!
Congratulation on the successful launch of SVOM satellite !