## Slide 1: Cavity Haloscope for High-Frequency Axion Search at IBS-CAPP
SungWoo YOUN
iBS-CAPP
Axion Quest 2024
07. 08. 2024, ICISE, Quy Nhon, Vietnam

## Slide 2: Axion searches
Helioscope (solar axion)
LSW (axion at lab)
Haloscope (DM axion)
Cosmological boundary
Astrophysical constraints
1 GHz = 4.2 ueV

## Slide 3: Cavity haloscope – in a nutshell
Most sensitive for DM axion search in eV region
Quantum noise limited amplifier T
Signal amplification w/ minimal noise added
High field Magnet B
Boosting a→γγ conversion
*
P ~ 10–23 W
Cryogenics T
Lowering thermal noise
Tunable High-Q resonator
V, Q, C, Δf
Resonant frequency tuning
B. Evanov

## Slide 4: IBS-CAPP
CAPP-8T
CAPP-12TB
CAPP-8TB
CAPP-9T
CAPP-12T
S. Ahn

## Slide 5: Searches vs. predictions
Multiple
small cavities
Large
volume
Single
large cavity
Single
small cavity
Higher frequency
Strategy pursued by ADMX
CAPP confirmed the methodology Astropart. Phys. 97, 33 (2018)

## Slide 6: Multi-cell (pizza)
Multiple-cavity
  Inefficient volume usage (< 50%)
  Multiple antennae / signal combination / frequency-matching
Multiple-cell design
  More effective volume use (>90%)
  Single antenna / tuning structure => simple design
  Field configuration => In-situ cavity characterization
Multiple-cell cavity with a gap
Various advantages
Larger
volume
Multiple-cell cavity
(pizza cavity)
Multiple
small cavities
Single
large cavity
Large
volume
Single
small cavity
Higher frequency
Pizza with a saver
~4 x fTM010
TM010-like
TM110-like
Cavity center
Cell 2
Cell 1
PLB 777 412 (2018)
NIMA 1053 168327 (2023)

## Slide 7: Higher-order modes
TM010
TM020
TM030
Mode | frel | Qrel | Vrel | Cabs
TM010 | 1 | 1 | 1 | 0.69
TM020 | 2.3 | 1.5 | 1 | 0.13
TM030 | 3.6 | 1.9 | 1 | 0.05
Dielectric hollow
C ~ 0.4
How to tune the frequency?

## Slide 8: Higher-order modes
Frequency tuning for higher-order modes
Thick
Thin
Thickness | Frequency [GHz]
λ/5 | 8.99
λ/4 | 8.20
λ/3 | 7.22
λ/2 | 7.05
λ/1.5 | 6.86
TM030
Frequency
Tuning step
JPG 47 035203 (2020)
4 K

## Slide 9: Photonic crystal
Dielectric array
(photonic crystal)
Wire array
(plasma metamaterial)
PRL 123 141082 (2019)
ALPHA consortium
Large conversion volume for high frequency search
Metal |  | Dielectric
TM010-like | Resonant mode | Monopole
~ 0.9 | Form factor C | ~ 0.2
< 103 | Quality factor Q | > 105
> 3/cm2 | # density | ~ 1/cm2
Challenging | Construction / frequency tuning | Doable
S/m, ,
Unit cell
Unit cell
>10 x fTM010

## Slide 10: Photonic crystal
Frequency tuning
  2D (isotropic) expansion/contraction
Kirigami tessellations w/ auxetic behavior
Rotation of the center block
  Achievable using a single rotator
Nature materials 18, 999
Rotating regular squares

## Slide 11: High-frequency (III): Demonstration
dfadsfa
Consistent with simulation
PRD 107 015012 (2023)
4 K
Extending to a 5x5 array for larger volume
Experimental seutp for > 10 GHz ongoing

## Slide 12: Horn antenna array
PRD 108 L051101 (2023)
~THz
PRL 128 131801 (2022)
BREAD
Reflector
in solenoid
Axion-induced EM radiation from metal surface
JCAP 04 016 (2013)
Solenoid
Array of horn antennas
Parabolic mirror
Photo-detector
Dielectric lens for high directivity
Broadband search (~THz)
Less sensitive than resonant search
Sensitivity surface area
Dish antenna
Notes: Cassegrain reflector with a secondary convex mirror

## Slide 13: Search highlight (I)
CAPP-9T
(9T/127mm)
2-cell pizza
(2.1→3.2 GHz)
PRL 125 221302 (2020)
CAPP-8TB
(8T/165mm)
8-cell (1.6→5.9 GHz)
+ JPA (400 mK)
Near KSVZ sensitivity
Paper in preparation
CAPP-12T
(12T/96m)
3-cell (2.9→5.3 GHz)
+ JPA (400 mK)
KSVZ sensitivity
NM algorithm
PRL 133 051802 (2024)

## Slide 14: Search highlight (II)
CAPP-9T
(9T/127mm)
TM020 (2.9→5.2 GHz)
+ Kirigami tuning
Demonstration
arXiv:2403.13390
CAPP-12T
(12T/96m)
TM020 (2.9→5.1 GHz)
+ Kirigami + JPA (600 mK)
KSVZ run is about to begin
CAPP-9T
(9T/127mm)
Photonic crystal (>10 GHz)
Ready for physics run

## Slide 15: HTS cavities
Uniquely developed and matured fabrication technique
Integration with HF cavity designs
 | 1st Gen. | 2nd Gen. | 3rd Gen. |  | 4th Gen.
Material | YBCO | GdBCO | EuBCO + APC |  | EuBCO + APC
Volume [L] | 0.3 | 1.5 | 1.5 | 0.2 | 37
Freq. [GHz] | 6.9 | 2.3 | 2.2 | 5.4 | 1.2
Q-factor @ 8 T | 0.33 M | 0.5 M | 3.5 M | 13 M | 1.1 M
D. Ahn
QHTS ~ 10 x QCu

## Slide 16: Summary
Cavity haloscope stands out as the most sensitive method for dark matter axion search
Sensitive experiments are limited in the low mass region, while theoretical predictions favor the higher region
Novel designs for HF approach developed by IBS-CAPP and successfully demonstrated and implemented in searches
  Multi-cell / Higher-order modes (< 10 GHz)
  Photonic crystal (> 10 GHz)
  HF searches are currently ongoing
Integration with HTS technology will improve search speed
+

## Slide 18: Cavity haloscope
Most sensitive for DM axion search in eV region
  Resonant conversion of axions into microwave photons
Axion-photon conversion power (a→γγ)
Signal-to-noise ratio (SNR)
Unknown mass = > scanning rate (F.O.M.)
System noise (in temperature)
ex)
(~120 photons/sec)

## Slide 19: Equipment
Manufacture | Model | TB [mK]
BlueFors (BF3) | LD400 | 10
BlueFors (BF4) | LD400 | 10
Janis | HE-3-SSV | 300
BlueFors (BF5) | LD400 | 10
BlueFors (BF6) | LD400 | 10
Oxford | Kelvinox | 30
Leiden | DRS1000 | 5
Refrigerators
Magnets
Manufacture | Bmax [T] | Bore [mm]
AMI | 12 | 96
Cryo Magnetics | 9 | 125
AMI | 8 | 125
AMI | 8 | 165
SuNAM | 18 | 70
Oxford | 12 | 320
Name |  | 
CAPP-12T |  | 
CAPP-9T |  | 
CAPP-8T |  | 
CAPP-8TB |  | 
CAPP-18T |  | 
CAPP-12TB |  | 
Conducting parallel experiments targeting different mass regions!
Experiments
Notes: Start, describe, discuss, make a few wards

## Slide 20: High-quality factor
Minimal energy loss under a high magnetic field
ReBCO HTS
  Biaxially-textured 2D tapes (commercially available)
Normal state
Vortex state
Meissner state
High critical field BC2
&
High depinning frequency fdp
↓↓
ReBCO-based
High-Temperature Superconductor (HTS)
Stabilizer (Cu) 20 um
Protection layer (Ag) 2 um
Superconducting
layer (GdBCO) 2 um
Buffer layer (MgO) 0.7 um
Substrate [Hastelloy) 50 um
GdBCO HTS tape
Tapes on 2D pieces
Assembly
3D SC cavity
H
Hm
f
fdp
Vortex depinning
(high dissipation)
Vortex pinning
(low dissipation)

## Slide 21: HTS cavities
PRA 17 6 (2022)
 | 1st generation
Material | YBCO
Manufacturer | AMSC
Volume [L] | 0.3
Freq. [GHz] | 6.9
Q-factor @ 8 T | 0.33 M
Application | Demonstration
AMSC
Chart: Magnetic Field (T)
TM010
TM011
3rd generation | 
EuBCO + APC | 
Fujikura | 
1.5 | 0.2
2.2 | 5.4
3.5 M | 13 M
AQN search | Axion search
2nd generation
GdBCO
Theva
1.5
2.3
0.5 M
Axion search
cf. Qa ~ 106

## Slide 22: HTS cavities
Uniquely developed and matured fabrication technique
Integration with HF cavity designs
Q0 = 1.1M
cf. Qo = 140k for Cu
37-L HTS cavity
HTS rod
Q0 = 1.0M
cf. Qo = 120k for Cu
O. Kwon
D. Ahn

## Slide 23: QNL amplification
Flux-driven Josephson parametric amplifiers (JPAs)
SQUID
(nonlinear inductance)
U. of Tokyo & RIKEN
Frequency tuning
Parametric amplification
Standard quantum limit
SST 34 085013 (2021)
Best performance
in axion search application
Notes: quarter-wave coplanar waveguide resonator

## Slide 24: QNL amplification
Flux-driven Josephson parametric amplifiers (JPAs)
SQUID
(nonlinear inductance)
SST 34 085013 (2021)
Best performance!
Frequency tuning
S. Uchaikin
~30 chips
U. of Tokyo & RIKEN
Parametric amplification
But, … limited bandwidth!

## Slide 25: QNL amplification
Flux-driven Josephson parametric amplifiers (JPAs)
S. Uchaikin
~30 chips
U. of Tokyo & RIKEN
But, … limited bandwidth!
Parallel-Serial configuration
Standard quantum limit
Wideband search
Pump

## Slide 26: JPA optimization
Properties of JPA
  Optimized in 2-D space (Ib, Pp)
  Pre-determined over the full range
    => time-consuming
  Sensitive to experimental surroundings
    => less reliable
Nelder-Mead algorithm
  Numerical pattern search algorithm
    Nonlinear functions in multidimensions
    Iteratively refining a simplex of n+1 vertices
  Enables in-situ optimization => reliable
  ~10 iterations => time-efficient
  Prompt application to axion search (arXiv:2312.11003, PRL)
Electronics 12 2127 (2024)
Method | Pros | Cons | Char. time [s]
Predetermined | Comprehensive | Time-consuming / less reliable | 
Method | Pros | Cons | Char. time [s]
Predetermined | Comprehensive | Time-consuming / less reliable | 
Nelder-Mead | In-situ / optimal solutions | Heuristic | O(101-2)
JPA optimization: Nelder-Mead