## Slide 1
DRD3 WP1 R&D project : TPSCo 65nm MCMOS with high precision timing
and FCC-ee simulation work at IP2I
Discussion EoI FCC-ee, APC, 9 July, 2024
G. Boudoul, D. Contardo

## Slide 2
DRD3 WP1 R&D project : TPSCo 65nm MCMOS with high precision timing
for outer tracking layers* or inner high granularity digital electromagnetic calorimeter layers,
and ultimately 4D tracking, in a detector at the FCC-ee**
(full project description submitted to DRD3 WP1)
At large radii, precision timing (≲ 50 ps) will allow ToF PID and also ultra-high granularity in a pre-shower electromagnetic calorimeter section with a compact design
The constraints in position resolution, radiation length, and rates are relaxed at these radii, allowing to envisage high precision timing, despite its subsequent increase in power consumption.
Eventually, the project could extend to 4D tracking in layers at lower radii depending on the system radiation length that would be achieved.
* to some extend this work can aplly to layers in a full silicon tacker or in the layers surrounding a large gas volume detector w/o precise timing
** some intermediate projects, ALICE-3, LHCb-2 Belle-3 foresee central tracking with MCMOS

## Slide 3
DRD3 WP1 R&D project : TPSCo 65nm MCMOS with high precision timing
deployment and participants
1st stage - foundry submission
  Investigate TPSCo 65 nm performance for high precision timing (w/o amplification)
    the study can be done on few pixels matrices, with pitch down to < 10 μm & other configuration parameters (electrode size, epitaxial layer thickness...)
    pixels could be readout indivually through waveform digitisation and with different grouping to a fast preamplification and discrimination readout.
    the implementation could build on work already started in the first TPSCo 65 nm ER runs, & possibly benefit from synergies with R&D foreseen for the ALICE-3 VD and the “Fine-Pitch CMOS Sensors with Precision Timing" DRD3 project.
  Readout architecture
    implementing high precision timing ToA and ToT TDC feature in a pixel matrix of O(1) cm2, at the end of column and configurability of the pixel grouping at the amplification discrimination stage
    this part can benefit of synergies (or be merged) with the Fine-Pitch CMOS Sensors with Precision Timing" DRD3 project (targeting other applications than a VD detector)

## Slide 4
DRD3 WP1 R&D project : TPSCo 65nm MCMOS with high precision timing
deployment and participants
2nd stage – foundry submission
  demonstrator including both sensor analog part and the readout architecture in a reticule size pixel matrix and considering low power consumption and later extension to large size (stitched) sensors
  sensors w/amplification could be considered in synergies with the “CMOS Active SenSor with Internal Amplification - CASSIA" and the "Large electrode sensors with intrinsic amplification for ultimate timing performance" DRD3 projects if they evolve toward TPSCo 65nm
3rd stage - foundry submissions
  Large size stitched sensor prototype, benefiting form ITS3 and ALICE-3 developments and progress in DRD7 on low power comsumption
  Investigation of 3D wafer to wafer stacking for separation of the sensor analog and digital part of the readout
Further related R&D contributions being investigated at IP2I
contribution to mechanics and integration
Can build on experience in design of central tracking mechanical structures, integration & characterization
  implementing an integrated approach with modern AITV methods
  with deployment in mockups and prototypes

## Slide 5
FCC-ee simulation work
develop sensor signal digitizer* for full simulation and apply to PED studies
  Provide realistic simulation to :
    evaluate rate requirements (and physics inputs for readout architecture design)
    evaluate sensor performance parameters on reconstruction and physics performance
    optimise tracker configuration
  Software development :
    Key4hep framework
    EDM4hep data formats
    Geometry description built with DD4 hep
  Deployment
    1st version of cluster size (w/o simulation of signal collection) for initial FCC-ee feasibility studies
    2nd version (w/ electron collection) by end 2024
    Interfacing to physics and background simulation in close collaboration with the “software and computing” FCC PED team
    PED studies starting early-2025, in collaboration with IPHC