## Slide 1
Main Telescope
Auxiliary Telescope
AuxTel
Hologram recording
Use as disperser
Atmospheric calibration
auxTel french team
Notes: Ne pas rentrer dans les détails

## Slide 2: System throughput
Y4-Band out atm.
l (nm)
Transmission
or efficiency
in %
1 m
Atmosphere
Optics (mirrors, lenses)
Detector (CCD QE)
u
g
r
i
Z
y
Throughput =
telescope transmission x
Filter transmision x
QE(detector)
- ugriZy throughputs do not include atmosphere
- But the instantaneous effective passband, which governs the quantity of photons detected, includes the transmission of the atmosphere

## Slide 3: The atmospheric transmission (Stubbs et al. PASP, 119: 1163–1178, 2007)
Photometrists use photometric quality nights and narrow band filters
  No cloud
  Low humidity
  Low aerosols
LSST wants to use all nights with wide band filters
  Few clouds (grey absorption)
  Humidity (affects I & Z)
  Aerosol (affects U & G)
After correcting for Airmass:
O2, rayleigh depends on pressure
Determine vertical H2O, O3 and aerosols
Rayleigh scattering a 1/l4
O2
O3
aerosols
H2O
H2O
H2O
O2

## Slide 4: Photometric calibration
General principle
The photometric estimates of similar
objects are equally affected by the
local and instantaneous transmission
Instrumental response is controlled through
- Flat-fielding : image of a uniform sky brightness
-> Showing vignetting, dust and stains on optics (slow variations) and CCD pixel-to-pixel area variations (fast).
- Variation of passband with position on detector (slow)
- Slow variations of instrument throughput with time due to reflectivity changes
-…
Atmospheric transmission
- Global transmission of atmosphere: clouds/aerosols -> grey factor
- Variation of transmission with wavelength (depends on water, ozone and aerosols)
In the last 10km of the light travel, the transmission of atmosphere can vary rapidly with time AND its impact on the photometry depends on the objects’ color
-> AuxTel spectrograph mission
(i.e. identical colors)

## Slide 5: Variability of the atmospheric transmission

## Slide 6: 6 months of transmission measurements
H2O
H2O
H2O
O3
Aerosols
effective (instantaneous) passbands
=
Atmospheric transmision (variable)
Instrument throughput (stable)
u
g
r
i
Z
y
X
Airmass
@airmass=1

## Slide 7: Atmospheric compensation
what is it? We are going to take images in all atmospheric conditions. Effective bandwidths will then vary, which will complicate comparisons. To make light curves, the ideal is to relate all measurements to a standard atmospheric situation, i.e. PWV=2mm, z=1.2.
(It would also be interesting to think about what the average atmosphere is after co-addition: otherwise winter sky regions could give a different cosmology than summer sky regions...)

## Slide 8: Atmospheric compensation
The question: How can we determine the effect of the atmosphere on the photometry of a given object (so as to be able to compensate for it)?
Knowing that: it depends on the object's SED, and that we only know UGRIZY.

## Slide 9: Impact of precipitable water vapor (PWV) on the integrated flux of different stars
When PWV increases:
fy within the effective passband is more impacted for blue than red objects
X
dl
y passband
800
1000
l (nm)
Blue star
Red star spectrum
fy =
X
Atmospheric
transmissions
y passband effective
transmissions
i
Z
y
800
1000
l (nm)
900

## Slide 10: Atmospheric compensation
The question: How can we determine the effect of the atmosphere on the photometry of a given object (so as to be able to compensate for it)?
Knowing that: it depends on the object's SED, and that we only know UGRIZY.
Ingredients
  Atmospheric absorption curve in the passband T
    Main mission of AuxTel
    An open question (axe 1)
      atmosphere model (LibRadTran) measured from CAlSPEC standards possibly far from the LSST field -> requires confidence in the model
      curve directly obtained in the same direction as LSST with a Gaia standard
  Object’s SED (axe 2): most of the time only UGRIZYLSST will be known (after a few months)
    Interpolating an SED, but not always simple
    Black body thermal emission spectrum -> unrealistic
    Find the nearest object class in a library -> looks promising
With these ingredients
  Compute expected magnitudes for standard atmosphere at z=1.2 (T1.2) and current atmosphere at current z (Tz)
  Compensation to return to standard atmospheric conditions at z=1.2 is then (T1.2 – Tz)

## Slide 11: Color changes due to precipitable water vapor (PWV)
- If PWV increases -> flux in Y decreases -> All objects look bluer
- If the object is hot (blue), as the flux Y decreases mainly on the blue side, it loses more light in Y than a cold object (red). It therefore turns more bluer than a red object.
Reference atmosphere
Hot <---> cool
(Martin Rodriguez-Monroy)

## Slide 12: Color changes due to precipitable water vapor (PWV)
- color shift between PWV=3 and 9mm is between ~ - 40-100mmag depending on the stellar type
- Ignoring this variation means using average color shift -> object per object shift uncertainty ~20mmag
- If the stellar type is known and PWV measured with <0.5mm of precision =>
the differential shift between (K and F) or (F and O) stars is known with ~ 1mmag precision
Knowing PWV with <0.5mm allows to return to reference atmospheric conditions with 1mmag precision
Reference atmosphere
Hot <---> cool
(Martin Rodriguez-Monroy)

## Slide 13: Atmospheric compensation in action
Simulated compensation process on stellar SEDs (waiting for data)
Up: dotted = true SED, full = reconstructed SED from (UGRIzY)
Down: (corrected magnitude – true magnitude) @ standard atmosphere and z=1.2

## Slide 14
Atmospheric compensation in action
Simulated compensation process on stellar SEDs (waiting for data)
Up: dotted = true SED, full = reconstructed SED from (UGRIzY)
Down: (corrected magnitude – true magnitude) @ standard atmosphere and z=1.2

## Slide 15: Current developpements
- Spectrator: gets better every day
  Transmission curve available
  PWV OK : repetability ( precision?) < 0.3mm
  O3 on the right track
  Aerosols (including clouds) in progress
- LibRadTran: to what extent are 4 parameters enough to describe the atmosphere: pression, PWV, ozone, VAOD ?
  Many absorbers do not behave linearly, i.e. t(l,z) = t(l,1)z is often not exact (due to saturating absorbing lines).
- Estimating the best SED from (UGRIZY) alone: stars, galaxies and more…
- Catalog of stable spectrophotometric standards
  From Gaia data (out-of-atmosphere spectra)
  From AuxTel data (home-made catalog)

## Slide 16: Not discussed today
- pseudo flat-fielding in spectroscopy
- Interaction with FGCM
  Provide atmospheric parameters?
  Or provide the computed compensations?
  Or compensate after FGCM… (if FGCM uses an average nightly atmosphere).
    This would be the major income of the procedure: a non-photometric night would be as good as a photometric night…
- Compensation in U for variation of aerosols and pressure
  Expect similar procedure than in Z and Y

## Slide 17: Photometry atmospheric compensation: 3 ingredients to go from (zcur ,PWVcur) to (zstd ,PWVstd) – case of passband Y
1-Data: LSST current image in Y
Slope within Y passband
2-Data from LSST catalog : (UGRIZY)source
-> Top of atmosphere 1rst order SED model
3-Data from AuxTel : current atm. transmission
Water vapor standard
absorption band
Effective passband = Throughput x atm. transmissions
For each source on the LSST image
- Extract current LSST instrumental flux finstY,cur.
- Consult LSST catalog to interpolate its spectrum within passband Y
- Compute FpredY,std predicted flux in LSST-Y with standard atmosphere
and FpredY,cur predicted flux in LSST-Y with current atmosphere
Flux back to the standard atmosphere is then:
finstY,std = finstY,cur x (FpredY,std /FpredY,cur)
Integrate instrumental fluxes through standard and current atmospheres
Current atmosphere
zcur , PWVcur
standard atmosphere
zstd , PWVstd
finstY,cur
finstY,std
Water vapor current
absorption band

## Slide 18: Atmospheric compensation
Consider a source (star or galaxy) with current LSST instrumental flux in passband T (among UGRIZY) given by finstT,cur.
Procedure to obtain the estimation of this flux back to the standard atmosphere and airmass z=1.2 :
- Start with the top-of-atmosphere spectrum (toa) of the source SEDtoa(l)
if it is not known (general case if it is not a SN or a in a catalog of spectra):
    Modelize it from (UGRIZY)toa previously measured by LSST and a black body model or interpolation
    Or from (UGR)toa or (IZY)toa previously known and flux interpolations
    A good first approximation is to use (IZY)std or cur
- Estimate the current effective passband in LSST: Tcur(l) = Tinst (l) x tatmcur(l), where Tinst is the instrumental passband including filter + telescope throughput, and tatmcur(l) is
    deduced from the atmospheric parameters estimated with the AuxTel and Spectractor
    or directly obtained by the ratio SED(CALSPEC)curAuxTel /SED(CALSPEC)toa
- Compute FpredT,std (predicted flux in LSST with standard atmosphere and z=1.2)
    By integrating SEDtoa(l) x Tstd(l)
- Compute FpredT,cur (predicted flux in LSST with current atmosphere and airmass)
    By integrating SEDtoa(l) x Tcur(l)
- Flux back to the standard atmosphere is then finstT,std = finstT,cur x (FpredT,std /FpredT,cur)

## Slide 19: COMPLEMENTS

## Slide 20: Flat-fielding in spectroscopy
Flat-fielding is not standard for spectroscopy
  Ultimately, the CBP will be the best tool
  In the meanwhile,we use approximations :
    Keep only fluctuations due to camera window + CCD (dust & pixel-to-pixel gain variations)
    spatial and wavelength efficiencies factorize
  A line of light to produce a special flat-field
flat after filtering slow variations due to upstream optics
Blue flat pixel value
Red flat pixel value
Normal flat FELH0600
Vignetting affects direct image but not spectrum

## Slide 21: Signal from red star with V=10 (30s exposure, airmass 1)
First order only (with Z’ filter)
965+/- 1.5nm band
Simulation from SDC using
AuxTel CCD QE official curve
Measured HOE transmission curves
Atmospheric absorption model
AuxTel optical throughput
The less illuminated band
965nm+/-1.5nm (1’’ seeing equivalent)
For the hologram
30s exposure
Expect > 25000ge- from V=10 stars redder than V-I=0.5 (Teff<7300K or F0)
Worst sky bkgd will be 23000ge-/(‘’)2 (full moon)
-> Computation cross-checked (@10%) with the Pic-du-midi spectra obtained through holo-70
hologram
2nd order contamination
Sky bkgd/(‘’)2

## Slide 22: Compensation atmosphérique
C’est quoi? On va faire des images dans toutes les conditions d’atmosphère. Lss filtres effectifs seront variables, ce qui compliquera les comparaisons. Pour faire des courbes de lumière l’idéal est de rapporter toutes les mesures à une situation atmosphérique standard, soit PWV=2mm, z=1.2.
Il serait bon de réfléchir à ce qu’est l’atmosphère moyenne après co-addition: sinon les régions du ciel d’hiver pourraient donner une cosmologie différente des régions du ciel d’été…

## Slide 23: Compensation atmosphérique
La question : Comment connaître l’effet de l’atmosphère sur la photométrie d’un objet donné? (pour pouvoir le compenser).
Sachant que: il dépend de la SED de l’objet, et qu’on ne connaît que UGRIZY.

## Slide 24: Compensation atmosphérique (1)
La question : Comment connaître l’effet de l’atmosphère sur la photométrie d’un objet donné? (pour pouvoir le compenser).
Sachant que: il dépend de la SED de l’objet, et qu’on ne connaît que UGRIZY.
Ingrédients nécessaires
  Courbe de l’absorption atmosphérique dans la bande passante T
    Mission principale de AuxTel
    Question encore ouverte (axe 1)
      modèle d’atmosphère (LibRadTran) mesuré à partir de standards éventuellement loin du champ de LSST
      courbe directement obtenue dans la même direction que LSST
  SED de l’objet (axe 2): la plupart du temps on ne connaîtra que UGRIZYLSST (après environ 1 an)
    Interpoler une SED, mais pas toujours simple
    Trouver la classe d’objet la plus proche dans une librairie
Avec ces ingrédients
  Calcul des magnitudes attendues pour atmosphère standard à z=1.2 (T1.2) et atmosphère courante à z courant (Tz)
  La compensation pour se rapporter à une atmosphère standard à z=1.2 est alors (T1.2 – Tz)

## Slide 25: Current developpements
- Spectrator: gets better every day
  Transmission curve available
  PWV OK : repetability ( precision?) < 0.3mm
  O3 on the right track
  Aerosols (including clouds) in progress
- LibRadTran: to what extent are 4 parameters enough to describe the atmosphere: pression, PWV, ozone, VAOD ?
  Beaucoup d’absorbants ne se comportent pas de façon linéaire, autrement dit t(l,z) = t(l,1)z n’est souvent pas exact (raies saturantes);
- Estimation de la meilleure SED à partir de (UGRIZY) seul: étoiles, galaxies et autres…
- Catalogue de standards spectrophotométriques stables
  A partir de Gaia (spectres hors atmosphère)
  A partir des données AuxTel

## Slide 26: Pas abordé
- equivalent du flat-field
- Amélioration throughput -> travelling CBP
- LibRadTran: jusqu’à quel point 4 paramètres suffisent pour décrire l’atmosphère: pression, PWV, ozone, VAOD ?
  Beaucoup d’absorbants ne se comportent pas de façon linéaire, autrement dit t(l,z) = t(l,1)z n’est souvent pas exact (raies saturantes);
- Estimation de la meilleure SED à partir de (UGRIZY) seul: étoiles, galaxies et autres…
- Catalogue de standards spectrophotométriques stables
  A partir de Gaia (spectres hors atmosphère)
  A partir des données AuxTel

## Slide 27: Variability of the atmospheric transmission
Same airmass
Same O2
Same O3
No clouds (grey)
Change
  H2O (PWV)
  Aerosols
Wet / dry
Aerosol /
no aerosol

## Slide 28: Max. expected colour changes (airmass=1)
« Worst » stellar type
« Worst » galactic types
Water vapor
Aerosols
1 trajectory
= 1 SED
= 1 vector
@airmass=1
For airmass=1

## Slide 29: Auxtel : First estimates of atmospheric parameters
Variation of EQW for atmospheric lines illustrates sensitivity to atmospheric parameters (EQW)
EQW definition
Stellar lines
EQW independent on atmosphere
Atmospheric absorption lines
EQW depends on atmosphere
H2O
H2O
H2O
  ‘’fit’’ H2O :
  PWV ~ 3.2mm
data/simu(LibRadTran) for several hypothesis (PWV)
O2 atm. absorption lines
O3 atm. absorption bands
H2O atm. absorption bands
Hg
Hb
Ha
H2O
(720nm)
H2O
(820nm)
O2
(760nm)

## Slide 30: Control tool : EQW(O2) should depend only on airmass x pressure
EQW definition
After checking EQW(O2), we will measure
EQW(H2O(A)) and EQW(H2O(B))
H2O(A)
H2O(B)