## Slide 1: Non-uniformity study
Denys Klekots
(Taras Shevchenko National University of Kyiv)
denys.klekots@cern.ch denys.klekots@gmail.com

## Slide 2: Quick recap
The simulation gives the energy deposited in a strip for each simulated event.
Each strip has the dimensions of 1x1x400 mm. There are 167 by 167 such strips in the detector.
WLS fibres are located each 7 mm and the energy deposited in in grey square (see on a picture) is not recorded in the simulation output.
1 mm
1 mm
Fiber
Hit position
One virtual strip
Area where shower is developing as well, but the deposited energy in put to zero in simulation output.
x
y

## Slide 3: Simulation setup
The position of the primary hit was quasi-uniformly distributed in the square between fibers.
The energy deposited in each strip was multiplied by the weights from the beam test map
7 mm
7 mm
Fibers
x
y

## Slide 4: Total deposited energy gamma 25 GeV
7 mm
7 mm
Fibers
Hits inside entire cell

## Slide 5: Total deposited energy gamma 1 GeV
7 mm
7 mm
Fibers
Hits inside entire cell

## Slide 6
Non-uniformity map 25 GeV

## Slide 7: Non-uniformity map 1 GeV

## Slide 8: Conclusions
Based on the result of the simulations is it possible to conclude that:
  The sigma of total deposited energy (energy resolution) is about 1 % for 25 GeV gammas
  The sigma of total deposited energy (energy resolution) is about 1,5 % for 1 GeV gammas
  The deviation of the non-uniformity map is under about 2 % for 25 GeV gammas
  The deviation of the non-uniformity map is under about 1,5 % for 25 GeV gammas
  The difference in the development of the shower in the fiber affects the non-uniformity map

## Slide 9: Thank you for your attention

## Slide 10: Backup slides

## Slide 11: Previous mesh
1 mm
Fiber
Hit position
One virtual strip
Area where shower is developing as well, but the deposited energy in put to zero in simulation output.
Frame of non-uniformity map