## Slide 1: SiPM board EIC calorimetry
Frederic DULUCQ – Pierrick DINAUCOURT
July 22 2024

## Slide 2: Boards with 16 3x3 mm SiPM
Stacking based on 2 boards:
  SiPM board with an array of 16 SiPMs (3x3 mm² reference S14160-3015PS)
  Daughter boards to set the SiPM configurations /arrangements
1 SiPM board | 3 daughter boards | Description
16 fully independent 3x3 mm SiPMs | Name: v_ind Independent | Independent SiPM but common HV
 | Name: v_4p Grouped by 4 (in parallel: 4p) | 4 groups of 4 SiPMs
 | Name: v_2s Grouped by 2 (2 series): 4 groups with variant 1 4 groups with variant 2 | 8 groups of 2 SiPMs
  Dimension extended to 18.4 mm in one direction (in the other if needed)
  (due to SiPM footprint size in X)

## Slide 3: Daughter boards configurations
+ HV
Vout
+ HV
Vout
V_ind
(HV filter not shown)
V_4p
(HV filter not shown)
V_2s
If not possible to have 8 groups of 2 SiPMs
 Move to only 2 groups (1 for each variant)
NTC resistor connected to pin 1-2 of first connector
If possible LED connecter to pin 1-2 of second connector (then remove the 2-pin dedicated connector)
HV filtering done on daughter board (for ILCLab board, 1 per connector)
HV
2x HV

## Slide 4: Panel
SIPM
Vind
4 //
2s
2s
16 //
2s
16 //
16 //
16 //
SIPM
SIPM
Vind
Vind
4 //
4 //
Baseline
If possible
(16 // new)
If easier
2s

## Slide 5: Hamamatsu schematics
  HV filtering ( < 100 volts)

## Slide 6: Open questions (meeting July 19 2024)
Remove LED connector ? use pin 1-2 of first connector
  See slide 3
NTC resistor use 1-2 pin of the second connector
  See slide 3
Size 18.4 mm on 1 dimension or 2 dimensions ?
  See slide 2
V_2s2p only for 1 group ? other not used
  Sees slide 3
Perpendicular connection to daughter board 2s2p ?
  Remove daughter board in this case ? Still open

## Slide 7: Links for specs
Links
  SiPM board spec: https://cernbox.cern.ch/s/vt5BTljNIVfUQJK
  Daughter boards: https://cernbox.cern.ch/s/mCTOspGW7W6wDcl