## Slide 1: Le ²²²Rn comme traceur des apports d’eau souterraine vers les zones humides méditerranéennes : vers une standardisation des mesures et une aide à la gestion de ces espaces naturels
santoni_s@univ-corse.fr
Diana lagoon, Corsica Island, France
Sébastien Santoni1,2, P.-A. Guisiano1,2, A. Guerin1,2, D. Orticoni1,2 E. Garel1,2, T. Leydier1,2, F. Huneau1,2
1 Université de Corse Pascal Paoli, Département d'Hydrogéologie, 20250 Corte, France
2 CNRS, UMR 6134 SPE, 20250 Corte, France
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 2
Introduction
Mediterranean Wetlands
Coastal lagoons, alluvial wetlands, river banks and mouths, temporary ponds, low and high altitude peatlands.
Wetlands are essential for humankind
Food security
Climate change mitigation
provide
ecosystem services: water regulation, biodiversity conservation
High seasonality of hydroclimatic conditions in Mediterranean areas
Groundwater ensure part or total needs of human societies and sustainability of wetlands
Temporary pond of Tre Paduli, Corsica, France
Pink flamingo, Corsica, France
Palo lagoon, Corsica, France
Pink flamingo, Corsica, France
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 3
Introduction
Mediterranean Wetlands
Mainly attributed to :
Population growth
Water withdrawal
Agricultural land extension
Climate change
Lack in functioning knowledge
Population density of coastal regions and large coastal cities (over 500,000 inhabitants).
Source : UN - Barcelona Convention - Mediterranean 2017 Quality Status report
https://www.medqsr.org/fr/node/233c
Since 1970 : area of wetland worldwide decreased by 35%
Mediterranean : 48%
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles
Only 6% are in good conservation status (2013 - 2018).
41% of emblematic sites have seen their environment deteriorate (2010 -2020).
Notes: État de conservation des habitats humides d’intérêt communautaire : Seuls 6 % sont en bon état selon les évaluations de 2013 à 2018.
Évolution de l’état général des zones humides : 41 % des sites emblématiques ont vu leurs milieux se dégrader entre 2010 et 2020.
https://naturefrance.fr/indicateurs/etat-de-conservation-des-milieux-humides-naturels
https://www.statistiques.developpement-durable.gouv.fr/les-zones-humides-en-france-synthese-des-connaissances-en-2021?

## Slide 4
Introduction
 Especially their connectivity to groundwater.
Our main objectives using ²²²Rn:
Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn as a tracer of groundwater-wetland interactions.
Discussing challenges in measurement protocols and related uncertainties
Exploring ways to integrate radon into wetland management strategies, particularly in defining "Hydrogeological watershed-scale management area”.
High elevation peatlands « pozzines » of Corsica, FR
Little is known about Mediterranean wetlands hydrogeology
Mediterranean Wetlands
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 5
Introduction
²²²Rn is an interesting tracer of GW discharge because :
  Short half-life (3.8 days)
  Chemically inert nature
  Significant enrichment in GW
      (≈ 3 orders of magnitude)
Map of worldwide publications dealing with GW discharge using 222Rn to coastal oceans, rivers, lakes (incl. lagoons and ponds), and coastal oceans
(1996 – 2021 period, n = 336, in Adyasari et al., 2023).
Combined with other tracers such as temperature (T), electrical conductivity (EC), and Radium isotopes, ²²²Rn has proven effective tracer in detecting and quantifying significant groundwater fluxes to large continental and transitional wetlands or at coastal aquifer outlets in the sea.
In contrast, low and diffuse GW fluxes remain understudied, despite their role in sustaining the rich and threatened biodiversity of smaller, numerous, and scattered wetlands, as seen in the Mediterranean area.
Radon-222 as a Groundwater Discharge Tracer in Mediterranean Wetlands
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 6
Introduction
and more
Less than 0
Urban areas
France
Corsica
Mediterranean Sea
Rate of population growth in Corsica (%/year) :
Source : www. Insee.fr
Source : initiative PIM pour les îles de Méditerranée
All the compartment of the continental water cycle
↗ pressure from : climate change, population growth, agriculture and tourism.
High geology diversity, including hercynian granites = high uranium content
Wetlands of national and international interest (RAMSAR…).
Source : www. Infoterre.fr
Representative of the Mediterranean conditions with lots of ²²²Rn sources
Geology
Wetlands
The Corsica Island (FR), an observatory of Mediterranean Wetlands
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 7
Mountain lakes
Rivers and streams
Temporary ponds
Coastal lagoons / estuary
Ninu lake, Corsica (1709 m a.s.l)
Oriente lake, Corsica (2062 m a.s.l)
Padullelu, Bonifacio
Biguglia coastal lagoon, Bastia
Fiume Santu micro-estuary
Taravu
Gravona
Ascu
Introduction
The Corsica Island (FR), an observatory of the diversity of Mediterranean Wetlands
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 8
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 9
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
2 RAD7 Durridge® with accessories
“Soda Bottle setup”
Collect 1.5 l plastic bottles of surface water and groundwater potential end-members (if accessible).
Run the analysis for 5 minutes, six to eight times (total: 30 to 40 minutes).
Discard the first 10 minutes during data post-processing (equilibration).
Methodology
(remote areas)
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 10
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Methodology
(remote areas)
2 RAD8 Durridge® with accessories
“wat250 setup”
Collect 250 ml glass vials of surface water and groundwater potential end-members (if accessible).
Run the analysis for 5 minutes, six to eight times (total: 30 to 40 minutes).
Discard the first 10 minutes during data post-processing (equilibration).
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 11
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Results and discussion
²²²Rn activities with std. dev. close to zero for 9% of the samples (n = 44 / 493)
 There is no evidence of groundwater input, although this cannot be excluded.
²²²Rn activity clearly detected for 91% of the samples (n = 449 / 493)
 Evidence of groundwater input.
Most of Mediterranean wetlands investigated here can be considered as GDEs
Since 2022, we performed ²²²Rn analysis on 493 water samples from Mediterranean wetlands
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 12
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Results and discussion
Upstream
Downstream
Estuary
Coastal Lagoon
Alpine lakes
Rivers and temporary ponds
Distance to the sea
Rain and snow influence (recharge area)
Groundwater contribution
Seawater
There is an upstream-downstream evolution of EC in wetlands
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 13
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Results and discussion
Distance to the sea
Mixing processes
²²²Rn and EC “correlated”
= GW dilution with seawater
Estuary
Coastal Lagoon
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 14
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Results and discussion
Distance to the sea
Mixing processes
²²²Rn and EC
“NOT correlated”
= Decay and degassing
Alpine lakes
Rivers and temporary ponds
²²²Rn signal loose
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 15
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Results and discussion
Magmatic rocks
granites
Metamorphic rocks
Calcite
High U-bearing minerals
Low U-bearing minerals
Calcarenites
Metamorphic rocks
Weathering products of granites
Water-rock interactions
Distance to the sea
Mixing processes
²²²Rn signal loose
There is a clear influence of the lithology of the underlying rocks on the ²²²Rn signature
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 16
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Results and discussion
Focus on GW end-members
EC values in GW ranges from 20 to 1400 µS/cm
²²²Rn activities in GW ranges from 39±15 to 460,000 ±13,150 Bq/m3
End members displays a wide range of EC and ²²²Rn contents, with more or less strong contrasts in between GW and surface water
²²²Rn activities are 1 to 3 orders of magnitude higher in magmatic rocks
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles
Notes: 1400 - One thousand four hundred
460 000 - four hundred and sixty thousand

## Slide 17
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Good potential of ²²²Rn to trace GW flows to the river system
Focus on Rivers
Guisiano et al.
Magmatic context
(high U)
Baseflow index (%GW/total river discharge) and ²²²Rn activity display same trend
Results and discussion
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 18
Focus on alpine lakes : RINOSU (2066 and 2083 m asl)
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Focus on Alpine lakes
Corte city (400 m asl)
Ninu Lake (1709 m asl)
Capitellu Lake (1930 m asl)
Melu Lake (1746 m asl)
Rinosu Lake (2083 m asl)
Ninu Lake
Capitellu Lake
Melu Lake
Rinosu Lake
Oriente Lake (2062 m asl)
Oriente
Lake
Despite their mountain-top location, all these alpine lakes are GW-dependent.
Results and discussion
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles
Notes: we looked for radon in the water of 5 Alpine mountain lakes and obtained values between one and six thousand Bq/m3

## Slide 19
Or1
Or2
Or3
Or4
4076 Bq/m3
4063 Bq/m3
601 Bq/m3
210 Bq/m3
4
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Surface water
Groundwater
The correlation between T, EC, and ²²²Rn is not clear.
T and EC are also likely affected by snow patches near the lake in some areas.
Maximum ²²²Rn values agree with clearly visible NE-SW oriented lineaments in the surrounding granite basement (OR1 & OR4).
Clear input of radon-rich groundwater into the Oriente lake
Focus on Alpine lakes
Oriente Lake (2062 m asl)
Results and discussion
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 20
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Focus on temporary ponds
Padulu (Bonifacio calcarenites)
Ground level
5 months
2 months
Water Level (m asl)
²²²Rn activity (Bq/m3)
The water level in the pond varies with the seasons.
During high-water periods, low ²²²Rn activity follows rainfall events.
Rain contribution
GW contribution
Temporary ponds are GDE.
The GW contribution extends the hydroperiod.
The rest of the time, ²²²Rn activity is high, indicating groundwater input, especially during low-water periods and drying phases.
Results and discussion
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 21
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
April (14/04/2022)
May (13/05/2022)
Focus on coastal lagoons : spatial trend
S1
S2
S3
S4
S5
S1
S2
S3
S4
S5
Rainfall (surface water input)
NO Rainfall (GW input ?)
Guerin et al.
Maximum ²²²Rn activity detected in S2 and S1  Indicates lateral and upstream GW inputs.
Decrease in ²²²Rn activity towards the sea channel.
Increase in ²²²Rn as low-water periods approaches
Strong spatial variations in ²²²Rn activity, and thus in GW inputs.
Sediment influence on the lowest ²²²Rn activity levels?
EC (µS.m-1)
Results and discussion
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 22
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
S2
S2
Rainfall (surface water input)
NO Rainfall (GW input ?)
Guerin et al.
Focus on coastal lagoons : depth heterogeneity
EC (µS.m-1)
Consider the sampling depth !
Results and discussion
Low depth GW inputs : fresh water is less dense than brackish water
April (14/04/2022)
May (13/05/2022)
Bottom-up flows: groundwater inputs by artesianism? (seepage flows)
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 23
2. Challenges in Standardizing ²²²Rn Measurement Protocols for Highlighting GW-Wetland Connectivity
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 24
Some suggestions / recommendations
To highlight GW-wetland connectivity, In situ ²²²Rn measurement is always preferable. However, given the low and diffuse GW fluxes in the Mediterranean smaller, numerous, remote, and scattered wetlands, sampling remains an interesting alternative to save time, money, energy and gain resolution in space and time.
2. Challenges in Standardizing ²²²Rn Measurement Protocols for Highlighting GW-Wetland Connectivity
Before sampling
During sampling
When possible, identify groundwater sampling points (springs, wells, and boreholes) to establish the local ²²²Rn baseline.
Take into account :
  Seasonality : e.g. Δ GW discharge dynamics.
  GW input depth : i.e. make an EC profile.
Try to gather hydrogeological framework information (topographic, geological, and piezometric maps…) to target wetland sampling areas.
About bottles
  Note date and TIME (decay).
  Avoid any head-space
  Prefer glass jugs with a septum (to prevent the glass bottle from exploding due to altitude variations).
  Otherwise, use plastic bottles not to loose the sample, even if not perfectly gas-tight.
  1 liter for RAD7, 250 ml for RAD8
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 25
Match the number of samples taken in the field to the analysis time, to avoid losing the signal due to radioactive decay.
Increase analysis time or prefer RAD8 to RAD7 for water samples from wetlands (low ²²²Rn levels). “RAD8 boosts sensitivity 70% higher than RAD7, significantly reducing data uncertainty.”
Running the analysis for 5 minutes, six to eight times (total: 30 to 40 minutes) on Mediterranean wetland samples gave good results with acceptable std. dev.
Data post-treatment : remove the two first 5 min of measurement due to equilibration.
Some suggestions / recommendations
2. Challenges in Standardizing ²²²Rn Measurement Protocols for Highlighting GW-Wetland Connectivity
To highlight GW-wetland connectivity, In situ ²²²Rn measurement is always preferable. However, given the low and diffuse GW fluxes in the Mediterranean smaller, numerous, remote, and scattered wetlands, sampling remains an interesting alternative to save time, money, energy and gain resolution in space and time.
During lab analysis
During data interpretation
Consider the ²²²Rn activity may be impacted by :
  Sampling distance to GW source, aquifers heterogeneity
  Physical parameters : permeability, decay, diffusion, dispersion, degassing, turbulence, stratification …
  Waterbodies mixing processes
  Rocks lithology (Uranium abundance)
  Potential ²²²Rn source from sediments
The presence of ²²²Rn can be enough to SIMPLY highlight connectivity with GW, which is of particular interest to Wetland’s manager.
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 26
3. Exploring ways to integrate ²²²Rn into wetland management strategies
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 27
Challenges in Managing Small Mediterranean Wetlands
3. Exploring ways to integrate ²²²Rn into wetland management strategies
Lack of Adequate Management Framework
  Wetlands smaller than 50 ha often fall outside the European Water Framework Directive (WFD).
  As a result, they are rarely included in local water management plans.
Decision-Making Challenges for Local Authorities
  Management relies then on local authorities with limited scientific data and expertise.
  Decisions are driven by compromises between ecosystem preservation and socio-economic development.
  Protection measures are mostly limited to existing legal frameworks, which may not be adequate because limited to the strict wetland limits, excluding recharge areas.
Increasing Human Pressure & Low Visibility of small wetlands
  These wetlands suffer from low public awareness and poor communication about their ecological value.
  Growing anthropogenic pressure is observed, particularly in coastal and/or urban areas.
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles
Most Mediterranean wetlands are groundwater-dependent ecosystems (GDEs)
  Better resilience to drought and CC.
  Closely connected to the watershed (surface and groundwater), making them vulnerable to human-induced pressures (e.g., land use changes, water abstraction).

## Slide 28
Towards Improved Management of Small Mediterranean Wetlands
3. Exploring ways to integrate ²²²Rn into wetland management strategies
Define an ‘Hydrogeological watershed’ / Espace de bon fonctionnement
As scientifically defined hydrosystem-scale area with limited human activities, ensuring wetland sustainability. This requires :
  Considering surface & groundwater fluxes at regional scale.
  Using ²²²Rn as Relevant and SIMPLE indicator of GW-wetland connectivity
Implementing Scientifically Piloted Management
  Balancing socio-economic needs with ecological integrity.
  Improved stakeholder coordination
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles
Towards a Science-Based Protection Framework
  Small GDEs could be included in the European Water Framework Directive (WFD).
  Local authorities require effective financial and regulatory tools for conservation.

## Slide 29
This study highlights a clear spatial and temporal hierarchy in the dependence of Mediterranean wetlands on groundwater availability.
While this connection enhances resilience to drought, it also increases vulnerability to human pressures across the entire watershed.
In this context, ²²²Rn could become a key indicator for defining the Hydrogeological watershed management area of wetlands.
Integrating ²²²Rn into management strategies would help ensure long-term preservation, if a simple and reliable measurement/interpretation protocol is established.
Conclusion

## Slide 30: Le ²²²Rn comme traceur des apports d’eau souterraine vers les zones humides méditerranéennes : vers une standardisation des mesures et une aide à la gestion de ces espaces naturels
santoni_s@univ-corse.fr
Diana lagoon, Corsica Island, France
Sébastien Santoni1,2, P.-A. Guisiano1,2, A. Guerin1,2, D. Orticoni1,2 E. Garel1,2, T. Leydier1,2, F. Huneau1,2
1 Université de Corse Pascal Paoli, Département d'Hydrogéologie, 20250 Corte, France
2 CNRS, UMR 6134 SPE, 20250 Corte, France
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 32
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
The ²²²Rn signal is weaker (low U in rocks), and altered by degassing and decay
Baseflow index (%GW/total river discharge) and ²²²Rn activity display a complex trend
Guisiano et al.
Focus on Rivers
Metamorphic context
(low U)
Results and discussion

## Slide 33
Focus on alpine lakes : RINOSU (2066 and 2083 m asl)
Ri1
Ri2
Ri3
Ri4
Ri5
3913 Bq/m3
904 Bq/m3
1161 Bq/m3
5887 Bq/m3
4463 Bq/m3
8
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Focus on Alpine lakes
Rinosu Lake (2083 m asl)
Low temperatures associated with low EC and high ²²²Rn activity
Knowledge:
GW temperature is close to the annual atmospheric average of the area
Groundwater is weakly mineralized and ²²²Rn-rich
Clear input of cold, weakly mineralized, and radon-rich groundwater into the Rinosu lakes
Surface water
Groundwater
Results and discussion
Despite their mountain-top location, all these alpine lakes are GW-dependent.

## Slide 34
1. Are all small Mediterranean wetlands dependent on groundwater? Insights from ²²²Rn
Focus on coastal lagoons : seasonal trend
April (14/04/2022)
May (13/05/2022)
June (16/06/2022)
February (17/02/2022)
March (09/03/2022)
March (15/03/2022)
Hydroclimatic conditions strongly influence the hydrology of this small coastal lagoon :
After rainfall via runoff (February and March)
During low-water periods via groundwater input (June).
Guerin et al.
These maps spatialize EC data using kriging and homogeneous EC scale.
Lower EC values in February and March followed rainfall events.
Sea Channel Opening
NO Rainfall (GW input ?)
Rainfall (surface water input)
Rainfall (surface water input)
Rainfall (surface water input)
Higher EC values in May campaign took place after a mechanical opening of the sea channel, which quickly closed before the June campaign experiencing a decrease in EC.
NO Rainfall (GW input ?)
EC (µS.m-1)
Results and discussion
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles

## Slide 35
2. Discussing protocols challenges
Sampling volume experiment with Durridge® RAD7
Tests on 36 radon-222 measurements (8 sites with 4 replicates each) to compare 1.5, and 1 liter plastic water bottles with in situ rad Aqua (reference)
RAD7
Cycle : 5 minutes
Recycle : 6 times (12 for RadAqua)
Total: 30 minutes (60 for RadAqua).
 | Radon 1L (Bq/m3) | Radon 1.5L (Bq/m3) | Radon in situ (Bq/m3)
Min | 3 | 3 | 3
Median | 61 | 71 | 40
Max | 356 | 670 | 770
 | Radon 1L (Bq/m3) | Radon 1.5L (Bq/m3) | Radon in situ (Bq/m3)
Min | 10 | 0 | 240
Median | 826 | 870 | 1063
Max | 6180 | 6683 | 6449
²²²Rn activities
²²²Rn std. dev.
After normality and variance tests, we performed 1-Way ANOVAs to compare the obtained values :
On ²²²Rn activities, in the end, no significant differences in between the three methods
p(same) = 1
p(same) = 0.999
Radon in situ seems display a better sensitivity to low ²²²Rn levels
Data still in validation process
p(same) = 0.998
p(same) = 0.978
p(same) = 0.591
p(same) = 0.466
..but…
the ²²²Rn std. dev. is higher for 1.5 l plastic bottles, and comparable in between in situ RadAqua and 1 l plastic bottles !
Rencontre Scientifique interdisciplinaire sur le Radon
14-16 Mai 2025
Université Aix-Marseille, Campus Saint Charles