## Slide 1
«Mass» & Z selection of post accelerated beams in SPIRAL1
Bertrand Jacquot, GANIL

## Slide 2
Summary : M & Z selection of post-accelerated beams
Introduction (SPIRAL1 & CIME)
Cyclotron selectivity: M/Q selection
Ion Stripping: Z selection at high energy
Exemples: 56Ni* and 20O*

## Slide 3
- RIB purety is of utmost importance for many scientific cases
typical stable ion intensity : 108-13 pps
Radioactive beams intensity for reaction study : 104-7 pps
Final Selectivity is a result of
(production + ionization+ acceleration & transport + detection)
Focus on the 2 methods used after RIB production
a) M/Q selection in the Cyclotron CIME
b) Z selection with Stripping and Brho selection in Z-spectrometer
Introduction : Post accelerated beams in SPIRAL1

## Slide 4
introduction of SPIRAL1 : M/Q & Z selectivity
4
SPIRAL1 Facility: selection with cyclotron and/or stripping (for a given ion source)
1 compact cyclo Kb =265
For radioactive ions
2 Separated Sectors cyclotrons Kb =380 MeV
-SPIRAL1 CIME
-Stripping
Stripper
Zspectrometer
RIB

## Slide 5
Synchronise ions with acceleration (Efinal => FRF = H. Frevolution)
RBr
(field B, Mass M, charge Q) gives Frevolution
FRF= H. Frevolution
H=integer called « harmonic »
Frevolution ~ function (M/Q , B)
Cyclotron theory : How to get a beam accelerated
FRF =H. Frevolution

## Slide 6
.
if FRF≠ H Frevolution
If B field is adjusted for given ion (M1,q1) H. Frevolution= FHF
good transmission
Ion revolution not synchronized with RF cavity : ion Deceleration
Contaminants are eliminated
What happen if B not ajusted to M/Q : M/Q selection
For a contiminant (M2,Q2) FHF ≠ H. Frevolution
zero transmission

## Slide 7
1) For an ion of interest M1,Q1 tune B1 at given FRF
2) A small dB reduces strongly the cyclo. transmission
Very clean selection (many turns )
selection not sufficient
Ion of interest
Cyclotron resolution R=1/ (2p H Nturn)
dB/B1
~ d M/Q
FRF=H.Frevolution/ ~ Q. B1 / M

## Slide 8
Light beams (He, N,O,Ne, Ar): Purety possible with CIME
Large isobar mass difference good for Cime cyclotron
ex: 17Ne – 17O dM /M= 8 . 10-4
Fwe can get fully stripped ion, even at relatively low energy
Heavy beams :
very small isobar mass difference ex: 56Ni*- 56Co* dM/M= 3 . 10-5
56Ni*- 56Fe dM/M= 1.2 10-4
~ Mass selection not sufficient in Cime
- Stripping at high energy is needed
RIB purification at SPIRAL1 : is CIME sufficient ?

## Slide 9
Stripping and Br selection in the « Z-spectrometer »
- Stripper foil
Zspectrometer
Br= g M v /q
Brho selection
Stripping for RIB purification at SPIRAL1
Velocity determined by Cyclotron acceleration
Q~ F(Z,E) if Q=Z (fully stripped ions) easy selection

## Slide 10
Stripping is a Z selective process
Charge distribution is centered at <Q> = F1(Energy, Zbeam)
Charge distribution width sq= f2(E, Z)
At large energy <Q> = Z ( fully stripped beam )
Stripping with carbon foils
Fully stripped beam is desirable Q=Z , but « high energy » is needed
What is the energy required for 50% efficiency ? (F(Q=Z)>50%
  O E> 2.7 MeV/A
  Ar E> 9.1 MeV/A
  Ni E>22,5 MeV/A
  (no possibility at SPIRAL1)
Stripping for RIB purification at SPIRAL1
What is the energy required for 20%
efficiency ? ? (F(Q=Z)>20%
  O E>1.6 MeV/A
  Ar E> 5.4 MeV/A
  Ni E>15 MeV/A

## Slide 11
Heavy beam purification : only a possiblity at high energy with stripping
For Ni*, very small isobar mass difference ex: 556Ni*- 56Co* dM/M= 3 . 10-5
56Ni*- 56Fe dM/M= 1.2 10-4
-No mass selection in Cime cyclotron
- Stripping at 15 Me/A can be envisaged
56Nickel* purification at SPIRAL1
Acceleration in 56Ni14+ (105pps) polluted by 56Co14+ (10(5-6pps)
polluted 56Fe14+ (109pps) (febiad+booster)
Downstream a C stripper we have 56Ni28+,27+,26+ 56Co,27+,26+,25+ 56Fe26+ ,25+,24+
Selection by Brho of (A=26 Q= 28 +) 20% efficiency …
Charge state Q=28+, Nickel is pure
but only 20% remaining :
    F(Ni, Q=28+) =20%
    F(Ni, Q=27+ )=52%
    F(Ni, Q=26+) =19%
Br
Q=28+
Ni
Q=27+ Co+Ni
Q=26+
Fe +Co
+ Ni

## Slide 12
20O
RIB purification at SPIRAL1 : one light exemple
Transmission as a function of M/Q ~ Bcyclo : ajusting Bcyclo (Frf fixed)
Purification of 20O3+ with 40Ar 6+ , 20Ne3+, 20F3+ at 3.0 MeV/A
with M/Q selection (no stripping)
20Ne
40Ar
20F
Elimination of
All contaminants is possible
But 20F3+ tricky
20O2+ was polluted by molecules (not identified) , Q=3+ better

## Slide 13
Light beams can be purified most of time (A<40) :
Avoid stable beams at dM/Q< 0.001 , think to standard contaminants
Heavy beams purification : CIME cyclotron is not sufficient
Only a possiblity at high energy with stripping
  (but low efficiency at low energy limit strongly, the applicability of the method : ex for Nickel*, no solution under 15MeV/A
Source selectivity is always desirable
Nanogan : select only gazeous atomes or molecules
1+// N+ with (febiad +ECR booster) produces many contaminants
Stable contaminants are very dangerous because of their intensity
Conclusion : purification of post-accelerated beams

## Slide 14
CIME Properties
Typical pollutions induced by the charge booster // Febiad // Nanogan
Improving resolution in Cime : slight gains are possible
Additive slides

## Slide 15
CIME CYCLOTRON
15
CIME CYCLOTRON (H=2,3,4,5 marginally H=6)
M/q resolution function(Nturn, Harmonic)
1 compact cyclo Kb =265
For radioactive ions
2 Separated Sectors cyclotrons Kb =380 MeV
cyclotron CIME Bromax#2.4 T.m |  |  |  | 
Harmonique et inflecteur |  | Energies en MeV/A | Nombre de tours Nt (Nominal) | Résolution Nominale 1/2pHNtour
H=6 | r = 45mm | [ 1.20 , 1.70] | 80 (low transmission) | 3.3 10-4
H=5 | r = 45 mm | [ 1.70 , 3.93] | 101 | 3.1 10-4
H=4 | r=45 ou 34 | [ 2.72, 6.20] | 121 | 3.2 10-4
H=3 | r=45 ou 34 | [ 4.85 , 11.0] | 280 | 1.8 10-4
H=2 | r=34mm | [ 11.0 , 25.0] | 330 | 2.2 10-4
Energy limit : K=265 MeV
Brmax = 2.4 T.m
Emax 8He1+= 4.3MeV/A
20O3+= 6.2MeV/A
20O4+= 11.0MeV/A

## Slide 16
CYCLOTRON: typical pollution with sources
Selection of Radioactive ions not sufficient : many stable contaminants
  Metalic chamber : 56Fe , 58Ni, 60Ni, 48Ti , 52,53,54Cr, Mo (Febiad)
  Alumium chamber : 26Al (Booster) Fluorin: 19F (Nanogan)
  Copper : 63,65Cu (waveguide of ECR Nanogan , Booster)
  « Natural gases » 14,15N //20,21,22 Ne // 40, 36Ar // 86,….,78Kr // 129,…Xe// 4He Water : 16O, 17O, 18O
Residual beams Measured with ECR booster | Intensity, typical
14N4+ 16O4+ + 12C3+ | 1012pps
15N4+ 13C3+ 18O3+ | 107-9pps
84Kr19+ | 107pps
56Fe15+ | 105pps (booster), 108pps (febiad)
22Ne5+ intéret ? | Imax=105pps
40Ar9+ | Imax=108pps
129Xe29+ | 105pps
58Ni13+ 48Ni12+ | Imax= 105pps
63,65Cu14+ | Imax=106pps
27Al7+ | Imax=106pps
Efforts on source
selectivity are
very importants

## Slide 17
Nturn =112
Nturn= 130
Selectivity can be increased
Increasing the turn number by 20%
Cyclotron resolution R=1/ (2p H Nturn)
Increasing turn number & Cyclotron resolution)
Transmisison is sharper
With 130 turns than 112
Doubling the turn number
not possible:Transmission =0%
(Problem at injection)