## Slide 1: SPIRAL1 beams from AGATA
Pierre Delahaye for the Target/Ion-source group

## Slide 2: Outline
Historic GANIL
SPIRAL1
Experimental areas
SPIRAL1 and its limitations
  Beam production : sources
  Beam purity
Beam requests
Conclusion

## Slide 3: Introduction – SPIRAL
Charge breeder
TISS
To CIME
To IBE
To LIRAT/ DESIR

## Slide 4: Beam production
Nanogan
For gaz
MonoNaKe
For alkaline
TULIP(-FEBIAD)
For proton-rich isotopes
FEBIAD
For condensable
58 primary beams from 12C to 238U
Graphite target (so far)
4 ion sources
Target/stopper
Primary beam
Ion source
Separator
TISS
The ISOL technique
To user/
acceleration
N+
1+
1+

## Slide 5: Beam production
Nanogan
For gaz
MonoNaKe
For alkaline
TULIP(-FEBIAD)
For proton-rich isotopes
FEBIAD
For condensable
58 primary beams from 12C to 238U
Graphite target (so far)
4 ion sources
Target/stopper
Primary beam
Ion source
Separator
TISS
The ISOL technique
To user/
acceleration
N+
1+
1+
Advantages
Intensity (directly N+ beam)
Purity (gases only)
Disadvantages
Lower charge states (and energy)
Gases only
Advantages
Broadband
Disadvantages
Non selective
Advantages
Intensity (high efficiency for most alkali)
Purity (low ionisation energies only)
Disadvantages
Only a few elements
Advantages
Very fast release
Disadvantages
Rather low in-target production

## Slide 6: Focus on the FEBIAD
Objective: production of radioactive metallic ions
Future
Post acceleration of 56Ni in 2025.
On-going development of target-ion source systems for Fe-Co-Ni beams (PhD work of Erwan Le Villain) and target fragmentation (Postdoc work of Sophie Hurier)
April 2023 (50Cr)
July 2024 (58Ni)
September 2024
(129Xe)
Before 2023
Since 2021
Irradiated with 48Ca (2021), 36Ar, 84Kr (2022), 50Cr (2023), 58Ni (2024),129Xe (2024)
100+ radioactive isotopes/isomers seen, including around 60 at post-accelerable intensities (>1E5pps).
48,49Cr produced for the first time in 2023
Fe/Co/Ni beams produced for the first time in 2024
« Heavy » ions produced in 09/2024

## Slide 7: Contamination & Purification
Source
D1P
Charge Breeder
D3P
CIME
Stripping

## Slide 8: Contamination & Purification
Source
D1P
Charge Breeder
D3P
CIME
Stripping
MonoNaKe
For alkaline
Nanogan
For gaz
FEBIAD
For everything
>
>
Chart: 
The best is to have a pure beam from the source

## Slide 9: Contamination & Purification
R≈200
Keeps isobars of the ion on interest
Source
D1P
Charge Breeder
D3P
CIME
Stripping

## Slide 10: Contamination & Purification
Increase the CS of both the ion of interest and its contaminants
Re-introduce stable contamination
  Gases (100 nA-10µA)
  Metals (< 100 pA)
Source
D1P
Charge Breeder
D3P
CIME
Stripping

## Slide 11: Contamination & Purification
R≈200
Keeps N+ isobars and ions of similar A/Q as the ion of interest
Source
D1P
Charge Breeder
D3P
CIME
Stripping

## Slide 12: Contamination & Purification
CIME can be used as a mass spectrometer
R = 2000-3000
Example for H=4 (Energy range 2.7-5.8 MeV/A)
Possible to detune CIME to get less contamination at the cost of lower intensity for the ion of interest
Source
D1P
Charge Breeder
D3P
CIME
Stripping
credit: B. Jacquot

## Slide 13: Contamination & Purification
Full stripping at high energy
n-deficient only
The higher the energy, the higher the efficiency (typically >12 AMeV)
Model, not measurement
Source
D1P
Charge Breeder
D3P
CIME
Stripping
credit: B. Jacquot

## Slide 14: Beam requests
This Workshop:
13O, 62Zn, 44Ti, 55Co, 56Ni, 57Ni
Rate on target > 1E5 pps
Purity > 50%
Energy > 8 AMeV
Last Workshop:
Rate on target > 1E4 pps
Max rate : 1E6 pps (limited by VAMOS 0°)
Purity > 1%

## Slide 15: 13O
 | Intensity (pps) | Energy (AMeV) | Purity
Request | 1E5 | > 8 | 50%
TGT - Nanogan | 1.6E3 | 7 - 19 | ≈100%
Never done, never seen
1E8 pps in-target production, but estimated 1E4 pps 13O4+ at the source (very short T1/2 = 8ms)
Estimated 1.6E3 pps in post-accelerated beam, no real contamination problem
Improving the release efficiency is possible but very unlikely to reach 1E5 pps
Conclusion : not feasible at the required rate. R&D necessary to increase the rate

## Slide 16: 44Ti
 | Intensity (pps) | Energy (AMeV) | Purity
Request | 1E5 | > 8 | 50%
TGT – FEBIAD + CIME detuning | 1E5? | 7 - 18 | ≈50%
TGT – FEBIAD + stripping | 1E5? | 7 - 18 | 100%
Ti does not diffuse in the target : not possible to produce in SPIRAL1
Has to be produced in batch mode. A sample of 5-10 MBq should be sufficient for a 2-week experiment at the required post-accelerated rate (already done by PSI for ISOLDE)
Test with stable Ti necessary to estimate the release time and the source efficiency.
Unknown difficulties with procuring the sample and safety regulations
Conclusion : probably feasible, but to be confirmed

## Slide 17: 62Zn
 | Intensity (pps) | Energy (AMeV) | Purity
Request | 1E5 | > 8 | 50%
TGT – FEBIAD | 1.1e5 | 6 - 17 | 0.5%
TGT – FEBIAD + CIME detuning | 1.5E4 | 6 - 17 | ≈30%
TGT – FEBIAD + stripping | Max 2.2E4 | 14 - 17 | 100%
Estimated post accelerated rate is sufficient, but strongly contaminated with 62Cu (radioactive) and 62Ni (stable)
Purification by CIME or stripping possible but not while keeping the 1E5 pps rate goal
Contaminants could perhaps be « frozen » at the source if the target is cold enough, but this has to be tested offline AND online
Conclusion : feasibility uncertain at required rate and purity. Online test necessary

## Slide 18: 56Ni
 | Intensity (pps) | Energy (AMeV) | Purity
Request | 1E5 | > 8 | 50%
TGT – FEBIAD | 4.7E4 | 6 – 16.5 | 0.002%
TGT – FEBIAD + CIME detuning | 3.0E3 | 6 – 16.5 | ≈50%
TGT – FEBIAD + stripping | Max 1.2E4 | 13 – 16.5 | ≈100%
Estimated post accelerated rate is already below the 1E5 pps mark, without any purification
After stripping at max energy, the rate will be ≈ 1E4 pps
End-of-year experiment will confirm feasability of full stripping for 56Ni but also for 57Ni and 55Co
Conclusion : not feasible at the required rate.

## Slide 19: 55Co
 | Intensity (pps) | Energy (AMeV) | Purity
Request | 1E5 | > 8 | 50%
TGT – FEBIAD | 4.8E5 | 7 – 18 | 0.8%
TGT – FEBIAD + CIME detuning | 4E4 | 7 – 18 | ≈99%
TGT – FEBIAD + stripping | Max 1.8E5 | 12 – 18 | 100%
Estimated post-acceleration rate sufficient, but strongly contaminated with 55Fe (radioactive) and 55Mn (stable)
Contamination can be reduced with CIME or stripping.
The 1E5 pps rate goal is still achievable after stripping, but only for the highest energies
If the 56Ni stripping experiment is succesful, 55Co purification by stripping will be confirmed
Conclusion : Most likely feasible. Confirmation expected at the end of the year

## Slide 20: 57Ni
 | Intensity (pps) | Energy (AMeV) | Purity
Request | 1E5 | > 8 | 50%
TGT – FEBIAD | 5.6E5 | 6 – 17 | 0.3%
TGT – FEBIAD + CIME detuning | 6.1e4 | 6 – 17 | ≈80%
TGT – FEBIAD + stripping | Max 1.6E5 | 13 – 17 | ≈100%
Estimated post-acceleration rate sufficient, but strongly contaminated with 57Co (radioactive) and 57Fe (stable)
Contamination can be reduced with CIME or stripping.
The 1E5 pps rate goal is still achievable after stripping, but only for the highest energies
If the 56Ni stripping experiment is succesful, 57Ni purification by stripping will be confirmed
Conclusion : Most likely feasible. Confirmation expected at the end of the year

## Slide 21: Takeway messages
55Co, 57Ni and 44Ti probably technically feasible
56Ni and 62Zn not feasible at the 1E5 pps rate goal without contamination
55Co, 56,57Ni are being developed, others have to be supported by LoI, proposals, etc (otherwise no development)
Laser ionization would help all of those beams but 13O to exploit the full post-accelerated rate.
More beam could be feasible
  Check the possible rates on the beam chart
  Keep sending us requests with minimum purity, minimum rate and energy
Basic information on beams: https://u.ganil-spiral2.eu/chartbeams/
inquiries to be sent at chartbeams-spiral1@ganil.fr

## Slide 22: Thank you for your attention

## Slide 23: Operating modes
L. Maunoury et al, 2018 JINST 13 C12022
1+ shooting through, for identification, low energy (10-20 keV) physics in LIRAT and since 2024, low energy (2 MeV/u) post-acceleration of very light ions (up to A≈12)
N+ shooting through for post-acceleration (up to 24 MeV/A)
1+/N+ for post-acceleration
SP1CB as a source for post-acceleration tuning or experiments with stable or long-lived isotope beams (gaz only)
Using a 1+ TISS without primary beam as a source for stable beams (to tune CIME) or long-lived isotopes (batch mode)

## Slide 24: Acceleration
Up to 24 MeV/u, limited by:
charge state distribution at the output of the charge breeder
platform limitations
Chart: Z
| 10 | 11 | 12 | 17 | 18 | 19 | 26 | 36 | 37 | 54
 | 6 | 7 | 7 | 9 | 10 | 10 | 15 | 18 | 19 | 26
Emax

## Slide 25: MonoNaKe (credit P. Jardin) Thick target + SIS
Low ionization potential atom
+
High work function surface
= Surface ionization
Designed and tested in 2006
Recently, interest for Li beams
Successful production test of 8Li (2e7pps) and 9Li (1e5pps) at low energy in 03/2024
Successful experiment with post-acc. 8Li (5e5pps at 1.2MeV/A) in 06/2024
In the future
Development and tests with Re ionizer to enable other elements

## Slide 26: TULIP (credit P. Jardin) Thin 58Ni target + SIS
20Ne Primary beam
Mo-Ni-Mo target
(fusion-evaporation)
DLC window
Graphite catcher
Radioactive ion beam
60 mm
TULIP cavity
On-line test 2023: production of 74-78Rb+ ions (≈10%)
Ongoing
Off-line test of the TULIP-FEBIAD coupling (metallic ions) + rotating wheel (production x7)
In the future
Off line test of Re ionizer
On-line production of 74Rb (2025?)
On-line test of the TULIP-FEBIAD with a 54Fe
target and a 14N beam (2026?)
Rotating wheel
Production rate (calculated PACE4)
Measured rate
Isotope mass
LE rate

## Slide 27: Production summary
48,49Cr, 50Mn, 53m/gFe 55Co, 56,57Ni, Cs isotopes down to A=117,
Other isotopes (ongoing analysis)
n-deficient Rb isotopes
8,9Li
All beams >1E3pps at low energy
Chart: Test/experiments with SPIRAL1 beams
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Nanogan | 2 | 7 | 7 | 8 | 8 | 5 | 9 | 10 | 6 | 6 | 5 | 2 | 4 | 0 | 0 | 0 | 0 | 1 | 3 | 2 | 1 | 0 | 1 | 1 | 3
FEBIAD/TULIP/MonoNaKe | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 2 | 2 | 0 | 2 | 3 | 3 | 4 | 1
We can/could do many exotic beams !
(Operational limit at 1 TISS/month)

## Slide 28: Post accelerated FEBIAD beams - intensity
M. Assié, WS Cible-Source, 09/2023
All radioactive beams > 10^4 pps after acceleration
Direct measurements (19, mostly Nanogan)
Extrapolation from direct measurements (46)
Estimates (107, FEBIAD only)
172 isotopes + possible batchmode beams

## Slide 29: Post accelerated FEBIAD beams - purity
Usable without any purification
Requirements
Min rate : 1E4 pps
Max rate : 1E6 pps (limite VAMOS 0°)
IoI/contaminant > 1/100
172 isotopes
3 isotopes
Disclaimer
contaminants not measured for A>57
Contaminants not formally identified
Other possible contaminants

## Slide 30: Post accelerated FEBIAD beams - purity
Usable after mass separation in CIME
Using CIME as a mass spectrometer
172 isotopes
26 isotopes
Requirements
Min rate : 1E4 pps
Max rate : 1E6 pps (limite VAMOS 0°)
IoI/contaminant > 1/100
Disclaimer
contaminants not measured for A>57
Contaminants not formally identified
Other possible contaminants

## Slide 31: Post accelerated FEBIAD beams - purity
Usable after stripping at max E
172 isotopes
36 isotopes
With full stripping
Requirements
Min rate : 1E4 pps
Max rate : 1E6 pps (limite VAMOS 0°)
IoI/contaminant > 1/100
Disclaimer
contaminants not measured for A>57
Contaminants not formally identified
Other possible contaminants