## Slide 1
Possibilities offered by (3He,n) reactions with AGATA and NEDA
Jose Javier Valiente Dobón
IFIC-CSIC, Valencia

## Slide 2: Overview
Introduction
  What is NEDA
  NEDA detectors
  NEDA electronics
  General properties
Some possible physics cases (3He, n) for NEDA+AGATA
What about 3He targets?
Summary

## Slide 3: What is NEDA?
Versatile neutron detector designed to be coupled to gamma-ray arrays
Neutron detection is based on the liquid scintillator EJ301 with good neutron-gamma discrimination capabilities.
FEE fully digital system:
  200 MHz and ENOB 11,3
  Global Trigger System - GTS
Predecessor Neutron Wall
AGATA
NEDA

## Slide 4: NEDA detectors
Regular hexagon to tile up a surface
20 cm depth detector
5” PM Hamamatsu R11833-100HA QE 33%
PSA liquid EJ301  3 liters
TiO2 Reflexion paint
Expasion chamber ΔT =10-50 degrees
Voltage divider transistorized for large counting rates
Single to differential converter
1mm mu-metal shielding
Self produced
Expansion chamber

## Slide 7: General properties of NEDA
Flexible array – variability of focal positions (experiment dependent) or configurations (mechanics to be done)
  Various campaigns of physics depending on the configuration
Neutron multiplicity filter. Efficiency 1n 30%
Pulse shape discrimination – online trigger selectivity
Off-line implementation of traditional algorithms and/or Neural Networks
Angular resolution: Dθ(0.5 m) = ±7° - Dθ(1 m) = ±4°
Timing better than 1 ns. Same performance digital/analog.
Energy resolution ΔE/E: NEDA 1m – 40%, NEDA 7m – 5%

## Slide 8: First physics campaign with NEDA
M. Bentley
65As – isospin symmetry
Boso
71Kr-71Br – isospin symmetry
B. Cederwall
T=0 pairing 88Ru
B. Cederwall
T=0 lifetimesPd-Ru
E. Clement/J.J. Valiente-Dobon
Octupoles N=Z region Ba
S. Leoni/B. Fornal
Gamma decay near threshold 14C
D. Mengoni
Shape coexistance 60Zn
D. Ralet
84Mo T=0 pairing
M. Palacz/M. Gorska
Pd high spin
N. Redon
Sm, Pm deformations
N=Z
Fusion-evaporation reactions involving 1 or 2 neutrons tagging.
B.S. Nara Singh
A=50 – isospin symmetry
S. Lenzi
Iso. Symmetry Breaking A~63
J.. Nyberg
102,103Sn excited levels
~ 44 beam days
18th of april until 29th of July 2018
TO BE DONE

## Slide 9
The NEDA time line
2017-2019
NEDA@GANIL
2021-2025
NEDA@HIL
2026-2028
NEDA@LNL
?

## Slide 10
(3He,n) reactions
2p transfer  large exoticity of final neutron deficient nucleus
2p

## Slide 11: Coupling GRIT-NEDA-AGATA
One could imagine it as a campaign dedicated NEDA+AGATA+VAMOS or a unique configuration NEDA+AGATA+GRIT+VAMOS
Mechanical integration
Electroncis integration
…

## Slide 12
Broken mirrors: the 36Ca-36S case
32Ca
N=Z
Z
N
MEDJ = EJ,Z> - EJ,Z<
N=Z
Mirror Energy Differences
Isospin symmetry Island of inversion
33Ca
Island of inversion

## Slide 13
LSSM calculations for 36Ca-36S
Sdpfu-mix interaction: model space (sdpf)pn and (sd) pn
two-body matrix elements of the Coulomb potential
u
(sd)12
p
(sd)12
d5/26s1/21d3/21
d5/26s1/22
d5/26s1/21d3/21
d5/26s1/22d3/22 (pf)2
36Ca
d5/2
d3/2
s1/2
p
8 ns
The proton being further away feels less the Coulomb repulsion and therefore is more bound

## Slide 14
Experimentally CMED in 36Ca-36S
Neutron detector NEDA 2p
Angular distributions with NW
DWBA calculations (Twofnr) – One step process  Potel more realistic calculations
Optical potential: C.T. Liang et al. JPG 36 (2009) 085104
3He target
36Ar (3He,n)36Ca
Populate the 2+/02+ via 34Ar (3He,n) 36Ca
Proton nature of the 2+ in 36Ca?
Measure the 0+ 0+ transition internal pair production e+e- The e+e- pair production branch in the 0+  0+ transition is 50 more intense than the EC branch. Lifetime?

## Slide 15: Spectroscopy of 20Mg
18Ne (3He,n) 20Mg
M. Borrajo, T.R.Rodriguez, J.L. Egido, PLB 746, 341 (2015)

## Slide 16: Transfer 18Ne (3He,n) 20Mg
DWBA calculations (Twofnr) – One step process
SF x
θLab(degrees)
Energy (MeV)
Energy of the neutrons emitted in the laboratory reference frame
Optical potential: C.T. Liang et al. JPG 36 (2009) 085104
17
3
0+ (6p2h)

## Slide 17: Wealth of transfer reactions
14O (3He,n) 16Ne  2.7 105 ions
18Ne (3He,n) 20Mg  7.7 106 ions
22Mg (3He,n) 24Si  1 105 ions
34Ar (3He,n) 36Ca  9 105 ions
52Fe (3He,n) 54Ni  3 104 ions
54Fe (3He,n) 56Ni  stable
…
F. Galtarossa, A. Gadea, A. Goasduff, A. Gottardo, S. Bottoni, D. Mengoni, M. Rocchini, …

## Slide 18
8B = 1p halo nucleus
9C = good candidate for 2-proton halo and 2p structure
. 1st excited state : two proton halo
. Higher levels : 2 proton structure observed
T. Zerguerras et al, Eur. Phys. J. A 20, 389–396 (2004)
J.D. Ovejas PLB 843 (2023) 138007
. Waiting in CNO cycle : direct 2p capture rate
on 15O
CNO cycle
pure 2p emission
3-body decay
X. Xu, Physics Letters B 727 (2013) 126–129
28S  correlation between 2p emitted from high lying states
N. Furutachi et al, Prog. Theor. Phys., 122,2009
Study of two-proton structures
Marlene Assie
Case of 7Be(3He,n)9C
Case of 15O(3He,n)17Ne
Case of 26Si(3He,n)28S

## Slide 19
3He target possibilities
Solid target
Cryogenic target
Density: 1020 − 1021 at/cm2
Cost:?
Density: 1018 - 1019 at/cm2
Cost: 100 euros

## Slide 20: Summary
Versatile neutron detector to be coupled to gamma-ray arrays and charged particle detectors.
High efficiency neutron detector based on the liquid scintillator EJ301 with good neutron-gamma discrimination capabilities.
NEDA can be used in:
  Fusion evaporation reactions
  Transfer reaction, such as (3He,n), (d,n), etc.
  …
A discussion on compatibility with GRIT and AGATA—both in terms of mechanics and electronics—is necessary; however, I believe the possible anticipated physics outcomes fully justify the effort.
One could also imagine a campaign only NEDA+AGATA …
Collaboration G. Pottel (Uni. Sevilla) for the 2p transfer crossection calculations

## Slide 21: END

## Slide 22: Transfer reactions 3He,n
One neutron detector NE213 n/γ discrimination and one HPGe detector
58Ni (3He,n) 60Zn
Let’s look at one example: 60Zn
Angular distribution

## Slide 23: Shape coexistence in 80Zr
Five 0+ states below 2.25 MeV that correspond to different minima in the triaxial potential energy landscape which constitutes a unique example of multiple shape coexistence in the nuclear chart.
T. Rodriguez and J.L. Egido, Physics Letters B 705 (2011) 255–259
S.M. Fisher et al., PRL87, 132501 (2001)
Fusion-evaporation reaction 24Mg (58Ni,2n)

## Slide 24: Shape coexistence in 80Zr
NEDA 2π
DWBA calculations (Twofnr) – One step process
78Sr (source – 2.2 106 ions/μA) considering 1.4 μA of protons and 5% charge/acc. efficiency  1.5 105 ions/s
78Sr (3He,n) 80Zr
4.0 MeV/u
Optical potential: C.T. Liang et al. JPG 36 (2009) 085104
SF x

## Slide 25
25
The tests are being performed at LNL with the following instrumentation:
2 x BC501A (5” x 5” cylindrical prototype detector)
2 x BC537 (5” x 5” cylindrical prototype detector)
SIS3302 100 MS/s, 16 bits 8 ch. digitizer (analog setup)
SIS3350 500 MS/s, 12 bits 4 ch. digitizer
Digital PSA
VD tests
Prototype tests
Relative efficiency performance
Cross-talk between the detectors
Timing
NEDA test setup at LNL
BC537
BC501A
BaF2

## Slide 26: Simulations: Single cell unit
Detailed study of GEANT4 simulations for a single detector of NEDA.

## Slide 27
PSA measurements for NEDA
Algorithm for digital PSA for various Photomultipliers (fast to slow HQE 5’’)
FOM for various PM
PM tests for best PSA NEDA capabilities

## Slide 28
Timing measurements for NEDA
Algorithm for digital timing for various Photomultipliers (fast to slow HQE 5’’)
The time resolution is obtained with a 60Co source and for two frequencies 500 MHz (the nominal) and 200 MHz (final NEDA one)
PM tests for best timing NEDA capabilities

## Slide 29
P.A. Soderstrom et al., to be submitted NIM A
Pulse shape discrimination for NEDA
NN
Traditional
NEDA test: PSA Neural Network