## Slide 1
test bench 28nm

## Slide 2: outline
28nm chip layout
1st results on pixels matrix chip
DAQ board
Pixel configuration
Transistors setup

## Slide 3: 28nm chip Layout
4 independents sub-chips
  Matrix of 432 pixels – « Pixel_28nm »
  Bank of ring oscillators – « RO_28nm »
  Transient signal detection – « SET_28nm »
  Bank of transistors – « DEVICES_28nm »
    N&PMOS in 0.9V & 1,8V
Each chip is bonded on boards
Sortie CSA ouput (pixel 36)

## Slide 4: Test bench for 28nm chips
Test benches are ongoing
  Firmware not fixed
  Still big work for the C++ software
  …
Test setup for a ring oscillators chip in TJ65nm

## Slide 5: DAQ board
  Mother board V3 – V4
  Features:
  nanoPC BeagleBone card (RJ45 linlk)
    RJ45 link
    Linux Debian OS integrated in a SDCard
    Connected as a local network on a PC
  FPGA (Cyclone III – Quartus 13.1)
  Digital signals availables
    40 TTL signals (local tests (1)-HE10 connectors)
    32 LVDS signals (irradiation tests (2)- DB37 connectors)
  Analog channels available
    4 SAR ADC’s 16 bits
    4-10 DAC (16 bits)
  Monitoring (°C, current supply)
  Charge injector
  Lab tests
  Compatible with irradiation tests
ADCout vs Gain

## Slide 6: RO28nm
30 RO’s per size (7T, 9T, 12T)
Power supply:
  VDDIO (1,8 V),
  VDDD (0,9 V - ~10-20 mA)
Configuration through a shift register
  It doesn’t work but implemented in the firmware
10 inputs/ 4 outputs:
Pinout ASIC RO 28nm
Readout chronogram
Sizes 7T, 9T, 12T

## Slide 7: Firmware/software RO 28nm
Start/stop as a parameter
  Tunable in the C++ file
Software side:
  Power supply management
  Each sequence can be tested
  Counters readings in a console or in a file
firmware RO 28nm synoptic
Cell vs code mux.
Main menu RO 28nm

## Slide 8: VHDL example: RO28nm
address decoder
Commands from BeagleBone management
ro28nm_readout
1
1
2
Peripheral registers
registers to store parameters from data
Regulators enable
DAC’s data
Width counting
…
2
4
3
PLL’s
Clkin = 100 MHz
Clkout (4 max.)
200 MHz for SIGNAL TAP
100 MHz for clk_state
10 MHz
1 MHz
…
3
Multiplexors
IN/OUT locally
- CONxx
IN/OUT remotely
- LDVS drivers
4
2
1
ro28nm config
Management of 30 configuration bits
1
3
2
ro28nm acquisition
Management of 2 signals:
rstb: reste active low
start/stop: width of pulse count tunable
3
ro28nm readout
Reading of 3 output (7T, 9T, 12T)
- store counters values in a shift register
- Read values in BeagleBone through data bus
1
1
Control registers
Normally use to control the status of a command
Can help to synchronize read/write sequences and know their status
Can avoid also sleep, wait.. in a sequence
carte_test_28nm.vhd (top view)

## Slide 9: Synoptic firmware (simplified)
peripherals_registers.vhd
data registers
parameters registers
periph_reg_sel (32b)
address_decoder.vhd
address building
DAC’s : 0x3000
periph.: 0x4000
config.: 0x2000
…
cs_dac<4..0>
address (15b)
DEVICE TREE:
GPIO-> bus GPMC
- address (15b)
data (16b)
I2C (2bus 1&2)
- power supply adjustment
- readings I/V
- RTC
- …
SPI
- Pt100
BeagleBone Black
dac.vhd
data (16b)
ctrl_reg_sel (16b)
cmd_start/stop
sck
sdi<15..0>
to 10 DAC’s
synchro
gpmc_oen_ren
gpmc_wen
reset
read
write
reset
200 MHz
(SIGNAL TAP)
PLL
clk_in : crystal 100MHz
100 MHz
10 MHz
1 MHz
locked
config.vhd
(ro chip)
data config
control_registers.vhd
s_data
s_ck
s_mux<5..0>
RO chip
acquisition.vhd
(ro chip)
- launch counting in Ro chip
rstb
(*): pulse width tunable
start/stop(*)
ro_config_sel
ro_acq_dec
readout.vhd
(ro chip)
- launch counting in Ro chip
ro_readout_dec
s_ck_readout
s_ld_readout
data 7T, 9T, 12T
sdi
adc.vhd
sck
to/from ADC
firmware FPGA Cyclone III -> Quartus 13.1

## Slide 10: Address declaration in the software RO28nm
C++ files used address/data previously defined in the address_decoder .vhd

## Slide 11: Pinout BeagleBone
Bus GPMC
Power supplies
GPIO
Slow control
SPI (Pt100)
JTAG
I2C

## Slide 12: BeagleBone environment
OS embedded Linux Debian
  C++ environment
All project files are in the TestBoard folder
Library folder
c++ project files in SRC_USER
DAC, ADC, temp. in SRC_SHARED
GPIO,… in SRC_UTILS
Makefile: allow to compile cpp file and generate .o output binary file
Critical file, syntax very important

## Slide 13: START UP
GPMC bus and GPIO must be configured and certainly specified inside the boot of the beaglebone
  DEVICE_TREE in debian/STARTUP folder
  .dts file compiled to a .dtbo and move in /lib/firmware/
Normally follow the sequence inside the init.sh file
GPMC configuration in a .dts file
config_pin

## Slide 14: Slow control
I2C
  Chip power supply
    4 I/V monitoring (MAX9611)
      0xE0
      0xE6
      0xF8
      0xFE
    4 programmable resistors (tpl102)
      0x51
      0x52
  RTC (ds1307)
    W: 0xD0
    R: 0xD1
  EEPROM (cat24c256)
    W: 0xA0
    R: 0xA1
I2C bus – tpl102-100
100k
20k
0.1
to chip
I2C bus – MAX9611
3.3V
LT3021
MAX9611
Synoptic per regulator (*)
(*): modified on V4 DAQ board
on V3:
- 4 × LT3021 (500mA max.)
on V4:
- 2 × LT3021 (500mA max.)
- 2 × LTC3026 (1.5A max.)
- need to integrate this modification in the software

## Slide 15: DAQ V3 V4
V3
V4
V3 ≠ V4
- regulators
- swap pins
- add connectors for debug
-…