## Slide 1
Gauthier Guignard
LP2iB
Status PIPERADE 2025
Notes: Hello
New PHD student on PIPERADE
Present status 2025

## Slide 2
PIPERADE at DESIR
PIPERADE
GPIB
Cooling & bunching of the beam
Beam purification
& mass measurement
PIPERADE at LP2iB
Notes: -> DESIR : we are working on two devices designed for the DESIR hall at GANIL : GPIB for ….. And PIPERADE for ….
-> LP2iB : Currently this two device are here at LP2IB, so what is on this beam line ?

## Slide 3
PIPERADE at LP2iB
Ion bunch
Stable-ion source
(⁺ and ⁺ )
General Purpose Ion Buncher (GPIB)
PIèges de PEnning pour les RAdionucléides à DESIR (PIPERADE)
Ion beam
Position-sensitive MicroChannel Plate (MCP)
Continuous
Notes: -> On this beam line we have : - stable ion source, use primarly K and Rb – GPIB –PIPERADE – the detectior whish is a position sensitive Microchannel plate
-> show arrow : we go from continuous to bunched, after that what happen when the ion bunch arrived in PIPERADE ?

## Slide 4
PIPERADE
P. Ascher et al., PIPERADE: A double Penning trap for mass separation and mass spectrometry at DESIR/SPIRAL2, Nucl. Instrum. Methods Phys. Res. A 1019 (2021) 165857
Purification trap
Measurement trap
Extraction optics
Injection optics
Diaphragm
From
GPIB
MCP
Counting
ToF
Position
Designed and machined at MPIK Heidelberg
Notes: -> here we have a view inside PIPERADE : he a double penning trap with : Magnet of 7 tesla field and multiple electrode stacking
-> Red dot : simulate ion ->[….PT…MT…] -> MCP : count the numbers of ions, measure the time of flight of each and reconstruct the position of each
-> Now we will see what happen inside the two traps ?

## Slide 5
Purification trap
Measurement trap
Extraction optics
Injection optics
From
GPIB
MCP
Counting
ToF
Position
Designed and machined at MPIK Heidelberg
Diaphragm
PIPERADE
He
Purification Trap (PT)
Measurement Trap (MT)
Helium buffer-gas cooling
Separate ions of interest from the contaminants
Determine with:
    Time-of-Flight Ion-Cyclotron-Resonance (ToF-ICR)
    Phase-Imaging Ion-Cyclotron-Resonance (PI-ICR)
Notes: -> PT : inject gas through the flowmeter(point) for buffer gas cooling. Used for separation of IoI (green) which are going through the diaphragm's hole and the contaminant (red) which are stopped by it
-> MT : In the traps, the ions have a complex motion that can be related to the cyclotron frequency, itself related to the ion's mass through this equation. The cyclotron frequency will be measured at PIPERADE with two methods :
-> Now I will explain the basic principle of those two methods

## Slide 6
Measurement analysis
PI-ICR
ToF-ICR
Systematics studies in progress
Reduced cyclotron
Magnetron
Center
= 100 ms
- n
Routinely used
Development under progress
Systematics studies started
Notes: -> ToF-ICR : see a resonance around nu_c (value in the center) -> find m with this equation -> with multiple ToF-ICR measurement -> mass plot (longer excitation time give smaller error bar) -> we routinely use it
-> PI-ICR: this method use position of 3 spot : center {reduced cyclotron and magnetron} which constitute the cyclotron motion in the traps -> extract the angle between the two -> obtain nu_c with this equation -> same as ToF-ICR after that multiple Pi-ICR -> mass plot -> need more development for the moment
-> both need systematics studies -> I will add a little more explanation on the ToF-ICR analysis

## Slide 7: A little more on ToF Analysis
Simultaneous fit of ToF-IRC resonances with different with shared parameters
When ↗ :
Deterioration of the ToF-ICR shape ↗
Uncertainty of ↘
Notes: -> ToF-ICR shape : multiparameter equation -> use numerical fit to determine nu_c precisely
-> Plot : when we see the excitation time augment the shape of the ToF-ICR deteriorate and the become thinner -> show range reducing -> The longer the excitation time is the heavier the deterioration of the ToF-ICR shape is but the lower the uncertainty is
->all this fitting and mass determination will be supported by our software IPA

## Slide 8
Interface for PIPERADE Analysis (IPA)
Software dedicated to ToF-ICR and PI-ICR fitting and mass determination
Notes: -> show plot ToF-ICR with data gating -> parameter window all ToF parameter for changeable -> mass determination working also -> Pi-ICR analysis under development
-> now I will talk about one parameter specifically the pressure

## Slide 9
Pressure effect
= 1 s
Reduced cyclotron
Magnetron
Center
Calculation of the ToF-ICR shapes
Reduced cyclotron
Magnetron
Center
= 100 ms
He
He
He
Notes: -> Why the pressure ? -> When we use the buffer gas cooling 1st trap -> small gas transfer to 2nd trap through diaphragm
-> what effect in the second trap
-> ToF-ICR effect -> small range of low pressure -> Strong damping of the resonance
->also to PI-ICR -> 100ms to 1s ->deterioration of the spot (reduced cyclotron ++)
-> In order to limit the gas transfert, we planned to change the diaphragm

## Slide 10
Diaphragm change
Diaphragm
2mm Ø  1mm Ø
Notes: -> the intervention happened in January
->pressure will only be lower in the second trap after that
->So now how do we know the in-trap pressure the trap are working ?

## Slide 11
In-trap pressure measurement: 1st Trap
Cooling
Extraction
Injection
Time
Bunch dispersion
Notes: ->measurement of pressure ->use ToF measurement -> show cooling scheme -> during cooling time we let the ion interact the helium gas -> energy of the ion decrease -> decrease bunch dispersion
->after that we extract the standard deviation of each step and plot it

## Slide 12
Fit of the bunch dispersion as a function of the cooling time in the first trap
In-trap pressure measurement: 1st Trap
Equation used to fit this data
Notes: -> plot the evolution of bunch dispersion for different flowmeter opening -> use this equation for fitting
-> show pressure graph –> linear evolution of the pressure
-> this method work so will we use it for the second trap also

## Slide 13
In-trap pressure measurement: 2nd Trap
Preliminary
Notes: -> not definitive slide
-> plot bigger valve opening because only a very small effect on the pressure
-> pressure plot : observe a similar linear response

## Slide 14
Correction of the trap center movement
Last ISOL-France meeting, we showed that the projection of the trap center on the MCP was moving
We found the culprit:
Ions “see” the insulator
We added an electrode extension to shield the ion from the insulator:
Bunch FWHM
Notes: -> We see that the size of the spot is of the same order of magnituder than the motion of the center -> unusable for PI-ICR
-> culprit insulator -> hypothesis : some charge effect happen on it which change the extraction optics
-> after extension addition-> motion of the center much smaller than the size of the spot
-> lastly a quick vision about our acquisition software

## Slide 15
Python Trap Scanner for DESIR (PTSD)
Scan all EPICS variables
Control trapping sequence
Signal acquisition
Position reconstruction
Data gating and fitting
End goal :
Adaptable to any DESIR detector type
Notes: -> PTSD stand for Python Trap Scanner for DESIR
-> Wish to develop it to be Adaptable to any DESIR detector type

## Slide 16
Conclusion and perspectives
Conclusion
- Intervention to change the diaphragm
- Study of pressure behaviour inside the traps
- Software development (IPA, PTSD) under progress
- Solved trap center movement
Perspectives
- Investigation of the trapping potentials’ stability
- PI-ICR mass measurement for 1s
- Design new MCP chamber
- Systematic studies (potential anharmonicities, B-field inhomogeneities and fluctuations, mass-dependent errors, image distortion, etc.)
- Preparation for the move to GANIL
Faraday cup
Attenuation grid
Iris
MCP
delay line

## Slide 17
Thanks for your attention!
P. Alfaurt, P. Ascher, D. Atanasov, A. Balana, B. Blank, L. Daudin, M. Flayol, M. Gerbaux, S. Grévy, G. Guignard, M. Hukkanen, A. Husson, G. Jevelot,
B. Lachacinski, S. Lechner, S. Perard, E. Rey-herme, M. Roche, A. de Roubin,
C. Roumegou

## Slide 18
Strong homogeneous magnetic field : radial confinement
  (2 homogeneous regions < 1 ppm over 1 cm3)
Weak quadrupolar electrostatic field : axial confinement (correction electrodes to limit the anharmonicities)
 Superposition of 3 motions with 3 eigen frequencies:
Ion motions in a Penning trap
nz : Axial motion ( ~100 kHz)
n+ : Reduced cyclotron motion (~ MHz)
n- : Magnetron motion (~ kHz) (mass-independent)
Amplitude of these motions can be modified by buffer gas or RF-excitations
    Dipolar to increase/decrease a motion
    Quadrupolar to convert one motion into another one
Cyclotron frequency
Reduced by the gas
Three main purification/measurement techniques :
- Buffer gas cooling
- Time-of-Flight Ion-Cyclotron-Resonance (ToF-ICR)
- Phase-Imaging Ion-Cyclotron-Resonance (PI-ICR)

## Slide 19
Transfer (30-50 ms)
Dipolar excitation at the magnetron frequency (5 ms)
Quadrupolar excitation at the frequency nc  radial energy increases (40 – 1000 ms)
Extraction through the magnetic field gradient  conversion to axial energy
MCP detection  time of flight shorter at the resonance
ToF-ICR (Time-of-Flight Ion-Cyclotron-Resonance)
1 second

## Slide 20
+1
Measured thanks to a reference (well-known mass)
ToF-ICR mass measurements
Experimentally, we measure
Mass determination 
 Precision :
Studies of systematical uncertainties in progress (magnetic field fluctuations, number of ions, mass of the reference, etc…)

## Slide 21
M. Hukkanen et al. Phys. Rev. C 107 (2023) 014306
PI-ICR (Phase-Imaging Ion-Cyclotron-Resonance)
c
1
1
2
2
c
Projection of radial motion phases on a position-sensitive detector
High sensitivity (“non scanning method”)
Gain of a factor of 5-10 in precision and 40 in resolution compared to ToF-ICR (up to R = 107)
Measurement of ground state masses and isomer excitation energies
Capable of separate isomers  high-resolution purification for DESIR

## Slide 22
PI-ICR at PIPERADE
Initial conditions
Magnetron damping
n+ excitation
Conversion magnetron
Step 1
Step 2
Step 3
Step 4
Step 5
Eliseev, S et al. Appl. Phys. B 114 (2014) 107–128

## Slide 23
Base flange 250 mm
Mounting ring
DLD
Holder plate
MCP rings

## Slide 24: Magnetic field fluctuations
Linear interpolation of a reference nuclei is used to determine the value of the magnetic field for the two methods

## Slide 25: Electric field anharmonicities

## Slide 26
Multiple Hit Readout of a Microchannel Plate Detector With a Three-Layer Delay-Line Anode
u1
u2
U
Isometric view