## Slide 1: Study of the impact of sources of variability on soil mineralogical characterization using hyperspectral imaging
Director: Stéphane Jacquemoud (IPGP/U. Paris Cité)
Co-director: Rodolphe Marion (CEA)
2 years funded by CEA and the Académie Spatiale d’Île de France
22 May 2025
Corentin Feray

## Slide 2
What am I looking for?
Source : Terracore
About 10 minerals of interest presenting absorptions features in the solar domains (VNIR/SWIR)
22/05/2025
Corentin Feray

## Slide 3
22/05/2025
Corentin Feray
Spectroscopic data
Example of kaolinite
Absorption bands = Chemical effects
Continuum = Physical effects

## Slide 4
Acquisition chain: acquisition parameters, camera calibration …
Environmental conditions: lighting (direct/diffuse), acquisition geometry, atmosphere, shadows…
Physical properties: grain size and shape, porosity, compaction …
Chemical properties : mineralogical composition, water content, organic matter content, pollutant content …
Factors affecting reflectance spectra
Water content [2]
[1] Verpoorter (2009)
[2] Sadeghi et al. (2015)
22/05/2025
Corentin Feray
Average grain size [1]
Wavelength (µm)
Wavelength (nm)

## Slide 5
Logarithm of a reflectance spectrum:
Spectral deconvolution
22/05/2025
Objectives: reduce data dimensionality, the impact of noise, correlations between parameters, and improve parameter interpretability.

## Slide 6
22/05/2025
Chosen absorption model: EGO (Asymmetric Gaussian) [3]
4 parameters:
Amplitude s
Position μ
Width σ
Asymmetry k
Spectral deconvolution
8 + 4N parameters
(8 for the continuum, 4N for the absorptions)
Continuum :
~1000 wavelengths → A few dozen parameters
[3] Pompilio et al. (2009)

## Slide 7
Deconvolution procedure
22/05/2025
reflectance spectrum
associated noise covariance matrix
Continuum pre-estimation and removal
pre-estimated absorption parameters
pre-estimated continuum parameters
Based on the work from Ronan Rialland’s PhD thesis (2021) [4]
Absorption pre-estimation
Joint optimization

## Slide 8
Dataset
22/05/2025
Soils from Thann mainly composed of gypsum
Reflectance spectrum acquired using an ASD spectrometer
13 moisture content levels
Dry
Wet
[5] Uccellatori (2023)

## Slide 9
Continuum pre-estimation
22/05/2025
Geometric initialization [4]
Continuum extraction (mathematical)
[4] Rialland (2021)

## Slide 10
22/05/2025
Continuum pre-estimation

## Slide 11
22/05/2025
Wavelet transform
2D matrix of wavelet coefficients
Scaled and translated wavelet
Mother wavelet: Mexican Hat
f(t): signal; a: scale factor; b: translation; w(t): mother wavelet
Convolution of the wavelet and the signal
Wavelet coefficients
Wavelength (nm)
Wavelength (nm)
Intensity

## Slide 12
22/05/2025
Ridge detection
Computation of ridge lines, trough lines and zero-crossing lines
Position: position of the ridge line at the smallest scales
Width: scale where the ridge line reaches its maximum value
Amplitude: maximum value of the ridge line
Asymmetry: angle between the ridge line and a vertical line

## Slide 13
22/05/2025
Absorption parameter analysis
Fit result on the spectrum corresponding to dry soil
Centers of the different Gaussians

## Slide 14
22/05/2025
Absorption parameter analysis
Absorption spectra

## Slide 15
Conclusion and perspectives
22/05/2025
Conclusion:
Algorithm applicable to different types of data
Noise taken into account
Good estimation of the number of Gaussians
Limitations: difficult initialization in case of overlapping
Perspectives:
Improve Gaussian initialization for overlapping cases
Integration with machine learning methods
Understand and quantify the impact of moisture content on model parameters (detection limits)
Develop robust models to these effects for mineral quantification

## Slide 16
22/05/2025
Bibliography
[1] Verpoorter, C. (2009). Télédétection hyperspectrale et cartographie des faciès sédimentaires en zone intertidale: application à la Baie de Bourgneuf (Doctoral dissertation, Université de Nantes).
[2] Sadeghi, M., Jones, S. B., & Philpot, W. D. (2015). A linear physically-based model for remote sensing of soil moisture using short wave infrared bands. Remote Sensing of Environment, 164, 66-76.
[3] Pompilio, L., Pedrazzi, G., Cloutis, E. A., Craig, M. A., & Roush, T. L. (2010). Exponential Gaussian approach for spectral modelling: The EGO algorithm II. Band asymmetry. Icarus, 208(2), 811-823.
[4] Rialland, R. (2021). Télédétection hyperspectrale pour l’identification et la caractérisation de minéraux industriels (Doctoral dissertation, Université Paris-Saclay).
[5] Erica, U. (2023) Impact of surface humidity on the spectral signature of industrial and mining minerals and implications for their detection by hyperspectral imaging (Master's thesis, University of Pavia)