## Slide 1: A_RD_24 Study of laser-beam arrival time synchronisation towards sub picosecond level
A. Aryshev (KEK) and A. Martens (IJCLab) on behalf of
KEK (Kaji, Popov)
IJCLab (Back, Charlet, Esnault, Johora+, Zomer)
+: non-permanent contract
The research leading to these results has received funding from the European Union's Horizon Europe MSCA under grant agreement no. 101086276

## Slide 2: SuperKEKB polarization upgrade
Only for electrons
Beam transport of polarized beam
Top-up injection at nominal energy
Spin rotators (combined function magnets from BNL)
Preservation of polarization
See Belle II upgrade framework CDR arXiv:2406.19421; M. Roney talk at ICJHEP 2024
Compton polarimeter

## Slide 3: Potential of polarization upgrade
Just an example of measurement of interest
See Belle II upgrade framework CDR arXiv:2406.19421; M. Roney talk at ICJHEP 2024

## Slide 4: Compton polarimeter
D. Charlet et al., JINST 18 (2023) P10014
laser (Eλ)
θ
e- beam
Initial electron energy (7 GeV)
Initial photon energy (2.4eV at 515nm)
Crossing angle of beams
Emitted photon energy
scattered photons ()
Differential cross-section
Electron beam polarization independent
Electron beam polarization dependent
Transverse laser polarisation: nuisance parameter to minimize and keep under control
Transverse electron beam polarisation: intervenes as an asymmetry in the transverse plane
⚠️ Transverse e-beam polarimetry implies measuring geometrical asymmetries in the detection plane
Notoriously difficult task due to a narrow cone for scattered particles along e-beam direction
For integration ease, concentrate on photon detection and longitudinal polarization

## Slide 5: Longitudinal Compton polarimetry
Polarization dependent term generates a left-right asymmetry function of
that reflects also as a function of the energy of the emitted electron
Using a 515nm laser provides higher sensitivity
Landau-Lifshitz QED book paragaphs 86 and 87

## Slide 6: Mechanical system integration
450 mm
910 mm
Crossing Angle Horizontal : 8 deg
Crossing Angle Vertical : 4 deg
+ some neutron + lead shielding around electronics to be located below the table
+ some lead shielding around the table to protect the laser
D. Charlet et al., 2023 JINST 18 P10014
e- beam

## Slide 7: Expected performance
Now in a Technical Design phase
Expected performance :
For each bunch every 5 min
To be confirmed with more detailed GEANT4 simulation
Requirement: fast, radiation tolerant, calorimetry of scattered photons every 4 ns
R&D with BaF2 detector
Precise and low cost electron/laser beam and DAQ synchronisation (bunches are ~3ps long)
D. Charlet et al., 2023 JINST 18 P10014

## Slide 8: Laser system
Box with rough temperature control
Box with rough temperature control
Elliptic beam can be delivered with cylindrical lenses/mirrors (not planned for a first step)
Key aspect: remote operation of the system that will be located in the tunnel
250MHz
Possibility to insert mirror for laser polarization calibration
D. Charlet et al., 2023 JINST 18 P10014
Typical picosecond pulse duration

## Slide 9: Clock distribution issue
Time propagation delay in optical fiber over time
Typical residual jitters are in the range of hundreds of picosecond due to thermal drifts over kilometric fibres
 Very expansive optical measurement and compensation systems
Possibility to synchronize the laser on the RF clock of the accelerator using the WhiteRabbit technology and improvements implemented in IDROGEN board of IJCLab
H. Kaji, PASJ2020 WEOT09

## Slide 10: Laser synchronisation – concept
Master Oscillator (510MHz/51)
4km fibre link
IDROGEN board
tailored for low noise with WR node
FPGA mezzanine card with high speed ADC
WhiteRabbit switch
D. Charlet et al., https://cds.cern.ch/record/2893372?ln=en
IDROGEN Board initially thought for radio-astronomy experiments
WhiteRabbit allows to minimize implementation cost and meet performance ?
A simple fibre to bring to the laser
No expensive/complicated fibre length compensation system to implement
Possibility to embed DAQ for the calorimeter
WhiteRabbit (CERN) :
IEEE protocols over ethernet (SyncE, PTP)
State of the art digital technics to recover clocks
High interest in ATF team for investigating possibility of simplifyin ATF clock distribution
Expected to be used in the next accelerator being implemented at IJCLab (PERLE)

## Slide 11: Arbitrary frequency generation
Rubidium
fibre link
RF
Arbitrary frequency
Precision of 1 Hz, accuracy excellent (no drift over several hours)
Consistency of KEK and IJCLab measurements.
Identical phase noise for various different output frequencies
Same configuration but two totally different qualification schemes
Orsay team at KEK June and Oct ‘24

## Slide 12: Long term drift
Reference freq.
Generated freq.
X
X
split 50:50
split 50:50
Low Pass
Low Pass
~0.3degree RMS phase jitter (at 357MHz) i.e. 2.3ps RMS (below 1Hz)
NB: measurements made in a regular office, no thermal stabilization
ATF team visit at IJCLab (Jan’25)

## Slide 13: Last results at Orsay (March’25)
Phase noise comparison
Rubidium
WR_LJ switch
Rubidium
IDROGEN master
IDROGEN slave
IDROGEN slave
Subtantial phase noise improvement
Obtain down to <0.9ps RMS (1hz, 10MHz)
Good enough for direct lazer synchronization

## Slide 14: Integrated time jitter
IDROGENDROGEN BOARD: 2x better than Switch Low Jitter from Safran/Seven Solution
Integrated jitter according to integration window
Also in collaboration with LTE
(P.-E. Potie, M. Lours)

## Slide 15: ADC capabilities
The motivation of the development of a new mezzanine :
  includes its own PLL & External ADC clock source
Mezzanine main features :
  VITA57.1 (FMC), ADC 9680, 2 channels 1GSPS 14 bits
  ADC acquisition JESD204B protocol,
  2GHz analog bandwidth
  External trigger in
Bandwidth 500 MHz to 1.5GHz
Synchro & timing by WR
Data transfer 40G Ethernet (currently 2x 10Gbs)
Configuration by IPBus 10G
1.250GSPS capability
5ns pulse & 10mv dynamic
System time resolution : 2.5 ps

## Slide 16: Planned activities at KEK this year
Performance demonstration
Long term phase stability in representative accelerator conditions
NB: extended interest to use the IDROGEN board for instance to diagnose early beam oscillations and fasten aborts before occurrence of sudden beam losses. Cf Yun-Tsung Lai presentation
Several publications in preparation, triggered by the support of FJPPN
178.5MHz

## Slide 17: Conclusion & prospects
Exploits IJCLab know-how developed initially for Astrophysics projects now expanded into TimeD IN2P3 R&T
KEK know-how in accelerator synchronisation and time distribution
SuperKEKB polarization upgrade motivates development
of new synchronisation scheme for laser and e-beam
High-potential for a revisited way to synchronise accelerator components
arbitrary fibre length can be used (on accelerator scales)
Works already well with commercial WhiteRabbit switch
better with IDROGEN master : <0.9ps RMS jitter can be reached
Planned tests at KEK Accelerator Test Facility to make convincing demonstration
FJPPN support for travels to help achieving this experiment
Exchanges funded by FJPPN:
2-3 visits a year at KEK cofounded with EAJADE
Visit of KEK colleagues at Orsay + long term 1 month visit funded by KEK

## Slide 19: SuperKEKB

## Slide 20: Luminosity projection
Additional possibility being considered: e- beam polarization upgrade
Goal : transparent upgrade for accelerator --> negligible luminosity loss, possibility to operate w/ and w/o polarization
Today

## Slide 21: IDROGEN board performances
Measurements made at LTE (P.-E. Pottie)
IDROGEN BOARD: 4x better than Switch Low Jitter from Safran/Seven Solution
Phase noise measurement
Phase noise measurement
Integrated jitter according to integration window

## Slide 22
The motivation of the development of a new mezzanine instead of an off-the-shelf ADC mezzanine :
  includes its own PLL;
  ADC clock source : External clock
Mezzanine main features :
  VITA57.1 (FMC), ADC 9680, 2 channels 1GSPS 14 bits
  ADC acquisition JESD204B protocol,
  2GHz analog bandwidth
  External trigger in
Bandwidth 500 MHz to 1.5GHz
Synchro & timing by WR
Data transfer 40G Ethernet (currently 2x 10Gbs)
Configuration by IPBus 10G
1.250GSPS capability
5ns pulse & 10mv dynamic
2 channels 1GSPS 14b ADC FMC board

## Slide 23
2 IDROGEN boards synchronize by WR
Same RF signal (312.5MHz) split on boards
FFT 8K point
Cross correlation
FMC ADC_9680: Synchronization
ps
s
System time resolution : 2.2ps
Notes: Plot du haut
Temps acquisition en ~minutes
Moyenne de moyenne 2+180 fs de dispersion
Plot du bas c’est vue “instantané” echelle temps courte

## Slide 24
The motivation to develop the FMC-ADS42JB69
  ADC Clock directly from IDROGEN FMC connector
4 channels 250MSPS 16bits
One external trigger
  Interface JESD204B
  Analog input 900MHz
  2.5v input voltages
4 channels 250MSPS 16b ADC FMC board

## Slide 25
High speed data acquisition & Low phase noise WR node
White Rabbit Design & development done by IJCLab (based on CERN schematic): Component upgrade and EMC design rules compliant → High stability timing distribution
xTCA4.0 form factor board → Modularity
Base on ARRIA 10 FPGA → High data rate transfer
Standalone capability
FMC Slot (ADC, DAC, clock synthesis, ...)
SFP+ connector for WR
QSFP connector for data transfer (Ethernet, GBT, ...)
RTM Connector
µTCA connector
1Gb Ethernet
PCIe (8GT/s)
IDROGEN board v3

## Slide 26
The motivation of the development of a new mezzanine instead of an off-the-shelf ADC mezzanine :
  includes its own PLL;
  ADC clock source : External clock
Mezzanine main features :
  VITA57.1 (FMC), ADC 9680, 2 channels 1GSPS 14 bits
  ADC acquisition JESD204B protocol,
  2GHz analog bandwidth
  External trigger in
Bandwidth 500 MHz to 1.5GHz
Synchro & timing by WR
Data transfer 40G Ethernet (currently 2x 10Gbs)
Configuration by IPBus 10G
1.250GSPS capability
5ns pulse & 10mv dynamic
2 channels 1GSPS 14b ADC FMC board

## Slide 27
2 IDROGEN boards synchronize by WR
Same RF signal (312.5MHz) split on boards
FFT 16K point
Cross correlation
FMC ADC_9680: Synchronization

## Slide 28
The motivation to develop the Fractionnal PLL (FPLL) FMC
  Generate any frequency disciplined by WR clock
  Replace very expensive system with recent component
Fractional PLL SI5362
  Ultra-high-performance jitter attenuator
  Ultra-low phase jitter (<55 fs typ)
  18 outputs 10KHz to 2.75GHz
FMC_SI536X
  4 single ended independent outputs clock
  Configuration by PCIe or IPbus
  Currently in cabling
Measurement of phase
jitter with SI5361
FMC clock synthesizer