## Slide 1
Measurement and simulation of injection losses and
resulting detector backgrounds at SuperKEKB
2025 Joint workshop of FKPPN and TYL/FJPPN, 14-16 May, 2025
FJPPN- A_RD_30
IJCLab, Orsay, France
P. Bambade*
M. Li
S. Wallon
KEK, Tsukuba, Japan
N. Iida*, Y. Funakoshi, H. Kaji
T. Koga, Y. Ohnishi, K. Uno
S. Uehara , H. Nakayama

## Slide 2
SuperKEKB/Belle II project
Achieving the target design luminosity remains a major challenge.
2

## Slide 3
SuperKEKB/Belle II project
Injection strongly limit higher luminosity during recent operation
high currents  reduced lifetimes  tried during 2024c run
Small  reduced DA  tried 0.8mm during 2022ab run
Huge background appear just after beam injection and continues more than 10ms -> limit data taking efficiency
-Belle II trigger is vetoed for a while after injection ->large DAQ deadtime of 5~15%
Achieved injection efficiency during physics run almost lower than half of the required -> limit beam current
SVD first layer occupancy
-ECLBG –Injection Veto
～10ms
ECLTRG injectionBG duration
3
Detailed injection-related beam loss and background simulation is essential for improving injection efficiency and BG
Injection-related issues are expected to become more severe for higher luminosity -> serious issue for target luminosity

## Slide 4
FJPPN- A_RD_30
Title | Measurement and simulation of injection losses and resulting detector backgrounds at SuperKEKB | 
Subject | LumiBelle2 fast luminosity monitor at SuperKEKB -> high peak and integrated luminosity Injection-related beam loss and backgrounds at SuperKEKB ->necessary for high luminosity&data taking efficiency | 
Member | IJCLab, Orsay, France P. Bambade* M. Li (PhD) S. Wallon | KEK, Tsukuba, Japan N. Iida*, Y. Funakoshi, H. Kaji T. Koga, Y. Ohnishi, K. Uno S. Uehara , H. Nakayama
Activities | France->Japan: improve injection simulation; conduct injection validation experiment; join LumiBelle2 operation 2024.02.14-03.15(M. Li, supported by EAJADE) 2024.02.24-03.07(P. Bambade, supported by JENNIFER2) 2024.05.12-07.11(M. Li , supported by TYL and EAJADE) 2024.11.10-12.28(M. Li, supported by TYL and IHEP) 2025.02.24-03.08(M. Li, supported by TYL and EAJADE) Japan->France: disscuss project progress and plan 2024.09.20-09.28(H. Kaji, supported by FJPPN) 2024.10.30-11.01(H. Kaji, supported by FJPPN) | 
Articles, conference talks | “Status and Performance of LumiBelle2 in the 2024 Beam Operation of SuperKEKB“, by Meng LI et al., presented at the IBIC 2024, Beijing, China (THP16) “Investigation on injection-related beam loss at SuperKEKB”, by Meng LI et al., Invited talk at eeFAC2025, Tsukuba, Japan (TUA14) … | 
4

## Slide 5
IJCLab–KEK Collaboration within FJPPN-TYL
Since 2012: Collaboration on fast luminosity monitor at SuperKEKB(LumiBelle2)
-> Developed a fast luminosity monitor LumiBelle2 based on sCVD diamond detectors
-> Fast luminosity measurement and feedback(1% relative precision@1kHz )
-> Bunch by bunch luminosity diagnostic(1% relative precision@1Hz)
-> IP vertical beam size measurement + tuning at very low currents
-> Maintain optimum collision conditions & maximize luminosity
5

## Slide 6
LumiBelle2 fast luminosity monitor at SuperKEKB
Install LGAD sensors in LumiBelle2 -> radiation hardened version from IHEP-Beijing used in Atlas
LGAD sensor from IHEP with C2HV0235 and RF splitter / inverter
500μm diamond herd42 with C2HV0235
Trigger level -20mV
Trigger level 13.8mV
sensitivity@500um diamond
Conducted data analysis based on 2024 run to estimate the performance of Diamond sensors
- Internal data handling/archiving software instability
- Sensor sensitivity drift in one diamond detector
In 2024, the LumiBelle2 was operated successfully at KEK
Observed variation of B-by-B lifetimes -> B-by-B luminosity data for machine tuning required by SuperKEKB group
6

## Slide 7
IJCLab–KEK Collaboration within FJPPN-TYL
Since 2024: Extended the collaboration  injection-related beam losses at SuperKEKB
-> reliable injection simulation for accelerator operation
-> Improve injection performance and reduce injection BG
-> Achieve high luminosity & data taking efficiency
7
A detailed simulation of injected beam losses and related backgrounds was developed
-Injection errors mainly affect injection efficiency
-Beam-beam effect, cancel coil error have a large effect on injection-related background
-Beam loss in IR can be suppressed by minor collimator aperture adjustment
Validation experiments conducted in collaboration with SuperKEKB, MDI, and Belle II groups
Progress
-New CLAWS loss monitor installed for dedicated measurements
-CsI & EMT monitors and Belle II ECL sub-detectors reconfigured with 1 Hz injection trigger
The results show good qualitative agreement between the simulations and measurements

## Slide 8
Injection simulation based on realistic operation settings
Beam-beam(weak-strong model)
Collimator (2024-06-26)
Machine error: sextupole vertical mis-alignment ( global coupling: )
Bunch-by-bunch feedback(damping time=0.5ms) Gaussian stored beam also included
Lattice: HER_CW60_0.9mm-can_rev.sad: (from Onishi-san)
-with measured chromaticity ()
-with cancel coil correction error
Injection distribution (from Yoshimoto-san) + emittance adjustments () + injection error ()
(based on 2024-6-27 operation emittance and bunch current)
8

## Slide 9
originate from the beam core
originate from the edge of bunch
Injection efficiency and beam loss
There are 2 different types of beam loss:
1) large and fast beam loss in the first 100 turns(30%) injection efficiency
2) small and continuous beam loss until 1000 turns(10%) injection BG duration
A: Large rapid beam loss
B: Small continuous beam loss
A: Large rapid beam loss
B: Small continuous beam loss
9

## Slide 10
Injection horizontal offset
Finding1: Injection errors mainly affect injection efficiency
10

## Slide 11
Beam-beam interatcion
Beam-beam interaction can reduce the beam loss rate in the first 100 turns but increase the loss rate after 100 turns.
Strengthening the beam-beam interaction decreases DA, lowers injection efficiency, and increases injection background-related beam loss.
Finding2: Non-linearity in HER lattice affect both efficiency and background
11

## Slide 12
D01V1 plays a major role in this suppression
-relative aperture to the injection beam size of D01V1 is almost the same as that of the IR beam pipe
Finding3: IR Beam loss can be suppressed by minor collimator aperture adjustment
Current collimator settings are effective in protecting the IR region, but IR losses remain.
12

## Slide 13
Main findings from simulation
Injection errors mainly affect injection efficiency
-> injection offset; injection angle; injected emittance; injection phase; x-y coupling
Beam-beam effect, cancel coil error have a large effect on injection-related background.
Beam loss in IR can be suppressed by minor collimator aperture adjustment
-> When closing all the vertical collimators by 0.1mm, the beam loss in IR can be significantly suppressed
-> D01V1 plays a major role
Based on the findings obtained from simulations, we conducted corresponding validation experiments:
-> Injection tolerance measurement ( with Iida-san, Onishi-san)
-> Beam-beam study related to injection BG (with Kaji-san, Koga-san, Bela-san, Funakoshi-san)
-> Collimator study related to injection BG (with Uno-san, Ueki-san, Kaji-san, Koga-san, Bela-san)
The results showed good qualitative agreement between the simulations and measurements.
13

## Slide 14
“CsI scintillator + PMT”, “EMT” loss monitor installed near the collimator and injection point
EMT
-they have good time resolution
-record spatial and temporal loss pattern during several ms
Loss monitor and Belle II detector for injection BG measurement
Belle II subdetector ECLTRG record the injection BG duration signal shot by shot injection.
-fast beam loss monitor, consist of the plastic scintillator and SiPM
-sensitive small beam loss, record time structure of injection BG
A dedicated CLAWS scintillator for injection background study newly installed near the collimator D01V1.
Oscilloscope
E > 100 MeV; #cluster>6
1Hz Inj trigger
Injection trigger
ECL trigger signal
These three types of loss monitors and TbT monitors are triggered by a 1Hz injection trigger, record the injection efficiency, beam loss patten and injection BG duration.
14

## Slide 15
Injection tolerance measurement (2024-06-06)
Vertical Position Scan[mm]:
Septum Position Scan[mm]:
from Onishi-san
Septum Angle Scan[mrad]:
Vertical Angle Scan[mrad]:
The trend of injection efficiency with respect to the variation in error is consistent, but the simulated absolute values are higher than the measured values.
15

## Slide 16
Collimator D01V1 and beam-beam measurement
Experiment setting
( close 200um )
( close 100um )
( open 100um )
( open 200um )
The injection BG is very sensitive to collimator D01V1 aperture
16

## Slide 17
The injection BG increases as the beam intensity (beam-beam strength) increases.
Experiment setting
( close 200um )
( close 100um )
( open 100um )
( open 200um )
17

## Slide 18
Detailed data analysis
18
Compare with simulation
Measured injectionBG duration increases with stronger beam–beam interaction ->qualitative agreement with simulation
Measured injectionBG duration sensitive to collimator D01V1 settings -> qualitative agreement with simulation

## Slide 19: Conclusions and Prospects
  A more realistic simulation mechanism for injection-related beam loss has been developed.
  Verification experiments have been conducted based on its main findings.
  The simulation results are qualitatively consistent with the experimental observations.
  Tune scan study (betatron-synchrotron resonance,…)
  Further nonlinearity including fully implemented crab-waist collision
  More realistic IR beam pipe and collimator model including tip-scattering
  Assessment for higher luminosity in 2025 and beyond
  More validation experiments (CLAWS at D01V1, ECLTRG,…)
  Further investigation of injection-related beam loss and background
  Bunch by bunch luminosity online monitor
  Compare LGAD and CVD diamond sensors (radiation hardness)
LumiBelle2

## Slide 20
Back up

## Slide 21
Comparison between simulation and measurement on collimator
18

## Slide 22
R² = 0.81
R² = 0.84
R² = 0.29
4.98ms
6.11ms
22.64ms
Positive linear correlation between beam loss at D01V1 and ECLTRG duration, under fixed D01V1 aperture settings.
reduce the average level of injection BG duration
mitigates the impact of injection fluctuation on IR beam loss
Closing the D01V1 aperture
Stronger beam-beam interaction
(higher luminosity)
higher beam loss at D01V1,
increases IR beam loss
longer injection BG duration
16

## Slide 23
noise, baseline, shift
Integration=d01v1*sampling_interval
15
Reconstruction CLAWS data waveform

## Slide 24
deltGx[1]= -0.02*Gx0;
deltGpx[1]=-0.02*Gpx0;
Initial total center of gravity
Gx0; Gpx0
total center of gravity
Gx[n]; Gpx[n]
feedback kick calculated based on beam position from last turn:
deltGx[n+1]=-0.02*Gx[n];
deltGpx[n+1]=-0.02*Gpx[n];
track the injection beam and storage beam at the same time turn by turn, calculate the center of gravity of injected and stored beam, and feedback kick, update the horizontal coordinates of the particles turn by turn.
her-initial-particles_1.dat(9972)
Initial gravity center of x, px : Gxi0, Ggxi0
beamI0={1,{xi,pxi,yi,pyi,zi,deli,flgi}};
Injected beam
start loop
beamItrack[n]=TrackParticles[beamI[n-1],start,1];
beamI[n]
beamI[n][2,1]+deltGx[n];
beamI[n][2,2]+deltGpx[n]
add feedback
remove lost particles
Gxi[n]; Gpxi[n]
beamI[n]
beamRtrack[n]=TrackParticles[beamR[n-1],start,1];
beamR[n]
beamR[n][2,1]+deltGx[n]; beamR[n][2,2]+deltGpx[n]
add feedback
Remove lost particles
Gxr[n]; Gpxr[n]
Gaussion distribution(9972*2)
Initial gravity center of x, px : Gxr0, Ggxr0
beamR0={1,{xs,pxs,ys,pys,zs,dels,flgs}};
stored beam
start loop
beamR[n]
applied in the next turn