Backscattered light noise in the Virgo interferometer
1rst year CSI seminar
PhD advisors : Michal Was & Romain Gouaty

---
Gravitational wave
- Space-time metric’s deformation
- 2 polarisations (+, ×)
A prop frac { 1 } { d }
v = c
Gravitational Wave Illustration
Credit : Swinburne Astronomy Productions

---
Detection principle
- Space-time deformation → change distance between free-falling masses
- Use electromagnetic wave to measure displacement
Test mass 1
Test mass 1
d
d+δd
Test mass 2
Test mass 2

---
Michelson ITF
phase difference between arms → amplitude on the anti-symmetric port
Dark fringe offset:
%delta { { P } _ { t } } prop %delta %DELTA L

---
Sensitivity curve
ASD of h(t)
Affected by various noises

---
Benches layout
Benches :
SNEB
SWEB
SDB1
SDB2
End-of-arms benches
Detection benches
In vacuum
Suspended

---
Work done
Measurement of noise from bench displacement
Measurement of backscattered light from sample
Simulation of TF for backscattered light

---
Noise measurement
31th of october 2024
 NI
 NE
SNEB
Pin
Pout
SNEB
SWEB
SDB1
SDB2
SQB1
 injected displacement
→v(t) = A·sin(2πf)
backscattered light

---
Commissioning shift
- On cascina server with Romain Gouaty
- Injecting A·sin(2πf) on benches
- Control loops engaged
Here an injection on SNEB with f=0.2 Hz and A≈15 um
https://logbook.virgo-gw.eu/virgo/?r=65440

---
Bench vibration : result
Sensitivity curve with (blue) and without (violet) SNEB displacement

---
Transfer function
Constructive/Destructive interference :
→ change amplitude of the beam
→ change radiation pressure
⇒ Named
Quadratic interference :
→ add phase noise
→ directly change measurement
⇒ Named
{ { K } _ { frac { %delta P } { P } } }
{ { K } _ { { n } _ { %phi } } }

---
Computing backscattered factor
mirror transmission
sensitivity
bench movement
h_r(f) = sqrt {f_r} cdot {frac {P_out} {P_{ital "in"}}} cdot lbrace K_{n}(f) cdot fourier [ sin({frac {4 cdot %pi} {%lambda}}(x(t))) ] + K_{P}(f) fourier [ cos({frac {4 cdot %pi}{%lambda}}(x(t))) ] rbrace
fraction of backscattered light
Pin
bench
Pout
transfer function by radiation pressure (Kp) and phase (Kn)
x(t)

---
Software development
- Python library built from already existing matlab code
- Use already simulated Optickle simulation
- Data taken :
  - Bench movement (with a calibration factor)
  - Mirror movement: reference (with a calibration factor)
  - h(t)
- Cut high frequency movement due to sensor’s noise
- Find the backscattered light factor (fsc) which match observation

---
Principle
- Noise background :
- Measure with an excitation :
- Find to have :
- Minimize :
- Minimize on a frequency range [a, b] :
h _ {ref} (f)
h _ {exc} (f) approx h _ {ref} (f) + h _ { r _ { real } } (f)
{ h } _ { { r } _ { theory } } (f, { f } _ { sc })
{ { h } _ { { r } _ { theory } } } (f, { { f } _ { sc } } ) approx { { h } _ { { r } _ { real } } } (f) = { { h } _ { exc } } ( f ) - { { h } _ { ref } } ( f )
drarrow { { h } _ { exc } } ( f ) - ( { { h } _ { ref } } ( f ) + { { h } _ { { r } _ { theory } } } ( f ) ) approx 0
{ { h } _ { { r } _ { diff } } } ( f , { { f } _ { sc } } ) = { { h } _ { exc } } ( f ) - ( { { h } _ { ref } } ( f ) + { { h } _ { { r } _ { theory } } } ( f , { { f } _ { sc } } ) )
m ( { { f } _ { r } } ) = { int ^ { b } _ { a } { { df } cdot { { { h } _ { { r } _ { diff } } } ( f , { { f } _ { sc } } ) } } }

---
Computation result
bench	fsc during O3	fsc during commissioning	Current fsc (O4b)
SDB1	2×10-9	3.1×10-10	2.07×10-9
SDB2	4×10-10	4.1×10-13	1.62×10-12
SNEB	2.5×10-8	4.4×10-9	5.02×10-9
SWEB	4.0×10-8	2.5×10-9	3.05×10-9
Unphysical transfer function
Source for O3 values : https://arxiv.org/abs/2011.03539 (photodiode shutter open) and https://tds.virgo-gw.eu/?r=21958 for SDB1 and SDB2 values

---
Requirement for O5
- Bench speed requirements
- fsc requirement for new benches before SDB1

---
Future work on the interferometer
- O4 end on 7 of october 2025
  → Planned measurement with SR aligned
- Code and data can be used to determine future requirements

---
Backscattermeter
laser power
Sample
{ { P } _ { 1 } } ( t ) - { { P } _ { 2 } } ( t ) = frac { { P } _ { 0 } } { sqrt { 2 } } sqrt { { f } _ { sc } } cos (2 %pi frac { %DELTA L ( t ) } { %lambda })
Suspended bench
wavelength
P1
fraction of backscattered light
P2
bench movement
A ( t ) = frac { { { P } _ { 1 } } ( t ) - { { P } _ { 2 } } ( t ) } { { { P } _ { 1 } } ( t ) + { { P } _ { 2 } } ( t ) } = sqrt { 2 { { f } _ { sc } } } cos ( 2 %pi frac { %DELTA L ( t ) } { %lambda } )

---
Computing BRDF
- Assuming :
  - scattered light : spherical wave
  - gaussian beam
  ⇒ overlap =
BRDF = frac { 1 } { %pi cos ( %theta ) }
frac { { %lambda } ^ { 2 } } { { %pi } ^ 2 { w } ^ { 2 } }
{ { f } _ { sc } } = Overlap cdot %pi BRDF ( %theta ) cos ( %theta ) = BRDF ( %theta ) frac { { %lambda } ^ { 2 } cos ( %theta ) } { %pi { w } ^ { 2 } }

---
Telescope design
optics	fsc on bench	BRDF
mirror	6×10-10	3×10-4
antireflective coating	1×10-11	6×10-6
substrate	4–10×10-11	2–6×10-5
⚠commercial optics

---
Characterization of crystals
optic	angle	BRDF	fsc on SDB1
EOM crystal	17.5 mrad	7,7·10-6	1,6·10-12
EOM crystal	40 mrad	4,6·10-6	9,7·10-13
Faraday 13 mm	17.5 mrad	3,0·10-4	5,4·10-11
Faraday 13 mm	40 mrad	2,4·10-5	5,1·10-12
Faraday 12 mm	25 mrad	3,1·10-4	6,6·10-11
Faraday 12 mm	40 mrad	6,2·10-5	1,3·10-11
Faraday 12 mm	220 mrad	1,1·10-4	2,2·10-11
Polarizer	Brewster’s angle	1,4·10-5	3,0·10-12
- Crystals : critical elements
  - Low incidence
  - Long crystals :
  rayleigh diffusion

---
Parallel with measurement on Virgo
fsc of SDB1 during commissioning:
{ f } _ { { sc } _ { SDB1 } } = 3.1 cdot 10 ^ { - 10 }
frac { { f } _ { { sc } _ { SDB1 } } } { { f } _ { { sc } _ { faraday } } } = 5.7
Not using latest results for now → waiting for new TF
⇒Faraday isolator highly contribute to the backscattered noise

---
Future analysis
- More measurements on the dependance of the incidence angle for various faraday crystals
- Optics used in O5
- OMC ?
Analyse of the distribution of speckles

---
Simulation of TF
- Model already created by M. Was, using Optickle
- Cannot model mirror misalignement:
  - Adding losses on SR
  - Lowering transmission on SR
- Unmaintened for more than 5 years
⇒ Needs for a new simulation
Physically incorrect

---
Finesse 3
- Python based interferometer simulation
- Modal simulation
- Will be used (and is already used) by members of the collaboration

---
Current model
- Simple model with :
  - Laser
  - Power Recycling cavity
  - Fabry-Perot cavity
  - Signal Recycling cavity
  - benches

---
Comparison with Optickle
Same laser power, dark fringe offset and SR aligned

---
Current & future work
- Current work
  - Added high order TEM mode
  - Added an angle to SR → modelize misalignement
  - Still interpreting the result
- Future work
  - Adding antireflective surface on beam splitter
  - Getting a result compatible with current observation
  - Modelize future O5 configuration

---
Conclusion & outlook
- Measurements on the backscattermeter :
  - Faraday crystals
  - Various O5 optics
  - OMC ?
- Simulation results :
  - Add anti-reflective surface of BS (allows to model B5 beam) & finish O4 modelization
  - Modelize future O5 configuration
- Work on photodiode design to measure polarization fluctuations
⇒ Work on upgrade for O5 on backscattering noise
Side project : RRT shifts (level 0) before the end of O4b

---
Training courses
- Mandatory : « Research Ethics », « Scientific Integrity »
- « Physics in the XXIst century », 18h
- « Statistics courses using a data driven approach, using R software », 15h
- MaNiTou Summer School on Gravitational Waves, 4 day

---
Thanks you for listening
Any questions ?