## Slide 1: PBR Tilting & Shutters
Lawrence Wiencke, Levi Bar-On, James Brague, Auston Froid, Josh Moses, Steve Meyers, Ben Stillwell
June 5th, 2025
EUSO Collaboration Meeting
Paris France

## Slide 2: Take Home Message
We are on track
Lots of fabrication to do, and some design & procurement remaining
Working a solution to an 8g failure mode identified in FEA
Friendly request to finalize ST status bytes allocation so we can program this in. (We requested 50 bytes)

## Slide 3
PBR Telescope Assembly Tilt System
Rotate elevation angle during flight for data taking at
many angles from +13 degrees to -90 degrees
-90 degrees
0 degrees
-45 degrees

## Slide 4
Controller
PLC
Tilt Mechanism
Shutter (Lower)
Motor (1),
RTD (1)
Limit Switches (4)
Shutter (Upper)
Motor (1),
RTD(1)
Limit Switches (4)
Motor (1),
RTD (1)
Limit Switches (4)
Inclinometer
2
Inclinometer (analog)
Power (TEC, heater)
RTD (1)
TEC (USB-GSE)
Inclinometer 1
Inclinometer (analog)
Power
RTD (1)
TEC (USB-GSE)
Light Sensors (Port, Starb, In)
RTDs
PBR Shutter/Tilting
System Architecture
14 DIO
8 Analog Inputs
8 RTD (Temperature Sensors)
10 DO (motor steps, direction)
network
PLC Software
Update SBP2 version
Added limit switches, RTDs
Auto Close if N light sensors read light
!Open (open, ignoring light sensors)
More status bytes
power

## Slide 6
T-Vac tests of PBR telescope rotation mechanism in
CSBF BEMCO T/Vac chamber
Test bearing design, tilt mechanism at 7mbar, -40c, -50c, -60 c
Simulated load of 2000 lbs (telescope weight), 100 ft-lbs (imbalance of telescope)
Planning for Sept or Oct 2025 for tests. About 4 days @ CSBF
Test stand
(does not fly)
Turn buckle
Tension 1000 lbs
100 lbs
Telescope
Rotation
Mechanism
(flies)
L. Wiencke Colorado School of Mines
5-27-2025
48(+7)”
32”
64”
Test assembly is designed to fit inside the ~70”x~70”x~70” BEMCO chamber.
SPB2 Test Oct 2022

## Slide 8: PBR Tilt Drive Mechanism Design – Will tilt mechanism gears and structure survive worst-case loading?
Worst-case torque due to rotated mass (telescope plus radio antenna) under load cases prescribed by the Structural Requirements Document is:
(8g)(2000 lbm)(1 in)= 16,000 in-lb
Axial force on worm:
Ft,max = 16,000 in-lb/ 6.25 in = 2,560 lb
The tilt mechanism is attached to the telescope with 6x M6 alloy steel screws, the nearest of which is 5.5” from the rotation axis. Assuming they are all at this distance (conservative), the shear stress in the screw is:
(16,000 in-ln)/(5.5 in)/6/(π)/(0.09 in)^2 = 19 ksi
Yield strength of M6 class 8.8 alloy steel screw = 76.5 ksi
Ben Stillwell (U. Chicago)

## Slide 9: PBR Tilt Drive Mechanism Design – Will tilt mechanism structure and mounting screws survive worst-case loading?
Peak stresses in gear teeth at 8g ∼ 55,000 psi
Assuming worm wheel is C90700, yield strength =21,800 psi
Teeth would tolerate (21,800 psi/55,000 psi)8g = 3.2 g
Deformation and stresses in aluminum structure are low.
Ben Stillwell (U. Chicago)

## Slide 12
“Bang Bang”
Thermal Switch
$12
EUSO-SPB2
Swiss Thermoelectic
Controller
$600 + (tariff du jour)
PBR
James Brague
Reducing Radio Noise

## Slide 14
EUSO-SPB2 2022
PBR