## Slide 1
AGATA Project
STARE
(Serial Transfer And Readout over Ethernet)

## Slide 2: Plan
  STARE Firmware
  STARE Production Status
  12 Links Crate for Readout
  Tests production

## Slide 3
STARE
INFN & U. Milano
IFIC Valence
IJCLab Orsay

## Slide 4: STARE characteristics
FMC Vita57.1 connector
Input data rate from pre-processing : 4 x 10 Gbps serial (AURORA)
Network Bandwidth up to 4 x 10 Gbps in parallel.
Spare LVDS I/O with the pre-processing for future use
Full clock management inside the SOM and the FMC carrier.
1 Gbps IPBus for slow control.

## Slide 5: Data processing (1 * 10Gb/s)
UDP interface
(David Zidler – Zurich)
Data manger
Splicer
Aurora interface
10 Gb/s
Aurora
64 bit
@156,25 Mhz
Paquets de X KB
Y Paquets de 8 KB
10 Gb/s
Ethernet SFP
_ Slow control
_ EEPROM
_ Clock manager
_ Spare LVDS link
Standalone data generator
64 bit
@156,25 Mhz
Generators available (compute by Ipbus, independant, rate ajustable) :
_ byteANDpackage_counter : data can be checked by SQM ; size of event 8 Bytes -> 256 MBytes
_ 2 Rams of 8KB : can be fill by Ipbus ; TS and EV is managed by firmware
_ adf_DTH : particular format asked by Olivier S.
Data check

## Slide 6: Splicer
Splice X KB of one event on paquets of 8 KB
Add header
Sent paquets to UDP transmiter IP

## Slide 7: RUDP (if mandatory - see tests)
UDP interface
(David Zidler – Zurich)
64 bit
@156,25 Mhz
X Paquets de 8 KB
10 Gb/s
Ethernet SFP
Reuse of D.Zidler’s code
Modification of frame size
Managed by slowcontrol (via EEPROM) :
_ MAC @ of each SFP
_ IP @ of each SFP (no DHCP)
_ other network stuff (IP server, port, gateway, etc)
Later improvement : RUDP : resent lost paquets

## Slide 8: IP_Bus SlowControl (CERN + LPSC Grenoble)
_XML module description
_Python scripts
_uHAL
Ipbus interface
1G Ethernet
STARE
Ipbus fabric
Slave
EEPROM
Slave
Splicer
Slave
PACE_SPI_bridge
network
IP Bus Protocol
Adress
Data
SPI protocol
Ipbus interface
SPI
Ipbus fabric
PACE
Slave
Slave
Slave
Slave
Prog_bitstream (new)

## Slide 9: Production
Manufacturer : STAE
150 Stare produced (+10 Pre-production)
63 SOM mounted but 5 cards fails (at least 2 differents issues -> under investigation)
15 SOM just arrived, not yet transfered to STAE
Needed (without spare) :
_ 72 SOM
_ 91 SFP -> RJ45
_ 260 optical SFP

## Slide 10: 12 Links Bay for Future Development
STARE Data Readout
Up to 2 Pizza boxes
(8 DAQ servers)
PACE Test Bench (in a crate *)
STARE 12 links
100 Gbps Optical Switche
Power Switch for remote control
Cristal emulator *
A new Bay to be designed to house all the STARE facilities
New PACE crate with cooling, Fans, PS mechanics to fix the backplane and up to 38 channels.
12 links Stare bench
100 Gbps switches
Power switch
8 DAQ servers (4 are there already)
External control via mini-PC
Cristal emulator (pulser + faninfanout + single_diff)
* Missing some parts

## Slide 11: Tests – 8*10Gbps
Stare boards generate 8*10Gbps
Acquisition on C6400 is OK for 1*10 Gbps per server -> 40 Gbps acquissition OK
More than 10 Gbps on one server is usually not possible, but some times it can works (???)
Acquisition test between building and more switches : is RUDP mandatory ?
Acquisition with a 25 Gbps network board on C6400
Validation from digitizer, PACE, STARE to PSA requires a hight resolution pulser.

## Slide 12
MERCI