## Slide 1: Recent results from FAZIA@CNAO
Sandro Barlini, Andrea Stefanini,Catalin Frosin and Lucia Baldesi
FAZIA days June 2025

## Slide 2: Main Objective
The aim was to study the efficiency of the FAZIA CsI(Tl) scintillators for high energy light charged particles
a significant decrease in identification efficiency has been reported for thick CsI(Tl) when used for energetic light particles
impinging particles can undergo nuclear interactions:
  transmutation of the colliding nucleus
  scattering of the particle out of the crystal
part of the initial energy not released in the crystal
  affect the energy measurement
  affect the identification of the particle
➡ Incomplete Energy Deposition (IED) event
IED contribution increases with the particle energy
given an energy, the IED contribution depends on the geometry
LCPs detection and identification mainly based on the CsI(Tl) ➡ the effect of IED cannot be neglected when energetic LCPs are produced
…but also: what happens in the Fazia detectors when the rate is very high (>1KHz)?

## Slide 3: FAZIA @ CNAO Setup
We wanted to extend the previous study by evaluating the efficiency under realistic experimental conditions.
a complete FAZIA block placed, in air, at 1 m from the target
polar angles from 1° to 5°
beam spot dimension at the target position from 10 to 25 mm FWHM
  before the target brass collimator 5 cm thick with a 10 mm diameter aperture.
beam profiler not used
  massive blocks of copper and lead arranged around the brass collimator.

## Slide 4
Published
Main results: Experimental Efficiency vs. Energy in CsI in the «standard» FAZIA configuration well described by a GEANT4 simulation!
.. but is this effect «relevant» in our FAZIA@GANIL experiment?
NCED from CsI(Tl) PSA
NCED +NIED from dE vsE

## Slide 5: The most problematic case: E818 58Ni+58Ni@74AMeV
Etot (MeV)
Counts
…about multiplicity, the total number of protons increases from 8.69 107 to 10.39 108 particles (i.e. a factor 1.19)
black no correction
red corrected
Etot (MeV)
Counts
Cut due to the finite length of CsI(Tl) (10 cm)
Protons not fully stopped
NO SELECTION!!!!!
Preliminary!!!

## Slide 6: The most problematic case: E818 58Ni+58Ni@74AMeV
black no correction
red corrected
Preliminary!!!
Etot (MeV)
Etot (MeV)
Counts
Counts
1114
…about multiplicity, for tele 141 there is a factor 1.23, for tee 1114 a factor 1.19
NO SELECTION!!!!!

## Slide 7: FAZIA @ CNAO: what about α-particles?
We start from the 12C+12C reactions at 150, 200, 250 and 300 AMeV to generate a continuous energy distribution of α particles. Still problem of high rate!!
sQ3max (a.u.)
fQH1+fQ2 (a.u.)
Carbon beam (150,250,300 AMeV)
As example, this is the 11 telescopes
No condition!!
..very dirty!

## Slide 8: FAZIA @ CNAO: what about α-particles?
sQ3max (a.u.)
fQH1+fQ2 (a.u.)
Zoom on dE-E with no conditions!!
sQ3max (a.u.)
fQH1+fQ2 (MeV)
Zoom on dE-E with all conditions!!
Baseline conditions
Cut on tcfd
Condition to remove «evident» pile-up
Problem: you cannot separate the 3He contribution in terms of IED!!
4He
Z=1

## Slide 9: FAZIA @ CNAO: what about α-particles?
fQ2 (a.u.)
fQH1(a.u.)
Zoom on Si1 vs Si2 with no conditions!!
Carbon line
Alfa particles line
A cut on the Si1+Si2 energy corresponds to a «diagonal» cut here. There is a strong mixing beetween alpha and heavier p.t. ions. Moreover, with a simple cut on Si1+Si2, some not p.t. events are present!!
Alpha particles selection
fQ2 (a.u.)
fQH1(a.u.)
Heavier fragments p.t.

## Slide 10: FAZIA @ CNAO: what about α-particles?
Cleaning conditions (baseline, Tcfd, and pile-up) + graphical cut in Si1 vs. Si2)
Then, for each «selected» dE (Si1+Si2) interval:
Complete Energy Deposition events counted in CsI(Tl) PSA for Z=2 and Z=1
(NCED)Z=2 = (NCED)3He+ (NCED)4He
(NCED)Z=1
(Ntot)Z=2 = from the dE selection
efficiency for Z=2
Of course, for the energy values we keep the mean of the energy distribution of Z=2 (so we need to calibrate the CsI for 3He and 4He !)
Experimentally:
sQ3max (a.u.)
sQ3fast/sQ3max
Alpha p.t. the CsI!
sQ3max (a.u.)
sQ3fast/sQ3max
Cut on dE: 3.9 MeV ≤ Si1+Si2 <4.1MeV

## Slide 11: FAZIA @ CNAO: what about α-particles?
Experimental final results:
ECsI (MeV/n)
Efficiency
T4
Q1
Q2
T2
Q4
Q3
T1
T3
T4
T2
T1
T3
T4
T2
T1
T3
T4
T2
T1
T3
Increasing rate…
Using dedicated cuts and energy calibrations, the final results for the last 3 Columns are coherent within ±3%
Beam

## Slide 12
FAZIA @ CNAO: α particles
GEANT4 simulations
Two different GEANT4 simulations for 3He and 4He including:
the 3He or 4He interaction process
the full experimental set-up
  geometry of the FAZIA block
  dead layers and passive collimator
  3He and 4He particles are directly created after the target, with angular and energy distributions similar to the experimental ones.
  The 3He/4He ratio is calibrated in order to obtain a similar (NCED)3He/(NCED)4He with respect to the experimental data
Count (a.u.)
4He
3He
GEANT
Exp. data
Angular Distr.
Energy Distribution
«Mean» ECsI (MeV)
θ
θ
θ
«Mean» ECsI (MeV)

## Slide 13
FAZIA @ CNAO: α particles
GEANT4 simulations
ECsI (MeV)
dE (MeV)
Event selection with the same «cut» on Si1+Si2
NCED events in GEANT are selected directly in the program looking to their energy loss!
Example of one telescope
ECsI (MeV/n)
Efficiency
With respect to protons, the scattering contribution to inefficiency is lower!
In any case, the 3He «geometrical» efficiency is lower with respect to 4He
GEANT4 results:

## Slide 14
FAZIA @ CNAO: α particles
GEANT4 simulations
ECsI (MeV)
Efficiency
From the point of view of GEANT4 simulation, the quartet behaviour’s is very similar…
ECsI (MeV/n)
Efficiency
GEANT4
.. the simulated efficiency is slightly over (3-4%) the experimental data
We are trying to change the nuclear cross section (using for example «shein» option as for protons»

## Slide 15
Baseline distribution CNAO exp.
cosmic rays
Baseline effects could affect the LO measurement:
if high rate ➡ baseline distribution very different from that observed at low rates, such as in cosmic ray run
  right tail: pile up
  left tail: the baseline can take lower values compared to those observed in low-rate conditions. So the «real» baseline value is accesible only with LOW rate!!
..but similar effects also in Ni+Ni@32,52,74 MeV!
Thanks to Enola Roberts, ENSICAEN
RMS value of the baseline distribution as a function of the angle
FAZIA @ CNAO: what are we learning about high rate condition?
Lower the energy, higher the rate and consequently the RMS of the baseline distribution

## Slide 16
dE vs E plot @CNAO: proton elastic peak is not «well» isolated
Baseline vs. Energy for the red selection: elastic energy is correlated to the baseline value!
Si1+Si2 (a.u.)
sQ3max (a.u.)
Baseline value
An increasing of rate can produce a loosing of energy resolution!
.. can this problem affect also the identification capability of FAZIA?
FAZIA @ CNAO: what are we learning about high rate condition?

## Slide 17
FAZIA @ CNAO: what are we learning about high rate condition?
Thanks to Enola Roberts, ENSICAEN
FOM for Si1vs Si2 identification between proton and deuteron as a
function of the angle with respect to the beam
It is evident as the most near to the beam telescope where elastic beam is present are suffering pile-up problem, affecting the energy measurement and consequently also the identification capability!
.. of course in any case we are well below the threshold of FOM=0.7…
58Ni+58Ni@32,52,74 AMeV

## Slide 18
FAZIA @ CNAO: what are we learning about high rate condition?
QL1 (a.u.)
I1max (a.u.)
I1max (a.u.)
QL1 (a.u.)
Telescope 1114
Telescope 212
12C Pile-up
Double 12C
Out-of-time 12C
High rate
Low rate
Similar effect due to high rate?
12C+12C@8.75 AMeV

## Slide 19
Conclusion and outlook
Using proton beam @CNAO data, a first paper about proton efficiency for the FAZIA block has been published. The effect is sensible at least for 58Ni+58Ni@74AMeV in terms of energy spectra and multiplicity
Using carbon beam@CNAO data, the same work has been done to estimate alpha-particle efficiency. The agreement between exp. data and GEANT4 is still good.
High-rate condition tested @CNAO are present also in our «standard» experiment when the elastic reaction is detected: Ni+Ni@32,52 AMeV and 12C+12C@8.75AMeV show similar behavior with respect to CNAO in terms of baseline distribution. This can affect energy value calculation and consequently also identification capability
For the future:
GEANT simulation to test different cross section to obtain a better agreement between exp.data and simulation
Test (with Simone) of an off-line procedure to obtain a pole-zero cancellation in order to minimize the effect of high rate in the energy measurement