## Slide 1: Measuring the neutron Electric Dipole Moment for CP violation searches with the n2EDM experiment
Katia Michielsen, LPSC Grenoble, neutrons ultra froids
7th November 2025

## Slide 2: Outline
Context
Overview of the n2EDM experiment
Hg co-magnetometer
n2EDM status and outlook

## Slide 3: I- Context What is the Electric Dipole Moment ? - a CP-violation probe - a new physics probe
I – Context
Shakarov criteria for matter-antimatter asymmetry during baryogenesis
  C and CP violation
  Baryon number violation
  Out of equilibrium
One can quantify the sensitivity of observables to new physics using Effective Field Theories (EFT).

## Slide 4: What is an Electric Dipole Moment?
Spins couple to electric fields. EDM is the coupling strength
Non-relativistic limit of the fermion-photon interaction:
Spins couple to magnetic fields. Magnetic moment is the coupling strength
I - Context
Larmor precession of a spin in a magnetic field
at frequency
Larmor precession of a spin in an electric field
at frequency
Energy
not T invariant
not CP invariant
Notes: Comment faire le lien avec une distribution de charge à l’intérieur du noyau??

## Slide 5: What do we know about the nEDM?
Non-zero measurement:
But where from??
Complementary EDM measurements required:
proton, electron, muon EDM
Theory:
Current limit:
n2EDM sensitivity goal:
I - Context
Measurement compatible with zero:
Contrains either:
CP violation in the strong sector “strong CP problem” led to the introduction of the axion
CP violating new physics
with mass scale of >1 PeV (EFT).
Measurement of the Permanent Electric Dipole Moment of the Neutron, nEDM collaboration, 2020
weak interaction
strong interaction
new physics?

## Slide 6: II- How do we measure the neutron EDM at
1. Measurement concept
I – Context II – n2EDM overview

## Slide 7: nEDM measurement concept
Larmor precession frequency measurement.
in a weak magnetic field and strong electric field.
I – Context II – n2EDM
I – Context II – n2EDM overview
In n2EDM, electric/magnetic term
any magnetic drift is prohibitive!
Measurement of the Permanent Electric Dipole Moment of the Neutron, nEDM collaboration, 2020
Hz
We measure the neutron spin at the end of a precession duration of 3 min.

## Slide 8: nEDM measurement concept
Larmor precession frequency measurement.
in a weak magnetic field and strong electric field.
I – Context II – n2EDM
I – Context II – n2EDM overview
affected by magnetic drift
after correction
Measurement of the Permanent Electric Dipole Moment of the Neutron, nEDM collaboration, 2020
Effect of the magnetic field drift in the nEDM experiment
In n2EDM, electric/magnetic term
any magnetic drift is prohibitive!

## Slide 9: Measure the neutron EDM: frequency ratio
I – Context II – n2EDM
I – Context II – n2EDM overview
Ratio R
Measurement:
(destructive)
spin asymmetry
continuous
optical reading
Reduced limit on the permanent electric dipole moment of Hg 199. Graner, Brent, et al. PRL (2016) :Hg EDM cm
Hg co-magnetometer

## Slide 10: Measure the neutron EDM: frequency ratio
Ratio R
I – Context II – n2EDM
I – Context II – n2EDM overview
Reduced limit on the permanent electric dipole moment of Hg 199. Graner, Brent, et al. PRL (2016) :Hg EDM cm
But neutrons and mercury do not see the same magnetic field…
study of the systematic effects affecting R is ongoing (Morgan Ferry)
Hg co-magnetometer
Measurement:
(destructive)
spin asymmetry
continuous
optical reading

## Slide 11: II- How do we measure the neutron EDM at
I – Context II – n2EDM overview
2. Experimental setup

## Slide 12
Superconducting
magnet
UCN spin detectors
Active magnetic shield
Passive magnetic shield
Vacuum vessel
Proton beam on Pb target
UCNs
Solid D
Switch
I – Context II – n2EDM overview

## Slide 13
contributions
Switch (UCN guiding)
Hg polarisation chambers
I – Context II – n2EDM overview
Photograph of the n2EDM precession chambers , october 2025
n2EDM precession chambers design scheme with subsystems.
Magnetic field mapper
Data Monitoring Interface
Hg injection system
Hg spectroscopy cells

## Slide 14: Enriched spectroscopy cell (L4M, LPSC)

## Slide 15: III- The Hg co-magnetometer
Concept, setup and performances.
I – Context II – n2EDM overview III – Hg co-magnetometer

## Slide 16: Measuring magnetic fields with Hg vapour
Transmitted light modulated at
Hg precession
1/2
1/2
-1/2
-1/2
spin 1
Excited states
Ground states
relevant quantum states
UV resonant light
I – Context II – n2EDM overview III – Hg co-magnetometer

## Slide 17: Optical reading of Hg precession in n2EDM
Vacuum vessel
Optical tower
Optical fiber
Monitor
photo-diode
Precession chambers
UV probe light
Polarisation cells
Polarising optics
UV pump light
Optical fiber
Optical fiber
circular
polarization
nEDM: Circularly polarised probe.
One signal per chamber.
I – Context II – n2EDM overview III – Hg co-magnetometer
Probe
photo-diodes

## Slide 18: Optical reading of Hg precession in n2EDM
Vacuum vessel
Optical tower
Optical fiber
Monitor
photo-diode
Precession chambers
UV probe light
Polarisation cells
Polarising optics
UV pump light
Optical fiber
Optical fiber
waveplates
Probe
photo-diodes
p polarization transmitted
s polarization
reflected
circular polarization
linear
polarization
n2EDM: linearly polarised probe.
Two signals for each chamber.
Cancellation of common noise.
I – Context II – n2EDM overview III – Hg co-magnetometer

## Slide 19: Probe photo-diode signals
1/2
1/2
-1/2
-1/2
spin 1
Excited states
Ground states
spin during precession
1/2
1/2
-1/2
-1/2
spin -1
Excited states
Ground states
spin during precession
TOP chamber
BOT chamber
reflected
transmitted
transmitted
reflected
UV light
I – Context II – n2EDM overview III – Hg co-magnetometer

## Slide 20: Probe photo-diode signals
1/2
1/2
-1/2
-1/2
spin 1
Excited states
Ground states
spin during precession
1/2
1/2
-1/2
-1/2
spin -1
Excited states
Ground states
spin during precession
TOP chamber
BOT chamber
reflected
transmitted
transmitted
reflected
UV light
I – Context II – n2EDM overview III – Hg co-magnetometer
Linearly polarised probe lowered the uncertainty by a factor 3.

## Slide 21: Performance of the Hg magnetometer
Precision:
TOP chamber
BOT chamber
Accuracy: unbiaised estimator?
effect of non-white noise,
magnetic field drifts within one cycle
I – Context II – n2EDM overview III – Hg co-magnetometer
status
ongoing

## Slide 22: n2EDM status and outlook
UCN production, detection, polarization, spin transport
Magnetic shielding and characterization
Magnetic field generation and characterization
Electric field
Hg co-magnetometer injection, polarization, optical reading
Cs magnetometers installation, polarisation & optical reading
2027-2028
Accelerator shutdown
2026
EDM
2029-Magic EDM
2025
EDM test run
Today
2025
n and Hg
2026
systematics
Neutrons available
Neutrons unavailable
Operational
Not yet operational
I – Context II – n2EDM overview III – Hg co-magnetometer IV – Conclusion

## Slide 23
Thank you for your attention!
Questions?

## Slide 24: Additional slides

## Slide 25: An EDM violates Charge Parity symmetry.
CPT symmetry Lorentz invariance of the Standard Model.
T violation CP violation
T-invariant
not T-invariant
Observable = magnetic moment
Observable = electric moment d
I - Context

## Slide 26: Measure the neutron EDM: Ramsey method of oscillatory fields
Larmor precession frequency measurement.
in a known magnetic field and strong electric field.
I – Context II – n2EDM
I – Context II – n2EDM overview
In n2EDM, electric/magnetic term
any magnetic drift is prohibitive!
spin flip
spin flip
Spin asymmetry

## Slide 27: Current most sensitive measurement: nEDM at PSI
Measurement of the Permanent Electric Dipole Moment of the Neutron, nEDM collaboration, 2020
In n2EDM:
Increase satistics in larger volume with a better controlled magnetic field: simultaneous measure is two chambers for both electric polarities.
Same principle of co-magnetometry: Hg and Cs.
Homogeneity of B
Number of neutrons
E
B

## Slide 28: The mercury co-magnetometer

## Slide 29: Linearly polarised light: two signals oscillating with opposite phase
unpolarised cross section
mercury density
length of the precession volume
polarisation of the mercury vapour
Transmission/reflection factors:
ideally
Derive
Derive knowing
1st fit provides
- Absorption
- Leakage time of precession chamber
2nd fit provides
- Polarisation of mercury vapour
- Depolarisation time
- Noise spectrum
- Precession frequency

## Slide 30: nEDM, one of the most sensitive probes to CP-violating new physics
Figure by Adam Falkowski, Lectures on SMEFT EPJC (2023)
Comparison of the sensitivity of different observables with the Standard Model Effective Field Theory: all coupling constants to one.
Example: dimension 6 operators
Set to 1
derived
measured
13 TeV

## Slide 31: 2. Offline control of the magnetic field: mapping
Fluxgate moving in cylindrical coordinates provides , , .
Composed of non-magnetic parts to measure the remnant field, and the generated .
I – Context II – n2EDM overview 2.
French technical contribution

## Slide 32
B
E
E
+
neutrons
mercury
I – Context II – n2EDM
neutrons
mercury
BOT
TOP
-
I – Context II – n2EDM overview

## Slide 33
Top ground electrode
Bottom ground electrode
HV electrode
Vacuum vessel
UCN guide
Coil generating B field
B
E
E
I – Context II – n2EDM overview 1.
Polarization cell

## Slide 34
B
E
E
neutrons top
neutrons bottom
But there is a vertical magnetic gradient…
I – Context II – n2EDM overview 1.

## Slide 35: Observation of gravitational shift on
Susceptibility to vertical gradient
Result:
Provides information of the energy spectrum of neutrons!
Neutrons have a lower center of mass than Hg atoms because of gravity
R slightly depends on the vertical gradients
I – Context II – n2EDM overview III- n2EDM results
top chamber
bottom chamber
cm
Preliminary

## Slide 36: R- curve: sensitivity to earth rotation
I – Context II – n2EDM overview III- n2EDM results
in the lab!
Earth rotation
and
Laboratory referential is rotating (earth rotation)
Depending on one frequency is enhanced, the other is diminished.
Measured period: hours
Magnetic field up
Magnetic field down
Result:
Rotation period
hour

## Slide 37: 1. Neutron Spin Analyzer: measure
Simultaneous detection of both spin components in gaseous detector:
Analyzing foil: spin down transmitted (spin up reflected).
Two arms: - one with a spin flipper: detects spin up neutrons
- one without: detects spin down neutrons
spin ↓ detection
spin ↑ detection
I – Context II – n2EDM
I – Context II – n2EDM overview 1.

## Slide 38: 2. Magnetic field specifications
I – Context II – n2EDM overview 2.
Specifications | fT/cm | Measured by…
Mode 1 of the magnetic field |  | Hg, online
Mode 3 of the magnetic field |  | Cs, online
Mode 5 of the magnetic field |  | Mapper, offline
Specifications | fT/cm | Measured by…
Mode 1 of the magnetic field |  | Hg, online
Mode 3 of the magnetic field |  | Cs, online
Mode 5 of the magnetic field |  | Mapper, offline
The design of the n2EDM experiment. nEDM Collaboration, EPJ C, 2021
Expansion in harmonic modes :
Non uniformities (modes ) affect the frequency ratio .
Odd-modes result in an EDM-like signal
Gradient terms
: Uniform vertical magnetic field
: vertical gradient
: non uniformities
Legendre polynomials

## Slide 39: Measuring magnetic fields with Hg vapour
spin flip
Transmitted light modulated at
Polarized Hg
Hg precession
1/2
1/2
-1/2
-1/2
spin 1
Excited states
Ground states
relevant quantum states
UV resonant light
Vapour spin polarization