## Slide 1: PICMIC* concept
I.Laktineh
* PICosecond subMICron detection concept

## Slide 2: PICMIC
X,Y
T2
T3
T4
T5
T6
T1
Grid
Pixels
MCP
Time + position
Position+ time
Patented concept:
PCT/EP2020/050058
Delay plane concept
Woven strips concept
A new concept to reach simultaneously 1 ps and submicron measurement resolutions

## Slide 3
First demonstrator:
Doublet of MicroChannel Plate
Time measurement using waveform techniques
Position measurement with a new sensors using
interconnected pixels of 5 µm
5 µm pixel
6.5 mm x 7.5 mm
A collaboration between French groups ( IP2I, IJCLAB, IPHC ) and Chinese groups ( SDU, Nankai)

## Slide 4
First demonstrator:
Doublet of MicroChannel Plate
Time measurement using waveform techniques
Position measurement with a new sensors using
interconnected pixels of 5 µm
s (Ti -Tj) is better than 100 ps
sabs is around 25-30 ps
Spatial dispersion < 70 µm
Next version of pixels sensor has been submitted and we expect to reach 10 µm
Even with our first version we have better results than Timepix4

## Slide 5
NCP
A new kind of MCP that we call NanoChannel Plate (NCP) is being developed.
It aims at producing structures with nanoholes that could be coated with
emissive and resistive materials to achieve unprecedented performances
Three technologies are followed:
Anodized Aluminium Oxide AAO (IP2I-IMP)
Silicon electrochemical etching. (IP2I-INL)
Femto-laser digging (IP2I-LabHC)
Time and spatial resolutions are expected to be 10 times better.

## Slide 6
A new generation of photocathodes with sub-micron diameter
with conic shape to exploit the NCP.
This is based on using electrochemical etching on Silicon wafer (INL)
Highly granular Photocathode

## Slide 7
1 cm radius
Photonis has produced a 1cm MCPs for us to be used with this future photocathode
Highly granular Photocathode

## Slide 8
arXiv:2303.10801v4 :Efficient site-resolved imaging and spin-state detection in dynamic two-dimensional ion crystals by R.N Wolf et al.
Study with Timepix3  PICMIC could do much better
Controlling the quantum states always need an excellent photodetector device. PICMIC could provide the best one in standard conditions
PICMIC and quantum technologies