## Slide 1
Towards Patient-Realistic PET Simulations:
Benefits and Challenges of 4D Extended Cardiac-Torso Phantom Integration into OpenGATE Simulation Frameworks
Wenhong Lan & Elnaz Olyaei
W. Lan1, E. Olyaei1,2, S. Weigel1, C. la Fougère1,3, F. P. Schmidt1,2
1Department of Nuclear Medicine and Clinical Molecular Imaging, University Hospital Tübingen, Tübingen, Germany
2Werner Siemens Imaging Center, Department of Preclinical Imaging and Radiopharmacy, University of Tübingen, Tübingen, Germany
3Cluster of Excellence iFIT (EXC 2180) “Image Guided and Functionally Instructed Tumor Therapies”, University of Tübingen, Tübingen, Germany

## Slide 2: Motivations of XCAT simulation
GATE model
PET Image Data
Patient Simulation Model
Listmode data
(proprietary)
Offline Image reconstruction
Root2lm
With respiration motion
Motion corrected
(1) Ground truth for motion correction development
Real patient
Motion corrected
Image Data
(2) Novel insert development

## Slide 3: Simulation strategies optimization with XCAT phantom

## Slide 4: Challenges of OpenGate simulation with XCAT phantom
GATE model
Image Data
Patient Simulation Model
Listmode data
(proprietary)
Offline Image reconstruction
Root2lm
Challenge 1: dramatical increase of particles
From simple geometries to patient-like phantom [4]
Simple geometric cube:
100ml with 2kBq/ml activity  200×103 particles / sec;
  60 million particles
Patient-like phantom:
3MBq/kg  189 million particles / sec. (300s)
  56 billion particles (900 times more)
Challenge 2: from static to dynamic
Static
Dynamic
we need >600 frames of the high precise patient-like 3D matrices.
One frame: 1 GB data size.
Phantom generation takes long time.
[4] W. P. Segars, G. Sturgeon, S. Mendonca, J. Grimes, and B. M. W. Tsui, ‘4D XCAT phantom for multimodality imaging research’, Med Phys, vol. 37, no. 9, pp. 4902–4915, Sept. 2010, doi: 10.1118/1.3480985

## Slide 5: Challenges of OpenGate simulation with XCAT phantom
GATE model
Image Data
Patient Simulation Model
Listmode data
(proprietary)
Offline Image reconstruction
Root2lm
Challenge 3: heavy I/O demand for data conversion
…
0.3s
300s
Data chunking:
×1000 pieces
Data conversion:
1GB
2MB
Listmode data format
The whole 300s simulation

## Slide 6: High performance computing with XCAT simulation

## Slide 7: Benchmark for computation time
+
Local workstation
NEMO2
Patient-like phantom: female XCAT
Height: 163 cm; weight: 66 kg;
Lesion number: 14;
Real patient respiration motion;
End-to-end test:
From phantom generation to LM file output
Local workstation | 
CPU | Core i9-14900kf
RAM | 128GB DDR4
ROM | HDD 8TB CMR

## Slide 8: Results of Benchmark
no motion
with motion
motion corrected
 | Voxel size | XCAT generation | Monte Carlo Simulation | Postprocessing
Local workstation | 3.1 mm3 | 73 h | 21 days | 1.5 days
NEMO2 | 1.5 mm3 | 5 h | 15 h | 40 mins
Implementation of selected motion correction algorithm:
In total, NEMO HPC is 29 times faster than local workstation.

## Slide 9: Voxelization on XCAT phantom

## Slide 10: Motivation: Voxelization in Simulation
Real Patient
Voxelization in simulation
(Voxelizaion: To replicate the complex structure)
Small voxels
Large voxels
Under different Voxel sizes:
How good of performance of replication in Image Quantification?
How good of the reproduction of motion, such as respiration, heart beating?
Small voxels
Large voxels
After reconstruction:

## Slide 11: Spheres mimicking lesions
Ø = 10 mm
Ø = 15 mm
Voxel size
[mm]
Cold BG
0.75
1.0
1.25
1.5
1.75
2.0
2.25
2.5
3.125
2.75
3.0
Reference*
…
…
…
…
…
…
Warm BG
Reference*: Geometric sphere defined at OpenGate.
Background VOI
Sphere VOI
Mean activity Concentration;
Contrast Recovery (CRC)
To Answer:
How much biases are introduced during the voxelization?

## Slide 12: Partial adult female XCAT phantom
Partial adult female XCAT phantom
(163 cm, 66 kg, [18F]FDG, 2 MBq/kg)
14 lesions from 20 patients.
Lesion:
  SUV values: 3.5, 7 and 14;
  Ø = 10 & 15 mm
  Lung & liver area
0.75 mm voxel size
3.125 mm voxel size
To answer:
  Which voxel size performs the most robust lesion representation?
Reference*: Geometric lesions defined at OpenGate + voxelized partical XCAT
Voxel size: 0.75, 1.0, 1.25, …, 3.0, 3.125 mm
Reconstruction protocol:
5 mins scan
4i, 5s
OP-OSEM + PSF-TOF
No post-filter
Geometric lesions
(Reference)
Voxelized lesions
(3.125 mm)

## Slide 13: Absolute change of Mean activity concentration and CRC
Mean activity concentration biases:
0.75 → 1.25 mm: 11.6% ± 1.1%;
1.5 mm: 14.9% ± 2.1%;
1.75 → 3.125 mm: (up to 19.0 ± 8.2%).
Geometric lesion
Voxelization
How much biases are introduced during the voxelization?
CRC:
1.5 mm: 0.80  0.90 (Ø=15mm); 0.70  0.84 (Ø=10mm);
1.75 → 3.125 mm: ( up to 0.9, ↑29%, Ø=10mm).
sphere
Background

## Slide 14: Relative change of SUV at delineated lesions
Which voxel size performs the most robust lesion representation?
Ø = 10 mm lesion:
std = 0.03 (liver, 1.25mm)
std = 0.05 ( lung, 1.5 mm)
Geometric lesions
(Reference)
Voxelized lesions
(3.125 mm)
Lower standard deviation  more robust configuration of voxel size
Ø = 15 mm lesion:
std = 0.01 (liver, 0.75 mm)
std = 0.01 (lung, 0.75 mm)
Balancing the computation and lesion fidelity
1.5 mm voxel size.
14 lesions (lung and liver regions)

## Slide 15: Conclusion and outlook
Voxel size of digital phantom  lesion fidelity.
For lesion Ø=10 & 15mm,
  Voxel size of 1.5 mm: balancing lesion fidelity ↔ computation feasibility
Future work:
  Varying respiratory patterns
  More lesion types
Spheres mimicking lesions
Partial XCAT

## Slide 16: XCAT motion modelling

## Slide 17: Motion definition at XCAT
Two parameters:
max_diaphragm_motion (at parameter input tab)
Respiration curve files
max_diaphragm_motion [cm]
With respiration motion
Respiration curve control points
Maximum amplitude: -10 mm
How do they interact and define motion?
Which motion config closer to real patient?

## Slide 18: Change of max_diaphragm_motion
10 mm
20 mm
max_diaphragm_motion:
1.0 cm
2.0 cm
DiaMax: 4.0
DiaMax: 2.0 (default)
20 mm
40 mm
Max amp [mm] | max_diaphgram_motion [cm] | Diaphragm Moving [mm]
-10 | 1.0 | 10 mm
-10 | 1.5 | 15 mm
-10 | 2.0 | 20 mm
-10 | 4.0 | 40 mm
-10 | 8.0 | 80 mm
Maximum amplitude: -10 mm

## Slide 19: Change of Respiration curve
Maximum amplitude: -20 mm
Curve max. [mm] | max_diaphgram_motion [cm] | Diaphragm moving [mm]
-10 | 1.0 | 10 mm
-10 | 1.5 | 15 mm
-10 | 2.0 | 20 mm
-20 | 2.0 | 40 mm
-10 | 4.0 | 40 mm
-20 | 4.0 | 80 mm
-10 | 8.0 | 80 mm
-20 | 8.0 | 160 mm
Max_diaphragm_motion: 4.0 cm, Curve max.: -20 mm
Max_diaphragm_motion: 2.0, Curve max.: -10 mm
80mm
20 mm

## Slide 20: Head-to-toe XCAT phantom with respiration motions
Head-to-toe adult female XCAT phantom
(163 cm, 66 kg, [18F]FDG, 2 MBq/kg)
*Extracted from real patients by vendor specific software.
[1] Paul J Schleyer et al 2009 Phys. Med. Biol. 54 1935; (Deviceless motion management for PET imaging, Siemens Healthineer)
*
+
Voxel size: Optimized setting
Motion correction [1]:
End-to-end verifications
Respiration replication
max_diaphragm_motion = 2.0 cm
Respiration curve, max. = 10 mm

## Slide 21: End-to-end verification with XCAT phantom
Reference
With motion
Motion corrected
[mins]
Frequency spectrum correlation = 1.00
With motion
Motion corrected
Respiration Curves
[mins]
Frequency spectrum correlation = 1.00
Real patient scan
Voxel size: 1.5×1.5 ×1.5 mm3

## Slide 22: End-to-end verification with XCAT phantom
Reference
With motion
Motion corrected
max_diaphragm_motion = 2.0 cm
Respiration curve, max. = 40 mm
max_diaphragm_motion = 2.0 cm
Respiration curve, max. = 20 mm
A proper configuration for 163 cm XCAT:
max_diaphragm_motion = 2.0 cm
Respiration curve, max. = 10 mm

## Slide 23: Tackling overlapping object, truncation and towards more realistic breast phantoms

## Slide 24: Integration of XCAT Phantom into Other Scanners
Developing a dedicated breast PET/MR insert integrated with the Biograph mMR to improve breast cancer diagnosis.
2 Cylinders , 5 Rings , 32 Detectors per ring
We aiming for building a patient based realistic breast phantom to study in the simulation of the hybrid system (mMR and Breast Insert)
Get advantage of XCAT phantom for primary studies and as a foundation to develop a realistic breast phantom
Voxel size: 1.5×1.5 ×1.5 mm3
Partial adult female XCAT phantom
(163 cm, 66 kg, [18F]FDG, 2 MBq/kg)
Breast Insert and mMR Scanner GATE model
PET Image Data
Offline Image reconstruction
Patient Simulation Model
Root2Sinogram
Main Goal

## Slide 25
Voxel size: 1.5×1.5 ×1.5 mm3
Partial adult female XCAT phantom
(163 cm, 66 kg, [18F]FDG, 2 MBq/kg)
PET Image Data
Offline Image reconstruction
mMR Scanner GATE model
Root2Sinogram
Primary Workflow
Integration of XCAT Phantom into Other Scanners
Main Goal
Breast Insert and mMR Scanner GATE model
PET Image Data
Offline Image reconstruction
Root2Sinogram

## Slide 26
Voxel size: 1.5×1.5 ×1.5 mm3
Partial adult female XCAT phantom
(163 cm, 66 kg, [18F]FDG, 2 MBq/kg)
Insertion of XCAT phantom into the GATE mMR – Only scanner to solve the primary challenges of Overlapping
Study the effect of the Breast Insert in the terms of lesion detection and activity recovery
Integration of XCAT Phantom into Other Scanners
PET Image Data
Offline Image reconstruction
mMR Scanner GATE model
Root2Sinogram
Primary Workflow

## Slide 27
Voxel size: 1.5×15 ×1.5 mm3
Partial adult female XCAT phantom
(163 cm, 66 kg, [18F]FDG, 2 MBq/kg)
Challenges of XCAT inside Smaller Scanners
mMR Biograph Bore Size: ~60cm
Quadra Scanner bore size: 78 cm and Axial FOV: 106cm
Challenge One

## Slide 28
Voxel size: 1.5×15 ×1.5 mm3
Partial adult female XCAT phantom
(163 cm, 66 kg, [18F]FDG, 2 MBq/kg)
Challenges of XCAT inside Smaller Scanners
Axial PET FOV: 258 mm
(i.e., ~25.8 cm)
~25.8 cm
Challenge Two
How to tackle these issues ?
mMR Biograph Bore Size: ~60cm
Quadra Scanner bore size: 78 cm and Axial FOV: 106cm

## Slide 29
Suggested Solutions to avoid Overlaps and have a full body simulation
Challenge 1 Solution
Challenge 2 Solution
Air Box
XCAT Phantom ready to be inserted in the Simulation
~25.8 cm
Slice 1
Slice 2
~25.8 cm
~25.8 cm
Slice 3,…

## Slide 30
Acknowledgments
Christian la Fougère
Fabian Schmidt
Stefan Weigel
Wenhong Lan
The authors would like to thank the state of Baden-Württemberg for its support of bwHPC and the German Research Foundation (DFG) for funding under "Project number 455622343" (bwForCluster NEMO 2).
Thanks for your attention
Jorge Cabello
Maurizio Conti
Noah Birge
Paul Schleyer
Fabian Schmidt
Elnaz Olyaei
Lukas Rauscher
Janina Hohnholz
Christian Pommranz