## Slide 1: Stray Light Assessment for IRT A phase, M7 proposal
State of work
INAF - OABr

## Slide 2
INAF - OABr
Introduction: Real Image degrading effect

## Slide 3
INAF - OABr
Introduction: Real Image degrading effect
Irradiance plot
Perfect Image
Diffraction
In field scatter

## Slide 4
INAF - OABr
Introduction: In Field Scattered light
Light Scatter Cone
Scattered Light Distibution (BSDF) modelled by Harvey – Shack Parameters
Caused by microscopic mirror imperfection
Divided in two categories:
Surface roughness
Particle Contamination
(b0,l,s)

## Slide 5
INAF - OABr
Modelling Modeling Parameters and Approach:
1: Surface roughness
Surface power spectum distribution is modelled with empirical machining data (ABC -model)
Harvey Parameters are determined empirically from RMS
RMS
b0,l,s (Scattering Cone)
Value of 2 nm RMS was used

## Slide 6
INAF - OABr
Modelling Modeling Parameters and Approach:
2: Particle Contamination
Total Scattered Energy (TIS)
Scattered Light Distribution
Parameters in the model:
PAC: % of dust area coverage
Particle diameter distribution
Calculated from cleanroom fallout and exposure time
Empirical: different model are available

## Slide 7
INAF - OABr
Modelling Modeling Parameters and Approach:
2: Particle Contamination: approach
Determine the expected PAC
from cleanroom fallout and exposure time
Make a hypothesis on the distribution two are presented

## Slide 8
INAF - OABr
Modelling Modeling Parameters and Approach:
2: Particle Contamination: approach
Expected PAC : 7000 ppm
IRT Telescope Design Description, Trade-off and Analysis Report , Airbus , 2023
Time in Cleanroom | 7000 ppm | 10000 ppm
ISO - 5 | 84 days | 121 days
ISO - 4 | 502 days | 717 days
ISO - 3 | 2900 days | 4250 days

## Slide 9
Modelling Approach: IRT Telescope
M1
+
M2
Peterson model
(NA, D)
…
+
Scattering Model (e.g. Roughness)
M1
+
M2
…
+
Scattering Model (e.g. Dust)

## Slide 10
Results: Effect Comparison

## Slide 11
Results: IRT Optical System
Two particle distributions are plotted
~3 OoM below general system requirement

## Slide 12
Results: Roughness sensitivity
Parabolic sensitivity
General Requirement met at 230 nm RMS

## Slide 13
Results: Sensitivity to contamination
Linear Sensitivity curve

## Slide 14
Next Steps: Out of Field contribution
PST: Total sensor irradiance as function of
Critical Path Determination:
Detector FoV
Outside lluminated

## Slide 15
Next Steps: Out of Field contribution
Build Stray light model:
  Black Surface Treatment
  Detailed Mechanical model: Mirror Edges, Spider-M2 interface

## Slide 16
Next Steps: Roadmap
Build Stray light model:
  Black Surface Treatment
  Detailed Mechanical model: Mirror Edges, Spider-M2 interface
First Order Analysis:
  Critical Path Determination (and mitigation proposal)
Higher Order Analysis:
  PST: wide band/low resolution
  PST: emphasis on targets exclusion angle (Earth/Sun/Moon)