## Slide 1: EPICS legacy at Saclay 1993 to 20xx… and focus on recent projects
Françoise Gougnaud – CEA Paris-Saclay

## Slide 2: Joining the EPICS community in 1993
1

## Slide 3: First steps with the Tesla Test Facility Injector control
  TTF (DESY): project to demonstrate the feasibility of a large superconducting positron electron collider
  French collaboration in charge of the Injector including an electron gun, a subharmonic buncher, a superconducting capture cavity … and beam diagnostics
  2 French Labs LAL (Orsay) and (Dapnia) Saclay for the control
Schematic Layout of TTF Injector
Synoptic Display for the Injector

## Slide 4: EPICS platform used
  DESY pushed for EPICS
  With VME/VxWorks and an MVME162 Motorola CPU
  Saclay chose the ADAS boards already used
      ICV150 (A/D) 14 bits
      ICV712 (D/A) 12 bits
      ICV196 (BI/BO)
  Fast A/D OMNIBYTE COMET
  SUNOS workstations, SUNDIALS knobs
  medm, km, dct, and some EPICS tools of that time
  SNL sequencer also widely used
Superconducting Capture Cavity Control

## Slide 5: TTF Injector controls
  TTF Injector completely installed late 1997
  Software development was rather fast
  The community was small but very supportive
  Finally only the French Labs and the DESY cryogenics group used EPICS
  Then DOOCS, the DESY control framework was used for TTF
Parameter Page

## Slide 6: Spiral2 in 2007
Rare Ion Beam Facility
2

## Slide 7: Next significant step: Spiral2 collaboration
  Spiral2 aims to produce and study rare ions currently running at Caen in Normandy
  2 kinds of sources, preaccelerated by an RFQ, rebunchers and a superconducting Linac
  EPICS selected in 2010, control system has always been under the responsibility of Ganil
  Efficient collaboration between 3 French laboratories: Ganil, IPHC and Irfu Saclay

## Slide 8: Injector lines, some diagnostics & LLRF
Deuteron source & LBE2 & LBEC tested at Saclay
Ion source (q/A=1/3)& LBE1 tested at Grenoble
TOF tested at Ganil
LBEC Slits
VME64X digital LLRF

## Slide 9: Common Hardware Platform
  EPICS platform for the whole project
    Based on VME (Emerson MVME 5500)/VxWorks and Linux PCs
    Still used NEXEYA/ADAS previous boards (150, 712, 196)
    A new set of boards for faster acquisition
      ICV108: a controller board with RAM 4 Mbytes, external trigger
      ICV178 : 8 ADCs, 16 bit resolution, 50 K Samples/s up to 1.2 M Samples/s
    An EPICS driver was developed for the synchronized intensity measurement based on ICV108+ICV178

## Slide 10: Common EPICS software platform for the 3 labs
  Homogeneous development to ease integration
  Automatic installation of VxWorks tools and EPICS distribution
      VxWorks 6.9
      EPICS 3.14.12.4
  Rules for naming PVs, files and global functions
  A development model used by each developer:
      Top directory topSP2: in-house architecture
      An automatic building of IOCs:
        makeBaseApp templates for Apps and IOCs
  Available from SVN server at Ganil
  EDM CSS BOY in 2011
  Saclay ceased to be involved in 2012

## Slide 11: Spiral2: my feeling
The 3 control teams had different cultures.
The choice of EPICS, the common platform, a positive attitude within the control teams, led to having an injector, including its diagnostics, up and running quite quickly.
Christophe Haquin who is the head of the Spiral2 control will provide us with a status presentation of Spiral2 this morning.

## Slide 12: Collaboration with ESS in 2014
3

## Slide 13: Collaboration with ESS
For 5 years Irfu has been involved in several in-kind contracts
  Source and LEBT controls at Catania (Sicily, Italy)
  Cold RF test stands for ESS cryomodules at Saclay
ESS recommended we use VME Linux based solutions on IOxOS boards.
  First step to give up VxWorks
In parallel ESS decided to migrate to MTCA.4
We could observe their progress with the IOxOS boards and the advantages to use both MTCA.4 and MRF Timing
RF test stand at Saclay
Allison Emittancemeter at Catania

## Slide 14: Saraf-Linac and migration to MTCA.4 in 2018
4

## Slide 15: Saraf-Linac context
Phase II
Saraf is being built in Soreq
Collaboration between CEA-Irfu and IAEC-SNRC for the upgrade of the Saraf accelerator
  Saraf-Linac
Irfu is in charge of design, building and commissioning of the Medium Energy Line and the superconducting Linac
Main goals of this programme:
  Develop an experimental infrastructure in the field of nuclear sciences
  Produce radioisotopes for medical use
  Expand research and applications based on neutrons
  5 mA CW, Energy: 40 MeV and beams of protons and deuterons

## Slide 16: Saraf-Linac
The MEBT includes 3 rebunchers (3 warm cavities, 176 MHz), 8 quadrupoles and 8 steerers
The superconducting Linac: 4 cryomodules comprising 28 cavities, 20 solenoids and 20 BPMs
Cryomodules are separated by warm sections
EPICS chosen in 2017 and the fast acquisition system and synchronization based on MTCA.4 in summer 2018
20 MTCA crates, 19 PLC crates and 32 cabinets of instrumentation
Injector
MEBT
Super Conducting Linac

## Slide 17: Migration to MTCA.4
In 2018 SNRC and CEA agreed to migrate to an MTCA.4 platform for the Saraf EPICS control system
This platform is based on the very compact NATIVE-R2 crate with a common core in each crate:
  NAT-MCH-PHYS80 board (80-port PCIe Gen3 switch) combined with
Rear Transition Module CPU: RTM-COMex-E3 then RTM-COMex-Ce16
    A set of IOxOS boards was also added (ADC-3117, ADC-3111, DIO-3118)
    MRF boards for the Timing System

## Slide 18: Standardization based on COTS solutions
Event generators generate events at a repeat frequency
Event receivers generate an electrical signal when an event occurs
Communication through Optical Fibre
neutron Beam Loss Monitors (SCL)
Saclay EPICS driver
Saclay EPICS driver
Faraday cups , ACCTs, slits, B-Blockers
Community EPICS driver
Event generators generate events at a repetition frequency
Event receivers generate an electrical signal when an event occurs
Communication through Optical Fibre

## Slide 19: Saraf-Linac overview

## Slide 20: Saraf: MRF Timing System Architecture
EVM Master is synchronized by the Master Oscillator (distributes reference frequency) and by GPS (Pulse Per Second & Universal Timing Coordinated)
Comex synchronized by NTP server from GPS
EVR receives PPS from EVM Master
One receiver board in each MTCA crate
Events generated at the repetition frequency from the Master event generator and transferred to all receivers through Optical Fibre
Receivers analyse the events and generate the requested signals
Upstream communication (Saraf Machine Protection System)
Presentations by Alexis Gaget on Tuesday and Thursday on the Timing

## Slide 21: Saraf:LLRF & BPM outsourced
Outsourced to Seven Solutions/Safran
Each LLRF MTCA Native-R2 crate includes 2 LLRF boards:
    2 LLRFs/board so 4 LLRFs/crate
    1 RF Fast Interlock (RFFI in-house development) system based on IOxOS 3117 + 3118
    RFQ, 3 rebunchers and 27 LLRFs on the Cryomodules
Each BPM MTCA Native-R2 crate includes 3 Seven Solutions BPM boards
    2 BPMs /board
    BPMs on MEBT and Cryomodules

## Slide 22: Use case of MTCA backplane: RF Fast Interlock
EVR
COMEX
LLRF x 2
LLRF X 2
4 * PUe
3118 3117 3117
(Cavity+Coupler)
*4
Analogue converters
4 * PM
Ts3_1a
Ts3_1b
Ts3_2a
Ts3_2b
IOxOS 1410
U Amp
  Use of MTCA backplane: allows many wire connection problems to be avoided
    More reliability and flexibility
  RFFI: stops RF if PM or PUE overrun to protect couplers and cavities
  Sensors: PM (PhotoMultiplier), PUE (Peak-Up Electron)
  Acquisition range IOxOS-3117: 5 Mhz, +/-10V
Cut Off
the RF command
Simplified schematic

## Slide 23: Irfu EPICS Environment (IEE) server
CEA team updated the Irfu EPICS Environment for MTCA.4 and IOxOS boards
IEE server to share:
  EPICS environment as NFS folders
  Same environment mounted on MTCA boards, IPC …
  DHCP, NTP, TFTP and NFS to boot embedded devices (IPC or MTCA boards)

## Slide 24: IEE Development Environment
for developers to implement new EPICS modules and IOCs using the EPICS environment shared by the IEE server
provides the EPICS folders mounted by NFS:
  /iee/base, /iee/extensions, /iee/modules, /iee/support, …
IEE was used by developers of the Lab, for Saraf and its test stands,by our subcontractors and the IPHI facility
but now only by Saraf because there is EPNIX!
  See Rémi’s presentation « Why EPNix? »
      on Tuesday

## Slide 25: Saraf Machine Protection System
Tested on the MEBT since 2024
Presentation « Timing, MPS and control of beam operation at Saraf»
    by Alexis Gaget
Relies on 3 sets:
  Beam Destination Master (PLC master)
  Section Beam Current Transmission
  TiMinG system

## Slide 26: Saraf Main Control System
Specific work to:
  Standardise the appearance of the displays: graphical guidelines, display sizes…
  Standardise the control for navigation
  Same menu and same location in each display (left side panel)
MEBT
LEBT

## Slide 27: Saraf MCS drill down structure
Cryomodule Vacuum
Cryomodule Cavities and Solenoids
Top Level View
HOME button to go back to the Top Level View
Migration from CSS to Phoebus summer 2023
Phoebus tools integrated: Alarm, Olog, Save-and-Restore, Archiver Appliance, Channel Finder
« SARAF-Linac high-level applications »,
    Antoine Choquet
HOME
button

## Slide 28: Saraf status
Injector completely commissioned in 2023.
DC 20% 4 mA on DB2 (end of the line) MEBT in November 2024.
Currently CryoModules CM1 and CM4 entirely installed,
  CryoModule CM2 in progress and CryoModule CM3 pending.
CM1 including 6 cavities, 7 solenoids and 7 BPMs warm tested.
  Issues with the cryogenic part.
See presentation: « Remote commissioning of an EPICS-controlled accelerator »
  by Gabriel Desmarchelier

## Slide 29: Titan
4

## Slide 30: Linac IPHI -> Titan
  Proton source (SILHI) + LEBT + RFQ + Diagnostics
  Continuous beam of 100 mA protons accelerated up to 3 MeV (beam power: 300 kW)
  Test tool for our collaboration to other projects and acquisition of technological expertise
  VME (with VxWorks) and SIEMENS PLC technologies
  Controlled with EPICS in 2000. HMI with MEDM
Improvement and extension of the IPHI high-intensity proton accelerator with targets to produce neutrons
Industrial tool for neutronography
9 MTCA (with Linux), 10 SIEMENS PLCs, MRF timing technologies
EPNix environment. HMI with Phoebus. VM managed with Proxmox
Presentation of Titan control system by Yannick Mariette
    on Tuesday
IPHI (Injector of Proton with High Intensity): started in 1996
Titan: started in 2019

## Slide 31: CEA workpackage for PIP2
4
Phase II

## Slide 32: PIP2 CEA workpackage
RF cold tests of 10 cryomodules
  each one including 4 Low-Beta cavities
EPICS control based on:
  MTCA.4 standardized platform
  EPNix environment

## Slide 33: Thank you