## Slide 1: OPC UA EPICS Device Support
Interfacing Industrial Controllers
Ralph Lange, ITER Dirk Zimoch, PSI

## Slide 2: The OPC UA Standard Interfacing SCADA to Controllers (PLCs)
Industrial standard (2008) to interface controllers
  Covers data, alarms, events, historical data, remote methods
  Symbolic addressing
  Browsable
Based on OPC Classic (Microsoft, 1996), adding
  Portability (does not require DCOM/Windows)
  WAN Support (TCP instead of DCOM)
  Safety/security (certificate-based authentication and encrypted connection)
  Information modeling (user-defined structures)

## Slide 3: EPICS Device Support Module Two Low-Level OPC UA Client Choices
Commercial C++ Client SDK by Unified Automation
  4k€ for source code and 1 year support (extend support: 20% per year) one developer/many products or many developers/one product
  Binaries can be deployed/distributed royalty-free
  Platforms: Windows and Linux; evaluation bundles available
  Newest versions (1.7.9 and 1.8) have issues
New (2024): Free open62541 SDK C client libraries
  Work by Dirk Zimoch (PSI) and Carsten Winkler (HZB/BESSY)
  Not trivial to set up
  More complexity on the Device Support side
  Platforms: Windows and Linux
  Less documentation than the Unified Automation SDK

## Slide 4: EPICS Device Support Module Status
Requirements Specification v1.1: https://bit.ly/opcua-srs-11
Design done (no formal doc)
Implementation nearly complete
  All basic data types and arrays thereof (read/write/subscribe)
  Supporting all applicable EPICS record types (bidirectional outputs)
  User-defined structures (read/write/subscribe), timestamps from data
  Server-side queues, configurable connection behavior
  Configurable server-side deadband filters
  OPC UA Security (encrypt, sign, authenticate) Lots of testing help by Roland Fleischhauer (HZB/BESSY)
  Integrated end-to-end test against a software server Work by Ross Elliot and Karl Vestin (ESS)

## Slide 5: EPICS Device Support Module New in version 0.11
Better Enum support
  Automatic choice strings from server for string and mbbi/mbbo records
Support for Unions and OptStructs
More OPC UA string types
  LocalizedText and QualifiedName (as string or structure)
  XmlElement (as string)
  ByteString (as hex string or UCHAR array)
Limited support for server-side deadband filters

## Slide 6: EPICS Device Support Module Roadmap
Started:
  Wiki pages: List of servers that have been integrated Useful tricks and hints (zero feedback so far)
Currently:
  Performance improvements for large data structures (Ralph)
  User Manual (Ralph)
  Support for array/matrix slicing and arrays of structures (Dirk)
Soon:
  Support for OPC UA methods (remote execution of PLC code) (Ralph)
  Support for servers that change structures on-the-fly (Karl)

## Slide 7: Users (as known)
Facility | OPC UA Server | Status
ASIPP | LabVIEW | production
 | PLC Siemens S7-1500 | production
Australian Synchrotron | PLC Siemens S7-1500F | near production
BESSY II @HZB | PLC Siemens S7-1500 | production
 | Phoenix Contact | production
 | SoftIng uaGate | production
CHIMERA @CCFE | PLC Siemens S7-1500 | development
 | LabVIEW | development
ESS | PLC Siemens S7-1500F | production
 | ABB Power SCADA | near production
 | Siemens DESIGO | development
Fermilab | Kepware KEPServerEX | testing
 | PLC Siemens S7-400 | development
IPR | PLC Siemens S7-1500 | testing
ITER | PLC Siemens S7-1500 / S7-1200 | production
 | Siemens WinCC OA | production
 | PCVue | production
 | LabVIEW (compactRIO) | prototyping
KATRIN @KIT | LabVIEW | prototyping
IBPT @KIT | PLC Siemens S7-1500 | production
PSI | PLC Siemens S7-1500 | production
 | PLC WAGO 750-8212 | production
 | PLC Beckhoff | production
 | open62541 server on Red Pitaya | near production
Varian ProBeam | PLC Siemens S7 | production
 | PLC Beckhoff | production

## Slide 8: EPICS Device Support Module Download
Device Support under EPICS license
Upstream repository, Wiki pages, binaries, (future manual): https://github.com/epics-modules/opcua
The GitHub download area has statically linked shared libraries containing the Unified Automation SDK client (i.e., plug-in libraries to link your IOCs against)
  Easy to use, fully functional, free forever
  Needs to match exactly your Linux distro and EPICS Base