## Slide 1: EPICS Module for Gating EPICS Alarms (and more)
21.04.2026
E. Blomley – Spring EPICS collaboration meeting 2026

## Slide 2: KIT Accelerators
  KARA (Karlsruhe Research Accelerator)
      Mix of user operation and accelerator research
      Injection: 1h, energy ramp 3 min, operation: 23h
  FLUTE (Ferninfrarot Linac- und Test-Experiment)
      Experiments with very different operational setups
  cSTART
      Storage ring for non-equilibrium physics
      Injector: FLUTE OR laser plasma accelerator
      Installation starts ~ Mid 2026, commissioning ~ 2027
          Many different operational modes

## Slide 3: Motivation: Alarms Guide the Operator
  Alarm summaries mapped to navigation menu
  Support operator to quickly identify potential issues
  Lead to panel where the issue can be fixed
1. and 2. level alarm hierarchy reflects our navigation
Panel shows at least one minor alarm

## Slide 4: Gating Alarms?
  “Alarms” in EPICS and this talk:
      The alarm severity and alarm threshold fields of records
  Make “alarms” (dis)appear based on certain conditions
      Kicker magnet OFF  Alarm, ON  No alarm
      Kicker magnet OFF  No alarm, ON  Alarm,
record(bi, Kicker:Status:On) {
field(ZSV, “MAJOR“)
field(OSV, “NO_ALARM“)
}
record(ai, Magnet:Current) {
field(LOLO, “5“)
field(LLSV, “MAJOR“)
field(LOW, “8“)
field(LSV, “MINOR“)
field(HIGH, “14“)
field(HSV, “NO_ALARM“)
}
  Not talking about actual (hard-wired) alarms & interlocks: machine protection, personal safety systems, …
          Gating Alarms  Dynamic EPICS notifications to support operators

## Slide 5: Possible System Designs
          Best approach? Depends…
Configuration
Deploy
Execute
Global file
File per IOC
Per record
Condition
Adjustment
Central application
Part of IOC(s)
New Alarm PVs
Change existing records
          System we used for the last 10 years
          Setup we are moving to

## Slide 6: Introducing New EPICS Module: Conditional Field Adjuster
  Features
      Use info fields for configuration
      Only requires EPICS base
      Passive while IOC is running
          In-place, compact & easy to understand and use.
          Scales with IOC.
record(bi, Kicker:Status:On) {
field(ZSV, “MAJOR“)
field(OSV, “NO_ALARM“)
info(cfa:select, „STATUS:PV CP“)
info(cfa:1:ZSV, „NO_ALARM“)
info(cfa:1:OSV, „MAJOR“)
}
STATUS:PV == 0: Injection
STATUS:PV == 1: Operation

## Slide 7: Configuration & Usage
  info(cfa:select, “<PV> CP”) - gate PV, expects positive integer
  info(cfa:<int>:<field>, “<value>”)
      <int>: integer to match the select PV
      <field>: any field which exists for the record and is writable while IOC is running
  Default values are the actual record fields
  info(cfa:scan, “Passive”) – optional
Configuration
- configure/RELEASE
- myIocApp/src/Makefile
myIoc_DBD += conditionalFieldAdjuster.dbd
myIoc_LIBS += conditionalFieldAdjuster
No st.cmd modifications

## Slide 8: Backend
  Auto-generated records injected into IOC during startup
  initHookAfterInitDevSup
  Record naming:
      cfa:<30 random characters>
      Avoid potential PV length conflicts
          Considering to add configuration options for record naming

## Slide 9: More on the Gate PV
Magnet IOC
Timing IOC
Vacuum IOC
PV:GlobalOperation:Mode
Global Approach
RF IOC
PV:InternalState
Error:PV1
Error:PV2
Error:PV4
Error:PV5
Error:PV6
Error:PV3
Local Approach
Error:PV4
Error:PV5
Error:PV6

## Slide 10: Only for Alarms?
  Adjust SCAN rate?
  Precision?
  LOPR/HOPR?
  CALC parameters?
  …
          Can be used for any writable EPICS field
          Limitations:
  Using as a central application
  Embedded systems
  Python-based IOCs
  Changes require IOC redeployment

## Slide 11: Demonstration

## Slide 12: Summary
  Introducing new EPICS module: Conditional Field Adjuster (CFA)
  Allows to define (alarm) fields in a more flexible way
  Use cases beyond alarming
  Phoebus properly displays the field adjustments
          Next steps
  More real-word testing
  Add tests
  Add more examples
  Start using in production
  Release 1.0
https://github.com/KIT-IBPT/conditional-field-adjuster
Try current preview version!
More technical description in README

## Slide 13: Backup - Demonstration

## Slide 14: Demonstration Backup