## Slide 1: RTEMS 6 Migration and Driver Development for Motorola VME Boards
Ran Hong*, Andrew Johnson, Brendan chandler
Advanced Photon Source
Argonne National Laboratory
9700 S Cass Ave, Lemont, IL 60439
Apr 20th, 2026

## Slide 2: Outline
Backgrounds about the migration from VxWorks to RTEMS at APS
Overview of RTEMS and the application development workflow
RTEMS migration goals and milestones at APS
RTEMS and libBSD development at APS
EPICS-base development for RTEMS
IOC prototypes and benchmark tests
On-going efforts and near-future plans

## Slide 3: Backgrounds
More than 100 VME-based IOCs running on VxWorks at APS, in both the SR and the injector complex. Many more on beamlines.
Motivations for switching to RTEMS
  Real-Time Executive for Multiprocessor Systems (RTEMS)
    High-performance real-time operating system
    Designed for deterministic embedded applications
  Open source: transparent, configurable, no licensing costs and vendor lock-in
  POSIX API support: easier porting code from unix-like systems.
  Proven reliable in past space missions (Orion, Mars rovers, etc.)
EPICS Supports for RTEMS
  EPICS IOCs widely implemented with RTEMS4 and 5
  Modernization: upgrade to RTEMS6 or 7
    Modern network stack and protocols: NFSv4, TLS 1.3 , etc.
    Modern toolchain: GCC 10+ and LLVM
    Security: audit-ready and pre-qualified
APS-U Storage Ring
Booster
PAR
Linac
Board | Quantity Storage ring and injector complex only
MVME3100 | 60
MVME2500 | 25
MVME5100 | 14
MVME2100 | 11
MVME6100 | 1
MVME2700 | 1

## Slide 4: RTEMS and application development workflow
Application Development Workflow (Project repository: gitlab.rtems.org)
  Build tool suite (cross-compilers and etc.) using RTEMS Source Builder (RSB)
  Build RTEMS BSPs
    Configure and build RTEMS BSP
  Build Packages needed by the application
    libBSD: libraries for FreeBSD (open-source Unix-like OS derived from Berkeley Software Distribution)
    Network stack and device drivers
    Network services: NTP, etc.
  Build Application
    Build the application code: RTEMS initialization function, main function, shell, etc.
  Deploy Application
    Deploy compiled application binary file to the target device via tftp, pre-loaded image file, etc.
    Targets with qoriq_e500 BSP also needs a compiled device tree blob (dtb) file to boot
Build Tool suite
Build BSP
Build Packages
Build Application
Deploy

## Slide 5: EPICS on RTEMS
Legacy RTEMS releases
  EPICS 3.14 and 3.15 support RTEMS4.10
  EPICS 7.0 supports RTEMS 5
Current RTEMS releases
  EPICS 7.0.9+ supports RTEMS 6.x (current stable standard)
  Issues with current RTEMS 6 and libBSD releases
    Lacks BSPs (e.g. mvme5100)
    Lacks drivers for certain BSPs (e.g. network driver for mvme3100)
  Issues with current EPICS release
    Boot configuration is not standardized
    Static IP is not supported when using libBSD networking
    Performance issues: slow in establishing channel access link.
RTEMS Development branch
  RTEMS 7 (main branch of the rtems repository)
  Next release: EPICS 7.0.11 (7.0 branch of the epics-base repository)
  Repositories at APS are forked from the official repositories (upstream)
RTEMS BSP
libBSD
Packages…
EPICS Base
Support Modules
IOC
RTEMS Tools
Deploy to Hardware
RTEMS Application

## Slide 6: Milestones and Goals for APS
mvme3100
mvme2500
mvme6100
RTEMS tool suite and
BSPs
mvme2100
mvme2700
Packages
libBSD
Netservice
…
mvme3100
mvme2500
mvme6100
mvme2100
mvme2700
For each BSP
EPICS Base
mvme3100
mvme2500
mvme6100
mvme2100
mvme2700
For each BSP
mvme5100
mvme5100
mvme5100
EPICS Modules
mvme3100
mvme2500
mvme6100
mvme2100
mvme2700
For each BSP
mvme5100
IOC for test and evaluation
mvme3100
mvme2500
mvme6100
mvme2100
mvme2700
For each BSP
mvme5100
IOC Roll-out
For each IOC with BSPs
mvme3100
mvme2500
mvme6100
mvme2100
mvme2700
mvme5100
0%
100%
25%
75%
50%

## Slide 7: RTEMS and libBSD Developments
mvme3100
qoriq_e500 (mvme2500)
tsec network interface driver for libBSD
  Modified the tsec driver for qoriq
  Add tsec driver to the device tree
  RTEMS 6.1 and 7
  libBSD: 6-freebsd 12, 6-freebsd-14 and 7-freebsd-14
  Network latency evaluated
  Not yet merged to upstream
I2C driver loading issue:
  Still under optimization
New Development
Issues
U-boot environment interface
  API for uboot environment is added, same as that for gen5200 BSP.
  RTEMS configure option added
  Still under development
6-freebsd-12: nfsv4 bugs (deprecated)
6-freebsd-14: name conflicts (does not build)
7-freebsd-14:
  Link errors: Fixed upstream
  Missing macros in mpc85xx : Fixed upstream
  One device method ofw_pcib.c is not supported in RTEMS: Fixed at APS
New Development
Issues

## Slide 8: EPICS-base Development
BSP Independent
BSP Dependent
Update the RTEMS init function so that static IP can be used
  Obtain configurations (network, NFS mount, etc) from environment
  Keeping it compatible with legacy network stack
Fixed the issue of slow establishing CA link
Non-volatile memory access
  Revising the function setBootConfigFromNVRAM.c
  Add supports to boards with u-Boot
  Revising and standardizing environment variable names
VME support for qoriq in libBSD
  Tsi148 option should be turned on when compiling libbsd
  Added Till Straumann’s VME driver functions to devLibVMEOSD.c in epics-base.

## Slide 9: EPICS-base Development
Slow establishing CA links
  Symptom: long channel access establishing time, long loading time when opening or refreshing a screen, etc.
  Cause: long executing time of malloc_info call when found the requested PV
        Before replying whether or not to establish a CA link, check if there is enough memory
        Function malloc_info scans the entire memory to obtain the statistics, which is slow
  Fix: replace malloc_info with malloc_free_space
  Not yet merged into the repository.

## Slide 10: EPICS-base Development

## Slide 11: EPICS Modules Developments
EPICS Modules Github | Gitlab at APS Only
devlib2* | a16vme
iocStats* | iocstd*
mrfioc2* | acromag-9440
asyn | aps-mrf
busy | aps-fct
sequencer | gtr
autosave | pulserecord
calc | …
ipac | 
sscan | 
stream | 
… | 
* Module includes OS-dependent code that needs midofying for RTEMS
Need “USR_CFLAGS += -std=c99” in CONFIG_SITE to compile many modules
Compiled Successful
Test in progress
Under development
Compiled and Tested

## Slide 12: Performance Benchmark: Network Latency
Switch
Linux Host
tcp client
udp client
mvme2500
tcp server
mvme3100
tcp server
Office/Lab network
tcp/udp servers: running on mvme2500 and mvme3100 boards, echoing messages
tcp/udp clients: sending messages to a server and measure the response time
udp server
udp server
Switch
…

## Slide 13: Performance Benchmark: Network Latency
Same Switch

## Slide 14: Performance Benchmark: Float Point Calculation
BSP | mvme3100 | mvme2500
VxWorks: soft float | 123 ms | 267 ms
VxWorks: hard float | - | 7 ms
RTEMS: soft float | 234 ms | 201 ms
BSP | mvme3100 | mvme2500
VxWorks: soft float | 117 ms | 300 ms
VxWorks: hard float | - | 8 ms
RTEMS: soft float | 310 ms | 253 ms
Addition (1,000,000 doubles)
Multiplication (1,000,000 doubles)
BSP | mvme3100 | mvme2500
VxWorks: soft float | 103 ms | 153 ms
VxWorks: hard float | - | 5 ms
RTEMS: soft float | 179 ms | 148 ms
BSP | mvme3100 | mvme2500
VxWorks: soft float | 86 ms | 178 ms
VxWorks: hard float | - | 5 ms
RTEMS: soft float | 197 ms | 164 ms
Addition (1,000,000 floats)
Multiplication (1,000,000 floats)

## Slide 15: RTEMS IOC Prototype in a Test Stand
Software modules
  RTEMS 7 (main branch)
  libBSD (7-freebsd-14 branch)
    Local: mvme3100 tsec driver, u-boot supports
  epics-base (7.0 branch)
    Local: malloc_info fix, rtems_init, VME for qoriq, …
  devLib2 (v2.13, locally modified)
  mrfioc2 (v2.7.2 , locally modified)
  acromag-9440 (v1.5, APS Only)
  iocStat (v4.0.0 , locally modified)
  iocstd (v4.5.0, APS Only, modified)
Function and stability tests
  Tested all timing functions of MRF components
  Tested event-based time stamps
  Long-term stability: >1.5 weeks
VME CPU
VTM 200
MRF EVM 300
MRF EVM 300
MRF EVR 300
MRF EVR 300
MRF EVR 300
MRF EVR 300
MRF EVR 300
MRF EVR 300
AVME 9440
  CPU: mvme3100 or mvme2500
  VTM 200: console interface module
  MRF Timing modules
    Event Masters x2
        Generating events
    Event Receivers x6
        Pulse output upon events
        Event-based time stamps
        VME interrupts upon events
        …
  AVME 9440: digital IO

## Slide 16: On-going efforts and near-future plans
Merge recent development to the upstream repositories
Compile and test more device support modules with EPICS7 and RTEMS for mvme3100 and mvme2500
Test IOCs deployed to production environment in non-critical IOCs
Standardize the development and deployment of RTEMS IOCs at APS
Development plans for other CPUs
  Mvme2100, 2700 and 6100: test existing BSPs and libBSD, and then EPICS and support modules
  Mvme5100: develop BSP from scratch
Exploring the dynamic loading
Updating the EPICS RTEMS Initialization
  Working towards a new rtems_init function and boot configuration standard
Working group formed with EPICS + RTEMS developers across several sites
  Starting regular meetings (currently at 21:00 UTC so our Australian expert can attend)
  Contact Andrew Johnson for details

## Slide 17: Summary
RTEMS migration is on-going at APS
  Building RTEMS and EPICS for varieties of VME CPUs (mvme3100, mvme2500, etc)
  Added drivers and fixed bugs
  Benchmarking performances
  Testing IOC functions and stabilities
Plans to support more VME boards and new RTEMS features

## Slide 18: Acknowledgements
We thank Chris Johns, Heinz Junkes, Vijay Banerjee, Jeremy Lorelli, Mick Stepp for help in development and trouble-shooting.
  This work is supported by the U.S. Department of Energy, Office of Science, Office of Basic Energy Sciences, under Contract No. DE-AC02-06CH11357.

## Slide 19: Back-up slides

## Slide 20: RTEMS and libBSD Developments
Three-Speed Ethernet Controller (tsec) driver development for libbsd:
  Network interface tsec is not added to the Nexus bus (the root device) for mvme3100
  Added tsec configurations to nexus device header (Thanks to Jeremy Lorelli!)
  Modified the tsec driver config struct to add multiple tsec interfaces (Thanks to Jeremy Lorelli!)
  Fix the tsec driver source code (developed at APS)
    Obtain the correct base and physical addresses from the driver configuration struct
    Implemented the interrupt service routines and call back functions for Tx/Rx/Error Compatible with mvme3100 bsp.
        The existing tsec driver is tuned to the QorIQ BSP, which handles the interrupts differently
    The fix is under extensive tests.

## Slide 21: Performance Benchmark: Network Latency
Switch
Linux Host
tcp client
udp client
mvme2500
tcp server
mvme3100
tcp server
Office/Lab network
tcp/udp servers: running on mvme2500 and mvme3100 boards, echoing messages
tcp/udp clients: sending messages to a server and measure the response time
udp server
udp server
Switch
mvme2500
tcp server
udp server

## Slide 22: Performance Benchmark: Network Latency

## Slide 23: Channel Access Latency Benchmark
Switch
Linux Host
caget client
caput client
mvme2500
EPICS IOC
mvme3100
EPICS IOC
Office/Lab network
EPICS IOC: running test IOC with soft AO and AI records
Client: python scripts executing caget and caput and measure the response time

## Slide 24: Performance Benchmark: Channel Access Latency