## Slide 2: Managing IOC deployments at scale at ESS
Optional subtitle
PRESENTED BY Simon Rose

## Slide 3: Agenda
1 Abstract
2 What we once had
3 A warning
4 An overview

## Slide 4
Abstract
1

## Slide 5: Abstract
From humble beginnings of a hand-maintained list and a combination of ssh + screen to today, the European Spallation source currently has over 3,400 active IOCs which serve over 11,000,000 PVs. We will describe how we manage configuration for our systems emphasizing traceability, reproducibility, and quality control. We will also show how this allows us to monitor various aspects of our system including host and IOC logs, pv and archival status all from a centralised location. Finally, we will show how we are able to achieve fast updates to production systems as required to address the infamous “2am problem” or even worse, the “who deleted my control system” problem.
Sub-headline to strengthen the headline above

## Slide 6
What we once had
2

## Slide 7: What was once, once was
IOCs were managed by hand, artisinally.
  Internal documents described which IOCs were on which hosts deployed by whom
  EPICS was distributed by NFS
    Built manually, of course
      But we had scripts to help! (of course)
  Hosts were configured by hand
  IOCs were run manually
  Common user account with a “super secret” password
I suspect that this will sound familiar to many of you
Notes: Common user account at least avoids some issues!
Our first improvements were in how we built the NFS EPICS share:
Limited access build VM
Gitlab-CI on special runners to build VM
Eventually a home-built package manager that built everything for us

## Slide 8
First, a warning
3

## Slide 9: A warning
At ESS we use e3 (A ‘pest’ as per Ralph Lange 😃) for running IOCs. That is:
  IOCs run with a standard executable (softIocPVx)
  They use a variant of PSI’s require to dynamically load functionality at startup
  This massively simplifies a lot of our needs
Or a sales pitch?
Notes: One of the main things that is simpler for us is that we do not compile IOCs as they are just text files. There are other ways of achieving this (e.g. docker containers) that could give similar successes

## Slide 10
Short overview
4

## Slide 11: Extremely high level
The steps an IOC integrator or system owner uses to deploy an IOC:
  Push
  Generate
  Deploy
  Monitor
To the point of uselessness
Notes: Push: configuration update to gitlab
Generate: a new commit to an IOC repository
Deploy: Trigger an ansible playbook run to deploy the IOC
Monitor: Check on the IOC status (logs, alerts, etc.)

## Slide 12: Thanks!