## Slide 1
Apr. 21, 2026
Xiaohan Lu (卢晓含)，IHEP
EPICS-Integrated High-Level Application Development for HEPS
Spring EPICS Collaboration meeting 2026 ENS Paris-Saclay

## Slide 2
Outline
HLA development requirements of HEPS
Pyapas for HLA development
HLAs development for HEPS
Conclusion

## Slide 3
HLA development requirements of HEPS
Pyapas for HLA development
HLAs development for HEPS
Conclusion

## Slide 4: Introduction to HEPS
High Energy Photon Source
Linac
Booster
Storage Ring &Experiment Hall
User Service Building
 | APS-U | ESRF-EBS | MAX-IV | Sirius | HEPS
E(GeV) | 6 | 6 | 3 | 3 | 6
C(m) | 1104 | 844.4 | 528 | 518 | 1360.4
Lattice | 7BA | 7BA | 7BA | 5BA | 7BA
Cell | 40 | 32 | 20 | 20 | 48
Emittance (pm*rad) | 42 | 150 | 330 | 250 | 34
Brightness |  |  |  |  | 
Construction period | 2018-2024 | 2015-2020 | 2010-2016 | 2015-2018 | 2019~2025
 | APS-U | ESRF-EBS | MAX-IV | Sirius | HEPS
E(GeV) | 6 | 6 | 3 | 3 | 6
C(m) | 1104 | 844.4 | 528 | 518 | 1360.4
Lattice | 7BA | 7BA | 7BA | 5BA | 7BA
Cell | 40 | 32 | 20 | 20 | 48
Emittance (pm*rad) | 42 | 150 | 330 | 250 | 34
Brightness |  |  |  |  | 
Construction period | 2018-2024 | 2015-2020 | 2010-2016 | 2015-2018 | 2019~2025
One of the world's brightest fourth-generation synchrotron light sources
The facility has the capacity for more than 90 high-performance beamlines and can provide X-rays with energy up to 300 keV
The facility offers 10nm spatial resolution, 1MeV energy resolution, and picosecond time resolution for high-frequency dynamic detection

## Slide 5: Introduction to HEPS
The emittance is reduced by 1or 2 orders of magnitude, approaching the X-ray diffraction limit
The number of magnets increases by an order of magnitude
3rd generation
Layout
4th generation
Beam Profile
HEPS is currently the largest accelerator facility in China.
High control complexity
Large scale of control variables
High precision control required
Large number of HLAs required
More than 2,000 power supplies.
Notes: HEPS is the first 4-generation light source in china, compare to 3rd generation light source

## Slide 6: High Level Application
High-Level Application (HLA) is typically an integrated system that monitors, analyzes, and controls the accelerator’s operational status and beam parameters — serving as the accelerator’s “central nervous system”!
Energy / Energy Spread Analysis
Beam Emittance Measurement
Closed Orbit Correction
Lifetime calculation
BPM
Low-Level Hardware
Physical
Algorithm
High-Level Application
WireScanner
Control
Communication
Notes: For physics developers, the following steps are overly complex. Independent development by each individual would be time-consuming

## Slide 7: High Level Application
High Level Application(HLA)
Focus more on physical process:
optimization, simulation, feedback et.al.
High control complexity
Large scale of control variables
High precision control required
Large number of HLAs required
The overall structure of control system
Notes: For physics developers, the following steps are overly complex. Independent development by each individual would be time-consuming

## Slide 8: High Level Application
Idea
Algorithm Abstraction
Software implementation
Hardware and Beam Parameters
Physics Model Calculation
Human–Machine Interface
High Availability and Long-Term Operation
Data Management and Archiving
Real-time control and device communication
Integration of physical models and online computation
Development of visual,interactive interfaces
server deployment and reliable runtime
Establishment of connected data storage systems
HLA Framework
Providing a Systematic Solution
HLA Framework make the developer focus on the Algorithm Abstraction
Hardware comminucation tools
Invoke physical models online
A user-friendly interface
Implement server development
Real-time database connection
Notes: For physics developers, the following steps are overly complex. Independent development by each individual would be time-consuming

## Slide 9
HLA development requirements of HEPS
Pyapas for HLA development
HLAs development for HEPS
Conclusion

## Slide 10: New HLA framework: Pyapas
A Pure Python Framework for High Level Application Development. Python-based Accelerator Physics Application Set (Pyapas)
  Modular Design
  Model-Based
  Based on Physical Quantities
Dual-layer physical module
Friendly user interface module
Hardware communication module
Database connection module
Client-Server development module
Various phyiscal algorithm toolkits
Pyapas framework
Xiaohan Lu, et al, “A new modular framework for high-level application development at HEPS”, Journal of Synchrotron Radiation, 31: 385-393, 2024.
Notes: It is worth mentioning that we developed a new modular framework for high-level application development, named Pyapas, based on which we developed the required high-level applications and adopted them in the HEPS commissioning

## Slide 11
The “Connector” is responsible for invoking simulation algorithms
Abstraction of the Hardware
Ocelot
PyAT
Custom model
Low-coupling dual-layer physical module
Astract Object:
Name/Position/Length/ Field/Channel/Type/PS/ Physical parameter

## Slide 12: Low-Code development
filterable list, table, tree
Customize widgets for HLA development
Plot widget for physical image, e.g. plot prameters with lattice
Widgets with channel property to interact with PV directly.
“Drag and Drop”
More than 20 pre-built widgets for rapid development.
Notes: for the user interface, we extend the Qtdesigner and customize lots of widgets for HLA development, such as plot widget with lattice, widgets with channel to interact with PV directly

## Slide 13: Real-time Data Interaction System
Design the communication structure (active and passive channel data acquisition) ）
The Channel class contains the EPICS communication interface responsible for specific communication with the IOC
The 'Singleton Factory Pattern' centrally manages interaction channels in the program, avoiding redundant creation and improving interaction efficiency.
The channel factory has namespace functionality
One application can smoothly run while monitoring 10,000 PVs
Notes: Use the pyqt signal-slot feature and the ‘singleton factory pattern’, the interaction will be more efficient, a simple test was done to monitor 10K PVs in same application, it still run smoothly, meet the requirement of HEPS

## Slide 14: Client/Server Module
mDNS +XMLRPC
Luncher
Terminal
The system autonomously detects active Pyapas applications on the local area network and tracks their health and status.
These features are packaged into a full-featured Server class, allowing any subclass to instantly become a functional server.

## Slide 15: Multithreading-based scanner
Python's GIL locks up the UI during single-threaded scans, as the loop cannot be paused. This requires a forced close of the program, which is impractical and risky in a live machine setting.
A universal scanner was designed to address this limitation
Main Thread
scan Thread
DAQ Thread
Add scan information
Signal/Slot
Signal/Slot
Scan Control/ Start /Stop
Send data step by step
Signal for Data Acquisition
Send data upon completion of all scan commissions
Periodic Monitoring
Add Monitored Channel

## Slide 16
HLA development requirements of HEPS
Pyapas for HLA development
HLAs development for HEPS
Conclusion

## Slide 17: HLA Development for HEPS
LB Virtual Accelerator
Emittance Measurement
Orbit Correction
Beam-based Alignment
Local Orbit Correction 
LINAC
Linac Virtual Accelerator
Transimission Efficiency
Emittance Measurement
Orbit Correction
Phase Scan
Energy Spread Measurement
Beam-based Alignment
Linac Control
Transfer Line
Booster
Lattice Preparation
Booster Virtual Accelerator
First Turn Measurement
Dispersion Measurement 
Chromaticity Measurement
Tune adjustor
Global Orbit Correction
Local Orbit Correction
Beam Lifetime
Storage Ring
Lattice Preparation
Booster Virtual Accelerator
First Turn Measurement
Dispersion Measurement 
Chromaticity Measurement
Global Orbit Correction
Local Orbit Correction
Beam Lifetime 
Orbit Display 
Slow Orbit Feedback 
K-Value adjustor 
Fast BBA 
All HLAs are developed based on Pyapas
More than 40

## Slide 18: Design of A Multi-User Virtual Accelerator
Within the same network environment or on the same server, any number of virtual accelerators can be launched without conflicting with each other
Create virtual hardware to simulate real machines, providing corresponding PV channels and beam information
Multiple tasks running concurrently
Multiple users operating simultaneously
Unified management with one-click start and stop
C/S Architecture

## Slide 19: Virtual Accelerator of HEPS
Single Particle Tracking
Multi-Particle Tracking
Vritual PR
Full feature IOC
Errors included
Generate 'real-time' data for testing HLAs
All applications are initially tested via VA, which significantly reduces the overall time

## Slide 20: Pyapas-based HLAs for HEPS
Linac Control
Energy Measurement
Booster Control
SR Status Monitor
Orbit Display
Fist Turn Analysis
Virtual Accelerator
Local Orbit Correction
All the HLAs are developed based on Pyapas
Y.L. Zhao et al., Journal of Instrumentation, 2023; Y.M. Peng et al., Journal of Instrumentation, 2023;

## Slide 21: Beam Commissioning Milestones of HEPS
2025.10
passed the process
qualification and acceptance

## Slide 22: Deployment of Pyapas in Other Facilities
CSNS(Proton)
PWFA(electron& positron)
Pyapas architecture has been successfully applied to various accelerator facilities, including light sources, neutron sources, and novel accelerator concepts.
https://github.com/luxiaohan/pyapas.git

## Slide 23
Two more EPICS-based solutions to share......

## Slide 24: EPICS-Based Interlock System for HEPS Insertion Devices
Objective:
Coordinate insert control, feedforward, and long-coil power supplies for real-time compensation and interlock control during gap operation
Single Insert Structure
Dual Insert Structure
GAP
Long Coil
Feedforward PS x4
Interlock table
Interlock table
Interlock table
GAP
Long Coil
Feedforward PS x4
GAP
Long Coil
Phase Shifter
Interlock table
Interlock table
Interlock table
Interlock table
Interlock table
Interlock table
Interlock table
Interlock table
Interlock table

## Slide 25: EPICS-Based Interlock System for HEPS Insertion Devices
Challenges:
Multi-mode interlock (operation/calibration mode )
The interlock table should be updated online
Strict response time requirement (<10ms)
GAP
Long Coil
Feedforward PS x4
Interlock table
Interlock table
Interlock table
GAP
Long Coil
Feedforward PS x4
GAP
Long Coil
Phase Shifter
Interlock table
Interlock table
Interlock table
Interlock table
Interlock table
Interlock table
Interlock table
Interlock table
Interlock table

## Slide 26: EPICS-Based Interlock System for HEPS Insertion Devices
Limitations of the current EPICS system in interlock control, particularly in:
Fast switching among >8 modes with condition-dependent logic
Dynamic reconstruction of interlock tables
Solution: C-based interlock & computation modules in EPICS with “aSub”:
* One-click mode switching (>8 configurations)
* Reconfigurable interlock logic
* Response time < 5 ms
GUI with Phoebus

## Slide 27: EPICS-Based Orbit Feedback
Motivation: Low-frequency orbit noise (~3 Hz) was observed before FOFB (~ 22k Hz) was ready Python-based SOFB ( <1Hz ) cannot meet the required response speed
Proposed Solution: Develop an EPICS-based Medium-Frequency Orbit Feedback System (MOFB : 30Hz~ 100Hz )
Challenges: 1. ~2000 PVs interactions ( 1152 correctors and 1156 BPMs )
2. Lack of support for large-scale matrix computation
The aSub record supports up to 21 inputs, and therefore cannot be used directly.
aSub
aSub
aSub
Load 2000 PV Names
Load Matrix and Golden orbit
Perform calcualtion
SVD calculation
Global Variables
Feedback
The system can operate above 100 Hz,
But is limited to 40 Hz due to the BPM SA data refresh rate

## Slide 28: EPICS-Based Orbit Feedback
Motivation: Low-frequency orbit noise (~3 Hz) was observed before FOFB (~ 22k Hz) was ready Python-based SOFB ( <1Hz ) cannot meet the required response speed
Proposed Solution: Develop an EPICS-based Medium-Frequency Orbit Feedback System (MOFB : 30Hz~ 100Hz )
Challenges: 1. ~2000 PVs interactions ( 1152 correctors and 1156 BPMs )
2. Lack of support for large-scale matrix computation
5Hz Operation
10Hz Operation
40Hz Operation
ON
OFF
PS
Orbit

## Slide 29
HLA development requirements
Pyapas for HLA development
HLAs development for HEPS based on Pyapas
HLAs development for CSNSII based on Pyapas
Conclusion

## Slide 30: Conclusion
An EPICS-Based framework, Pyapas, was developed to enhance the efficiency of HLA development.
Pyapas has been successfully applied to the development of HLAs HEPS greatly improving development efficiency.
Pyapas is one of the very few frameworks applied to HLAs development for proton, electron, and pwfa. https://github.com/luxiaohan/pyapas.git
CSNS
HEPS
BEPCII (PWFA)

## Slide 31
Thank you for your attention!