## Slide 1: Development of Virtual Beamline Software Platform for Advanced Light Sources Based on EPICS
Spring EPICS Collaboration Meeting 2026, Paris-Saclay
Speaker：Miao Zhang Co-authors: Pengcheng Li, Yu Li, Yi Zhang Institute of High Energy Physics, HEPS | 2026.04
Email: zhangmiao@ihep.ac.cn

## Slide 2
Contents
Background
Platform Architecture
Core Design
Verification & Applications
Conclusion & Outlook

## Slide 3
01 Background
Notes: 首先，让我们进入第一部分：引言与背景。在这一部分，我们将探讨以HEPS为代表的第四代同步辐射光源带来的新机遇，以及随之而来的软件系统挑战。

## Slide 4
▍ Four Major Challenges
Highly Complex System
Massive Data Throughput
Extreme Stability Requirement
Rapid Iteration & Extension
海量数据吞吐
Background & Significance
These requirements cannot be fully met by existing tools in the EPICS ecosystem.

## Slide 5: Background & Significance
Core Limitations of Current Technical Solutions
Virtual Beamline
Optical Design
Device Control
Experiment Orchestration
Core Tools: SHADOW, OASYS
Core Tools: EPICS IOC Simulator
Core Tools: Bluesky, PyMCA
Key Limitation: No device virtualization capability
Core Function: Simulate PV variable response status of a single physical device
Key Limitation: Only single-device PV simulation;
Cannot reproduce multi-device timing
Key Limitation: No virtualization capability, high latency in loading historical data
User Interaction Layer
Virtual Device Layer
Data Management Layer

## Slide 6
02 Platform Architecture
Notes: 首先，让我们进入第一部分：引言与背景。在这一部分，我们将探讨以HEPS为代表的第四代同步辐射光源带来的新机遇，以及随之而来的软件系统挑战。

## Slide 7: Platform Architecture
Core Design Concept: Bidirectional mapping and bridging mechanism based on Protocol–Data–Timing to achieve deep coupling and real-time interaction.
Top Layer: User Interaction Layer
Middle Layer: Virtual Device Layer
Bottom Layer: Data Management Layer

## Slide 8: Platform Architecture
Core Design Concept: Three-Layer Architecture
User Interaction Layer
Based on Bluesky Framework
Providing a graphical interface
Flexible programmatic experiment orchestration interface
Virtual Device Layer
Core engine
Unifying heterogeneous physical devices into EPICS-standard virtual instances.
Data Management Layer
Deeply optimized for HDF5/NeXus
Providing high-speed reading, writing, and access for TB-Level massive data

## Slide 9: Platform Architecture
Core Innovation: Dual-Mode Driving Architecture
Full Simulation Experiment Mode
▌ Based on high-precision physical models
▌ Innovative design and pre-rehearsal of experimental schemes
Data Reproduction Mode
▌ Seamlessly load and high-fidelity replay historical experimental datasets
▌ Accurate retrospective and verification of experimental processes

## Slide 10
03 Core Design
Notes: 首先，让我们进入第一部分：引言与背景。在这一部分，我们将探讨以HEPS为代表的第四代同步辐射光源带来的新机遇，以及随之而来的软件系统挑战。

## Slide 11: Core Design (I)
① User Interaction Layer
② Virtual Device Layer
Three-Layer Architecture
③ Data Management Layer
Bluesky-Native Full- Process Experiment Orchestration
Dual-Interface Design
Ophyd Native Encapsulation
Intelligent Reverse Reconstruction
CA

## Slide 12: Core Design (II)
（1）Virtual Experiment Station Engine
Virtual Experiment Station Engine
Beamline Virtual Device
Data Simulation
Data Reproduction
Core Scheduler of the Platform：
Intelligent Device Instance Scheduling
Unified Working Mode Scheduling
Precise Timing Collaborative Control
Three-Layer Architecture
① User Interaction Layer
② Virtual Device Layer
③ Data Management Layer

## Slide 13: Core Design (III)
（2）Beamline Virtual Device
Virtual Detector Family
Virtual Motor Family
Special Optical Device for Beamline
Three-Layer Architecture
① User Interaction Layer
② Virtual Device Layer
③ Data Management Layer

## Slide 14: Core Design: Virtual Detectors
0D Detector Simulation
1D/2D Detector Simulation
PV | Parameter Meaning | R/W
EGU | Engineering Unit | W
SCAN | Sample Cycle | W
RBV | Actual Reading | RO
NOISE | Noise Intensity | W
VAL | Baseline Setpoint | W
Configurable PV Parameters:
Typical Applications:
Photodiode, lon Chamber(Keithley 6485/6487), Counter
Simulation Principle:
Baseline + Random Noise Model
Baseline
Random Noise
+
1D Detector
Ideal Intensity
Gaussian Noise
Linear Gradient /
Peak Distribution
+
Core PV Parameters:
ImageMode、Acquire、ArrayData、AcquireTime、NumImage、TriggerMode
2D Detector
Core PV Parameters:
ImageMode、Size_X/Size_Y、AcquireTime、Acquire、ArrayData、NumImage、TriggerMode
Full Simulation+ Data Reproduction

## Slide 15: Core Design: Virtual Motors
Virtual Linear Translation Motor
Virtual Rotational Motor
Overall Architecture: Trapezoidal Velocity Profile + Error Injection + EPICS PV Standard Control
Application Scenarios: Sample stage X/Y/Z axis positioning, motorized four-blade slit blade drive.
Core Features: Trapezoidal velocity curve, backlash error injection (±0.001mm), soft limit protection
Core PV Parameters: VELO, ACCL, VMAX, DHLM, DLLM, VAL, RBV, Status
Application Scenarios: Sample stage attitude adjustment, CT experiment rotation axis, DCM Bragg angle control
Core Features: Same trapezoidal velocity curve, angle drift error injection (±0.01°/min), 360° continuous rotation, unit: degree (°)
Core PV Parameters: Fully compatible with linear motor PV specifications

## Slide 16: Core Design: Virtual Optical Device-DCM
Architecture:
Extended based on virtual rotational motor, realizing automatic linkage between energy and Bragg angle
Core Formula(Bragg’s Law):
Core PV Parameters:
Standard:
SIM:DCM:Bragg(Bragg angle)
New:
Energy.VAL/RBV(Target Energy)
Built-in Crystal Parameter Template (DCM)
Crystal Type | Si(111) | Si(311)
Crystal Plane Spacing（Å） | 3.135 | 1.637
Energy Resolution(ΔE/E) | 1e-4 | 5e-5
Thermal Expansion Coefficient(1/°C) | 2.6e-6 | 2.6e-6
Maximum Applicable Energy(keV) | 20 | 35
(n = 1, d : crystal plane spacing (Å), θ : Bragg angle (°))

## Slide 17: Core Design: Virtual Optical Device-Slit
Motorized Four-Blade Slit
▍Architecture
4 independent virtual motors
Top, Bottom, Left, Right
Motion Control Logic
Jog/relative move/absolute move
▍Core Innovation
One-Touch Aperture Control with Center Preservation
horizontal/vertical directions preform mirror-synchronized movement
Core Control Formula:
▍Core Features:
Dual-mode control:
independent blade adjustment / one-touch synchronous opening/closing
High-fidelity reproduction of real slit control logic
Zero beam center drift during aperture adjustment

## Slide 18: Core Design: Virtual Optical Device-XBPM
Architecture
Extended based on 0D detector, composed of 4 0D detectors forming a four-quadrant electrode array
Core Technology
Dynamic Signal Reconstruction
Core Calculation Algorithms:
Sum Signal: Σ=(A+B+C+D)
Position: P=(A+D-B-C)/Σ
Core PV Parameters:
SumSignal: Total Intensity
XPos / Ypos: Beam X Position
ChA ~ ChD: Four-Quadrant Electrode Signals
SCAN
Core Application:
Hardware-independent beam orbit monitoring, supporting multi-device linkage simulation

## Slide 19: Core Design (IV)
Three-Layer Model
（3）Data Simulation Module
（4）Data Reproduction Module
High-precision physical models for synchrotron radiation:
Error Injection Capability:
Efficient data stream playback
Intelligent parsing of experimental metadata from HDF5/NeXus files
Automatic generation of corresponding Bluesky acquisition scripts
- 2D Elliptical Gaussian Function Model:
- 3D Shepp-Logan Model + 3D Projection Integral Formula
- Inject Poisson noise into detector data to simulate dark current;
- Inject backlash/angle drift into virtual motors to restore real mechanical characteristics.
① User Interaction Layer
② Virtual Device Layer
③ Data Management Layer

## Slide 20: Core Design (V)
①User Interaction Layer
② Virtual Device Layer
Three-Layer Model
③Data Management Layer
（1）Core Challenge
Traditional I/O loading delay >100ms for GB/TB-level HDF5/NeXus scientific data, hindering real-time reproduction and analysis.
（2）Core Technical Solutions
（3）Performance Improvement
<10ms
EB
2:1
Two Core Modules:
Efficient Data Management & High-Speed Data Processing
Block Index Pre-building
Memory-Mapped Zero-Copy
Double-Buffer Pipeline
Reduce loading delay from >100ms to <10ms (10x+ improvement)
Support EB-level high-throughput concurrent access
2:1 lossless compression ratio via LZ4 algorithm

## Slide 21
04 Verification & Applications
Notes: 首先，让我们进入第一部分：引言与背景。在这一部分，我们将探讨以HEPS为代表的第四代同步辐射光源带来的新机遇，以及随之而来的软件系统挑战。

## Slide 22: Function Verification Case 01: CT Experiment
▌ Experimental Parameters:
Beam energy 10keV, scanning range 0°-180°, step 1°, exposure time 1s, detector output 1024×1024 2D projection
▌ Experimental
Workflow
01. Environment deployment
02. Optical system initialization
03. Experiment process orchestration
04. Virtual experiment execution
05. Data archiving
> 95%
Consistency between simulation data and real experimental data

## Slide 23: Function Verification Case 02: XRD Reproduction
▌Experimental
Workflow
Verification Result:
Device control logic and data acquisition timing are completely consistent with the original experiment.
01. Environment deployment
02. Standardized data parsing
03. Zero-copy data loading
04. Automatic virtual device creation
05. Automatic process reproduction

## Slide 24
05 Conclusion & Outlook
Notes: 首先，让我们进入第一部分：引言与背景。在这一部分，我们将探讨以HEPS为代表的第四代同步辐射光源带来的新机遇，以及随之而来的软件系统挑战。

## Slide 25: Conclusion & Future Outlook
▍Core Conclusions:
Realize full-process closed-loop virtualization
Innovative dual-mode driving architecture
Deep native compatibility with EPICS/Bluesky ecosystem
Efficient massive data processing technology, solving the bottleneck of TB-level data access delay
▍Future Outlook
Continuously improve virtual device library, complete HEPS beamline adaptation, and on-site verification
Integrate AI/ML algorithms to realize intelligent beam tuning pre-training

## Slide 26
Thank you for your attention!
zhangmiao@ihep.ac.cn

## Slide 27
Q & A