## Slide 1: IOCM: Managing EPICS IOCs
January 23 | ORNL
Webb, Brad
Notes: At SNS we run hundreds of EPICS soft IOCs across multiple servers. IOCM is the tool that lets us manage all of them consistently — from creation to startup, monitoring, and compliance.
A unified CLI for creating, validating, running, and discovering soft IOCs

## Slide 2: Why IOCM exists? - To ensure consistent standards applied across all IOCs.
Manual IOC creation (makeBaseApp.pl -what?)
Multiple teams of engineers creating soft IOCs (tribal knowledge!)
Hundreds of IOCs across many hosts
Inconsistent versions, configuration, and behavior
Hard to audit, validate and manage
Manual procServ management
  ssh'ing around (where's my IOC?)
  Permission escalation and ports
  Small helper scripts automate but do not scale
Single tool that managed the entire lifecycle of an IOC
Unified command-line interface
Consistent & standardized IOC creation
Support for EPICS support modules
Central start/stop/console control (No ssh'ing around!)
Wraps systemd & procServ (no sudo, ports managed)
Easy audits, validation & compliance
Scales to 100s of IOCs
Life Before IOCM:
What We Wanted:
Notes: Goal: standardized lifecycle management for soft IOCs
Most EPICS sites eventually hit this wall: lots of IOCs, lots of servers, and no single source of truth.
Managing soft IOCs at scale gets messy fast
Scripts, tribal knowledge, and snowflake setups
iocm was written to make IOC management boring and predictable

## Slide 3: What IOCM Provides?
Unified CLI interface
Python-based framework
IOC lifecycle management:
  Create
  Start/Stop/Restart
  Console Access
  Status & Health
  Support Module Management
  Configuration Validation
  Centralized logging and control
systemd
procServ
rsyslog
EPICS iocStats
SNS filesystem standards
Command-Line Tool + Background Service
Integrated With:

## Slide 4: Architecture Overview
systemd
|
├─ iocm-server.service
|
└─ iocm-worker@.service
└─ iocm-worker@ics-ioc101.service
iocm-client
User facing interface
Tab completion
Dynamic host discovery
Common Filesystem
TCP (IPC/RPC)
Soft IOC Server
Host-1
procServ
iocm-server
IOCs
systemd
Soft IOC Server
Host-2
procServ
iocm-server
IOCs
systemd
Soft IOC Server
Host-n
procServ
iocm-server
IOCs
systemd
Python-based client/server architechture
Single client manages multiple IOCs
Distributed across multiple hosts
Communication Flow:
User runs a command via iocm-client
Client resolves the appropriate hostname at runtime
Sends a request over TCP (RPC)
iocm-server on that host interacts with:
  systemd -> to control services
  procServ -> to manage IOC processes
IOC state is updated and feedback is returned to the client
Notes: iocm provides a centralized control layer for managing EPICS soft IOCs, delegating process supervision to procServ and integrating with systemd for reliable startup and recovery.
IPC=Inter-Process Communication
RPC=Remote Procedure Call

## Slide 5: CLI Overview
iocm create
iocm start
iocm stop
iocm restart
iocm status
iocm console
iocm find-ioc
iocm validate
iocm module-info
Command help (-h)
Lifecycle:
Operations:
Quality & Standards:
[ozzy@ics-opi-remote1 ~]$ iocm <TAB><TAB>
console create find-ioc module-info restart start status stop validate
[ozzy@ics-opi-remote1 ~]$ iocm console dtl-<TAB><TAB>
dtl-llrf-ioc-mo dtl-rccs-ioc1 dtl-rccs-ioc2 dtl-vac-ioc1 dtl-vac-ioc2
Tab completion:
Notes: These commands cover the entire IOC lifecycle — from creation to daily operations and troubleshooting.
Tab completion supported
Consistent CLI across hosts

## Slide 6: IOC Status: One command, all hosts
Lists all soft IOCs
Grouped by host
Owner
Uptime
Offline detection
Missing iocStats warning.
[ozzy@ics-opi-remote1 ~]$ iocm status
IOC Name | Hostname | IOC Owner | IOC Uptime (days, HH:MM:SS)
cryo-ioc01 | cryo-ics-softioc10 | Sharon Osbourne | 4 days, 22:11:42
ring-llrf-ioc-wcm | ics-srv-softioc1 | Ozzy Osbourne | OFFLINE
mps-ipmi-ioc1 | ics-srv-softioc6 | Jack Osbourne | 42 days, 03:03:37
ics-rf-ioc-pwrmtr-test | ics-srv-softioc8 | Zakk Wylde | * Missing iocStats *
pps-ioc-farwest | ics-srv-softioc8 | Randy Rhoads | 03:06:08
$ iocm status
Notes: Mention this is often the first command ops runs.
Emphasize quick situational awareness.

## Slide 7: IOC Status: deep-dive
Reads live iocStats over the network
EPICS version
CPU & memory
Connections & heartbeat
Ownership and location
[ozzy@ics-opi-remote1 ~]$ iocm status mps-ipmi-ioc1
IOC NAME : mps-ipmi-ioc1
IOC-STATS PREFIX : MPS_IPMI:IOC1
STARTTOD : 12/16/2025 09:39:50
TOD : 01/27/2026 13:23:45
UPTIME : 42 days, 03:44:12
HEARTBEAT : 3642236.0
RECORD_CNT : 3079.0
HOSTNAME : ics-srv-softioc6
ENGINEER : Jack Osbourne
LOCATION : 8600 J-105
EPICS_VERS : EPICS R7.0.8.1
KERNEL_VERS : Linux 4.18.0-553.87.1.el8_10.x86_64 x86
APP_DIR1 : /ics/iocs/soft/mps-ipmi-ioc1/iocBoot
ST_SCRIPT1 : ./st.cmd
MEM_FREE : 5557895168.0
MEM_USED : 71688192.0
MEM_MAX : 8338972672.0
FD_FREE : 906.0
FD_MAX : 1024.0
IOC_CPU_LOAD : 0.22522077130101203
SYS_CPU_LOAD : 8.483316034966624
CPU_CNT : 4.0
CA_CLNT_CNT : 10.0
CA_CONN_CNT : 2709.0
SUSP_TASK_CNT : 0.0
GTIM_TIME : 1138386225.6193907
GTIM_ERR_CNT : 0
$ iocm status <ioc-name>
Notes: Deep-Dive

## Slide 8: Creating a soft IOC
Generates complete IOC application
Enforces rules & standardization
Captures metadata (engineer, location & host)
Configuration consistency
Automatically integrates EPICS support modules
Optional Git integration
Interactive vs Non-interactive:
What IOCM Does Automatically:
$ iocm create \
--engineer "Ozzy Osbourne" \
--location "Building-1, Rm-2" \
--host "ics-srv-softioc2" \
--modules "autosave=R5-11, epics-snmp=v1.1.0.4" \
myIOC
$ iocm create -i myIOC
Notes: This replaces hand-crafted IOC skeletons and enforces SNS standards from day one.

## Slide 9: Starting and Stopping IOCs
$ iocm start myIOC
$ iocm stop myIOC
$ iocm start ioc1 ioc2 ioc3 iocn
$ iocm stop ioc1 ioc2 ioc3 iocn
Single console
Works across multiple hosts
start/stop multiple IOCs in a single command
Even if IOCs are on different hosts
Uses procServ via systemd
Auto-restart enabled
Transparent remote execution
Examples:
Key Points:
Notes: From one shell, I can manage IOCs on different servers without logging into each machine.

## Slide 10: IOC Console
Connect to a running IOC via procServ
No ssh hopping
Clear exit instructions
Auto-restart support
User commands are logged to rsyslog
[ozzy@ics-opi-remote1 ics-ioc99]$ iocm console ics-ioc99
[To end session type: '^Exit' and press enter]
@@@ Welcome to procServ (procServ Process Server 2.7.0)
@@@ Use ^X to kill the child, auto restart is ON, use ^T to toggle auto restart
@@@ procServ server PID: 1003252
@@@ Server startup directory: /ics/tools/iocm/src
@@@ Child startup directory: /ics/iocs/soft/ics-ioc99/iocBoot
@@@ Child "ics-ioc99" started as: ./st.cmd
@@@ Child "ics-ioc99" PID: 1003253
@@@ procServ server started at: Fri Jan 30 08:26:15 2026
@@@ Child "ics-ioc99" started at: Fri Jan 30 08:26:16 2026
@@@ 0 user(s) and 0 logger(s) connected (plus you)
"
ics-ioc99>
ics-ioc99>dbl
dbl
CF_CU:TT4015:T
ics-ioc99>dbgf CF_CU:TT4015:T
dbgf CF_CU:TT4015:T
DBF_DOUBLE: 27.4092102051
ics-ioc99>
ics-ioc99>^Exit
exit sequence detected.
[ozzy@ics-opi-remote1 ics-ioc99]$ ioc stop ics-ioc99
['ics-ioc99'] stopped successfully
$ iocm console <ioc-name>
Notes: From one shell, I can manage IOCs on different servers without logging into each machine.

## Slide 11: Console Logging
INFO - Accepted connection from ('192.168.1.128', 41288)
INFO - [ozzy@ics-opi-remote1:41288,tty=/dev/pts/149,pid=4185682] has requested a console session with 'ics-ioc99'
INFO - [ozzy@ics-opi-remote1:41288,tty=/dev/pts/149,pid=4185682] Opening connection to 'ics-ioc99', on localhost:5202
INFO - Writing user data from ('192.168.1.128', 41288) (user=ozzy, host=ics-opi-remote1) to ('127.0.0.1', 5202) Data: 'b'\n''
INFO - Writing user data from ('192.168.1.128', 41288) (user=ozzy, host=ics-opi-remote1) to ('127.0.0.1', 5202) Data: 'b'dbl\n''
INFO - Writing user data from ('192.168.1.128', 41288) (user=ozzy, host=ics-opi-remote1) to ('127.0.0.1', 5202) Data: 'b'dbgf CF_CU:TT4015:T\n''
INFO - Writing user data from ('192.168.1.128', 41288) (user=ozzy, host=ics-opi-remote1) to ('127.0.0.1', 5202) Data: 'b'\n''
INFO - Exit sequence detected from ('192.168.1.128', 41288) (user=ozzy, host=ics-opi-remote1) to ('127.0.0.1', 5202) Data: 'b'\x05xit\n'
INFO - Exiting IOC-writer task ('192.168.1.128', 41288) (user=ozzy, host=ics-opi-remote1) to ('127.0.0.1', 5202)
INFO - [ozzy@ics-opi-remote1:41288,tty=/dev/pts/149,pid=4185682] Exiting console session for 'ics-ioc99' on localhost:5202
INFO - Client ('192.168.1.128', 41288) is finished and exiting...
INFO - Accepted connection from ('192.168.1.128', 53548)
INFO - [ozzy@ics-opi-remote1:53548,tty=/dev/pts/149,pid=4187459] has requested to stop IOCs: ['ics-ioc99']
INFO - [ozzy@ics-opi-remote1:53548,tty=/dev/pts/149,pid=4187459] Preparing to stop 'ics-ioc99'.
INFO - [ozzy@ics-opi-remote1:53548,tty=/dev/pts/149,pid=4187459] 'ics-ioc99' has stopped successfully.
INFO - Client ('192.168.1.128', 53548) is finished and exiting...
Notes: From one shell, I can manage IOCs on different servers without logging into each machine.

## Slide 12: Validations and Compliance
EPICS version correctness
Required modules (iocStats & CAS)
Executables present
Proper directory structure
Ownership and paths
Prevents broken deployments
Enforces SNS ICS rules
Helps during upgrades (EPICS v7)
$ iocm validate
Why this matters:
$ iocm validate --iocs /ics/iocs/soft/cf-ioc-plcstats
/ics/iocs/soft/cf-ioc-plcstats:
User: Ozzy Osbourne
configure/RELEASE: EPICS_TOP is not set to the correct version. Please use EPICS_TOP=/ics/epics/7.0.8.1
configure/RELEASE: IOC_STATS is not set to the correct path. Please use IOC_STATS=/ics/epics/7.0.8.1/iocStats/3.2.0
Notes: This is where IOCM moves from “convenience tool” → operations-grade system.
Validation against site standards
This is huge for migrations (EPICS v7)
Catches problems before deployment

## Slide 13: Support-Module Management
List available support modules
Shows supported versions
Explains how to include them after creation
Automatic dependency handling
Central rules in modules.ini
$ iocm module-info -l
Name | Module Version for EPICS 7.0.8.1 | How to Include in Create Script
asyn | R4-44-2, Devel, R4-41-test | asyn=R4-44-2, asyn=Devel, asyn=R4-41-test
autosave | R5-11 | autosave=R5-11
busy | R1-7-4 | busy=R1-7-4
ether_ip | ether_ip-3-3 | ether_ip=ether_ip-3-3
StreamDevice | 2.8.26 | StreamDevice=2.8.26
[autosave]
dbd = asSupport.dbd
libs = autosave
[asyn]
dbd = asyn.dbd, drvAsynIPPort.dbd
libs = asyn
[calc]
dbd = calc.dbd
libs = calc
[StreamDevice]
depends = calc, asyn
dbd = stream.dbd
libs = stream
Modules.ini
Rules ------>
$ iocm module-info [-l] [module-name]
Notes: This avoids the classic problem of IOCs building differently depending on who created them.

## Slide 14: Support-Module Management
Consistent RELEASE + Makefile guidance
Dependency handling (depends = calc, asyn)
Central rules in modules.ini
Reduces copy/paste errors
Standardizes module usage
$ iocm module-info StreamDevice
StreamDevice has the following dependencies in order:
[1] calc
[2] asyn
[3] StreamDevice
# In your iocApp/configure/RELEASE file add the following lines:
CALC=$(EPICS_TOP)/calc/R3-7-5
ASYN=$(EPICS_TOP)/asyn/R4-44-2
STREAMDEVICE=$(EPICS_TOP)/StreamDevice/2.8.26
# In your iocApp/src/Makefile file add the following lines:
<ioc-name>_DBD += calc.dbd
<ioc-name>_DBD += asyn.dbd
<ioc-name>_DBD += drvAsynIPPort.dbd
<ioc-name>_DBD += stream.dbd
<ioc-name>_LIBS += calc
<ioc-name>_LIBS += asyn
<ioc-name>_LIBS += stream
$ iocm module-info StreamDevice
Notes: This avoids the classic problem of IOCs building differently depending on who created them.

## Slide 15: Find IOC by PV
Uses IOC.pvlist generated at boot
IOC application path and name
iocStats name
IOC type
Responsible engineer/owner
Hostname
Location
$ iocm find-ioc --pv CF_CU:AIT_CU001:TAAVG1M_F
Application : /ics/iocs/soft/cf-ioc-wx
IOC-Stats Name : CF:IOC_WX
IOC-Type : soft
Engineer : Ozzy Osbourne
Hostname : ics-srv-softioc8
Location : 8600 J-105
$ iocm find-ioc --pv <pv-name>
$ iocm find-ioc --pv Ring_Mag:PS_QTH_AB10a13:TrgLos
Application : /ics/iocs/vme/ring-ps-ioc6
IOC-Stats Name : RING_PS:IOC6
IOC-Type : vme
Engineer : Randy Rhoads
Hostname : ring-ps-ioc6
Location : 07-RM-05 Top
$ iocm find-ioc --pv Ring_Mag:PS_IKick_H03:V_Set
Application : /ics/iocs/utca/ring-inj-ioc-wf1
IOC-Stats Name : RING_INJ:IOC_WF1
IOC-Type : utca
Engineer : Zakk Wylde
Hostname : ring-inj-ioc-wfmon1
Location : Building 505, Rm-2
Notes: This avoids the classic problem of IOCs building differently depending on who created them.

## Slide 16: Closing
Faster IOC deployment
Reduced human error
Reduces operational risk
Scales to hundreds of IOCs
Enforces Standards
Easier audits and upgrades
Makes IOCs easier to support long-term
Tested with: Secure EPICS, PVACMS
Need to expand to use with µTCA