## Slide 1: Spring EPICS Collaboration Meeting Integration of non digital devices using modbus
Falk Rosenhahn
  Fritz Haber Institute
  PP&B and Elab Department
Paris-Saclay, 21.04.2026

## Slide 2: Benefit
No coding and
no hardware development required

## Slide 3: First Example

## Slide 4: UHV system for surface science
LEED
SPUTTER
GARAGE
VALVE

## Slide 5
Automate linear motion

## Slide 6: Integration
LAN
LAN
RS485
iCL42-RS06
Serial-Server
EPICS-Server
EPICS Client

## Slide 7: st.cmd
epicsEnvSet("PORTT", "LAN")
epicsEnvSet("SM", "ICL42MOTOR")
drvAsynIPPortConfigure("$(PORTT)", "10.0.0.100:4005", 0, 0, 0)
modbusInterposeConfig("$(PORTT)", 1, 2000, 4)
drvModbusAsynConfigure("POS_SET$(PORTT)", "$(PORTT)", 1, 16, 0x6201, 2 , INT32_BE, 0 , "$(SM)")
drvModbusAsynConfigure("POS_START$(PORTT)", "$(PORTT)", 1, 16, 0x6002, 1 , INT16 , 0 , "$(SM)")
epicsEnvSet("ARG_LEED$(SM)", "PORTA=POS_SET$(PORTT), PORTB=POS_START$(PORTT)")
dbLoadRecords("db/StepperMotor.template","$(ARG_LEED$(SM))")

## Slide 8: Steppermotor.template
record(longout, "$(P):$(M):Set_pos") {
field(DTYP, "asynInt32")
field(OUT, "@asyn($(PORTA) 0)")
field(EGU, "Steps")
field(FLNK, "$(P):$(M):Delay_start")
}
record(calcout, "$(P):$(M):Delay_start") {
field(SCAN, "Passive")
field(INPA, "$(P):$(M):Set_pos.VAL CP")
field(CALC, "A")
field(ODLY, "0.1") #Delay
field(OUT, "$(P):$(M):Start.PROC PP")
}
record(longout, "$(P):$(M):Start") {
field(DTYP, "asynInt32")
field(OUT, "@asyn($(PORTB) 0)")
field(VAL, "16")
}

## Slide 9: Second Example

## Slide 10: Ask for Automation

## Slide 11: Ask for Automation

## Slide 12: Integration
LAN
Analog
RS485
NF 1.60 DCB-4B
N4DAC2
EPICS-Server
EPICS Client

## Slide 13: ST.CMD

## Slide 14: USE

## Slide 15: USE

## Slide 16: Conclusion
What will be cost more for our institude?

## Slide 17: Thank you