## Slide 1: NICOS @ ESS An Experiment Control System on Top of EPICS
Vincent Hardion, on behalf of ECDC, ESS
Spring EPICS Collaboration Meeting 2026
April 20–24, 2026 · ENS Paris-Saclay, Gif-sur-Yvette, France
Notes: ESS cold commissioning phase → transition to hot commissioning, then operations
Focus on instrument control experience, not detailed architecture
Joint perspective: ECDC + LOKI

## Slide 2: Agenda
ESS Neutron Instruments
NICOS
NICOS Device with EPICS
Conclusion
April 2026

## Slide 3: European Spallation Source
16 Instruments with focus area:
Chemistry of Materials, Magnetic & Electronic Phenomena
Engineering Materials, Geosciences, Archeology & Heritage Conservation and Fast Neutron Applications
Life Science & Soft Condensed Matter
14 Hz Neutron Pulse => Time resolved
Long time structure => Time Of Flight
Neutron Instrumentation
ESS Pulse shape
ESS Neutron Instruments map
Neutron Experiment with Time Resolved

## Slide 4: ECDC Scope
Experiment Control to orchestrate experiments and perform commissioning.​
Event Formation Unit (EFU), collecting data from the different instruments detectors and reducing data to the minimal user raw data​ ​
Data Collection: pipeline recording data and MetaData, ensuring compliance with NEXUS and SciCAT standards.​
ECDC Architecture

## Slide 5: Experiment Control Requirement
The Gap Between IOCs and Scientists
Instrument Scientists needs
Technical Requirement
Scripted scan sequences
  Live data views & plotting
  Sample tracking & metadata
  Proposal management
  Multi-User
  Remote Access
Sits on top of EPICS
Python based
Modular and possibility to opt-out of unnecessary feature
Plug-and-play sample environment
Server based

## Slide 6
NICOS
An Integrated Experiment Control System

## Slide 7
Visit https://nicos-controls.org/

## Slide 8: What is NICOS?
Origin & Community:
Developed at FRM II / MLZ (Garching)
Active at: MLZ, ESS, PSI and more
Design goals:
User Friendly, Flexibility, and Reliability
Python scripting, Qt GUI, Daemon-based
Network Instrument COntrol System
Other facilities worldwide
LAHN (Laboratorio Argentino De Haces De Neutrones, Buenos Aires, Argentina)
Materials Growth & Measurement Laboratory at Charles University (Prague, Czech Republic)
ISIS (Didcot, UK)
Idaho National Lab (Idaho Falls, USA)
Neutron Radiography Facility (NRF) of Oregon State University (Corvallis, USA)
X-Ray Center of TU Wien (Vienna, Austria)

## Slide 9: NICOS Stack
5 / 15
NICOS Desktop Qt Client
NICOS Server
EPICS
TANGO
SECoP
Distributed: daemon + cache server + multiple GUI/script clients (TCP)
Simplified architecture
CARESS
Execution Daemon
Poller
Cache
Electronic Logbook
Watchdog
Collector
Kafka

## Slide 10: NICOS in Practice — Interface
11 / 15
Instrument information
Instrument status and emergency button
Applications: UI, CLI and Scripting, Sample management, Logbook, …
Settings: Proposal management, Instrument setup
Configurable multi-panel layout per instrument - Widget, Ploting, Imaging, …
Device tree, browse all connected devices and their live state
1
2
3
6
4
5

## Slide 11: A Rich, Scientist-Facing GUI
Device Control
Live readout, setpoints, alarm indicators for all connected devices
Live Plots
Real-time live view of the data acquisition
Set Up
Possibility to load different set up depending on the hardware.

## Slide 12: A Rich, Scientist-Facing GUI
Script Editor
Syntax highlighting, auto-complete, run/stop controls
Queue scripts; monitor execution progress
Scan Control
UI for scan control, management, and scan plotting
Every scan is recorded automatically in a
NeXus/HDF5 file
Template by configuration
Metadata captured at scan start
HDF5 File Template
'WONI:NXInstrument': {
'monochromator:NXcrystal': {
'wavelength': DeviceDataset('wavelength',
units=NXAttribute('angstrom', 'string')),
'rotation_angle': DeviceDataset('mtt'),
'd_spacing': DeviceAttribute('mono', 'dvalue'),
'type': ConstDataset('Si', 'string'),
}
}
HDF5/NeXus

## Slide 13: A Rich, Scientist-Facing GUI
CLI
Interactive Python prompt connected to instrument control system.
Tab completion on device names and commands
Commands
More than 100+ predefined commands
ipython
%load_ext nicos.clients.ipython.nicos %nicos /connect <host> <port> <user> <password>
var = %nicos /val <device>
var = %nicos /val <detname>_live
x, y, n = %nicos /val scandata
Accessing control and data from an ipython session: device value, parameters, live stream from detector, scan data

## Slide 14: A Rich, Scientist-Facing GUI
Electronic logbook
User Experiment log, synchronised automatically with counting and measurement
Proposals and Sample management
Historic
Visualisation of history value of Device from the cache for the current session.
User session connected to the User proposal. Possibility to add meta data related to the samples used in experiment.

## Slide 15
NICOS Device with EPICS

## Slide 16: Writing a new device class
Device: the root of all NICOS devices
Use for: auxiliary objects, configuration holders, communication handlers (e.g. a serial bus, an EPICS connection pool)
Readable: a device you can read a value from
Use for: sensors, encoders, monitors, anything with a scalar readout but no setpoint
Measurable: a detector or counting device
Use for: detector arrays, single counters, time-of-flight detectors, anything driven by a count/time preset
Moveable: a device with a target you can drive to
Use for: motors, temperature controllers, slits, attenuators, anything with a setpoint
4 types of NICOS Devices

## Slide 17: Writing a new device class
Combined with base classes to add specific capabilities without rewriting logic.
For example:
HasLimits: enforces software userlimits and abslimits before any move
HasOffset: transparent user/hardware position shift via an offset parameter
HasMapping: maps named positions ("open", "closed") to raw hardware values
HasAutoDevices: auto-attaches child sub-devices (e.g. encoder alongside a motor)
IsController: manages ordered start/stop of a group of sub-devices
CanDisable: adds enable() / disable() without removing the device from the setup
Mixins
Composite NICOS device example

## Slide 18: EPICS NICOS Devices
Predefined Device classes for EPICS:
EpicsMotor,
EpicsReadable,
EpicsStringReadable,
EpicsAnalogMoveable,
EpicsDigitalMoveable,
EpicsStringMoveable,
EpicsMappedReadable,
EpicsMappedMoveable,
EpicsManualMappedAnalogMoveable
Supports PVAccess (PVA) and Channel Access (CA)
Connection monitoring and automatic reconnect
NICOS mainly used to create high level composite devices.
Currently supported
ESS specific NICOS EpicsDevice
NICOS EPICS Class documentation

## Slide 19: Writing a new device class
Inherit from a base class and mixin
  pick the right parent: Device, Readable, Moveable, HasLimits, Actuator, etc.
Declare parameters
  use the parameters dict to define configuration values with type, default, and description:
Implement doRead()
  returns the current value from hardware; called by read()
Implement doStart()
  sends a trigger to hardwareto start acquisition
Optionally implement doStatus()
  returns (status_code, message) so NICOS knows if the device is moving, idle, or in error
Register in a setup file — devices are instantiated in a Python setup dict, not in code:
Key Points
devices = dict(
protoncurr=device(
"nicos.devices.epics.EpicsCounterPassiveChannel",
description="Monitor for proton current",
type="monitor",
readpv="IOC:PROTON",
),
)
Code for a generic counter from any readeable PV
Configuration of this generic counter

## Slide 20
Conclusion

## Slide 21: Conclusion & Invitation to Collaborate
ESS Neutron Instruments use NICOS as the main User Interface.
NICOS Proven at neutron facilities
Many feature toward Instrument Scientific usage
Easy to adapt
NICOS + EPICS: complementary
Try at nicos-controls.org
2nd NICOS collaboration meeting, PSI, March 2026

## Slide 22: Question?
2026-04-21