## Slide 1: ecmc:
Open-source EPICS-based motion control on EtherCAT
Anders Sandström
Saclay, 23 April 2026

## Slide 2
Agenda
01
Introduction/Overview
What’s ecmc
02
Motion
Axis configuration
03
Diagnostics
Panels / tools
04
Custom logic: PLC & scripting
Different ways to add custom functionality
05
Extending ecmc
Add functionality with plugins
06
Get started
Repositories, manual, community
ECMC · EPICS Collaboration Meeting 2026, Saclay
Agenda
2 / 23

## Slide 3
Introduction
Open-source motion control & DAQ framework, tightly integrated in EPICS
What it is
An open-source EPICS module that turns EtherCAT hardware into motion axes and I/O, also supporting soft-PLC scripting, plugin API.
Motion: positioning, jogging, homing, referencing, interlocks, latching
Synchronisation: axis-to-axis, external source, kinematics, PVT
DAQ: analog ≤100 kHz, digital ≤1 MHz (hardware-limited)
Soft-PLC: scriptable real-time logic, user plugins in C/C++
Standard EPICS: Motor Record, PVs, Channel Access, pvAccess
770+
axes in production
(SLS,HIPA, SwissFEL)
190+
ecmc IOCs
(motion + DAQ)
ECMC · EPICS Collaboration Meeting 2026, Saclay
What ECMC is
3 / 23
At PSI

## Slide 4
Client / GUI layer
caQtDM, Python scripts, CSS-PHOEBUS
EPICS IOC layer
Motor Record, PVs, asynDriver, Channel Access
ECMC real-time core
RT loop, Axis objects, trajectory gen, PLC logic
IgH EtherCAT master
Cyclic comms, distributed clocks, slave config
EtherCAT hardware
Drives, encoders, I/O modules, sensors, actuators
vs.
Overview: Comparison of two approaches
Both approaches are valid — the choice depends on your control system and workflow
Typical vendor-integrated stack
Client / GUI layer
caQtDM, Python scripts, CSS-PHOEBUS
EPICS IOC
Config PVs, records
ADS bridge, OPC-UA, ..
Protocol translation
TwinCAT runtime
Vendor runtime, Windows, TC/BSD, or Linux
TwinCAT project
IDE-edited, per-deployment
EtherCAT hardware
Drives, encoders, I/O modules, sensors, actuators
Open EPICS-native stack
ECMC · EPICS Collaboration Meeting 2026, Saclay
4 / 23
Open architecture

## Slide 5
Configuration
ECMC · EPICS Collaboration Meeting 2026, Saclay
5 / 23
Everything is linked from the startup file

## Slide 6
Act. position
Position setp.
Act. position
Velocity setp.
Act. position
Torque setp.
CSP
Cyclic Sync. Position
CSV
Cyclic Sync. Velocity
Control:
Pos.
Velo.
Torque
Control:
Velo.
Torque
- Trajectory gen.
- No control
-Trajectory gen.
-Position cont.
-Trajectory gen.
-Position cont.
-Velocity cont.
Control:
Torque
Controller: No loops needed
Drive: All control loops
Controller: Position loop
Drive: Velocity and current loop
Controller: Position, velocity loop
Drive: Current loop
CST
Cyclic Sync. Torque
Hardware
ecmc controller
Components
Servos
Some Steppers
SmarAct (EtherCAT)
Analog position drives
Most common:
Servos
Steppers
Analog velocity drives
Servos
Motion: Control Loops: CSP, CSV, CST
ECMC · EPICS Collaboration Meeting 2026, Saclay
6 / 23

## Slide 7
Act. position
Position setp.
CSP-PC-Mode
Cyclic Sync. Position with Dual Position loop
Control:
Pos.
Velo.
Torque
- Trajectory gen.
- Position control
Controller: No loops needed
Drive: All control loops
Act. position
Hardware
Controller
Components
Special case:
Servos
Some steppers (EL7062, currently a bug in CSV)
Analog position drives
Motion: Control Loops: CSP-PC, Dual Position Loop
ECMC · EPICS Collaboration Meeting 2026, Saclay
7 / 23

## Slide 8
Monitor
Axis
EtherCAT master
PLC (optional)
EcEntry
EcEntry
EcEntry
Hardware
Field
Custom logic
Trajectory
Motion
ECMC · EPICS Collaboration Meeting 2026, Saclay
Motion
8 / 23
PID cntrl.
Drive
EcEntry
EcEntry
EcEntry
Axis Object
EcEntry
EcEntry
EcEntry
Encoder
ax1enc.actpos:=(ax5.enc.actpos+ec0.s14.analogInput01)/2;
ax3.traj.setpos:=ax4.traj.setpos*5;
ax1.mon.ilockbwd:=ax2.mon.lowlim and ec1.s12.binaryInput03;
ax1.ctrl.kp:= abs(ax1.enc.actpos - ax1.traj.setpos) * static.kp;
ax3.drv.enable:=1;
Virtual Axis

## Slide 9
Axis
  CSV, CSP..
  General, name, auto enable/disable
Encoder
  Hardware link for actual position input, Scalings
Trajectory
  Default velo, acc, jerk
  Traj type
Monitoring
  Hardware links for limits, following error, max velo,..
Controller
  PID, Clamping, deadbands,…
Drive
  Hardware links to drive , Scalings, …
Motion: Configuration
Yaml config for the objects
ECMC · EPICS Collaboration Meeting 2026, Saclay
Motion
9 / 23
ecmc PLC exprtk code

## Slide 10
Synchronized axes: kinematics + state machine
Virtual masters drive physical slaves — one command, coordinated motion
Example: slit system
Gap
Centre
MASTERS (virtual)
Axis-PLC kinematics · axis_kin_2DoF.plc_inc
Left blade
Right blade
SLAVES (physical)
State machine guarantees consistency
IDLE
Waits for command. Routes to MASTERS or SLAVES.
MASTERS
Enables all axes · sets trajectory source to PLC for slaves · executes command · handles interlocks.
SLAVES
Direct command on physical axis · waits · returns to IDLE.
RESET
Resets errors across the group · returns to IDLE.
ECMC · EPICS Collaboration Meeting 2026, Saclay
Synchronized axes
10 / 23

## Slide 11
Application PLC-code
Generic 2DoF kinematics
axis_kin_2DoF.plc_inc
https://github.com/paulscherrerinstitute/ecmccfg/tree/master/plc_lib
ECMC · EPICS Collaboration Meeting 2026, Saclay
Synchronized axes
11 / 23
Synchronized axes: kinematics

## Slide 12
ecmcMain.ui: Access (almost) entire ecmc system:
  caqtdm –macro ”IOC=<IOC>” ecmcMain.ui
Diagnostics
Overview panel (dynamic)
ECMC · EPICS Collaboration Meeting 2026, Saclay
12 / 23

## Slide 13
Diagnostics
ECMC · EPICS Collaboration Meeting 2026, Saclay
Diagnostics
13 / 23
Hardware: “Dynamic” panels

## Slide 14
Diagnostics
ECMC · EPICS Collaboration Meeting 2026, Saclay
Diagnostics
14 / 23
Motion

## Slide 15
Closed loop
Open loop (steppers)
  BISS
  Openloop
Open/closed loop
ECMC · EPICS Collaboration Meeting 2026, Saclay
Diagnostics
15 / 23
Motion

## Slide 16
Tools
ECMC · EPICS Collaboration Meeting 2026, Saclay
Diagnostics
16 / 23

## Slide 17
Classic ecmc PLC: exprtk based ECMC syntax
  Access all PVs of all axes, I/O, and EtherCAT entries by name
  Kinematics
  Expose PLC variables as EPICS PVs
  Motion Library (MC_*), many utility functions and variables
Plugins:
  Integration of c/c++ modules
Next ecmc release:
  Direct C++ (cpp-logic). An extension to the existing plugin concept
  IEC 61131-3 Structured Text (ecmc_plugin_strucpp) trough strucpp*
Usecases:
Control tasks
Kinematics — mirror, slit, …
Sequences, state machines
Custom homing
Soft-PLC: scriptable real-time logic
A PLC object runs in-sync with the RT loop — custom interlocks, kinematics, math
ECMC · EPICS Collaboration Meeting 2026, Saclay
Soft PLC
17 / 23s

## Slide 18
Soft-PLC: scriptable real-time logic, exprtk
A PLC object runs in-sync with the RT loop — custom interlocks, kinematics, math
ECMC · EPICS Collaboration Meeting 2026, Saclay
18 / 23
variables (total 70)
  generic: 3
  ethercat: 2
  motion: 49
  plc: 9
  data storage: 7
functions (total 110):
  ethercat: 29
  master 2 master: 6
  motion: 30
  motion group: 27
  data storage: 15
  lookup tables: 1
  misc: 2

## Slide 19
Soft-PLC: scriptable real-time logic, C++
C++, minimal examples
ECMC · EPICS Collaboration Meeting 2026, Saclay
Ecosystem
19 / 23
Next Release

## Slide 20
Soft-PLC: scriptable real-time logic, Structured Text (strucpp*)
A PLC object runs in-sync with the RT loop — custom interlocks, kinematics, math. Plugin needed ecmc_plugin_strucpp and strucpp
ECMC · EPICS Collaboration Meeting 2026, Saclay
Ecosystem
20 / 23
Next Release

## Slide 21
Plugin architecture
Extend functionality without modifying ecmc
ecmc_plugin_daq
Waveform data acquisition with timestamps
ecmc_plugin_strucpp
IEC 61131-3 Structured Text PLC execution
ecmc_plugin_grbl
GRBL G-code / CNC interpreter
ecmc_plugin_fft
FFT on live EtherCAT signals (via kissfft)
ecmc_plugin_scope
Low-level scope for DC-enabled slaves
ecmc_plugin_socketcan
SocketCAN / CANopen bridge
ecmc_plugin_safety
Interface to Pilz motion-safety box (PSI specific)
ecmc_plugin_raspi
wiringPi — GPIO
Plugin API is minimal — a handful of callbacks.
ECMC · EPICS Collaboration Meeting 2026, Saclay
Plugins
21 / 23

## Slide 22
How to get started
Every link below is public — no sign-up, no NDA
epics-modules/ecmc
Core module — RT loop, axis objects, commands, APIs
github.com/epics-modules/ecmc
paulscherrerinstitute/ecmccfg
Configuration framework — YAML, Jinja2, loader scripts
github.com/paulscherrerinstitute/ecmccfg
paulscherrerinstitute/ecmccomp
Component library — motors, encoders
github.com/paulscherrerinstitute/ecmccomp
ecmccfg manual
Online docs, knowledge base, best-practice examples
paulscherrerinstitute.github.io/ecmccfg/manual
ECMC plugins
DAQ · Structured Text · C++ · G-code · FFT · PVA · scope · CAN · safety
github.com/paulscherrerinstitute (search: ecmc_plugin)
IgH EtherCAT Master
The underlying open-source EtherCAT master
etherlab.org
First try?
Clone ecmccfg → look at the examples in examples/PSI/best_practice/
ECMC · EPICS Collaboration Meeting 2026, Saclay
Get started
22 / 23

## Slide 23
https://git.psi.ch/motion/ecmc_plugin_grbl
Thanks to:
Felix Maier
Alvin Acerbo
Xiaoqiang Wang
Luka Debenjak
ECMC · EPICS Collaboration Meeting 2026, Saclay
Get started
23 / 23