## Slide 1: OPC UA Security
Demo / Hands-On Instructions
Ralph Lange

## Slide 2: Log Onto the Training-VM

## Slide 3: Start the Demo Server
Open a new terminal
Unpack the Unified Automation demo server
Run it
  Use CTRL-C and restart it to simulate an orderly server disconnect and reconnect
  Use CTRL-Z and “fg” to simulate network hang-up

## Slide 4: Start the UaExpert Browser
The first start requires you to create a self-signed certificate. Just enter any data.

## Slide 5: UaExpert: Add the Demo Server
Select Server, then Add…
Use the Advanced tab and enter the endpoint URL
opc.tcp://localhost:48010

## Slide 6: UaExpert: Connect
Connect by clicking on the Connect Server icon
Trust the unknown self-signed server certificate
and Continue

## Slide 7: UaExpert: Familiarize Yourself
Browse
Inspect
Monitor

## Slide 8: Build the IOC Two Steps
Change directory into the application cd training/opcua-support
Build the example IOC make

## Slide 9: Run the IOC
Change into the IOC’s startup directory
Run the IOC binary, giving the name of the startup file as argument
Using a subshell avoids having to change directory all the time
( cd iocBoot/iocUaDemoServer/; ../../bin/linux-x86_64/opcuaIoc st.cmd )
Always do a clean exit of the IOC, using CTRL-D or the exit command OPC UA servers don’t free their session resources when a connection breaks – if the same session is reconnected, it just continues

## Slide 10: Run the IOC

## Slide 11: Find out the IOC’s URI

## Slide 12: Prepare the xca Cert Manager
Powerful free Certificate and Key Management tool
Available on Linux, Windows, MacOS
Supports many key and certificate formats (including ssh)
Supports CA-based workflows (including sub-CA hierarchies) Nice visualization of CA signature chains
Allows to save and load templates Great help in creating correct certificates efficiently
Keeps keys, certs and templates in a database

## Slide 13: Create the xca Database
Start
Then File -> New DataBase
Give it a name
You can leave it without a password

## Slide 14: Import the IOC Cert Template
Tab Templates
Button Import
Select the template OPCUA_Client_IOC
This loads the template from the file into the xca database

## Slide 15: Prepare the Secure Connection
Set up the Client Certificate
Create the Key Pair and self-signed Client Certificate for the IOC
st.cmd: switch the IOC to use security
st.cmd: load the self-signed Client Certificate and its private key
Establish trust
Copy the Client Certificate into the server’s trusted/certs list
Copy the Server Certificate into the IOC’s trusted/certs list
Connect!

## Slide 16: Create a Key Pair for the IOC
Tab Private Keys
Button New Key
Call it IOC key

## Slide 17: Export the IOC Private Key
Tab Private Keys
Select the key
Button Export
Select PEM format
Click OK

## Slide 18: Create the IOC’s Client Certificate
Tab Certificates
Button New Certificate
Sub-Tab Source
Make it self-signed
Select and fully apply the template OPCUA_Client_IOC

## Slide 19: Create the IOC’s Client Certificate
Sub-Tab Subject
Minimal Setup:
Set the countryName to any two letters
Give it a nice commonName

## Slide 20: Create the IOC’s Client Certificate
Sub-Tab Extensions
Important Setup:
In the extensions, replace the placeholders <IOC> and <HOST>
The URI must match what the IOC uses
You can use IP: instead of DNS:
Click OK

## Slide 21: Export the Certificate
Tab Certificates
Select the certificate
Button Export
Select DER format
Click OK
Exit xca

## Slide 22: Set Up the IOC’s PKI File Store
Create the minimal necessary directories for the IOC PKI file store
Move the created self-signed Client Certificate and its private key into it

## Slide 23: Configure the IOC to use Security
Edit st.cmd (gedit is available)
Remove the setting that switches off Security
Instead:
Set the location of the PKI file store
Load the client certificate

## Slide 24: Establish Trust
Remember that trust needs to be established both ways:
Make the IOC trust the Demo Server’s certificate copy the server certificate in the IOC’s trusted/certs store
Make the Demo Server trust the IOC’s certificate copy the IOC certificate in the server’s trusted/certs store
Start the IOC … and …

## Slide 25: Connect securely
… and … yay!

## Slide 26: Using CA-Based Certificates
Very similar, but different:
Create your CA: a new key and a self-signed CA certificate
Export the CA Certificate
Create a new IOC Client Certificate, containing the IOC key, but sign it with the CA key (instead of self-signing)
Export the IOC Client Certificate and copy it to the IOC’s own folder
Change the st.cmd file to load the new Client Certificate
Create a new empty CRL, signed with the CA key
Copy into the server PKI: the CA certificate (into trusted/certs) and the CRL (into trusted/crl)

## Slide 27: Using CA-Based Certificates
Remember that I said “be prepared for a lot of frustration” ??
I verified this workflow in trustworthy documentation places (and using AI, obviously)
I spent a few hours yesterday creating and exporting certs and CRLs, experimenting with formats, file suffixes and locations
I could not get the f*@&#^$*&^$@!! thing to connect: “BadSecurityCheckFailed”
I am sorry. I will eventually get it to work and send you the updated slides.

## Slide 28: Thanks for Your Attention!
Any questions left unanswered?
OPC UA room on EPICS Chat