## Slide 1: oac-tree
Operations, Automation and Control using behavior trees
Gennady Pospelov Walter Van Herck

## Slide 2: Overview
Framework overview
Behavior trees
oac-tree GUI
Example patterns
Future plans
Links

## Slide 3: Framework overview
oac-tree is a C++ framework for the execution of control procedures, based on behavior tree semantics
oac-tree consists of a base library and plugins that extend the base functionality
oac-tree-gui is a Qt/C++ GUI to create, edit and run procedures

## Slide 4: Behavior trees: instruction trees
Control flow nodes:
Have child node(s)
Report all possible instruction statuses: success, failure or running
Condition node:
No child nodes
Immediately report success or failure
Action nodes:
No child nodes
Can report all statuses

## Slide 5: Behavior trees: control flow
Sequence with memory
system ok?
Action 1
Action 2
*
tick
tick
success
running
tick
running
failure
failure

## Slide 6: Behavior trees: control flow
ReactiveSequence
system ok?
Action 1
Action 2
tick
tick
success
running
tick
running
failure
failure

## Slide 7: oac-tree: base instructions
Sequence/ReactiveSequence: succeeds if all child nodes succeed (AND)
Fallback/ReactiveFallback: succeeds if one child node succeeds (OR)
ParallelSequence: custom success conditions (e.g. success on 2 child nodes’ success)
(User)Choice: only execute child nodes marked by user or workspace variable
Inverter: single child; invert success – failure
Repeat: single child; repeat child node execution
Listen: single child; trigger child node on update of workspace variable(s)
*
?
?
*

## Slide 8: oac-tree: base actions
Wait: return success after optional timeout
Fail: return failure after optional timeout
Copy: copy (subfield of) variable to (subfield of) variable
Equal, GreaterThan, GreaterThanOrEqual, LessThan, LessThanOrEqual: compare two variables (or fields thereof)
Input: allow user to set variable

## Slide 9: oac-tree: variables
Each procedure contains a workspace with a flat list of named, threadsafe variables that can be accessed by all instructions in the procedure
Variables have a common API, where you read/write (subfields of) an AnyValue:
Local: in-memory storage of AnyValue
File: JSON encoded storage of AnyValue in a file

## Slide 10: oac-tree-epics
Instructions:
ChannelAccessRead/ChannelAccessWrite: read/write ChannelAccess PV
PvAccessRead/PvAccessWrite: read/write PvAccess PV
Variables:
ChannelAccessClient: connects to ChannelAccess PV
PvAccessClient: connects to PvAccess PV
PvAccessServer: publishes a variable over PvAccess
PvAccessEncodedClient/PvAccessEncodedServer: same, but with encoded payload over PvAccess to support dynamic types and scalars

## Slide 11: oac-tree-mathexpr
MathExpression instruction:

## Slide 12: oac-tree GUI

## Slide 13: Example patterns: building blocks
Fallback
Sequence

## Slide 14: Example patterns

## Slide 15: Example patterns

## Slide 16: Example patterns

## Slide 17: Example patterns

## Slide 18: Example patterns

## Slide 19: Example patterns

## Slide 20: Example patterns
PPA

## Slide 21: Example patterns

## Slide 22: Future plans
Improve GUI: functionality and user experience (see e.g. Task Monitor during demo)
Expose oac-tree-server using WebSockets and create web client application
Containerized deployment of procedures

## Slide 23: Links
Source code https://github.com/oac-tree
Documentation https://oac-tree.github.io/oac-tree-docs Behavior trees in robotics and AI
Training material: https://github.com/oac-tree/oac-tree-training https://github.com/epics-training/training-vm
Support: mailto:Walter.Vanherck@iter.org mailto:Gennady.Pospelov@iter.org