Impact of the various HCAL mechanical design on its physics performance
(first look)
Jan BLAHA
Micromegas Physics Meeting, 23 March 2010, LAPP

---
Objective
Find the optimal mechanical design for HCAL which takes into account engineering as well as physics aspects
Evaluate the impact of various HCAL mechanical design on its physics performance
Study is focused on hadronic showers behavior close to the boundary between two HCAL modules for
projective and non-projective geometry
with and without supporting plate
2

---
Considered geometries
2 HCAL Modules
SiD LoI geometry
2 cm of steel plate
between modules
M1
M2
Geometries:
sid2Modules_FeAbs_NoFeP (ref. geometry without supp. plate)
sid2Modules_FeAbs_1cmFeP (1cm supporting plate)
sid2Modules_FeAbs_2cmFeP (2cm supporting plate)
sid2Modules_FeAbs_2cmFeP_WE - (2cm supporting plate and ECAL)
N.B. Detectors have double SiD depth (80 layers). Analysis has been	performed for both 40 and 80 layers detectors
20 GeV pions
3
Shower profile

---
Considered geometries
2 HCAL Modules
SiD LoI geometry
2 cm of steel plate
between modules
M1
M2
plate
Geometries:
sid2Modules_FeAbs_NoFeP (ref. geometry without supp. plate)
sid2Modules_FeAbs_1cmFeP (1cm supporting plate)
sid2Modules_FeAbs_2cmFeP (2cm supporting plate)
sid2Modules_FeAbs_2cmFeP_WE - (2cm supporting plate and ECAL)
N.B. Detectors have double SiD depth (80 layers). Analysis has been	performed for both 40 and 80 layers detectors
3
Shower profile

---
Considered geometries
2 HCAL Modules
SiD LoI geometry
2 cm of steel plate
between modules
M1
M1
M1
M2
plate
Geometries:
sid2Modules_FeAbs_NoFeP (ref. geometry without supp. plate)
sid2Modules_FeAbs_1cmFeP (1cm supporting plate)
sid2Modules_FeAbs_2cmFeP (2cm supporting plate)
sid2Modules_FeAbs_2cmFeP_WE - (2cm supporting plate and ECAL)
N.B. Detectors have double SiD depth (80 layers). Analysis has been	performed for both 40 and 80 layers detectors
3
Shower profile

---
Considered geometries
2 HCAL Modules
SiD LoI geometry
2 cm of steel plate
between modules
M1
M1
M1
M2
plate
M2
Geometries:
sid2Modules_FeAbs_NoFeP (ref. geometry without supp. plate)
sid2Modules_FeAbs_1cmFeP (1cm supporting plate)
sid2Modules_FeAbs_2cmFeP (2cm supporting plate)
sid2Modules_FeAbs_2cmFeP_WE - (2cm supporting plate and ECAL)
N.B. Detectors have double SiD depth (80 layers). Analysis has been	performed for both 40 and 80 layers detectors
3
Shower profile

---
Projective and non-projective geometry
Projective geometry
Non-projective geometry
N. Geffroy
HCAL SiD baseline geometries:
Projective geometry – 12 identical calorimeter modules
Non-projective geometry – 6 reqtangular and 6 trapezodial modules
Two rectangular modules are considered as a good approximation for
simulation study
4

---
Typical events for 50 GeV pions
Projective geometry
Non-projective geometry
Particles directed as from the vertex
Impact area restricted to 5 cm diameter around the boundary at front of the detector
For each configuration, data have been generated for pion energies between 3 to 200 GeV
5

---
Typical events for 50 GeV pions
Projective geometry
Non-projective geometry
Particles directed as from the vertex
Impact area restricted to 5 cm diameter around the boundary at front of the detector
For each configuration, data have been generated for pion energies between 3 to 200 GeV
5

---
Typical events for 50 GeV pions
Projective geometry
Non-projective geometry
Particles directed as from the vertex
Impact area restricted to 5 cm diameter around the boundary at front of the detector
For each configuration, data have been generated for pion energies between 3 to 200 GeV
5

---
Typical events for 50 GeV pions
Projective geometry
Non-projective geometry
Particles directed as from the vertex
Impact area restricted to 5 cm diameter around the boundary at front of the detector
For each configuration, data have been generated for pion energies between 3 to 200 GeV
5

---
Projective geometry
Number of hits versus cell id number
Configuration:
2 cm Fe plate between modules with 80 layers
50 GeV pions, 10k events
0.5 MIP readout threshold
6

---
Non-projective geometry
Number of hits versus cell id number
Configuration:
2 cm Fe plate between modules with 80 layers
50 GeV pions, 10k events
0.5 MIP readout threshold
7

---
Projective vs non-projective
Deposited energy (GeV)
Number of hits
More visible energy for non-projective geometry
Better energy resolution for non-projective geometry
8

---
Conclusions and outlook
The first look shows significant difference between projective
and non-projective geometry
Next work:
Study of different boundary configuration
with and without supporting plate
different size of death zone around modules
with and without ECAL module in front of
Impact of different vertex
Comparison of projective and non-projective geometry
Comparison of different readout
Evaluation over wide energy range
9