## Slide 1: News from GANIL
Hervé Savajols (GANIL/CNRS)
Emmanuel Touron (GANIL/CEA)

## Slide 2
New stable beams : Th and W and 235U soon available (fission program)
Spiral1 beam development : 74Rb and 2026 test : 50Cr + 58Ni → 98Ag, 103-104-105In
CSS2: Successful restoration after an insulation fault & a water leak
  August 2025 : insulation fault in the upper coil of sector C of CSS2.
Nominal operation was successfully restored on February 5th
Cause : water had infiltrated the resin core, causing a short circuit.
  April 2026 : water leak in the RF cooling system (inside de cavity)
Successfully repaired ; May 2026 and first beam extracted
CIME: problem of transmission (few %) under investigation (High priority)
Parallel operation ramping-up cyclotrons/SPIRAL2 : 4 weeks in 2025 – 7 weeks in 2026
  → Beam time gain 1,5 & data acquisition gain 2,45 – 5 experiments running in parallel : NFS brochette mode FALSTAF/EXOGAM, LISE/TAS experiment + SME + IRSUD
BUT :
  Heat wave made life difficult (90 kV transformer shut down, water cooling, electronic cards, … particularly for staff members
  Still too many equipment failures → Plan to improve the reliability of critical equipment underway (High priority)
GANIL accelerator complex
2

## Slide 3
CYREN : a renovation ambition for GANIL
to maintain scientific objectives at the best level
Infrastructure & utilities
Beam process
Safety system
  Objective n°1:
  Keep the installation in good operational conditions for the next 20 years
  Objective n°2:
  Optimise human resources for maintenance and further renovation
3
Project kickoff june 2026 (organisation, perimeter, cost)
Massive high-voltage power supplies replacement underway

## Slide 4
Rénovation terminée des 16 tourelles d’extraction d’air des bâtiments machine (BAM) et des aires expérimentales (BAE).
Rénovation des toitures du BAM et BEN, enlèvement de + de 100 tonnes de graviers et végétaux, pose d’une isolation renforcée (R= 4), étanchéité et pose de gardes corps. (en cours)
Nouvel onduleur pour les procédés des AE
Rénovation d’une centaine d’alimentation de puissance pour les aimants (33 baies) dans les galeries techniques GLS, GT7 et sous sol CSS1 avec opération de désamiantage, manutention, travaux électrique…
CYREN : a renovation ambition for GANIL
to maintain scientific objectives at the best level

## Slide 5
S3 beam commissioning postponed to 2027
Administrative shutdown of the liquefier ordered by ASNR on September 25, 2025
Non conformity of the internal heat exchanger located inside the liquefier cold box, subject to Pressure Equipment (PE) regulations (ESP54)
➔ Exemption application file approved by the ASNR on July 21, 2026 after implementation of compensatory measures
Superconducting magnet leak issues (LN2 and He sections)
➔ Intensive investigation and repair validated
Restart of superconducting magnet tests scheduled for October, continuing into 2027.
J6A : Accelerator & beam line tuning up to the target (End 2024)
J6B Spectrometer optical commissioning
  Direct and stripped beam up to the focal plane
  Progressive tuning of the elements (MA+ MS)
  Tools : diagnostics along the spectrometer
  ➔ Beam 40Ar ; E = 0.73 - 5 MeV/u
5

## Slide 6: DESIR
High resolution spectrometer room
Spiral1 beam line
Experimental hall
6
Building acceptance by GANIL 2026
First installation of the transfer beam lines
Safety file to authorise the operation is finalised
New organisation of the project under implementation
Building inauguration December 8th 2026

## Slide 7: NEWGAIN : New GANIL Injector
Existing
NEWGAIN
Main User
beam injector1 (injector2)
intensities 2023 2028 2030
Ions | Intensity (pµA) Phoenix V3 RFQ A/Q≤3 | Intensity (pµA) Phoenix V3 RFQ A/Q≤7 | Intensity (pµA) SC Ion Source RFQ A/Q≤7
18O | 80 | * | 375
19F | >15 | >40 | >40
36Ar | 16 | 70 | 45
40Ar | 3.6 | 70 | 45
36S | 2.3 | * | *
40Ca | 2.9 | 10 | 20
48Ca | 1.2 | 10 | 20
58Ni | 1.1 | 4 | 8
84Kr | 0.1 | 10 | 20
139Xe | 0.001 | 7 | >10
238U | <<0.001 | 0.1 | 6
* -> no estimation
Measured
Estimated
ASTERIC SC ion source
RFQ for heavy ions
World-record intensities
7
Magnet

## Slide 8
Objective: Increase GANIL’s capacity to provide heavy-ion and neutron beams for the irradiation testing of space components and systems from approximately 400 hours to 2,000 hours per year (a factor of 5 increase) by 2030.
 Strengthen and modernize existing capabilities while developing new irradiation facilities.
Key Challenges:
Meet the growing demand for testing services from industry and address the risk of a shortage
of suitable accelerator facilities.
Enhance national competitiveness and sovereignty in the space sector.
Develop long-term strategic partnerships with industry and research institutions.
Increase the international visibility and scientific influence of France in the space domain.
: Space Applications at GANIL Accelerators
SAGA

## Slide 9
LINAC 2019
CYREN – 2025-2031
NEWGAIN, injecteur
2029 PHOENIX
2033 ASTERICS
DESIR 2028-2029
Décret 2025
Neutrons for Science (NFS) 2021
Mise en service du Super
Separator Spectrometer (S3) 2024-2027
SAGA – 2025-2031
9
GANIL Horizon 2030
AGATA – 2029-2030

## Slide 10: Plannings prévus 2027-2035
Planning objective taking into account :
The ramp-up of parallel cyclotron/linac operation
The commissioning of S3, DESIR and NEWGAIN
The SAGA project
The CYREN project
CODIR 08/09/2025

## Slide 11
Thank you for your attention

## Slide 12
Installation GANIL-SPIRAL2
245 personnels permanents CNRS et CEA
  (ingénieurs, techniciens, 30 chercheurs)
  1 enseignant chercheur Univ. Caen
  2 chairs d’excellence (CAESAR, Région Normandie)
Environ 116 CDD
  66 CDD ingénieurs et techniciens, 26 PhD, 18 post-docs, 18 apprentis
Hébergeur du CIMAP : 24 personnels permanents + 7 PhD + 3 post-docs
Communauté internationale d’utilisateurs de ~800 membres (plus de 300 visiteurs annuels)
Entre 100 et 150 publications/an
Une installation de référence en physique nucléaire et en recherche pluridisciplinaire
Grande variété de faisceaux
Cyclotrons : multifaisceaux, grande gamme en énergie
Faisceaux d’ions radioactifs LISE et SPIRAL1
LINAC : intensités faisceaux records
NFS : faisceaux de neutron
Des spectromètres et des systèmes de détection de pointes
Fort ancrage local et régional
Des grands projets en cours
Très haut niveau de compétences des personnels

## Slide 13
VAMOS
AGATA
(2015-2021; 2029-2030)
EXOGAM
ACTAR TPC
MUGAST
LISE SPECTROMETER
INDRA + FAZIA
Experimental rooms
Porte échantillon pour irradiation
CYCLOTRON
SPIRAL1 GANIL CYCLOTRONS
SOURCES
5 cyclotrons
Stable beams: 12C à U
Energy : from < 1 MeV/u up to 95 MeV/u
SPIRAL1 radioactive ion beams
Up to 4 experiments in parallel
GANIL cyclotrons and experimental rooms
Fission
Exotic Nuclei Shell structure
Exotic clusters
EOS
Exotic radioactivity
13
New stable beams : Th and W
235U under investigation

## Slide 14
Exotic beam production – SPIRAL1
50 new isomers/isotopes
With intensities suitable
for acceleration
TULIP FEBIAD
Tested offline in 2024-2025
Calibrated Ar leak : EffAr > 6% (stable) and up to 17%
Ag, In, Sn tracers : Eff = 9-15%
« Intense » metalic isotopes
in the 100Sn region
AGATA campaign @ GANIL
DESIR
Beam OFF
Beam ON
11,2 µs
74Rb+
I20Ne = 2,7 p.µA
20Ne beam shopper 50 ms ON/10 ms OFF
Tcavity = 1600°C
2025 : Workshop on R&D for new ISOL beams at SPIRAL1 and ALTO
➔ Master project : IONS RADIOACTIS
AGATA-GRIT WS
June 2025
14
2026 : 50Cr + 58Ni → 98Ag, 103-104-105In

## Slide 15
New GANIL management & organisation
15
Hervé Savajols (CNRS)
Director
Emmanuel Tourron (CEA)
Deputy director
Lionnel Quettier (CEA)
Technical Director

## Slide 16
CYREN
Minister for Research
confirmed an
endowment of 40 M€
for GANIL projects:
CYREN, DESIR, NEWGAIN
FAIR – GANIL co-operation
16

## Slide 17
Nanogan
For gaz
MonoNaKe
For alkaline
TULIP(-FEBIAD)
For proton-rich isotopes
FEBIAD
For condensable
58 primary beams from 12C to 238U
Graphite target (so far)
4 ion sources
Target/stopper
Primary beam
Ion source
Separator
TISS
The ISOL technique
To user/
acceleration
N+
1+
1+
Exotic beam production : SPIRAL1 upgrade
17

## Slide 18
Converter room
SC linear accelerator (LINAC)
ION SOURCE
S3 (SUPER SEPARATOR SPECTROMETER)
NFS (NEUTRONS FOR SCIENCE)
SPIRAL2 and the new experimental rooms
DESIR (Decay,
Excitation and
storage of radioactive ions)
Beams :
33 MeV protons
40 MeV deutons
<14,5 MeV/A heavy ions
A new accelerator ramping up:
First operation experimental area and the first neutrons at GANIL/SPIRAL2:
NFS first campaigns and results
Super Separator Spectrometer
DESIR
Second injector (NEWGAIN)
SPIRAL2
High intensity stable beams
High intensity neutron beams
TOF room
18

## Slide 19
Some NFS Experiments
Pygmy dipole resonance in 140Ce using the (n,n’g) reaction, Marine Vandebrouck et al
Light ions production studies with MEDLEY at the NFS facility, Diego Tarrio et al
(n,xn g) reaction cross section measurements for nuclear energy, M. Kerveno et al
REPARE project: production of 211At for alphatherapy, Gilles de France et al
MEDLEY
Shedding new light
on the structure of
56Ni using (n,3n)
reaction at NFS,
E. Clement et al
235U fission fragment study with
FALSTAFF at NFS, D. Doré et al.
REPARE
19
➔ a scientific programme in full expansion

## Slide 20
Achromatic point
Primary beam dump
Target position
Secondary beam dump
Final focal plane
Momentum achromat
Mass separator
S3LEB
LHE-S3N
Accelerator & beam line tuning up to the target
J6A
Spectrometer optical commissioning with direct beam
J6B
Scientific commissioning, reactions at the target
Measure and optimise the rejection (case by case)
Estimate transmission
Detection systems : LEB / SIRIUS
J6C
LINAC
S3
Beam
J6x : commissioning milestones
20
Budget : 24,3 M€

## Slide 21
Laser, decay spectroscopy and mass measurement
21
First high resolution laser spectroscopy and mass measurement of stable Er isotopes
Laser spectroscopy : 200 MHz resolution (FWHM)
Transmission : S-RFQ-PILGRIM > 80 %
Mass resolution : R ~200.000
Low Energy Branch (LEB)
J. Romans, et al., Atoms 10, 21 (2022)
A. Ajayakumar et al., NIMB 539, 102-107 (2023)
➔ Off-line commissioning with stable and radioactive samples
ongoing

## Slide 22: NEWGAIN : New GANIL Injector
Existing
NEWGAIN
Main User
beam injector1 (injector2)
intensities 2023 2028 2030
Ions | Intensity (pµA) Phoenix V3 RFQ A/Q≤3 | Intensity (pµA) Phoenix V3 RFQ A/Q≤7 | Intensity (pµA) SC Ion Source RFQ A/Q≤7
18O | 80 | * | 375
19F | >15 | >40 | >40
36Ar | 16 | 70 | 45
40Ar | 3.6 | 70 | 45
36S | 2.3 | * | *
40Ca | 2.9 | 10 | 20
48Ca | 1.2 | 10 | 20
58Ni | 1.1 | 4 | 8
84Kr | 0.1 | 10 | 20
139Xe | 0.001 | 7 | >10
238U | <<0.001 | 0.1 | 6
* -> no estimation
Measured
Estimated
ASTERIC SC ion source
RFQ for heavy ions
World-record intensities
Budget : 25,3 M€
22
Magnet
➔ Fisrt beam with phoenix V3 to S3 in 2029
➔ Fisrt beam with ASTERICS to S3 in 2033

## Slide 23: DESIR Decay, Excitation, Storage of Radioactive Ions
Site inauguration Novembre 2023
Building construction November 2025
First stable beams 2028
First experiments 2028-2029
S3-LEB, SIRIUS
SPIRAL 1 Upgrade
  Fusion-evaporation
  (Multi-)nucleon Transfer
  Beam & target fragmentation
S3-LEB
Beams from SPIRAL1 and S3
Important beam preparation and purification capabilities
High resolution and high precision experiments
Studies of fundamental properties of nuclei:
masses, lifetimes, decay modes, spin, quadrupolar moments…
Nucleosynthesis, Fundamental interactions, study of weak interaction
Scientific aperture
Contribution to ESPPU
23
Budget : 39,5 M€
DESIR workshop March 2026 : 52 Letter of Intents

## Slide 24
Objective: Increase GANIL’s capacity to provide heavy-ion and neutron beams for the irradiation testing of space components and systems from approximately 400 hours to 2,000 hours per year (a factor of 5 increase) by 2030.
 Strengthen and modernize existing capabilities while developing new irradiation facilities.
Key Challenges:
Meet the growing demand for testing services from industry and address the risk of a shortage
of suitable accelerator facilities.
Enhance national competitiveness and sovereignty in the space sector.
Develop long-term strategic partnerships with industry and research institutions.
Increase the international visibility and scientific influence of France in the space domain.
: Space Applications at GANIL Accelerators
SAGA
39M€
2025-2031

## Slide 25: Thank you for your attention

## Slide 26
26